Basic Four Series 2000
Desktop Computer System
bfisd 8079a	Service Manual

BFISD  8079

# TABLE OF CONTENTS

Page

SECTION I      INTRODUCTION

1.1            General ............................................ 1-1

1.2            System Description ................................. 1-1

1.2.1            Central Microprocessor Board (CMB) ............... 1-2

1.2.2            Memory Array Boards .............................. 1-3

1.2.3            Winchester Disk Controller Board ................. 1-4

1.2.4            4-Way Controller Board  .......................... 1-4

1.2.5            Magnetic Cartridge Streamer Controller Board ..... 1-4

1.2.6            Local Area Network Controller Board .............. 1-5

1.3            Specifications ..................................... 1-5

SECTION II     INSTALLATION AND OPERATION

2.1            General ............................................ 2-1

2.2            Unpacking and Inspecting the Base Unit ............. 2-1

2.3            Installing the 2000 Series Computer System ......... 2-1

2.4            Switch Settings, Jumper Placements, Cable

Connections ...................................... 2-7

2.4.1            Central Microprocessor Board ..................... 2-7

2.4.2            Memory Array PCBA ................................ 2-14

2.4.3            Winchester Disk (Single-Board) Controller ........ 2-14

2.4.4            4-Way Controller PCBA ............................ 2-17

2.5            Installing the Local Area Network (LAN) ............ 2-20

2.5.1            Installing the LANG Board ........................ 2-20

2.5.2            Installing the Tap Box ........................... 2-24

2.5.3            Installing the Repeater .......................... 2-25

2.5.3.1            Connecting Network Segments .................... 2-27

2.5.3.2            Connecting A Network Branch .................... 2—27

2.5.3.3            Connecting Power to the Repeater ............... 2-28

2.5.4            Installing the LANG Software ..................... 2-28

2.6            Use and Care of Floppy Diskette and Drive .......... 2-29

2.6.1            Diskette Insertion ............................... 2-29

2.6.2            Write Protection ................................. 2-30

SECTION III    FUNCTIONAL DESCRIPTION

3.1            Introduction  . . . . . . . . . . . . . . . . . . .  3-1

3.2            Central Microprocessor Board (CMB) Description. . .  3-1

3.2.1            Clock Generator . . . . . . . . . . . . . . . . .  3-3

3.2.2            Function Code Decoder . . . . . . . . . . . . . .  3-3

3.2.3            Boot PROM . . . . . . . . . . . . . . . . . . . .  3-4

3.2.4            CMB Diagnostic Hardware . . . . . . . . . . . . .  3-5

3.2.4.1            CMB Status Drivers  . . . . . . . . . . . . . .  3-5

3.2.4.2            CMB Control Register. . . . . . . . . . . . . .  3-5

3.2.5            Main Memory Fault Detection Circuits. . . . . . .  3-6

3.2.5.1            Parity Error Register . . . . . . . . . . . . .  3-8

3.2.5.2            Status Register Parity Bit. . . . . . . . . . .  3-8

3.2.5.3            Parity Error Interrupt Cycle. . . . . . . . . .  3-9

iii

BFISD 8079

TABLE OF CONTENTS (continued)

Page

SECTION III    FUNCTIONAL DESCRIPTION (cont'd)

3.2.6            Interrupt Logic . . . . . . . . . . . . . . . . .  3-9

3.2.6.1            Interrupt Control Logic . . . . . . . . . . . .  3-10

3.2.6.2            Interrupt Acknowledge Decoder . . . . . . . . .  3-11

3.2.7            Reset and Power Fail Detection Logic. . . . . . .  3-11

3.2.8            System I/O Bus Control Logic. . . . . . . . . . .  3-12

3.2.9            Non-Volatile RAM. . . . . . . . . . . . . . . . .  3-12

3.2.10           Data Transfer Acknowledge Generator . . . . . . .  3-14

3.2.10.1           Timing Generation . . . . . . . . . . . . . . .  3-17

3.2.10.2           Timing Selection. . . . . . . . . . . . . . . .  3-17

3.2.10.3           Bus Error Generation. . . . . . . . . . . . . .  3-18

3.2.11           Bus Arbitration Logic . . . . . . . . . . . . . .  3-19

3.2.11.1           Bus Arbitration Cycle . . . . . . . . . . . . .  3-20

3.2.11.2           Fast Bus Grant. . . . . . . . . . . . . . . . .  3-21

3.2.12           Address Space Decoding Logic. . . . . . . . . . .  3-22

3.2.12.1           READ Cycle Decoding . . . . . . . . . . . . . .  3-24

3.2.12.2           WRITE Cycle Decoding. . . . . . . . . . . . . .  3-24

3.2.12.3           Memory Select Decoding. . . . . . . . . . . . .  3-24

3.2.12.4           Local I/O Decoding. . . . . . . . . . . . . . .  3-25

3.2.13           Byte Interface Control Logic. . . . . . . . . . .  3-25

3.2.14           Memory Address Bus. . . . . . . . . . . . . . . .  3-25

3.2.14.1           Memory Array Board Selection. . . . . . . . . .  3-26

3.2.14.2           Memory Array Bus Multiplexing . . . . . . . . .  3-26

3.2.15           Dynamic Memory Support. . . . . . . . . . . . . .  3-27

3.2.15.1           Memory Timing . . . . . . . . . . . . . . . . .  3-28

3.2.15.2           Row Address Strobe. . . . . . . . . . . . . . .  3-28

3.2.15.3           Column Address Strobes. . . . . . . . . . . . .  3-28

3.2.15.4           Memory Refresh. . . . . . . . . . . . . . . . .  3-30

3.2.15.5           Refresh Address and Request Generation. . . . .  3—31

3.2.15.6           Refresh Arbitration . . . . . . . . . . . . . .  3-32

3.2.16           Memory Management Unit. . . . . . . . . . . . . .  3—33

3.2.16.1           Segmentation. . . . . . . . . . . . . . . . . .  3-33

3.2.16.2           Swapping. . . . . . . . . . . . . . . . . . . .  3-34

3.2.16.3           Other MMU Functions . . . . . . . . . . . . . .  3-34

3.2.16.4           Supervisor and User Access of the MMU . . . . .  3-36

3.2.16.5           MMU Address Translation . . . . . . . . . . . .  3-37

3.2.16.6           Segment Attributes. . . . . . . . . . . . . . .  3-38

3.2.16.7           Segment Status. . . . . . . . . . . . . . . . .  3-39

3.2.16.8           MMU Error Generation. . . . . . . . . . . . . .  3-40

3.2.17           Serial Ports. . . . . . . . . . . . . . . . . . .  3-41

3.2.17.1           Serial/Parallel Conversion. . . . . . . . . . .  3-41

3.2.17.2           Communications Protocol Selection . . . . . . .  3-44

3.2.17.3           Electrical Configuration Selection. . . . . . .  3-46

3.2.17.4           Addressing and Control. . . . . . . . . . . . .  3-48

3.2.18           Parallel Port . . . . . . . . . . . . . . . . . .  3-50

3.2.18.1           Addressing and Control. . . . . . . . . . . . .  3-50

3.2.18.2           Data Transmission to a Printer. . . . . . . . .  3-51

3.2.19           Floppy Disk Controller. . . . . . . . . . . . . .  3-51

3.2.19.1           Soft Sectoring. . . . . . . . . . . . . . . . .  3-51

3.2.19.2           Double-Density Recording. . . . . . . . . . . .  3-55

iv

BFISD 8079

TABLE OF CONTENTS (continued)

Page

SECTION III    FUNCTIONAL DESCRIPTION (cont'd)

3.2.19.3           MFM Data Separation . . . . . . . . . . . . . .  3-57

3.2.19.4           Bit-Shifting. . . . . . . . . . . . . . . . . .  3-61

3.2.19.5           Floppy Drive Disk Control . . . . . . . . . . .  3-63

3.2.19.6           Buffered Data Transfer. . . . . . . . . . . . .  3-66

3.2.19.7           Floppy Disk Controller Section Control. . . . .  3-70

3.3            Memory Array Board Functional Description . . . . .  3—72

3.4            Base Unit Power Supply Functional Description . . .  3-72

SECTION IV

4.1            Introduction. . . . . . . . . . . . . . . . . . . .  4-1

4.2            Special Tools . . . . . . . . . . . . . . . . . . .  4-1

4.3            Preventative Maintenance. . . . . . . . . . . . . .  4-1

4.4            Trouble Analysis. . . . . . . . . . . . . . . . . .  4-2

SECTION V      REMOVAL/REPLACEMENT

5.1            Introduction. . . . . . . . . . . . . . . . . . . .  5-1

5.2            Replacing the Central Microprocessor Board (CMB). .  5-1

5.3            Replacing the Base Unit Power Supply. . . . . . . .  5-9

5.4            Replacing the Memory Array Modules. . . . . . . . .  5-11

5.5            Replacing the 4-Way Controller Boards . . . . . . .  5-14

5.6            Replacing the Winchester Drive Controller (WDC)

Board . . . . . . . . . . . . . . . . . . . . . .  5-17

5.7            Replacing the Magnetic Cartridge Streamer

Controller (MCSC) Board . . . . . . . . . . . . .  5-18

5.8            Replacing the Winchester Drive Controller Bus

Adapter Board . . . . . . . . . . . . . . . . . .  5-22

5.9            Replacing the Local Area Network (LAN) Board. . . .  5-23

5.10           Replacing the Winchester Drive. . . . . . . . . . .  5-26

5.11           Replacing the Floppy Disk Drive . . . . . . . . . .  5-27

SECTION VI     ILLUSTRATED PARTS LIST

6.1            Introduction. . . . . . . . . . . . . . . . . . . .  6-1

6.2            Index of Assemblies . . . . . . . . . . . . . . . .  6-1

SECTION VII    5.25" FLOPPY DISK DRIVE

7.1            Introduction. . . . . . . . . . . . . . . . . . . .  7-1

7.1.1            General Description . . . . . . . . . . . . . . .  7-1

7.1.1.1            Spindle Mechanism . . . . . . . . . . . . . . .  7-1

7.1.1.2            Positioning Mechanism . . . . . . . . . . . . .  7-1

7.1.1.3            Head Load/Interlock Mechanism . . . . . . . . .  7-2

7.1.2            Functional Concepts . . . . . . . . . . . . . . .  7-2

v

BFISD 8079

TABLE OF CONTENTS (continued)

Page

SECTION  VII     5.25" FLOPPY DISK DRIVE  (cont'd)

7.1.2.1            Stepper Motor Control . . . . . . . . . . . . .  7-5

7.1.2.2            Drive Motor Control . . . . . . . . . . . . . .  7-6

7.1.2.3            Head Load Circuit . . . . . . . . . . . . . . .  7-6

7.1.2.4            Motion Check LED. . . . . . . . . . . . . . . .  7-6

7.1.2.5            Track 00 Detection. . . . . . . . . . . . . . .  7-6

7.1.2.6            Write Protect Detector. . . . . . . . . . . . .  7-7

7.1.2.7            Index Detector. . . . . . . . . . . . . . . . .  7-7

7.1.2.8            Ready Detector. . . . . . . . . . . . . . . . .  7-9

7.1.2.9            Read/Write Heads. . . . . . . . . . . . . . . .  7-10

7.1.2.10           Write Circuit . . . . . . . . . . . . . . . . .  7-11

7.1.2.11           Read Circuit. . . . . . . . . . . . . . . . . .  7-12

7.1.2.12           Read/Write Select Circuit . . . . . . . . . . .  7-12

7.1.2.13           Read Amplifier Circuit and Filter Work. . . . .  7-13

7.1.2.14           Active Differential Circuit and Comparator  . .  7-13

7.1.2.15           Timed Main Filter and Crossover Detector  . . .  7-14

7.1.2.16           DC Control Circuit. . . . . . . . . . . . . . .  7-17

7.1.2.17           Power-On Reset Circuit. . . . . . . . . . . . .  7-17

7.1.3            Equipment Specifications. . . . . . . . . . . . .  7-17

7.2            Installation and Maintenance. . . . . . . . . . . .  7-20

7.2.2            Equipment Placement . . . . . . . . . . . . . . .  7-20

7.2.3            Electrical Installation . . . . . . . . . . . . .  7-20

7.2.4            Adjustment Procedures . . . . . . . . . . . . . .  7-20

7.2.4.1            Index Burst Position Adjustment . . . . . . . .  7-21

7.2.4.2            Track Position Adjustment . . . . . . . . . . .  7-21

7.2.4.3            Track 00 Position Adjustment. . . . . . . . . .  7-22

7.2.4.4            Rotation Adjustment . . . . . . . . . . . . . .  7-23

7.2.4.5            0-1 Head Gap Adjustment . . . . . . . . . . . .  7-23

7.3            Reference Information . . . . . . . . . . . . . . .  7-24

7.3.1            Interface . . . . . . . . . . . . . . . . . . . .  7-24

7.3.1.1            Signal Interface. . . . . . . . . . . . . . . .  7-24

7.3.1.2            Input Lines . . . . . . . . . . . . . . . . . .  7-25

7.3.1.3            Output Lines. . . . . . . . . . . . . . . . . .  7-27

7.3.2            Jumper Pin. . . . . . . . . . . . . . . . . . . .  7-28

SECTION VIII   20 MEGABYTE WINCHESTER DRIVE SYSTEM

8.1            Introduction. . . . . . . . . . . . . . . . . . . .  8-1

8.1.1            General Description . . . . . . . . . . . . . . .  8-1

8.1.2            Functional Concepts . . . . . . . . . . . . . . .  8-4

8.1.3            Equipment Specifications. . . . . . . . . . . . .  8-5

8.2            Installation and Operation. . . . . . . . . . . . .  8-8

8.2.1            Unpacking. . . . . . . . . . . . . . . . . . . . .  8-8

8.2.2            Equipment Placement. . . . . . . . . . . . . . . .  8-8

8.2.3            Shipping Lock (Read/Write Heads) . . . . . . . . .  8-8

8.2.4            Step Rate Selection. . . . . . . . . . . . . . . .  8-8

8.2.5            System Installation. . . . . . . . . . . . . . . .  8-9

8.2.6            Operation. . . . . . . . . . . . . . . . . . . . .  8-9

8.3            Functional Description . . . . . . . . . . . . . . .  8-11

vi

BFISD 8079

TABLE OF CONTENTS (continued)

Page

SECTION VIII    20 MEGABYTE WINCHESTER DRIVE SYSTEM (cont'd)

8.3.1            Basic Disk Principles  . . . . . . . . . . . . . .  8-11

8.3.2            Control Lines. . . . . . . . . . . . . . . . . . .  8-13

8.3.3            Winchester Drive  Controller . . . . . . . . . . .  8-14

8.3.3.1            Signal Definitions   . . . . . . . . . . . . . .  8-16

8.3.3.2            Detailed Description (Handshaking and Timing)  .  8-19

8.3.3.3            Programming Information  . . . . . . . . . . . .  8-21

8.3.3.4            Command  . . . . . . . . . . . . . . . . . . . .  8-22

8.4            Maintenance  . . . . . . . . . . . . . . . . . . . .  8-44

8.4.1            Diagnostics  . . . . . . . . . . . . . . . . . . .  8-44

8.4.1.1            Power-Up Diagnostics . . . . . . . . . . . . . .  8-44

8.4.1.2            Operational  Error Check . . . . . . . . . . . .  8-46

8.4.1.3            Fault Diagnostics  . . . . . . . . . . . . . . .  8-46

8.5            Removal and Replacement Procedures . . . . . . . . .  8-48

8.5.1            Master Electronics PCBA Removal and Replacement  .  8-48

8.5.2            Brack Removal and Replacement. . . . . . . . . . .  8-51

8.5.3            Motor Control PCBA Removal and Replacement . . . .  8-52

8.5.4            Preamplifier PCBA Removal and Replacement. . . . .  8-52

8.6            Parts List . . . . . . . . . . . . . . . . . . . . .  8-52

SECTION IX     50 MEGABYTE WINCHESTER DRIVE SYSTEM

9.1            Introduction . . . . . . . . . . . . . . . . . . . .  9-1

9.1.1            General Description  . . . . . . . . . . . . . . .  9-1

9.1.2            Functional Concepts  . . . . . . . . . . . . . . .  9-2

9.1.3            Equipment Specifications . . . . . . . . . . . . .  9-3

9.2            Installation and Operation . . . . . . . . . . . . .  9-6

9.2.1            Unpacking  . . . . . . . . . . . . . . . . . . . .  9-6

9.2.2            Equipment Placement  . . . . . . . . . . . . . . .  9—6

9.2.3            Shipping Lock  (Read/Write Heads)  . . . . . . . .  9-6

9.2.4            System Installation  . . . . . . . . . . . . . . .  9-6

9.2.5            Power and Interface Cables  and Connectors . . . .  9-7

9.2.6            Drive Addressing  and  Interface Termination . . .  9-7

9.2.7            Installation of the Winchester Drive and the

WDC PCBA . . . . . . . . . . . . . . . . . . . .  9-10

9.2.8            Operation  . . . . . . . . . . . . . . . . . . . .  9-13

9.3            Functional Description . . . . . . . . . . . . . . .  9-14

9.3.1            Basic Disk Principles  . . . . . . . . . . . . . .  9-14

9.3.2            Control Lines  . . . . . . . . . . . . . . . . . .  9-16

9.3.3            Winchester Drive Controller  . . . . . . . . . . .  9-18

9.3.3.1            Signal Definitions . . . . . . . . . . . . . . .  9-19

9.3.3.2            Detailed Description (Handshaking and Timing)  .  9-22

9.3.3.3            Programming  Information . . . . . . . . . . . .  9—24

9.3.3.4            Commands . . . . . . . . . . . . . . . . . . . .  9-25

SECTION X      SCHEMATICS

vii/viii

BFISD 8079

# LIST OF ILLUSTRATIONS

Figure                                                               Page

1-1            Model 4108 Base Unit. . . . . . . . . . . . . . . .   xvi

1-2            Block Diagram of the Base Unit Hardware System. . .   1-2

1-3            The Layout of the Central Microprocessor Board. . .   1-3

2-1            Rear View of Base Unit, Showing Location of all

Connectors  . . . . . . . . . . . . . . . . . . .   2-5

2-2            Location of Jumpers on Central Microprocessor

Board . . . . . . . . . . . . . . . . . . . . . .   2-8

2-3            Central Microprocessor Board Cable Part Numbers . .   2-9

2-4            Location of Address Switches on Memory Array

Module. . . . . . . . . . . . . . . . . . . . . .   2-15

2-5            Location of Jumpers on (Single-Board) Winchester

Disk Controller . . . . . . . . . . . . . . . . .   2-16

2-6            Location of Switches on 4-Way Controller PCBA . . .   2-18

2-7            Location of Switch on Magnetic Cartridge

Streamer Controller PCBA. . . . . . . . . . . . .   2-19

2-8            Location of Switches and Cable Information for

LANG PCBA . . . . . . . . . . . . . . . . . . . .   2-21

2-9            Outline of Tap Box, Showing Screw Connections . . .   2-24

2-10           Outline of Repeater Unit, Showing Screw

Connections . . . . . . . . . . . . . . . . . . .   2-26

3-1            Simplified Block Diagram, Central Microprocessor

Board . . . . . . . . . . . . . . . . . . . . . .   3-2

3-2            Timing Diagram, PDTACK- and Bus Error Generation. .   3-19

3-3            Address Space Decoding Logic. . . . . . . . . . . .   3-23

3-4            Timing Relationships for the Signals of a Dynamic

RAM Chip. . . . . . . . . . . . . . . . . . . . .   3-27

3-5            Simplified Block Diagram, Dynamic Memory Support

Subsystem . . . . . . . . . . . . . . . . . . . .   3-29

3-6            Memory Control Timing Diagram . . . . . . . . . . .   3-31

3-7            Refresh Timing Diagram. . . . . . . . . . . . . . .   3-33

3-8            Simplified Block Diagram, Memory Management Unit. .   3—35

3-9            Logical Block Diagram, MMU Status Reporting/Error

Detection . . . . . . . . . . . . . . . . . . . .   3-36

3-10           Simplified Block Diagram, CMS Serial Ports. . . . .   3-42

3-11           Simplified Block Diagram, 8530 SCC Chip . . . . . .   3-43

3-12           Simplified Block Diagram, CMB Floppy Disk

Controller. . . . . . . . . . . . . . . . . . . .   3-54

3-13           Signal Encoding and Derived Clock, Kansas City

Standard. . . . . . . . . . . . . . . . . . . . .   3-55

3-14           Maximum Data Rate Recording, Kansas City Standard .   3-56

3-15           Encoded Data for FM Recording...........3-57

3-16           Encoded Data for Modified FM (MFM) Recording. . . .   3-58

3-17           Simplified Block Diagram, Data Separator Phase

Detector Logic. . . . . . . . . . . . . . . . . .   3-59

3-18           Bit Shifting. . . . . . . . . . . . . . . . . . . .   3-61

3-19           Register Layout, WD1793 Floppy Disk Controller Chip   3-64

ix

BFISD 8079

LIST OF ILLUSTRATIONS (continued)

Figure                                                              Page

5—1            Location of Jumpers on Central Microprocessor

Board . . . . . . . . . . . . . . . . . . . . . .  5-3

5-2            Central Microprocessor Board Cable Part Numbers . .  5-4

5-3            Location of Address Switches on Memory Array

Module. . . . . . . . . . . . . . . . . . . . . .  5-13

5-4            Location of Switches on 4-Way Controller PCBA . . .  5-16

5-5            Location of Jumpers on the Winchester Drive

Controller PCBA . . . . . . . . . . . . . . . . .  5-19

5-6            Location of Switch on Magnetic Cartridge Streamer

Controller PCBA . . . . . . . . . . . . . . . . .  5-21

5-7            Location of Switches on Local Area Network

Controller PCBA . . . . . . . . . . . . . . . . .  5-24

6-1            CMB PCBA  . . . . . . . . . . . . . . . . . . . . .  6-2

6-2            Memory Array PCBA . . . . . . . . . . . . . . . . .  6-8

6-3            WDC Bus Adapter PCBA. . . . . . . . . . . . . . . .  6-10

6-4            4-Way Controller PCBA . . . . . . . . . . . . . . .  6-14

6-5            MTCS Controller PCBA. . . . . . . . . . . . . . . .  6-18

6-6            LAN Controller PCBA . . . . . . . . . . . . . . . .  6-22

7-1            Spindle Mechanism . . . . . . . . . . . . . . . . .  7-2

7-2            Positioning Mechanism . . . . . . . . . . . . . . .  7-3

7-3            Head Load/Interlock Mechanism . . . . . . . . . . .  7-3

7-4            Functional Block Diagram  . . . . . . . . . . . . .  7-4

7-5            Stepper Motor Control Circuit Block Diagram . . . .  7-5

7-6            Stepper Motor Timing Diagram (48 TPI) . . . . . . .  7-5

7-7            Stepper Motor Timing Diagram (96 TPI) . . . . . . .  7-5

7-8            Stepper Motor Phase Transfer Chart  . . . . . . . .  7-6

7-9            Head Load Circuit . . . . . . . . . . . . . . . . .  7-7

7-10           Head Load Timing Diagram  . . . . . . . . . . . . .  7-7

7-11           Track 00 Detection Circuit  . . . . . . . . . . . .  7-8

7-12           Track 00 Timing Diagram (48 TPI)  . . . . . . . . .  7-8

7-13           Track 00 Timing Diagram (96 TPI)  . . . . . . . . .  7-8

7-14           Write Protect Detector Circuit  . . . . . . . . . .  7-9

7-15           Index Detection Circuit . . . . . . . . . . . . . .  7-9

7-16           Ready Detector Timing Diagram . . . . . . . . . . .  7-10

7-17           Read/Write Head Connection  . . . . . . . . . . . .  7-10

7-18           Write Start Timing Diagram  . . . . . . . . . . . .  7-10

7-19           Write Circuit Block Diagram . . . . . . . . . . . .  7-11

7-20           Write Timing Diagram (FM) . . . . . . . . . . . . .  7-11

7-21           Simplified Erase Delay Circuit  . . . . . . . . . .  7-12

7-22           Erase Delay Timing Diagram  . . . . . . . . . . . .  7-12

7-23           Read Circuit Block Diagram  . . . . . . . . . . . .  7-13

7-24           Read Start Timing Diagram . . . . . . . . . . . . .  7-13

7-25           Read/Write Select Circuit . . . . . . . . . . . . .  7-14

7-26           Read Amplifier Circuit and Filter Network . . . . .  7-14

7-27           Active Differential Circuit and Comparator  . . . .  7-15

7-28           Timed Main Filter and Crossover Detector  . . . . .  7-15

x

BFISD 8079

LIST OF ILLUSTRATIONS (continued)

Figure                                                              Page

7-29           Read Timing Diagram . . . . . . . . . . . . . . . .  7-16

7-30           DC Control Circuit  . . . . . . . . . . . . . . . .  7-16

7-31           Power-On Reset Circuit  . . . . . . . . . . . . . .  7-17

7-32           Power-On Reset Timing Diagram . . . . . . . . . . .  7-17

7-33           Signal Interface Lines  . . . . . . . . . . . . . .  7-26

7-34           WRITE DATA Timing (FM). . . . . . . . . . . . . . .  7-27

7-35           Index Timing  . . . . . . . . . . . . . . . . . . .  7-27

7-36           READ DATA (FM)  . . . . . . . . . . . . . . . . . .  7-28

7-37           Factory Arrangement of Jumper . . . . . . . . . . .  7-29

7-38           Drive Timing Diagram  . . . . . . . . . . . . . . .  7-30

8-1            Major Component Location  . . . . . . . . . . . . .  8-1

8-2            Head Disk Assembly  . . . . . . . . . . . . . . . .  8-3

8-3            Simplified Block Diagram  . . . . . . . . . . . . .  8-4

8-4            Winchester Drive Block Diagram  . . . . . . . . . .  8-12

8-5            Surface and Head Geometry . . . . . . . . . . . . .  8-12

8-6            Controller, Functional Organization . . . . . . . .  8-15

8-7            Winchester Drive Controller Select Timing . . . . .  8-19

8-8            Data Transfer to Host, Timing . . . . . . . . . . .  8-20

8-9            Data Transfer from Host, Timing . . . . . . . . . .  8-21

8-10           Device Control Block (DCB) Format . . . . . . . . .  8-22

8-11           Completion Status Bytes . . . . . . . . . . . . . .  8-23

8-12           Winchester Drive Assembly . . . . . . . . . . . . .  8-49

8-13           Head Disk Disassembly . . . . . . . . . . . . . . .  8-50

9-1            Simplified Block Diagram  . . . . . . . . . . . . .  9-1

9-2            Power and Interface Connections . . . . . . . . . .  9-7

9-3            Drive Address Jumpers and Interface Terminator  . .  9-10

9-4            Location of Jumpers on the Winchester Drive

Controller PCBA . . . . . . . . . . . . . . . . .  9-12

9-5            Winchester Drive Block Diagram  . . . . . . . . . .  9-15

9-6            Surface and Head Geometry . . . . . . . . . . . . .  9-15

9-7            Head Selection Timing . . . . . . . . . . . . . . .  9-17

9-8            Index Timing  . . . . . . . . . . . . . . . . . . .  9-17

9-9            Controller, Functional Organization . . . . . . . .  9-18

9-10           Winchester Drive Controller Select Timing . . . . .  9-22

9-11           Data Transfer to Host, Timing . . . . . . . . . . .  9-23

9-12           Data Transfer from Host, Timing . . . . . . . . . .  9-24

10-1           PCBA, Central Microprocessor Board  . . . . . . . .  10-2

10-2           Logic Diagram, Central Microprocessor Board . . . .  10-3

xi/xii

BFISD 8079

# LIST OF TABLES

Table                                                                Page

1-1             Specifications, MAI 2000 Series Desktop Computer

System . . . . . . . . . . . . . . . . . . . . . .  1-5

2-1             CMB Jumper Configuration. . . . . . . . . . . . . .  2-13

2-2             Memory Array Module Address Switch Settings . . . .  2-14

2-3             Winchester Disk Controller Jumper Connections . . .  2-14

2-4             4-Way Controller PCBA Switch Settings . . . . . . .  2-17

4-1             Preventive Maintenance Summary. . . . . . . . . . .  4-1

4-2             Base Unit Power Supply Voltage Adjustments. . . . .  4-2

3-1             Central Microprocessor Board Status Bits. . . . . .  3-6

3-2             Central Microprocessor Board Control Register Bits.  3-7

3-3             NVRAM Contents. . . . . . . . . . . . . . . . . . .  3-15

3-4             Device Nybble Specifiers. . . . . . . . . . . . . .  3-16

3-5             Address Space Decoding. . . . . . . . . . . . . . .  3-22

3-6             Serial Ports Electrical Configuration Jumper

Connections . . . . . . . . . . . . . . . . . . . .  3-47

3-7             Bit Patterns for Serial Ports Configuration and

Data Rate Selection . . . . . . . . . . . . . . . .  3-49

3-8             Parallel Port  (J13)  Connector Signals . . . . . .  3-52

3-9             Centronics Protocol . . . . . . . . . . . . . . . .  3-53

3-10            Command List, WD1793 Floppy Disk Controller Chip. .  3-65

3-11            State Machine States. . . . . . . . . . . . . . . .  3-69

5-1             CMB Jumper Configuration. . . . . . . . . . . . . .  5-8

5-2             Memory Array Module Address Switch Settings . . . .  5-12

5-3             4-Way Controller PCBA Switch Settings . . . . . . .  5-15

6-1             CMB PCBA (P/N 903441-001) Parts List  . . . . . . .  6-3

6-2             Memory Array PCBA (P/N 903368-001) Parts List . . .  6-9

6-3             WDC Bus Adapter PCBA (P/N 903439-001) Parts List. .  6-11

6-4             4-Way Controller PCBA (P/N 903390-001) Parts List .  6-15

6-5             MTCS Controller PCBA (P/N 903406-001) Parts List. .  6-19

6-6             LAN Controller PCBA (P/N 903405-001) Parts List . .  6-23

7-1             Specifications  . . . . . . . . . . . . . . . . . .  7-18

8-1             Specifications  . . . . . . . . . . . . . . . . . .  8-5

8-2             Power Requirements  . . . . . . . . . . . . . . . .  8-9

8-3             Diagnostic and Failure Code  Indicators . . . . . .  8-10

8-4             Head Selet Decode Matrix  . . . . . . . . . . . . .  8-14

8-5             SASI Bus Status Signals . . . . . . . . . . . . . .  8-17

8-6             Summary of SASI Bus Status Signals  . . . . . . . .  8-17

8-7             Controller - Host Handshaking . . . . . . . . . . .  8-17

8-8             Host Bus Control Signals  . . . . . . . . . . . . .  8-18

8-9             Host Bus Data Signals . . . . . . . . . . . . . . .  8-18

8-10            Type 0 Error Codes, Disk Drive  . . . . . . . . . .  8-26

xiii

BFISD 8079

LIST OF TABLES (continued)

Table                                                               Page

8-11           Type 1 Error Codes, Controller  . . . . . . . . . .  8-26

8-12           Type 2 Error Codes, Command and Miscellaneous . . .  8-27

8-13           Request Sense Status Error Codes  . . . . . . . . .  8-27

8-14           Power-Up Sequence Error Codes . . . . . . . . . . .  8-45

8-15           Operational Error Codes . . . . . . . . . . . . . .  8-46

8-16           Fault Diagnostics . . . . . . . . . . . . . . . . .  8-47

8-17           Parts List  . . . . . . . . . . . . . . . . . . . .  8-52

9-1            Specifications  . . . . . . . . . . . . . . . . . .  9-3

9-2            Control Signal Connector J1 Pin Assignments . . . .  9-8

9-3            Data Transfer Connector J2 Pin Assignments  . . . .  9-9

9-4            DC Power Connector J3 Pin Assignments . . . . . . .  9-9

9-5            Power Requirements  . . . . . . . . . . . . . . . .  9-13

9-6            Head Select Decode Matrix . . . . . . . . . . . . .  9-17

9-7            SASI Bus Status Signals . . . . . . . . . . . . . .  9-20

9-8            Summary of SASI Bus Status Signals  . . . . . . . .  9-20

9-9            Controller - Host Handshaking . . . . . . . . . . .  9-20

9-10           Host Bus Control Signals  . . . . . . . . . . . . .  9-21

9-11           Host Bus Data Signals . . . . . . . . . . . . . . .  9-21

9-12           Type 0 Error Codes, Disk Drive  . . . . . . . . . .  9-29

9-13           Type 1 Error Codes, Controller  . . . . . . . . . .  9-29

9-14           Type 2 Error Codes, Command and Miscellaneous . . .  9-30

9-15           Request Sense Status Error Codes  . . . . . . . . .  9-30

9-16           Mode Select Parameter List  . . . . . . . . . . . .  9-36

9-17           Extent Descriptor List  . . . . . . . . . . . . . .  9-37

9-18           Drive Parameter List  . . . . . . . . . . . . . . .  9-37

9-19           Search Command Argument . . . . . . . . . . . . . .  9-46

9-20           Search Command Argument Required Data . . . . . . .  9-47

xiv

BFISD 8079

# PREFACE

This manual provides service information for the Model 4108 Base Unit, used in the MAI® 2000 Series Desktop Computer System.  The information is presented as an aid for field service personnel and supports the installation, operation and maintenance of each device contained in the Base Unit.

The major topics covered in this manual are:

Section I    Introduction

Section II   Installation and Operation

Section III  Functional Description

Section IV   Maintenance

Section V    Removal/Replacement

Section VI   Illustrated Parts List

Section VII  Floppy Disk Drive

Section VIII 20 Megabyte Winchester Drive System

Section IX   50 Megabyte Winchester Drive System

Section X    Schematics

NOTICE

MAI/Basic Four equipment is designed to meet the safety

requirements of Underwriters Laboratories (UL) and the

emission requirements of the Federal Communications

Commission (FCC) and Verbandes Deutscher Elektrotechniker

(VDE) as well as certain other applicable safety or

regulatory agencies.

Compliance requires the use of specific interconnecting

cables that have been determined to meet the applicable

criteria.  Use of cables not meeting these requirements

could result in violations of local building codes and

regulations, with resulting damages.

MAI/Basic Four shall have no responsibility for any results

whatsoever that flow from any use of any cables other than

those supplied or installed by MAI/Basic Four Information

Systems or our authorized representatives.

xv

BFISD 8079

Figure  1-1.  Model 4108 Base Unit

xvi

BFISD 8079

SECTION I

# INTRODUCTION

## 1.1  GENERAL

The MAI® 2000 Series Desktop Computer System is a general purpose, multi-user, multitasking, 16-bit microcomputer system.  The minimal system comprises a Base Unit (figure 1-1) and a video display terminal (VDT).

Device controller boards are available that plug into a Central Microprocessor Board, inside the Base Unit.  A full complement of these boards (4) can support a magnetic cartridge streamer and 12 additional VDTs or serial printers. Also available is the Local Area Network Controller board, giving the system a LAN capability, based on CORVUS-licensed OMNINET.  A maximum of six plug-in memory array boards provides 1.5 megabytes of system (main) memory.

## 1.2  SYSTEM DESCRIPTION

The configuration of the MAI 2000 Series Desktop Computer System is defined by the architecture of the Model 4108 Base Unit.  Hence the following discussion focuses on Base Unit components and on the optional  plug-in printed circuit boards.  The Base Unit contains a central processing unit (CPU) that embraces the integrated bus,  single board concept (the  Central Microprocessor Board).

Residing on the Central Microprocessor Board are two serial ports, a parallel port and a floppy disk controller.  All subunits either are located on or plug into the Central Microprocessor Board. Figure 1-2 is a block diagram of the Base Unit hardware system.  The minimal, or "entry level," Base Unit consists of no less than the following components:

•   A Base Unit power supply module

•   A Central Microprocessor Board (CMB)

•   Three (plug-in) main Memory Array boards

•   One 20 MB hard disk (Winchester) drive, with a controller board

•   One floppy diskette drive or one tape streamer controller board

The Base Unit provides an inherent capability of supporting a second hard disk drive (unless a floppy diskette drive is present); another  VDT (or a serial printer); and one parallel printer.  Additional I/O (input/output) options are printed circuit boards that plug into the Central Microprocessor Board (or plug into a previously-installed I/O printed circuit board).  These include 4-Way Controller boards (paragraph 1.2.4), a Magnetic (tape) Cartridge Streamer (MCS) Controller board (paragraph 1.2.5), and a Local Area Network Controller (LANC) board (paragraph 1.2.6).  Three additional memory array boards may be plugged into the existing memory stack (Paragraph 1.2.2).

1-1

BFISD 8079

Figure  1-2. Block Diagram of the Base Unit Hardware System.

1.2.1  Central Microprocessor Board (CMB)

The CMB logic comprises three major functional areas: (1) the central processor section, (2) the memory control section and (3) the I/O section. The sections are linked primarily by the system bus structure. Figure 1-3 shows the layout of the Central Microprocessor Board, with additional subareas indicated. The central processor section is designed about the high-performance Motorola 68010 microprocessor chip, running at a clock rate of 8 MHz.  The 68010 chip has a 32-bit internal architecture and a large, uniform memory address space. Other features include three major data sizes (byte, word, long word), supervisor and user states, and many flexible addressing options.  The central processor sec-tion also includes the local I/O bus and the boot/diagnostic PROMs (program-mable read-only memory).

A memory management unit (MMU) partitions the user portion of main memory into eight variable-length segments (per user).  The MMU also controls the swapping of these segments to and from main memory and provides address translation, protection, sharing and memory allocation.  Memory timing, address buffers and parity generation/checking logic also is part of the memory control section.

Onboard logic and controller can support two floppy diskette drives.  Both drives are mounted inside the Base Unit.  The driven diskette is 5.25 inches, soft-sectored, double-sided and double-density.

1-2

BFISD 8079

Figure  1-3. The Layout of the Central Microprocessor Board.

For an entry-level system, external peripherals are provided for by two serial (RS-232) connectors and one parallel connector.  Logic and controllers for these are located on the GMB.  The parallel connector allows attachment of the MAI/Basic Four® Model 4201 150/300 lines-per-minute parallel printer, or any similar plug-compatible printer with the Centronics interface.  The two EIA RS-232C (25-pin) serial ports will accommodate two industry-standard terminals or one terminal and one serial printer.

1.2.2  Memory Array Boards

The Memory Array boards contain the active elements (i.e., RAM chips and signal buffers) that make up the main (system) memory.  The array itself consists of industry standard 64K X 1 dynamic RAM chips.  Each board provides 256K bytes arranged as 128K words, plus byte parity.  Hence, the array contains 36 RAM chips.  These boards are physically stacked on the CMB, and a maximum of six boards may be installed.  Each array is plugged into the board below it.  A full stack of six 256K Memory Array boards provides 1.5M bytes of main memory.

Address space assignment of each Memory Array board is made by DIP switch se-lection.  The Memory Array board responds to any contiguous set of addresses starting on a 256K byte boundary.  At least three 256K byte Memory Array boards are required per Base Unit.

1-3

BFISD 8079

1.2.3 Winchester Disk Controller Board

The Winchester Disk Controller (WDC) board supports one or two Winchester (hard disk) drives, both residing in the Base Unit.  (Two drives are possible only in the absence of floppy disk drives.)  The WDC board, via its bus adapter, pro-vides high performance DMA (direct memory access) to the system memory.  The board is compatible with the many Winchester drives that conform to the Seagate Technology ST506 interface.  No more than two Winchester drives may be used with a single Base Unit; therefore, no more than one WDC board is ever needed.

The WDC board is piggy-backed to a WDC Bus Adapter board, and the combination plugs into either the Central Microprocessor Board or any previously-installed device controller board (stacked),  so long as the WDC board is at the top.

1.2.4  4-Way Controller Board

The 4-Way Controller board provides four additional serial ports for each 4-Way Controller board installed in the Base Unit.  This allows the user to add more display terminals and serial printers to the system.  In special circumstances up to 14 terminals/printers may be attached to one system.  However, system performance is specified for no more than eight terminals active simultaneously (two 4-Way Controller boards installed).

The 4-Way Controller ports conform to the primary subset of the EIA standard full duplex RS-232C interface via 9-pin D connectors, located on the 4-Way Controller board.  Modem capabilities are provided for remote terminal support.

The 4-Way Controller also supports eight-bit character transmission.

The 4-Way Controller board is intelligent (Z-80 based).  Transmission of data from the Central Microprocessor Board to the 4-Way Controller board is by di-rect memory access (DMA) of 16-bit (word-wide) memory locations. Transmission is through data packets and command blocks.  Reception of data by the Central Microprocessor Board from the 4-Way Controller board is buffered, program controlled and interrupt driven. Such parameters as stop bits, baud rate and parity are software programmable. Baud rates of up to 19.2K bits/second are allowable.

A partial set of the 4-Way Controller ports may be used to allow incremental growth of the system; remaining ports may go unused and will not affect the op-eration of the system.  The 4-Way Controller board plugs into either the Cen-tral Microprocessor Board or any previously-installed 4-Way Controller board (stacked).

1.2.5  Magnetic Cartridge Streamer Controller Board

The Magnetic Cartridge Streamer Controller (MCS) board will support a single, high speed, 1/4-inch magnetic cartridge streamer drive.  The drive itself is located external to the Base Unit.  A single cable connects the drive to the MCS board at the outside rear of the Base Unit. The MCS board is intelligent (Z80 based) and uses high performance direct memory access (DMA) to the system memory, on the Central Microprocessor Board, in the Base Unit.

1-4

BFISD 8079

Only one drive per Base Unit is ever required; therefore, no more than one MCS board is ever necessary.  The MCS board plugs into either the Central Micro-processor Board or any device controller board that may be present (stacked), but above the 4-Way Controller boards. (Note: information on the 1/4-inch MCS drive is contained in a separate service manual.)

1.2.6  Local Area Network Controller Board

The Local Area Network Controller (LANC) board allows the creation of a local area network (LAN) or, where possible, allows connection of the MAI 2000 Series Computer System to an existing network.  The LANC board is a single-channel communications controller, providing an interface to CORVUS-licensed OMNINET.

The LANC provides bit-serial data communication to other local subsystems as well (such as a file server, disk server, printer and workstations).  Up to 63 subsystems (nodes) can be connected via the LAN.  Each subsystem follows the Carrier Sense Multiple Access/Collision Avoidance(CSMA/CA) protocol when it is accessing the network.

The bit transfer rate on the network cable is 1M bits/sec when the cable is properly terminated.  No more than one LANC board per system may be installed.

The LANC board is plugged into either the Central Microprocessor Board or any previously-installed device controller board (stacked), but always immediately below the WDC Bus Adapter board.

## 1.3  SPECIFICATIONS

Specifications for the MAI 2000 Series Computer System are listed in table 1-1.

Table 1-1.  Specifications, MAI 2000 Series Desktop Computer System

PARAMETERS                             CHARACTERISTICS

PHYSICAL

Base Unit

Height                           6.1 inches (15.5 cm)

Width                            23.65 inches (60.1 cm)

Depth                            14.5 inches (36.8 cm)

Weight                           35 pounds (15.87 kg)

POWER SOURCE REQUIREMENTS

Line Voltage                       100-120 VAC range (108.5 VAC nominal) or

220-240 VAC range (225.5 VAC nominal)

Steady State Input Power           Less than 390 watts, maximum

1-5

BFISD 8079

Table 1-1.  Specifications, MAI 2000 Series Desktop Computer System (continued)

PARAMETERS                             CHARACTERISTICS

Input Surge Current                Less than 35 amperes , maximum peak

Frequency                          50 or 60 hertz

LINE FUSE

100-120 VAC                        6A, "Normal-Bio"

220-240 VAC                        3A, "Normal-Bio"

POWER SUPPLY OUTPUTS

Voltage                            +5.000 and +12.000 VDC (nominal)

Current                            20A @ +5 VDC (nominal); 0.3A @ -5VDC

(nominal); 2.9A @ +12 VDC (nominal);

0.4A @ -12 VDC (nominal)

ENVIRONMENTAL

Operating:

Temperature                      50°F to 98.4°F (10°C to 38°C)

Relative Humidity                20% to 80%, non-condensing

Altitude                         Sea level to 10,000 feet

Storage:

Temperature                      -50°F to 122°F (-10°C to 50°C)

Relative Humidity                10% to 90%, non-condensing

Altitude                         Sea level to 10,000 feet

OPERATIONAL

Microprocessor Unit                Motorola 68010 (16/32-bit @ 8 MHz)

Floppy Disk Drives                 One or two 5 1/4-inch, double-sided ,

double-density diskette drives (two

drives may be installed only in  the

absence of a second  hard disk drive).

Storage capacity: 640K bytes

1-6

BFISD 8079

Table 1-1.  Specifications, MAI 2000 Series Desktop Computer System (continued)

PARAMETERS                             CHARACTERISTICS

Winchester Disk Drives             One or two 5 1/4-inch, non-removable

hard disks (two drives may be installed

only in the absence of floppy drives)

Serial I/O Channels                Two to sixteen asynchronous, bidirec-

tional EIA RS-232C ports and one 2-wire

local area network (LAN) port

Parallel I/O Channels              One 8-bit output channel for connection

to any plug-compatible printer with the

Centronics interface

I/O Device Controller Boards       1 to 4 with LAN controller; 1 to 5 with-

out LAN controller

Main Memory                        768K bytes (minimum) to 1.5M bytes

(maximum); 64K X 1 dynamic RAM chips.

Word length: 16 bits

1-7/8

BFISD 8079

SECTION II

# INSTALLATION AND OPERATION

## 2.1  GENERAL

The Base Unit of the MAI® 2000 Series Computer System is designed to work in a normal office environment, free from dust and dirt.  Hence, there are few restrictions on the suitability of location.  Extremely nigh temperatures and humidity levels should be avoided.

The Model 4108 Base Unit has been fully tested at the factory and was in full working order when shipped.

## 2.2  UNPACKING AND INSPECTING THE BASE UNIT

The Base Unit is shipped in one carton, which also includes a power cable.  Ex-amine the carton upon arrival for signs of damage and mishandling.  (Any damage sustained during shipment is the responsibility of the shipper.)  Place the carton in an upright position, and open it.

CAUTION

Do not lift the Base Unit by the cover.

The cover may release from the main

chassis, causing the chassis to fall.

Lift the Base Unit from the carton as follows: grasp the Base Unit at opposite ends by wrapping your fingers around the bottom corners.  Make sure your fin-gers are supporting the Base Unit by the bottom surface of the main chassis.

Now lift.  Place the Base Unit on a flat surface. (Save the packing and the carton, in case you have to move the Unit at  a later time.)  Check the Base Unit and any other contents of the carton for signs of damage.

## 2.3  INSTALLING THE 2000 SERIES COMPUTER SYSTEM

This procedure assumes that all the desired peripherals that will be part of the 2000 Series Computer System have been set up (according to applicable ser-vice/installation manuals) and are waiting to be connected to the Base Unit.

(Required cables and their part numbers are shown in Section V, figure 5-2.) The Base Unit as shipped should match the utility power available to the user. The ac power outlets should be near the Base Unit so that extension cables are not necessary.

2-1

BFISD 8079

CAUTION

Only three-wire connectors and three-pronged plugs

with the third wire connected to earth ground are

acceptable electrical connectors.  No two-wire con-

nectors or plugs, with or without connection to a

conduit ground, are to be used.  Unstable equipment

operation may result.

The Base Unit is easy to install.  To prepare it for use, follow these steps.

1.  Remove the Base Unit cover by inserting a screwdriver, or a similar

device, in the slot at the bottom right-hand side  of the Base Unit

cover. Push in to disengage the latch. Repeat with the left-hand

side, remove the cover, and  place the cover top-down on a flat sur-

face. Remove all packing material from the disk drive(s) area.  Re-

move the cardboard device supporting the Memory Array and I/O device

controller boards.

2.  Install all device controller board options, following the procedures

in "REMOVAL/REPLACEMENT," Section V, in this manual. For convenience,

PCBA switch settings, jumper placements and cable connections are also

included in this section, in paragraph  2.4.

3.  Place the Base Unit on any convenient surface, such as a desk, table

or stand.  The Base Unit also may be positioned vertically, on end

(this requires a special stand).  In any case, be careful not to re-

strict the airflow through any of the Base Unit vents.  Allow approx-

imately four inches on all sides of the Base Unit for air ventilation.

4.  Verify that the Base Unit power switch, at the rear of the Base Unit,

is OFF (the "0" side of the switch is depressed).

CAUTION

Avoid plugging the Base Unit into a wall

receptacle with the Base Unit power switch

ON (with the "1" side depressed). This will

corrupt the file system.

5.   If the Base Unit includes a floppy diskette drive, push the drive

button and remove the protective shipping cardboard from the drive.

6.   Temporarily reposition the Base Unit so that you can easily reach the

back panel to make the proper cable connections.

2-2

BFISD 8079

7.  Connect a video display terminal to serial port 3 (the leftmost port

of the four serial ports on the bottom 4-Way Controller board, as seen

from the rear of the Base Unit. (Note: If you are connecting a Model

4310 EOT, the cable part number is 907753-001, and the PA end connects

to the Base Unit.) Secure all connector screws.

8.  Refer to the appropriate terminal manual for the setup procedure. The

proper initial default parameters are the following:

9600 bits/second

7-bit character

1 stop bit

odd parity

9.  Refer to the appropriate manual for electrical current specifications

for each device that will be plugged into the wall outlet.  To make

sure the system will not trip a circuit breaker,  the breaker rating

must be greater than the combined current ratings of all the devices

in the system.  The Base Unit requires a 6A rating for 100-120 VAC and

a 3A rating for 220-240 VAC.

10.  Plug in the power cables for both the Base Unit and the terminal, and

turn on the terminal.

11.  Turn on the Base Unit (depress the "1" side of the Base Unit power

switch), and press CTRL C during memory  self test (to interrupt normal

OS loading for system self-test verification).

12.  Compare the information on the screen with the actual hardware in the

Base Unit.  They should match. (Note: the minimal system must contain

at least three Memory Array boards; these provide 786,432 bytes of

system memory.  There also must be one Winchester Drive Controller

board in the Base Unit [it always is the topmost board in the I/O de-

vice controller stack].)  The following is an example of what you will

see on the screen at this point:

Basic Four Information  Systems

MAI 2000

System Self Test Bl.1.7: SSN 2000-90013

cmb                                   pass

memory   [size=1024 kbytes]           pass   c<alt load>

fd                                    pass

fw       [modules= 0]                 pass

wd                                    pass

cs                                    pass

ln       [modules= 0,nodes= 01]       pass

Boot device:

2-3

BFISD 8079

13.  Proceed with normal system load by pressing CR for Boot Device and

then pressing CR again for SYSTEM FILE.  Press CR again when the date

prompt comes on the screen.  (Note: If the operating system does not

load, refer to the User's Guide, BFISD 6203A.)  The following is an

example of what you will see on the screen at this point (last few

lines only):

Basic Four Information Systems

M A I   2 0 0 0

System name: MAI 2000                         System serial number:

Operating System version: EOS7121C, BOSS/IX release 7.1A*20 (Sep 21

12:57:43 PM, 10/03/84.  Update clock: hhmmssxx mtnddyy

Wed Oct 3 1984 12:57:45

<single user mode>

ADMIN>

14.  Shut down the system as follows:

a.  Press CTRL D.

b.  Type 'shutdown' (CR).

c.  Wait for the prompt, and then turn OFF the Base Unit power (by

depressing the "0" side of the power switch, at the rear of

the Base Unit).  The following is what you will see on the

screen prior to shutdown (last four lines only; the last line

is the prompt for power down):

ADMIN>

<EOF>

single,  multi, or shutdown? shutdown

Press 'RETURN' key to reboot ('C'=alt-load, 'S'=self-test):

CAUTION

An incorrect shutdown procedure will corrupt

the file system.   If this has occurred, refer

to Section IV, "MAINTENANCE," in this manual,

to recover.

•

15.   Turn OFF the Base Unit power.

2-4

BFISD 8079

16.  Connect the rest of the peripherals to the Base Unit.  Refer to the

appropriate installation/maintenance manuals for setup procedures.

A parallel printer may be connected to the Base Unit parallel I/O port

(port 2, 37-pin connector).  A serial printer or another terminal may

be connected  to Base Unit serial I/O  port 1 (25-pin RS-232 connector).

Additional serial printers and terminals may be connected to the re-

maining Base Unit serial I/O ports.

17.  If the system is equipped with the Magnetic Cartridge Streamer (MCS)

unit,  plug the PB end of the MCS cable into the back of the MCS unit.

Plug the PA end into the connector on the MCS Controller board, at the

rear of the Base Unit (see figure 2-1).

18.  If the system is to be part of a local area network (LAN), refer to

paragraph 2.4 in this section before proceeding.

19.  Turn ON the Base Unit power.

20.  When the operating system has booted, type in the time/date, and press

CR; or just press CR.  (Note: remain in the single-user mode.)

21.  Type 'menu' and press CR.

22.  Configure a port for each peripheral in the system as follows:

a.  Select the UTILITY programs (1).

b.  Select SYSTEM (8).

2-5

BFISD 8079

c.  Select PORT CONFIGURATION (2).  (Refer to the User's Guide,

BFISD 6203A, "Utilities" section, for details.)

d.  Press CR and select ADD DEVICE.

e.  Type in the port number.

f.  Type in the number corresponding to the device type.

g.  Type in the number corresponding to the device model.

h.  Select a device name.

i.  Select the appropriate parameters.

j.  Repeat this procedure from Step e for each periheral device in

the system.

(Note: Configuration changes will not occur until the operating system

is re-booted.

23.  Shut down the system and re-boot.

24.  Press CTRL D.

25.  Type in 'multi' and press CR.

26.  Type in 'admin' and press CR.

27.  Check all terminals by logging on and observing the login message.

28.  Check all printers as follows:

a.  Type in "menu1 and press CR.

b.  Select UTILITY programs.

c.  Select DIRECTORIES.

d.  Select DISPLAY.

e.  Select REPORT DEVICES.

f.  Select PRINTER NAME.

g.  Repeat this procedure from Step c for each printer in the

system.

h.  To exit, press Motor Bar IV (MBIV).

2-6

BFISD 8079

29.  Verify operation of the Magnetic Cartridge Tape Streamer (MCS) unit

(if present) as follows:

a.  Log on by typing in 'admin' to get to the command interpreter.

b.  Turn on the MCS unit,  and  insert a scratch tape.

c.  Label the tape by typing in

MCSLABEL SET=TEST ID=TEST SER=1 (CR)

(The utility will rewind the tape; replace an existing label,

or format the tape and write a  new label; and again rewind the

tape.  Upon completion of the process, the new tape label is

displayed on the screen.)

d.  As a final read verification, type in 'MCSLABEL1 to redisplay

the label.

30.  Shut down the system as follows:

a.  Type in 'shutdown 0.'

b.  Press CTRL D.

c.  Type in 'shutdown.'

d.  Wait for the prompt, and then turn OFF the Base Unit power (by

depressing the "0" side of the  power switch, at the rear of

the Base Unit).

31.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into place.

## 2.4  SWITCH SETTINGS, JUMPER PLACEMENTS, CABLE CONNECTIONS

The following paragraphs contain switch settings, jumper placements and cable

connection for the following:

o  Central Microprocessor Board (paragraph  2.4.1)

o  Memory Array PCBA (paragraph 2.4.2)

o  Winchester Controller PCBA (paragraph 2.4.3)

o  4-Way Controller PCBA (paragraph 2.4.4)

o  Magnetic Cartridge Streamer Controller PCBA (paragraph 2.4.5)

2.4.1  Central Microprocessor Board

See figure 2-2 for jumper locations and figure 2-3 for cable part numbers.

2-7

BFISD 8079

Figure 2-2. Location of Jumpers on Central Microprocessor Board

2-8

BFISD 8079

Figure 2-3.  Central Microprocessor Board Cable Part Numbers

2-9

BFISD 8079

Connect jumper N between points 1 and 2. (This jumper allows the master oscil-lator to be disconnected from the dividers and buffers.  An external oscillator can be injected at this point.  Normal operation is with jumper N installed.)

Connect jumpers C and P.  These jumpers configure the board to accept four dif-ferent size EPROMs, used for system diagnostics and the debugger.  The Central Microprocessor Board can handle 2732, 2764, 27128  and 27256 EPROMs.  As re-ceived, the CMB has jumpers in etch to handle either 2732s or 2764s; no modifi-cation is necessary.  To use the other size EPROMs, or to switch back to the 2732 or the 2764, after using a larger EPROM, follow the chart below.

EPROM                    JUMPER C         JUMPER P

2732 (4K x 8)            1 and 2          1 and 2

2764 (8K x 8)            1 and 2          1 and 2

27128 (16K x 8)          2 and 3          1 and 2

27256 (32K x 8)          2 and 3          2 and 3

NOTE: An earlier version of the CMB (Rev. 1) could only handle 2716s and 2732s.

On this CMB, jumper C must be connected as follows:

EPROM                   JUMPER C

2716 (2K x 8)           2 and 3

2732 (4K x 8)           1 and 2

Connect jumper R.  (This jumper, when disconnected, disables the memory refresh circuitry, thereby allowing easier debugging of memory and bus arbitration cir-cuits.  Normal operation is with jumper R connected between points 1 and 2.)

Connect jumpers A, B, G, H and K according to the following tables.  (The serial port has two programmable ports.  Each can be configured as RS-232 and support a modem, a printer or a terminal.  Additionally, port B supports X—21.

Note that only one cable is needed to support printers, terminals or modems.

All signal switching is done on the Central Microprocessor Board via the jump-ers.  The RS-232 cable is a pin-for-pin connection.  No signals or pins are cross-connected.)

PORT A:

MODEM                 TERMINAL              PRINTER

Name     Jumper A   Cable      Jumper A   Cable       Jumper A   Cable

CTS       7 and 8   pin 5       7 and 9   pin  4       7 and 9   pin 4

DSRA      3 and 4   pin 6      *1 and 3   pin  20      1 and 3   pin 20

DTR       1 and 2   pin 20     *2 and 4   pin  6       2 and 4   pin 6

RTSA      9 and 10  pin 4       8 and 10  pin  5       8 and 10  pin 5

RXDA     11 and 12  pin 3      11 and 13  pin  2       11 and 13 pin 2

TXDA     13 and 14  pin 2      12 and 14  pin  3       12 and 14 pin 3

RNGA     In Place   pin 22

TRXCA    In Place   pin 15

DCDA     In Place   pin 8

2-10

BFISD 8079

PORT  B:

MODEM                 TERMINAL              PRINTER

Name     Jumper B    Cable       Jumper B   Cable      Jumper B   Cable

CTSB      7 and 8    pin 5        7 and 9   pin 4       7 and 9   pin 4

DSRB      3 and 4    pin 6        3 and 1   pin 20      3 and 1   pin 20

DTRB      1 and 2    pin 20       2 and 4   pin 6       2 and 4   pin 6

RTSB      9 and 10   pin 4        8 and 10  pin 5       8 and 10  pin 5

RXDB     13 and 14   pin 3       13 and 15  pin 2      13 and 15  pin 2

TXDB     15 and 16   pin 2       14 and 16  pin 3      14 and 16  pin 3

Jumper G                Jumper G              Jumper G

RXDB     15 and 16   pin 3       15 and 16  pin 2      15 and 16  pin 2

DCDB     17 and 18   pin 8       17 and 18  pin 8

TRXCB    10 and 20   pin 15      19 and 20  pin 15

23 and 24               23 and 24

Jumper H                Jumper H

DCDB     1 and 2                 1 and 2

Jumper K                Jumper K              Jumper K

D422    *1 and 2                *1 and 2              *1 and 2

NOTE: Be sure to disconnect all unused jumper positions on port B.

PORT B - RS-422:

Jumper   Connect    AND    Jumper   Connect

G       1 and 2            B      11 and 12

G       3 and 4            B      15 and 16

G       5 and 6            H       2 and 3

G       7 and 8

G       9 and 10

G      11 and 12

G      13 and 14

G      21 and 22

NOTE: When RS-422 is used in port B, be sure that jumpers

G:15 and 16,

G:19 and 20,  and

K:  1 and 2

are disconnected.

*This jumper disables the RS-422 drivers.

2-11

BFISD 8079

Connect jumpers L and M.  (The serial ports are capable of communicating at a number of different speeds and can communicate both synchronously and asynch-ronously.  Jumper L connects the master clock to the Baud rate generator, used for asynchronous input/output.  Jumper M connects the synchronous clock to the port.  These clocks are disconnectable for service purposes.  Normal operation is with both jumpers [L and M] inserted, connecting pins 1 and 2 on each jumper block.)

Connect jumper D according to the following table. (The floppy disk drive sup-port logic, on the Central Microprocessor Board, can support both 2K x 8 and 8K x 8 static buffers.  This RAM is used as a sector buffer to speed up overall system performance when using the floppy drive. In addition, an optional 8K x 8 buffer may be used so that an entire track of information may be input/output to the 68010 microprocessor at one time without the processor having to read from the disk sector by sector.)

RAM SIZE       JUMPER D

2K x 8         2 and 3

8K x 8         1 and 2

Connect Jumper E.  (The floppy disk controller, located on the Central Micro-processor Board, has three different data separators available: the Analog, the Standard Microsystems Corp. [SMC], and the Western Digital [WD].  The instal-lation of the jumper depends on which data separator is used.)

SEPARATOR:

Analog               SMC                 WD

Data   1 and 2     Data   3 and 4       Data   5 and 6

Clock  7 and 8     Clock  9 and 10      Clock  11 and 12

Connect jumper F according to the following table.  (This jumper selects bet-ween Standard Density and High Density decoding on the Western Digital data separator.  The system described in this manual uses Standard Density disk drives.)

MEDIA            JUMPER F

Standard Density     1 and 2

High Density         3 and 4

Verify that jumper S is not connected.  (This jumper is only to be used when calibrating the Western Digital data separator.  The jumper grounds the VFOE input to the WD1691, simulating a read condition.  Normal operation is the jumper disconnected.)

2-12

BFISD 8079

For a standard Central Microprocessor Board configuration, recheck the jumper nstallation by referring to the jumper configuration table (2-1).  The fol-lowing assumptions are made:

2732 or 2764 EPROMs

2K x 8 sector buffer

Standard RS-232 DCE on serial ports A and B

Analog Data Separator

Standard density disk drives

Table 2-1.  CMB Jumper Configuration

JUMPER      CONNECT                      FUNCTION

A         7 and 9        Serial Port A - CTS

A         8 and 10       Serial Port A - RTS

A        11 and 13       Serial Port A - RXDA

A        12 and 14       Serial Port A - TXDA

B         1 and 3        Serial Port B - DSRB

B         2 and 4        Serial Port B - DTRB

B         7 and 9        Serial Port B - CTS

B         8 and 10       Serial Port B - RTSB

B        13 and 15       Serial Port B - RXDB

B        14 and 16       Serial Port B - TXDB

C          None          EPROM Size Select - 2732, 2764

D         2 and 3        Floppy Sector Buffer Size Select -  2K x 8

E         1 and 2        Floppy Data Separator Select - Data

E         7 and 8        Floppy Data Separator Select - Clock

F         1 and 2        Floppy Density Select

G        15 and 16       Serial Port B - RXDB

G        17 and 18       Serial Port B - DCDB

G        19 and 20       Serial Port B - TRXCB

G        23 and 24       Serial Port B - TRXCB

H         1 and 2        Serial Port B - DCDB

K         1 and 2        Serial Port B - RS-422 Disconnect

L         1 and 2        Baud Rate Generator Connect

M         1 and 2        Serial Communications Synchronous Clock Connect

N         1 and 2        Master Oscillator Connect

P          None          EPROM Size Select - 2732, 2764

R          None          Refresh Enable

S          None          WD Data Separator Enable (Floppy Calibrate)

2-13

BFISD 8079

2.4.2  Memory Array PCBA

Set the appropriate switches for the desired physical address of the Memory Array PCBA.  Refer to table 2-2 for a listing of switch settings, and see figure 2-4 for switch locations.  Be careful not to duplicate addresses of existing Memory Array PCBAs; compare the switch settings of all the PCBAs.

Table  2-2.  Memory Array Module Address Switch Settings

ADDRESS

(K Bytes)          S1        S2         S3          S4         S5         S6

0 to 256         ON        ON     DON'T CARE      ON         ON         ON

256 to 512         ON        ON     DON'T CARE      ON         ON         OFF

512 to 768         ON        ON     DON'T CARE      ON         OFF        ON

768 to 1024        ON        ON     DON'T CARE      ON         OFF        OFF

1024 to 1280        ON        ON     DON'T CARE      OFF        ON         ON

1280 to 1536        ON        ON     DON'T CARE      OFF        ON         OFF

Note: OFF = OPEN and ON = CLOSED

2.4.3  Winchester Disk (Single-Board) Controller

Connect the appropriate jumpers for the desired board address and drive type as listed in table 2-3.  See figure 2-5 for jumper locations and cable connections.

Table 2-3.  Winchester Disk Controller Jumper Connections

JUMPER A    BOARD  ADDRESS (HEX)   JUMPERS  B and C      DRIVE  TYPE

1 and 2            CCXXXX             1A and 2A        143 MB (Note 2)

2 and 3            CDXXXX             1B and 2B        10/20 MB (Note 3)

1C and 2C         50 MB (Note 4)

Notes: 1.  Jumper B controls drive 0;  jumper C controls drive 1.

2.  Write precompensation always off.

3.  Write precompensation always on.

4.  Write precompensation on at and above the reduced write

current cylinder.

2-14

BFISD 8079

Figure 2-4.  Location of Address Switches on Memory Array Module

2-15

BFISD 8079

Figure 2-5.  Location of Jumpers on (Single-Board) Winchester Disk Controller

2-16

BFISD 8079

2.4.4  4-Way Controller PCBA

Set the appropriate switches on the 4-Way Controller PCBA for the controller

board address/DMA arbitration number and for the kind of peripheral(s) served

by the Base Unit according to the listings shown in table 2-4.  See figure 2-6

for the location of the switches.

Table 2-4.   4-Way Controller PCBA Switch Settings

SWITCH S1

DMA Arbitration                       PCBA Address

--------------------------------------     ------------------------

S1     S2      S3     S4     S5     S6     S7     S8     S9     S10

Board 1    ON     OFF     OFF    OFF    OFF    OFF    OFF    ON     OFF    ON

Board 2    ON     OFF     OFF    ON     OFF    OFF    OFF    ON     OFF    OFF

Board 3    ON     OFF     OFF    ON     ON     OFF    OFF    OFF    ON     ON

Board 4    ON     OFF     OFF    ON     ON     ON     OFF    OFF    ON     OFF

SWITCHES PGM1-4*

For PGM1 through PGM4, connect the pins according to the PCB detail used:

PCB detail 904741-001               PCB detail 904943-001

(current production)                 (future production)

TERMINAL/PRINTER        MODEM       TERMINAL/PRINTER        MODEM

1 to 7           1 to 2            1 to 3             1 to 2

2 to 8           3 to 4            2 to 4             3 to 4

3 to 4           7 to 8            9 to 11            9 to 10

9 to 10          9 to 10          10 to 12           11 to 12

13 to 15         13 to 14          13 to 15           13 to 14

14 to 16         15 to 16          14 to 16           15 to 16

*PGM1 through 4 are actually jumpers (as opposed to switches) enclosed in plas-

tic rectangular "boxes."  Each box may be pulled from its position and then

reinstalled to connect any two adjacent pins.  There is one PGM "group" per

controller port, six boxes per PGM group, and 16 pins per PGM group.

2.4.5  Magnetic Cartridge Streamer Controller PCBA

Set the appropriate switches on the MCSC PCBA for the correct bus arbitration number and mode according to the listing shown below. See figure 2-7 for the location of the switches.

SWITCH SW1

_                   Bus  Arbitration                 _

S1        S2         S3        S4        S5        S6        S7        S8

ON        ON         ON        ON        OFF       OFF       ON        ON

2-17

BFISD 8079

Figure 2-6. Location of Switches on 4-Way Controller PCBA

2-18

BFISD 8079

Figure 2-7.  Location of Switch on Magnetic Cartridge Streamer Controller PCBA

2-19

BFISD 8079

2.5  INSTALLING THE LOCAL AREA NETWORK (LAN)

When the user purchases the local area networking option for his 2000 Series

system, he must obtain the following hardware and software components.

a.  The Local Area Network Controller (LANC) board

b.  A floppy diskette or cassette containing the LAN software

c.  One 15-foot tap cable

d.  One Tap Box™

e.  A user's manual

If this is the first 2000 Series system being installed, and a local area net-

work does not yet exist, the following hardware also may be required.

a.  Network cables in 1,000-foot lengths, or shorter (total length not to

exceed 4,000 feet)

b.  Two Tap Boxes

c.  A repeater for every 1,000 feet of cable after the first 1,000 feet,

and an additional repeater when there are more than 32 systems on the

network (63 systems, maximum)

The network cable is twin-lead, shielded or unshielded.  Local electrical and

fire regulations determine which type may be used and also determine where the

cable may and may not be placed.

The cable also must meet certain LAN transmission specifications.

The following cables are recommended for use.

Manufacturer     Part No. (22 AWG, shielded)     Part No. (20 AWG, unshielded)

Alpha                   9823                             1895

Belden                  9182                             8205

2.5.1  Installing the LANC Board

Before installing the LANC board, you must set the station address (the user

may have a number for you).  The address uniquely identifies this station to

all other stations on the network. To set it, first locate and identify the

address switch on the LANC board. It will be found next to the cable connector

(J3), as shown in figure 2-8.

2-20

BFISD 8079

Figure 2-8.  Location of Switches and Cable Information for LANC PCBA

2-21

BFISD 8079

The address switch comprises eight smaller switches, each set individually.

The "off" position of each switch represents binary 1.

SWITCH SW1

Bias   Terminator                     Station Address                     _

S1        S2        S3        S4        S5        S6         S7         S8

*         **        ↑         ↑         ↑         ↑          ↑          ↑

* represents the "bias." Switch 1 is set to 1 (off) on only one LAN con-

troller board in a network; all other LAN controllers must have this

switch set to 0 (on). A maximum of two LAN controller boards per Base

Unit is allowable, but one per Base Unit is the normal configuration.

** represents the terminator setting.  Only two controllers, one at each end

of the network, may have this switch on; all other controllers must have

the switch off.

T represents the binary coded station address bit positions. Switch S8 is

the least significant bit, and switch S3 is the most significant bit.

Each LAN controller board has one unique address: the first address is

000001, and the 63rd address is 111111 (all switches off). (Note: 000000

is illegal.)

Switch S1 is the Bias switch and normally is set to the on position; however, one station must have this switch turned off to bias the line. Switch S2 is on only at the ends of a network; all other controllers must have this switch off.

Switches S3 through S8 are set for the desired address; these may be treated as a 6-bit binary word, with switch no. 8 as the least significant bit.

There are 64 possible combinations of settings.  With on = 0 and off = 1, the switches may be set for any one of 63 addresses (address 00 must not be used); for example,

100101 = address 37, and 111111 (all switches off) = address 63.

Another set of switches also must be set for the bus arbitration number and board address.  These are set at the factory but should be verified by the installer before continuing.  See figure 2-8 for the switch location.

SWITCH SW2

Bus Arbitration                          Address Decode

S1        S2        S3        S4        S5        S6         S7        S8

OFF       OFF       OFF       ON        ON        OFF        ON        OFF

OFF       OFF       OFF       ON        ON        ON         OFF       ON

2-22

BFISD 8079

The Local Area Network Controller board now is ready to be Installed in the Base Unit.  To do so, proceed as follows:

1.  Shut down the system, and turn off the Base Unit power.

2.  Insert a screwdriver, or similar device, in the slot at the bottom

right-hand side of the Base Unit cover, and push in to disengage the

the latch.  Repeat with the left-hand side, and remove the cover.

3.  Unplug the ribbon cables from the Winchester Drive Controller (WDC)

PCBA, located in the card cage at the rear right-hand corner of the

Central Microprocessor Board (CMB).

(Note: two of the drive connectors on the WDC PCBA are situated side

by side; the right-hand connector [J0]  receives the "0" drive cable,

and the left-hand connector [J1] receives the "1" drive cable.)

CAUTION

Do not remove this board if power

is applied to the Base Unit.

4.  Unplug the WDC Bus Adapter PCBA and the WDC PCBA (which carries the

WDC PCBA) as a single unit from the top of the "stack."

5.  Plug the Local Area Network Controller PCBA into the CMB (or into the

PCBA at the top of the stack) at the rear right-hand corner of the

CMB.  Line up the connectors, then press down firmly to connect the

board, being very careful not to bend the pins.

6.  Plug the WDC Bus Adapter PCBA and the WDC PCBA (mounted above the com-

ponent side of the WDC Bus Adapter) into the LANC PCBA.

7.  Plug the ribbon cables from the Winchester  Drive  into the WDC PCBA.

(Note: the two narrower ribbon connectors on the  WDC PCBA are situ-

ated side by side;  the right-hand connector [J0] receives the "0"

cable, and the left-hand connector [Jl] receives the "1" cable.)

8.  Replace the cover on the Base Unit.  To do this, line up the side

grooves on the front and back panels of the Base Unit with the match-

ing grooves on the  side panels of the cover.  Now press down.  The

cover should snap into place.  If it does not, remove the cover, and

try again.

9.  Plug the tap cable into the LANC board connector, accessible at the

Base Unit rear panel. (The tap cable has a pressure fit connector at

one end, which slides onto the LANC board connector.)

10.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

2-23

BFISD 8079

2.5.2  Installing the Tap Box

The Tap Box connects the tap cable to the LAN cable.  It is a passive device, designed to allow easy connection of the Base Unit to the LAN cable.  Once in-stalled, it should not be removed;  to do so will break the network connection.

Tap Boxes can be installed anywhere along the network cable, with no minimum or maximum distance between them. The diagram in figure 2-9 shows the layout of the Tap Box, with labels added for reference.  Each Tap Box contains five pairs of screw terminals for connecting the network wires.  The five pairs are label-ed A1-B1, A2-B2, etc., to A5-B5.  The A and B sides of each pair are electri-cally connected.  The following instructions are for creating the network tap connection.

Figure  2-9.   Outline of Tap Box, Showing Screw Connections

2-24

BFISD 8079

The following instructionsare for creating the network tap connection.

1.  Cut the network cable at the place you wish the tap to be, and remove

approximately one inch of covering from each of the two ends of the

cable. This exposes the red, black and ground wires.

2.  Slide a rubber grommet over each end of the cable, and strip approx-

imately 3/8 inches of insulation from all four red and black wires.

3.  Insert the stripped ends of the two black wires into screw terminal

A1, and tighten the screw.

4.  Insert the stripped ends of the two red wires into screw terminal A2,

and tighten the screw.

5.  Insert the ground wires into screw terminal A3, and tighten the screw.

6.  Slide a rubber grommet over the wire end of the tap cable.

7.  Insert the stripped black wire into screw terminal Bl, and tighten the

screw.

8.  Insert the stripped red wire into screw terminal B2, and tighten the

screw.

9.  Insert the ground wire into screw terminal B3, and tighten the screw.

10.  Remove three cutouts from the Tap Box, and install the grommet for

each cable into a cutout hole.

11.  If the Tap Box is to be attached to a wall, use the mounting holes

in the back of the Box or the adhesive strip on the back of the Box.

12.  Place the lid on the Tap Box, and secure it with the four corner

screws.

2.5.3 Installing the Repeater

The repeater is an active device (amplifier) designed to compensate for the attenuation of the LAN cable signal after 1,000 feet of travel.  A repeater must be installed every 1,000 feet in the LAN cable, after the first 1,000 feet.  Hence, three repeaters are required for a maximum length network. (No more than 4,000 feet of LAN cable may be installed.)  An additional repeater must be installed at the midpoint of a 1,000-foot segment of cable when more than 32 Base Units are in that segment (63 Base Units per LAN system is maxi-mum).  Also, when a branch, or "T" connection to the LAN cable, is required, a repeater must  be installed at that point.

2-25

BFISD 8079

Figure 2-10 shows the layout of the repeater box, indicating the position of the two screw connector terminal strips. The terminal strip at the top of the box is for connecting the power tranformer.  The terminal strip at the bottom of the printed circuit board is for connecting the LAN cables.

TBD

Figure 2-10.  Outline of Repeater Unit, Showing Screw Connections

2-26

BFISD 8079

2.5.3.1  Connecting Network Segments

The following procedure may be used as a guide for installing a repeater to connect two network segments.

1.  Open the repeater by removing the screws at the four corners.

2.  Strip all wire leads on the two LAN cable segments to be joined.

3.  Insert the red wire from one segment into the left-hand + connector on

the terminal strip at the bottom edge of the repeater printed circuit

board, and tighten the screw.

4.  Insert the black wire from the same segment into the - connector im-

mediately to the right of the red wire just connected, and tighten the

screw.

5.  Insert the red wire from the second segment intothe right-hand + con-

nector of the terminal strip at the bottom edge of the repeater prin-

ted circuit board, and tighten the screw.

6.  Insert the black wire from the second segment into the - connector im-

mediately to the right of the red wire just connected, and tighten the

screw.

7.  Insert the ground wires from both segments into the adjoining "drain"

connectors, and tighten the screws.

8.  If a network branch is desired, continue with the following paragraph.

Otherwise, continue with paragraph 2.5.4.3, "Connecting Power to the

Repeater."

2.5.3.2  Connecting a Network Branch

A network branch, or "T" connection, may be made by attaching a third cable segment to the repeater.  The following instructions assume that the procedure in paragraph 2.5.3.1,  "Connecting Network Segments,"  has  been completed. The branch segment cable is shown in  figure 2-10 (labeled Segment 3).

To connect a network branch, follow this procedure.

1.  Verify that the repeater power transformer is disconnected, or unplug-

ged.

2.  Carefully strip both wire leads on the third segment of the network

cable.

3.  Insert the red wire into the + connector of the middle pair of screw

connectors, and tighten the screw.

4.  Insert the black wire into the - connector of the middle pair of screw

connectors, and tighten the screw.

2-27

BFISD 8079

5.  Insert the ground wire into either "drain" connector, and tighten the

screw.

6.  Reconnect the repeater power transformer, or follow the procedure in

paragraph 2.5.3.3, "Connecting Power to the Repeater."

2.5.3.3  Connecting Power to the Repeater

The power transformer that was supplied with the repeater unit now may be con-

nected.  To do this, follow these instructions:

1.  Determine how long the power cable must be, and cut it to the desired

length.  (The maximum length is 100 feet if you use the same type of

cable as the network cable.)

2.  Carefully strip the wire leads at both ends of the power cable.

3.  Insert a red wire into the connector labeled +V, at the top of the re-

peater printed circuit board, and tighten the screw.

4.  Insert the black wire from the same pair into the connector marked GND

on the same terminal strip, and tighten the screw.

5.  Insert the red wire at the other end of the power cable into the con-

nector labeled + on the power transformer, and tighten the screw.

6.  Insert the remaining black wire into the connector labeled - on the

power transformer, and tighten the screw.

7.  Plug the power transformer into the wall outlet.

8.  Verify that the power connection is good, and that power is being ap-

plied to the repeater, by noting whether the LED (light-emitting di-

ode) on the repeater printed circuit board is lighted.

9.  Unplug the power tranformer, and proceed with the next cable segment

installation, if any.

10.  Plug all power tranformers into wall outlets, check the LEDs, and

close the repeater boxes.

2.5.4  Installing the LAN Software

The local area network (LAN) software is supplied on a tape or a floppy disk-ette.  The LAN software must be installed before local area networking can be used on the 2000 Series System.

To install the LAN software, follow the procedure in Chapter 7, MAGNET 2000 Local Area Networking User's Guide, BFISD 6351C.

2-28

BFISD 8079

With the LAN software installed, the customer may use the LAN Configuration Utility, according to his manual, MAGNET 2000 Local Area Networking User's Guide, BFISD 6351B.

## 2.6  USE AND CARE OF FLOPPY DISKETTE AND DRIVE

The Model 4108 Base Unit may contain no more than two 5-1/4 inch floppy disk drives, mounted one atop the other in the front panel.  The drive has approxi-mately 640K bytes of double-density storage per drive (formatted).  The floppy disk drives use double-sided, double-density, soft sector diskettes.  It is recommended that only diskettes purchased from the following manufacturers be used for optimal performance and data integrity.

Manufacturer                   Double-Sided

Dysan                      No. 204/2D

Verbatim                   No. MD 577-01-18212

### 2.6.1 Diskette Insertion

Diskettes are inserted into the drive with the label side facing up and the large rectangular notch facing to the left.  Gently place the diskette as far into the drive as it will go.  Insert the diskettes only in this manner to avoid damage.

Diskettes should never be inserted into the drives when the power is not on; nor should the power be turned off when diskettes are in the drives.  Turning the power on and off with diskettes in the drives can result in damage to the diskettes and in loss of data.

A few simple precautions should be taken in handling floppy diskettes to avoid damage to their recording surfaces.  They should be treated with the same care you would give to other recording media, such as phonograph records or record-ing tape.  Handle them gently at all times, and do not touch the brown diskette surface.

Do not let them come in contact with liquids, ashes, paperclips, or anything magnetic.  Don't bend them out of shape or put heavy weights on top of them.

Never use pencils or ball point pens to write on the labels.  Use a soft felt-tip pen, or mark the labels before putting them on the diskettes.

Proper storage of diskettes also is important.  They should be kept in their protective jackets whenever  they are  not in use.  Diskettes should never be piled on top of each other - it is best to store them upright; the boxes in which they  are packaged are good for this purpose.

The user's office supply vendor can provide him with excellent filing and stor-age containers for his diskettes.  With proper care, the user can increase the life of his diskettes and avoid the loss of data.

2-29

BFISD 8079

### 2.6.2  Write Protection

Each box of diskettes provides a sheet of 3/4-inch foil stickers.  These are called write protect tapes and are used to prevent alteration of the contents of the diskettes.

Diskettes that have been write protected can be read by the drives, but no data can be recorded.  One use of this feature is to protect backup copies of soft-ware or data.  It is a good idea to write protect a master diskette and its backup copy, so that neither can be inadvertently erased or altered.

To write protect a diskette, fold a write protect tape over the large rectang-ular notch, being sure that the entire notch is covered and that the fold lines up with the edge of the diskette.  When write protection no longer is desired, simply peel away the tape.

2-30

BFISD 8079

SECTION III

# FUNCTIONAL DESCRIPTION

## 3.1  INTRODUCTION

This section provides a functional description of the Central Microprocessor Board (CMB) in the Model 4108 Base Unit and of the memory array boards, which plug into the CMB.  Functional descriptions of the peripheral controller boards and of the various disk drives are contained in other sections of this manual.

The functional description of the magnetic cartridge tape streamer used with the Model 4108 Base Unit is in a separate manual.

To fully appreciate the material in this section, the reader should have some exposure through the manufacturers' literature to the Motorola 68010 micro-processor chip and to the input/output controller chips used in the CMB.

## 3.2  CENTRAL MICROPROCESSOR BOARD (CMB) DESCRIPTION

The CMB is the central processing unit (CPU) for the MAI® 2000 Series Desktop Computer System.  The CMB embraces the single-board, integrated bus concept.

Architecturally, the CMB logic comprises three major functional sections:

•  Central processor

•  System memory control

•  I/O (input/output)

These are linked primarily by the system bus structure.  Figure 3-1 is a block diagram of the CMB logic, highlighting the flow of addresses and data.

The central processor section is based on the 16/32-bit Motorola 68010 micro-processor.  The functions of the central processor section include system bus control, timing signal generation, interrupt control, bus arbitration, memory parity error detection, and bus error detection.

In addition to decoding the address space, the system memory control section uses a memory management unit to partition a maximum of  two megabytes of main memory into eight variable-length segments;  this facilitates the swapping of programs between a hard  disk and main memory and provides user program snaring and protection.  The memory control section also includes dynamic RAM (random access read/write memory) timing/refresh circuitry for the memory array boards.

Onboard logic and controllers support one or two floppy disk drives.  External peripherals are provided  for by one  parallel and two serial connectors.  In addition to the local I/O controllers, the CMB includes a system I/O bus that allows full direct memory access (DMA) operation by plug-in peripheral device controller boards.

3-1

BFISD 8079

TBD

Figure 3-1.  Simplified Block Diagram, Central Microprocessor Board

3-2

BFISD 8079

### 3.2.1  Clock Generator

The 68010 microprocessor subsystem requires a master clock to make the system operate satisfactorily.  An 8-MHz clock signal is produced by a 16-MHz master oscillator (5K) whose output is divided in half by a 74S112 J-K flop-flop (5J). (Refer to the CMB Logic Diagram, sheet 5.)  Other clocks needed by the system are developed in a 74S161 4-bit  binary  counter (6J). The 4- and 8-MHz clock signals (K4MHZ-, K8MHZ-,  K8MHZ+  and CCLK-)  are buffered by a 74S240 tristate inverter (4H), as  they are distributed throughout the Central Microprocessor Board to many of the circuits described in the following paragraphs.

### 3.2.2  Function Code Decoder

In any multi-user computer system, one of the tasks of the operating system software is to provide a common set of input/output (I/O) subroutines for all the users' programs.  These are usually accessed from the user program through trap instructions.  (A trap is an internally generated [software] interrupt.)

To ensure the efficiency of I/O processing in the system, and the protection of users' programs, the system cannot allow a user to enter the system software partition of main memory (whether accidentally or maliciously).  To this end, the 68010 defines all I/O instructions to be privileged instructions and deter-mines two separate modes of operation: user mode and supervisor mode.  A bit in the 68010 status register indicates the current mode.

The 68010 allows privileged instructions to be executed only in the supervisor mode.  If an attempt is made to execute a privileged instruction in the user mode, the 68010 does not execute it but treats it as an illegal instruction and traps to the operating system.  This dual mode operation allows us to be sure that only the (system software) device drivers can perform I/O operations.

Thus when the 68010 makes a reference, it classifies the kind of reference be-ing made by using  the encoding of three function code output lines.  This al-lows external translation of addresses, control of access, and differentiation of special processor states, such as interrupt acknowledge.  The binary-coded set of function code, or  processor cycle status, signals are CFCO+, CFC1+ and CFC2+.  These identify the kind of bus activity currently being performed.

Three different kinds of major processor cycles currently are defined in the 68010.  The corresponding function code signals are decoded by a 74LS138 l-of-8 decoder (8R). (Refer to  the CMB Logic Diagram, sheet 7.) The three outputs of the decoder are as follows:

a.  Function DeCode 2 (FDC2+)  - when asserted means the 68010 is running

user programs

b.  Function DeCode 5 or 6 (FDC5R6+) -  when asserted means the 68010 is

operating in the supervisor mode

c.  Function DeCode 7 (FDC7-)  - when asserted (low) means the 68010 is

processing an interrupt acknowledge cycle

3-3

BFISD 8079

The function code outputs from the 68010 are valid whenever the CPU Address Strobe (CAS-) output is asserted.  Therefore, the decoder is gated by CAS- so that the decoding  happens  only  when the function codes are valid.  Also, the decoder is disabled when the 68010 has relinquished control of the bus (when the CPU Bus grant ACKnowledge [CBACK-] signal is asserted).

The FDC7- signal, from the function code decoder, also is used to provide an Interrupt ACKnowledge (IACK-) pulse to the system I/O bus. FDC7- is delivered "on time" as IACK- via a NAND gate (6L); however, FDC7- also is input to a D flip-flop (6K) whose Q output goes to the other input of that NAND gate. As a consequence, FDC7- is ORed with a delayed version of itself.

The delay is caused by the K8MHZ- clock triggering the flip-flop on positive-going edges, which occur at half of a clock cycle after the normal system clock cycle begins.  The result is that IACK- is "stretched" by an additional half of a clock cycle after address strobe  CAS- is negated.  This creates an interrupt acknowledge pulse that is long enough to hold off a new series of bus arbitra-tions (discussed in paragraph 3.2.11) by the peripheral device controllers, on the system I/O bus.

For local use, the non-decoded function code CFC2+ is buffered in a 74LS04 in-verter (7R) to become CFC2+A and CFC2-.  When these signals are asserted, they indicate to many circuits on the Central Microprocessor Board that the 68010 either is in the supervisor mode or is processing an interrupt acknowledge cy-cle (i.e., the 68010 is not in the user mode).

### 3.2.3  Boot PROM

Independent of the operating system software, the following programs and data are imbedded in read-only memory and may be used in the 68010 supervisor mode.

•  Symbolic debugger

•  Initialization tests

•  Bootstrap instructions

•  Diagnostic aids

•  Reset/exception recovery pointers

Two EPROMs (6N and 6S) are connected to the main address bus and to the 16-bit- wide data bus. (Refer to the CMB Logic Diagram, sheet 18.)  A Power-On Reset (POR-) cycle maps the EPROMs throughout the 68010 addressing range.  This is necessary because the reset vectors must be located in the eight lowest memory locations, which address RAM during normal system operation.

The first WRITE cycle, however, clears a 74LS112 J-K flip-flop (8T) and negates the BOOT+ signal.  The low BOOT+ is input to the address space decoder (7Z, CMB Logic Diagram, sheet 9) to assert PROMCE- (PROM Chip Enable). The EPROMs now may be read at a base address of 4XXXXX (hex), in the 68010 supervisor mode.

3-4

BFISD 8079

The Central Microprocessor Board can support three different size EPROMs:  8K bytes, 16K bytes or 32K bytes.  Whatever the size used, two EPROMs are wired in parallel with respect to the address bus to give a word size 16 bits wide.  The highest boot PROM address depends, of course, on the size EPROMs used; and READ and WRITE cycles  above  that address are undefined.  (Again, the only effect a WRITE cycle to the boot PROMs will have is to change the address space of the EPROMs.)

After the first WRITE cycle, the normal address ranges of the various boot PROM configurations are as follows:

ACCESS  RANGE                UNDEFINED

EPROM  SIZE             (HEX)                      (HEX)

8K bytes          400000 to 401FFF           402000 to  4FFFFF

16K bytes          400000 to 403FFF           404000 to  4FFFFF

32K bytes          400000 to 407FFF           408000 to  4FFFFF

### 3.2.4  CMB Diagnostic Hardware

The Central Microprocessor Board contains hardware designed to cooperate with diagnostic programs, in the 68010 supervisor mode. (These diagnostic programs may or may not be imbedded in the operating system software.)  This hardware includes the CMB status drivers and the CMB control register.

3.2.4.1  CMB Status Drivers

There are times when the diagnostic program requires a "snapshot" of the status of the Central Microprocessor Board.  The CMB status contains information about various conditions in the CMB. This may be obtained by a READ cycle to address 2XXXXA (hex), in  the 68010 supervisor mode. Table 3-1 is a list of the status bits, with descriptions.

Two 74LS244 tristate drivers (2M and 3M), when enabled, gate the status of the CMB onto the 68010 data bus. (Refer to the CMB Logic Diagram, sheet 19.)  The drivers form a 16-bit-wide, read-only status  register, whose address is 2XXXXA (hex).  Enable signal CMBSTRE- (CMB STatus REad) comes from the READ status de-coder, described  in paragraph 3.2.12.1.

3.2.4.2  CMB Control Register

A CMB control register, in the form of a 74LS259 8-bit addressable latch (10M), is provided for testing purposes.  (Refer to the CMB Logic Diagram, sheet 19.) The register can be written to at address 2XXXXX (hex), in the supervisor mode, and outputs seven bits.  Each bit may be set or cleared by a WRITE cycle to the appropriate unique address for the bit.  Writing a value of 1 sets the corre-sponding bit; writing a value of 0 clears the corresponding bit.

3-5

BFISD 8079

Table 3-1.   Central Microprocessor Board Status Bits

BIT            NAME                         DESCRIPTION

CDOO+          MMERF+            Memory management unit error flag

CD01+          PARITY+           Main memory parity error flag

CD02+          RTCZERO+          Hardware timer count zero interrupt flag

CD03+          PFD+              Power fail flag

CD04+          --                Always high

CD05+          --                Always low

CD06+          BUTTON+           Status of manual reset switch

CD07+          SSWARNF+          Memory management unit stack overflow flag

CD08+          RNGA-             Serial Port A ring indicator

CD09+          DSRA-             Serial Port A data set ready

CD10+          --                Always low

CD11+          RNGB-             Serial Port B ring indicator

CD12+          DSRB-             Serial Port B data set ready

CD13+          --                Always high

CD14+          --                Always low

CD15+          --                Always low

The CMB control register cannot be read.  The various bit functions are shown in table 3-2.

### 3.2.5  Main Memory Fault Detection Circuits

Main memory fault protection is provided by parity generation and checking cir-cuits. Parity bits are stored along with data bits in main memory (i.e., each data byte has an associated parity  bit) and are used to guard against the rare faults in a dynamic RAM chip.  A parity bit is generated on the Central Micro-processor Board for each WRITE cycle to a main memory byte or word location.

Odd parity is used; so, during a READ cycle, whenever the parity detection cir-cuits receive an even parity from a memory location, a fault signal is gener-ated.  (This is an input to the status drivers described in paragraph 3.2.4.1.)

3-6

BFISD 8079

Table 3-2.   Central Microprocessor Board Control Register Bits

ADDRESS  (HEX)   BIT NAME                      FUNCTION

200000        TSTOL          Drives testpoint TP8 high for testing

purposes; otherwise it is always low

200002        TSTERL         Drives test point TP9 high for testing

purposes;  otherwise it is always low

200004        TSTMD+         Inhibits the parallel port drivers; forces

erroneous  parity to be stored in main memory

during WRITE cycles when bit 3 (TSTPE+) of

the control register is high

200006        TSTPE+         Forces erroneous parity to be stored in main

memory during WRITE cycles when bit 2 (TSTMD+)

of the control register is high

200008        TSTSER+        Inhibits the serial port drivers for testing

purposes

20000A        LEDON-         Turns on the LED indicator on the Central

Microprocessor Board

20000C        PTPMSK-        Inhibits detection of parity errors, by

disabling bus error traps caused by parity

errors; any parity errors occuring while this

bit is low will be ignored; the setting of the

parity flag in the CMB status register is not

affected by this bit

The base address of the faulty memory chip is saved in a register (discussed in paragraph 3.2.5.1) to facilitate error logging and error recovery.  A more ob-vious response, however, is the bus error trap generated by the parity check, which discontinues user program execution.

Under normal system operation,  each time a main memory location is written to, a parity value is generated and then stored in the corresponding parity RAM bit.  (Refer to the CMB Logic Diagram, sheet 39.)  The parity value is produced by one of two 74S280 9-bit parity generator/checkers (2V and 3V); which 74S280 will be used depends on which of the two data strobes is active--the upper, the lower, or both.   (Data strobes are explained in the 68010 manual.)  The EVEN output from these devices is sent to the  memory array boards as signals MPARO+ (Memory PARity) and MPAR1+, via connector J3.

Then, when a memory location is read, the parity bits (now labeled MPRO+ and MPR1+) come in from the memory array boards via connector J3.  After passing through a PAL (programmable  array logic) chip (6Y, CMB Logic Diagram, sheet 40), the signals become IPARO+  (Incoming PARity) and IPAR1+ and enter the par-ity generator/checker chips (3V and 2V).  If a parity error is detected by one, or both,  of these  chips,  then three major events will occur in the CMB:

3-7

BFISD 8079

a.  The base address of the faulty memory chip and two bits of GMB status

are stored in a parity error register.

b.  The parity bit to the CMB status driver is set.

c.  A 68010 level 7 interrupt is generated.

3.2.5.1  Parity Error Register

The parity error signals from the 74S280s (2V and 3V) are gated in the parity logic PAL (6Y) to a parity latch (if the memory array boards are enabled [indi- cated by Memory Upper/Lower Data Strobes MUDS+ and MLDS+ active] and a READ cy- cle is in progress [indicated by 68010 Memory ReaD strobe MRD+ active]), inside the PAL.

The PAL parity latch output becomes signal SINT7- (Special INTerrupt, level 7) and is used to create the highest priority interrupt to the 68010,  if a parity error is detected.  The SINT7- output also is inverted by a 74S04 (8W) to be-come clock signal PERADCK+ (Parity ERror ADdress ClocK).  This will clock the base address of the faulty memory RAM, along with two bits of (MB status infor-mation, into the parity error register. (Refer to the CMB Logic Diagram, sheet 41.)  The parity error register comprises a 74S374 transparent latch (3N) and a 74LS240 inverter (3S).

The inputs to the parity error register include the following:

•   The four high-order memory array address bits from the 68010 or from a

peripheral device controller, when  that controller is bus master

•   Signals PERO- (Parity ERror) and PER1-, which indicate which two parity

error signals (MPARO+ or MPAR1+) generated the PERADCK+ signal (which

clocked the parity error register)

•   The non-decoded CFC2+A 68010 function code signal, which, when active,

indicates that the 68010 was not in the user mode.  If the parity error

occurred because of a peripheral device controller fault, this status bit

is undefined

•   The CPU Bus grant ACKnowledge (CBACK+) signal, which, when active,

indicates that a control subsystem other than the 68010 is bus master

The parity error information contained in the parity error register may be ob-

tained by a READ cycle to address 2XXXX2 (hex), in the 68010 supervisor mode.

3.2.5.2  Status Register Parity Bit

The two parity error signals (PERO- and PER1-) from the parity logic PAL (6Y) also are input internally to a parity status flag latch.  (Refer to the CMB Logic Diagram, sheet 40.)  The latch (inside the PAL) generates signal PARITY+.

PARITY+ is an input to the status drivers described in paragraph 3.2.4.1.

3-8

BFISD 8079

3.2.5.3  Parity Error Interrupt Cycle

When a parity error occurs, the SINT7- output from the parity logic PAL (6Y) is asserted.  SINT7- latches  a flip-flop whose Q output then sends a low to the 7 input of an 8-to-3 priority encoder.  (Refer to the CMB Logic Diagram, sheet 22.)  The output forms an interrupt request via three 68010 interrupt request lines, IPLO- through IPL2-.  Since no other interrupt can have a greater 68010 priority, an interrupt acknowledge cycle will begin upon completion of the cur-rent processor instruction.

The 68010 places the interrupt priority level on the lines carrying the three least significant address bits.  These are decoded by a 1-of-8 data selector.

For interrupt level 7, the CVPA- output is low.  In response to CVPA- low, the 68010 generates a vector number based on the interrupt level number.  The con-tent of the vector number is fetched from RAM and then loaded into the 68010 program counter, and normal instruction execution commences in an interrupt service routine.  (Interrupt logic is discussed further in paragraph 3.2.6.)

System software now can read the status register and discover that it was a memory parity error that initiated the interrupt cycle. The program can then go on to read the parity error register and find the base address of the RAM that caused the memory fault.

### 3.2.6 Interrupt Logic

There are at least two general strategies for control of input/output (I/O) in a computer system.  One is initiated by the processor (program-controlled), and the other is initiated by the I/O port (interrupt-driven).  The difference be-tween the two is in  the method used  to determine when a port has completed an operation.  In the case of interrupt-driven I/O, the port provides an interrupt request signal to the processor (CPU) when an operation has been completed.

Then, when the processor is at a point where the program in process can be sus-pended temporarily, the processor will commence with I/O operations.  Upon com-pletion of I/O operations, the processor continues with the suspended program.

Since there are several circuits and I/O devices in the Model 4108 Base Unit that require interrupt processing, a technique for identifying the source and the priority level of the interrupt request is provided.  The method used is vectored interrupts.

Generally, this means that a device requesting an interrupt is required to send a vector number to the processor for translation into the starting address of the appropriate interrupt service routine.  Specifically, the requesting device sends a priority number to the 68010 as part of the interrupt request signal; then it sends the vector number as a separate signal after receiving an inter-rupt acknowledge signal from the 68010.

There are seven levels of interrupts available on the 68010, with level 7 being the highest priority.  In the Base Unit, levels 2 and 4 may be auto-vectored or bus-vectored (both are explained in paragraph 3.2.6.1); levels 1, 3, 5, 6 and 7 are always autovectored.  The seven interrupt levels are configured as follows:

3-9

BFISD 8079

LEVEL                        SOURCE

1           Parallel port, from the PI/T (local)

2           System I/O bus peripheral device controllers

3           Floppy disk controller (local)

4           System I/O bus peripheral device controllers

5           Serial ports, from the SCC (local)

6           PI/T timer—real time clock count is zero (local)

7           Power fail, reset,  parity error (non-maskable interrupt)

3.2.6.1   Interrupt Control Logic

When a device requires interrupt servicing, it asserts one of the seven INT(X)-(INTerrupt level X) signals.  These are encoded by a 74LS148 8-to-3 priority encoder (3E). (Refer to the CMB Logic Diagram, sheet 22.)  The output consti-tutes an interrupt request via the three 68010 interrupt request lines, IPLO-through IPL2-. If the priority of the interrupt is greater than the current 68010 priority, then the interrupt acknowledge cycle begins as follows:

Autovectored Interrupts

The 68010 places the interrupt priority level on the lines carrying the three

least significant address bits.  These are decoded by a 74LS151 l-of-8 data

selector (10K). For interrupt levels 1, 3, 5, 6 and 7, the CVPA- (CPU Valid

Peripheral Address) output of the data selector is low (active); for inter-

rupt levels 2 and 4, the CVPA- output is active only when the AVTR- (Auto-

VecToR) input, from the system I/O bus, also is active.

In response to CVPA- active, the 68010 internally generates a vector number

that is determined by the interrupt level number.  (The vector number [when

multiplied by four] is the address, in the lowest 1K bytes of main memory,

containing the beginning address of the routine that handles the interrupt.)

The content of the vector number is fetched and then loaded into the 68010

program counter, and normal instruction execution commences in the interrupt

service routine.  This is the autovectored interrupt mode of the 68010.

Bus-Vectored Interrupts

Interrupt levels 2 and 4 are bus-vectored when (a) they are selected by the

data selector (10K) and (b) data selector input AVTR- (AutoVecToR), from the

system I/O bus, is inactive.  In this mode, the interrupt priority level on

the 68010 lines carrying the three least significant address bits also is

used as an address in a 68010 READ cycle.  During the cycle, the 68010 ob-

tains an 8-bit vector number from the peripheral device controller that is

addressed by those bits.

3-10

BFISD 8079

Then, as in the autovectored case, the content of the vector number (after

multiplication by four) is fetched and then loaded into the 68010 program

counter, and normal instruction execution begins in the interrupt service

routine.  This is the bus-vectored interrupt mode of the 68010.

The data selector (10K) thus is used to switch between autovectoring and bus-vectoring for interrupt levels 2 and 4. The data selector is enabled only when signal FDC7- (Function DeCode 7) is asserted,  signifying an interrupt acknowl-edge cycle is in process.

3.2.6.2  Interrupt Acknowledge Decoder

At the same time that the priority number on the address bus was being decoded to produce CVPA-, a 74LS138 l-of-8 decoder (10L, CMB Logic Diagram, sheet 20) also decoded those address bits.  The IACKL3-, IACKL5- and IACKL7- (Interrupt ACKnowledge Levels 3, 5 and 7) signals are direct outputs.  IACKL3- is used by the floppy disk controller, IACKL5- enables the byte multiplexer control logic, and IACKL7- is used by the interrupt control logic and the parity logic.  Two signals, IACKL5- and IACKL7-, also are decoded with the other decoder outputs to create signals RIACK+ and RIACK- (I/O bus Requester Interrupt ACKnowledge).

RIACK+ provides the Processor Data Transfer ACKnowledge (PDTACK-) signal back to the 68010, and RIACK- provides the data bus direction control.  Like the data selector, the decoder (10L) is enabled when FDC7- (Function DeCode 7) is active, and indicates a 68010 interrupt acknowledge cycle is in process.

### 3.2.7  Reset and Power Fail Detection Logic

The Central Microprocessor Board contains logic circuitry for three forms of reset: (1) power-on, (2) button, and (3) software.

Power-on reset and button reset are electrically similar.  Power-on reset is automatic on power-up and generates a 100- to  800-millisecond reset pulse via an NE555 timer (5B).  (Refer to the CMB Logic Diagram, sheet 21.)  Power-on reset also generates a level 7 interrupt.

Button reset is actuated by the case-mounted switch, which is debounced by a 74LS00 NAND gate (4E).  The output is RSTF2+, the master ReSeT Flag signal.

The signal becomes POR- (Power-On Reset), which maps the boot PROM in all mem-ory; generates HLT- (HaLT) for the 68010; and generates a RESET- for the system I/O bus and a CRESET- for devices on the Central Microprocessor Board.

The 68010 has a bidirectional reset pin (RST-), which receives the reset signal during a power-on reset or a  button reset.  On a software-created reset, the 68010 pulls RST- low, which causes the reset circuitry to issue a RESET- to the system I/O bus and a CRESET- for devices on the Central Microprocessor Board.

The signal PFD+ (Power Fail Detect) comes in on the system I/O bus to warn that power supply failure is imminent and generates an INT7- (INTerrupt level 7, the non-maskable interrupt).

3-11

BFISD 8079

### 3.2.8  System I/O Bus Control Logic

The system I/O bus provides data, address, timing and control functions to the various peripheral device controller boards that connect to the Central Micro-processor Board  (CMB).  The bus timing/control interface on the CMB includes arbitration logic, address and data gating controls, and bus transaction con-trol signals*

All control lines from the 68010 are driven onto the system I/O bus. (Refer to the CMB Logic Diagram, sheet 14.)  Signals CAS- (CPU Address Strobe), CLDS- (CPU Lower Data Strobe), CUDS- (CPU Upper Data Strobe) and CRNW- (CPU Read Not Write) are driven onto the system I/O bus by a 74S244 tristate buffer (1H) to become AS—, LDS-, UDS- and R/W-.  These signals are driven on the I/O bus when the 68010 has control of that bus (indicated by signal CBACK+ inactive).  Since both ends of the buffer are pulled up by resistors when the 68010 is tristated (indicated by CBACK+ active), the I/O bus end can be driven by a peripheral de-vice controller, when that controller has control of the system I/O bus.

Function code signals CFCO+ through CFC2+ (CPU Function Codes 0 through 2) are driven onto the system I/O bus by a 74S240 tristate inverter (IF) to become FCO-, FC1-, and FC2-.  The signals are driven onto the bus when the 68010 has control of the bus, Since the I/O bus end of the buffer is pulled up by resis-tors when the 68010 is tristated, the I/O bus end can be driven by a peripheral device controller, when that controller has control of the system I/O bus.

The CPU Lower and Upper Data Strobes, CLDS- and CUDS-, are ORed together by a 74S08 AND gate (7T) to provide signal CDS- (Combined Data Strobe), which is as-serted when either or both data strobes from the 68010 are asserted.  This sig-nal is not driven onto the system I/O bus.

The CRNW- (CPU Read Not Write) signal is buffered and inverted by a 74LS00 NAND gate (9T) to produce RD- (ReaD), which is asserted when the 68010 either is in a READ cycle or is tristated. CRNW- is buffered by a 74LS32 OR gate (9V) re-produce WR- (WRite), which is asserted when the 68010 is in a WRITE cycle.

### 3.2.9  Non-Volatile RAM

For flexibility; the MAI® 2000 Series system allows the system console to be chosen from several kinds of terminals and to be connected to any available serial port.  Likewise, the kind of device used to load, or boot, the operating system and the port location of that device can be chosen from several combina-tions.  Also, a serial or a parallel default printer can be chosen, and the ap-propriate baud rate can be selected for the serial printer. Finally, a down-load device (e.g., a tape streamer) and port location may be chosen.

During system initialization, all these hardware configuration parameters must be communicated to the boot program.  This is so the correct peripherals are logically connected to the system while, and after, the operating system soft-ware is loaded into main (RAM) memory.  The following list is a summary of the parameters required by the operating system software while that software is be-ing "booted."

3-12

BFISD 8079

•  System boot device, unit number and baud rate

•  System console terminal type, port and baud rate

•  System printer port and baud rate, if serial

•  System download port and baud rate

The Central Microprocessor Board provides a means for inputting the parameters and for storing them while power is off.  The parameters are stored in a 64 X 4 non-volatile random-access memory chip (4L), or NVRAM.  (Refer to the CMB Logic Diagram, sheet 36.)  The NVRAM comprises a read/write RAM section and an elec-trically-alterable read-only memory (EAROM) data storage section.

The address space in which the NVRAM resides is partitioned into two interlaced segments, each containing 32 addresses (only one segment currently is used).  A normal data READ or WRITE cycle is performed by a byte READ or WRITE to one of the (hexadecimal) addresses listed in table 3-3.

The addresses (bits A01+A through A08+A) come from the buffered address lines of the 68010.  Since there is no A00 bit from the 68010 with the correct timing for the NVRAM, A08+A is used for the A00 input to the NVRAM (this accounts for the interlaced segments previously mentioned).  Also note that the NVRAM does not have A6 and A7 address bit inputs; but the corresponding lines are connect-ed for future expansion to a 256 X 4 NVRAM.

The data lines (BDOO+ through BD03+) are the buffered data lines of the 68010.

The WRite (WR-) signal comes from the buffered CRNW- (CPU Read Not Write) line of the 68010.

Signals NVRCE- (Non-Volatile RAM Chip Enable), NVRST- (Non-Volatile RAM STore), and NVRRC- (Non-Volatile RAM ReCall) are I/O address control lines.  They are asserted when the following memory locations are addressed in the 68010 super-visor mode (X = "don't care").

ADDRESS

(HEX)             SIGNAL

68X000-68X03E         NVRCE-

68X100-68X13E         NVRCE-

6AXXXX                NVRST-

6CXXXX                NVRRC-

The two additional addresses, 6AXXXX and 6CXXXX, are provided for store cycles and recall cycles.  A recall cycle transfers data from the EAROM section of the NVRAM to the RAM section; and a store cycle transfers data from the RAM section to the EAROM section.  This allows the programmer to reconfigure the NVRAM to the requirements of the system.  After system power-up, data can be read from the NVRAM.

3-13

BFISD 8079

The data must first be recalled from the EAROM section by a supervisor READ to memory location 6CXXXX, which transfers the data to the RAM section.  Then, the data may be read by doing supervisor reads to as many 68XOYY locations as is necessary (OYY is the NVRAM internal address).  Remember: Bits A01 through A05 address one 32-location segment in the NVRAM; A08 addresses one of the two seg- ments;  and A06, A07 and A09 through A16 are "don't cares."

Data can be written to the NVRAM by doing as many supervisor writes to memory locations 68XYYY as is necessary.  If the newly-written data is to be stored after power-down, then a store cycle must be done before power-down by a super-visor READ to location 6AXXXX, which transfers the data to the EAROM section.

No further accesses of the NVRAM should be attempted for 9 milliseconds after a store cycle.

IMPORTANT

The vendor guarantees the NVRAM for

no more than 1,000 store operations.

Each location in the NVRAM is dedicated to a specific parameter. Programming information is contained in tables 3-3 and 3-4.

### 3.2.10  Data Transfer Acknowledge Generator

As an asynchronous processor, the 68010 requires signal PDTACK- (Processor Data Transfer ACKnowledge) to be returned during every memory bus cycle.  This input indicates that the data transfer is completed.  When the 68010 recognizes the PDTACK- signal during a READ cycle, data is latched in the 68010, and the bus cycle is terminated; when the 68010 recognizes PDTACK- during a WRITE cycle, the bus cycle is terminated.

This "handshaking" technique allows the 68010 to compensate for the different access times  of the various devices on both the local bus and the  system I/O bus. If PDTACK- is returned to the 68010 before the end of processor "state 4" (refer to the 68010 manual), then the 68010 will act like a synchronous proces- sor and complete the bus cycle at the maximum possible speed.

However, if PDTACK- is not returned by the end of state 4, then the 68010 will insert wait states until it receives the signal.  Moreover, if PDTACK- is not returned within a set amount of time, then a bus error will occur, causing the 68010 to process a bus error exception cycle (i.e., the 68010 is forced to stop processing the  current program and begin executing a special service routine).

During normal operation, though, when PDTACK- is returned, the 68010 continues with state 5 and completes the bus cycle.  At the end of the bus cycle, PDTACK-must be negated (sent  high) when the Address Strobe (AS-) is negated by the 68010, so it does not interfere with the beginning of another bus cycle.

3-14

BFISD 8079

Table 3-3.  NVRAM Contents

NVRAM ADDRESS                         CONTENT

680000       Boot device type

680002       Boot device unit number

680004       Boot device baud rate (if applicable)

680006       Console device type

680008       Console device unit number

68000A       Console device baud rate

68000C       Printer device type

68000E       Printer device unit number

680010       Printer device baud rate (if applicable)

680012       Download device type

680014       Download device unit number

680016       Download device baud rate

680018       Reserved

68001A       Reserved

68001C       Reserved

68001E       Reserved

680020       Reserved

680022       Reserved

680024       Reserved

680026       Reserved

680028       Reserved

68002A       Reserved

68002C       Reserved

68002E       Reserved

680030       Reserved

680032       Reserved

680034       Reserved

680036       Reserved

680038       Console terminal type

68003A       Not used

68003C       Checksum (left nybble)

68003E       Checksum (right nybble)

3-15

BFISD 8079

Table 3-4.  Device Nybble Specifiers

PARAMETER                            NYBBLE SPECIFIER

Device Type

Serial Communications Controller                      0

4-Way Controller                                      1

Floppy Disk Controller                                2

Winchester Disk Controller                            3

Winchester Disk Controller (NEC)                      4

Magnetic Cartridge Streamer Controller                5

Parallel I/O (PI/T)                                   6

Unit Number

Serial Communications Controller                      0-1

4-Way Controller                                      0-15

Floppy Disk Controller                                0-1

Winchester Disk Controller                            0-1

Winchester Disk Controller (NEC)                      0-1

Magnetic Cartridge Streamer Controller                0

Parallel I/O (PI/T)                                   0

Baud Rate

110                                                 1

150                                                 2

300                                                 3

1200                                                 4

2400                                                 5

4800                                                 6

9600                                                 7

19200                                                 8

Terminal Type

DUMB                                                  0

EVDT                                                  1

7270                                                  2

3-16

BFISD 8079

Although the main system RAM memory is designed not to require wait states, the various "slower" peripheral chips on the Central Microprocessor Board do need wait states.  The following paragraphs describe the hardware that generates the PDTACK- signal, and also introduce the Bus ERRor Flag (BERRF-) signal and in-clude a list of the wait states for the various slave devices.

3.2.10.1  Timing Generation

Circuits on the Central Microprocessor Board (CMB) produce appropriate timing signals for PDTACK-. A 74S299 8-bit shift register (7K, CMB Logic Diagram, sheet 6) generates the timing pulses, which are used throughout the CMB.  After selection and gating, the pulses produce PDTACK- signals with differing timing, depending on the device being accessed (discussed in paragraph 3.2.10.2).  Be-fore a 68010 bus cycle begins, the shift register is held reset during the fol-lowing two conditions.

•  Before the address strobe (AS-) is asserted during the memory READ or

WRITE portion of a normal (READ or WRITE) bus cycle

•  A READ-MODIFY-WRITE cycle (a 68010 TAS instruction), between the READ and

the WRITE portions of the cycle.  AS- stays asserted during this period;

therefore, the AND of UDS- and LDS- (Upper and Lower Data Strobes) resets

the shift register, both signals being high during the period.  The Read/

Write (R/W-) signal is ANDed with UDS- and  LDS-, which prevents the shift

register from being held reset for an additional clock cycle during the

beginning of a normal 68010 WRITE cycle

At the beginning of a READ or a WRITE cycle, address strobe AS- is asserted and sent, via a 74S02 NOR gate (9N) and a 74S08 AND gate (8Y), to the shift regis-ter CLEAR input, releasing the cleared condition.  The pulled-up high level on the SR input of the register then is shifted right with each K8MHZ+ clock tick.

Since the 68010 does not need PDTACK- for autovectored interrupt acknowledge cycles, the CVPA- signal, active during the autovector interrupt, is ORed in the AND gate (8Y) so that the bus error flip-flop (6K,  discussed in paragraph 3.2.10.3) is reset.

3.2.10.2  Timing Selection

To simplify the selection of the appropriate PDTACK- timing pulses, devices re-quiring the same timing are grouped  into common memory address spaces. Since eight spaces are provided (discussed in paragraph 3.2.12), the required timing signal can be selected merely by decoding three  high-order address bits A214A through A23+A. (Refer to the CMB  Logic Diagram, sheet 6.)  This is done with a 74S151 data selector (8K), which selects the  shift register output to be used to create the PDTACK- signal. The data selector is enabled only during the 68010 supervisor mode or an interrupt acknowledge cycle (when CFC2- is active).

The following list shows the number of wait states inserted in the 68010 bus cycle for each device addressed.

3-17

BFISD 8079

A23+A-A21+A WAIT STATES               DEVICE ADDRESSED

000          4            Boot PROM during boot; system memory otherwise

001          0            Local CMB status registers

010          4            Boot PROM

011          14            Local I/O (floppy controller; serial and

parallel ports;  Baud rate selection)

100          0             Memory management unit control

101          0             Memory management unit control

110          0             Peripheral I/O controllers (external DTACK-)

111          0             Interrupt acknowledge (external DTACK-)

Note: One cycle of the clock equals two wait states (125 nanoseconds).

The actual PDTACK- that goes to the 68010 processor comes from five different sources.  Three of these are enabled by 74S38 open-collector NAND gates.  One NAND gate (7N) enables PDTACK- for a system I/O bus-vectored interrupt acknowl-edge.  Another NAND gate (8J) enables PDTACK- from the data selector (8K); sig-nal CBACK- is ANDed in this gate for the following reason.  When the 68010 is tristated (i.e., is no longer bus master), the address and strobe outputs from the 68010 are floating.  This causes spurious outputs from the data selector, which would cause spurious PDTACK- signals.

One NAND gate (7N) does nothing.  A fourth NAND gate (7N) enables the PDTACK-signal from the floppy buffer memory.  This allows only 4 wait states during access of that memory,  instead of the 14 wait states required by the floppy disk controller registers.

The fourth PDTACK- source is from the 68230 PI/T,  which has a DTACK- generator built in.  The fifth PDTACK- source is from a memory array board, and depends on which board is selected and whether  or not a memory management error has taken place.  The PDTACK- signal from the memory array board is gated onto the system I/O bus by another  74S38 (8J)  when a system I/O bus peripheral device controller is bus master (indicated by the CBACK+ signal active).

3.2.10.3  Bus Error Generation

If, after eight shifts, the PDTACK- signal is not active, then the shift reg-ister (7K) will act as a "watchdog" timer.  The inactive (high) PDTACK- signal is ANDed in a 74LS08 AND gate (9S) with the least significant bit output (H/QH) from the register.  The result is latched by a 74S74 D flip-flop (6K), and the Q- output provides the Bus ERRor Flag (BERRF-).  (This bus error flip-flop is toggled on the rising edge of the K8MHZ- clock.)  The BERRF- signal then is re-turned to the 68010, forcing it to process the bus error exception cycle.

3-18

BFISD 8079

The bus error flip-flop will reset when the shift register (7K) is cleared or the CVPA- signal is asserted.  The timing of the shift register and bus error generation is shown in figure  3-2.

When a peripheral device controller is the bus master, the bus error flip-flop Q output is gated onto the system I/O bus as BERR- by the bus grant acknowledge signal (CBACK+, discussed in paragraph 3.2.11), via another 74LS38 NAND gate (3F).  After the bus error occurs, the bus error flip-flop is reset by the ad-dress strobe (AS-) going high when the bus error exception processing begins.

### 3.2.11  Bus Arbitration Logic

All peripheral controllers that plug into the Central Microprocessor Board use direct memory access (DMA) techniques to transfer data to and from the system main memory.  This means that each controller will need to have complete rule over the system I/O bus at some point in time, for some length of time.  The purpose of arbitration is to give that controller a guarantee of conflict-free access to the bus.

To achieve this, the system includes arbitration logic circuits, collectively called the arbiter.  Most of the logic is contained on the peripheral control-ler boards, allowing position-independence of the boards with respect to the system I/O bus slots.

W = Wait state

Figure 3-2. Timing Diagram, PDTACK- and Bus Error Generation

3-19

BFISD 8079

The arbiter prioritizes bus access requests by devices (i.e., peripheral con-trollers) aspiring to bus mastership.  The design of the arbiter is such that the 68010 always wants the bus, but gets it only when no other device wants it.

This means that the 68010 is the lowest-priority device in the system, giving up the bus to any requesting device as soon as possible.  Such a scheme allows the highest processing speed, because the 68010 never has to take the time to request the bus--access is automatic upon release by the current master.

Although the 68010 does not prioritize requests for bus accesses by external controller boards, or devices, it nonetheless is part of the arbitration logic circuitry.  There are three bus arbitration signals used in the 68010:

a.  Bus Request (BR-1)

b«  Processor Bus Grant (PBG-)

c,  CPU Bus grant ACKnowledge (CBACK-)

(Specific details of the signals can be found in the 68010 manual, under BR-, BG-, and BGACK-.)  When the 68010 is using the system I/O bus without competi-tion, input signals BR-1 and CBACK- and output signal PEG- are inactive (high).

System bus arbitration begins when the bus request signal (BR-1) is asserted (low).  A bus request can come from a system I/O bus peripheral (on connector J01, pin A13) or from the memory refresh circuitry.  (Refer to the CMB Logic Diagram, sheet 8.)  The bus request signal is buffered by a 74S244 tristate driver (IE) and sent to the 68010.  At the time of the bus request signal, the priority resolution cycle begins.

Bus access prioritization is done with the aid of three parallel arbitration signals: BPRO- through BPR2- (Bus PRiority).  These are placed on a special three-line priority bus by the contending devices.  The signals represent the priority number of the device, which is set by switches or held in a register. When the device issues the bus request signal, it places the unique priority number on the priority bus and samples the bus signals at the same time.

This is allowed because the bus lines are encoded in such a way that the three lines can represent only four possible numbers.  Each line carries the (wire-) OR of corresponding signals from all contending devices.  When a device places an asserted  signal on a line, the low level pulls down that line, taking pre-cedence over the highs.  Thus the signals always indicate the highest number placed on the priority bus.  The priority bus signals are synchronized by an 8-MHz Constant CLocK (CCLK-) signal, which is generated on the Central Micro-processor Board.  (Refer to the CMB Logic Diagram, sheet 5.)

3.2.11.1  Bus Arbitration Cycle

To minimize the number of priority bus lines required for the arbitration logic to be able to select up to 16 devices, logic is included that samples the three lines twice during each arbitration cycle.  The resulting two steps in the pri-ority bus examination process are as follows:

3-20

BFISD 8079

a.  The priority bus signals indicate the highest number of four groups

of four devices, one or more of which is requesting the system I/O

bus.  The group with the highest priority number on the bus qualifies

to continue with the second step; any competing groups with smaller

numbers may continue the bus request signal (BR-1).

b.  During the second half of the clock period, the priority bus signals

indicate the highest number of the four devices within the qualified

group.  At the end of the clock period, the contending device with the

highest priority number responds to the bus grant signal (PBG-).

After a system I/O bus device controller or the refresh circuitry has received the bus grant signal (PBG-),  the responding device must monitor the following three signals to determine when the system I/O bus actually is available for use.

•  Address strobe (AS-) - must be negated, indicating that the 68010, or

another bus  master, has completed the current bus cycle

•  Data transfer acknowledge signal (DTACK-) - must be negated, indicating

that the slave device accessed by the 68010 is no longer on the main

memory data bus

•  Bus grant acknowledge signal (CBACK-) -must be negated, indicating that

no other peripheral device controller presently is using the system I/O

bus

The winning device must wait until allthese conditions are met before it may assume control of the system  I/O bus.  When the conditions are met, the device taking the bus leaves its priority number on the priority bus and asserts the BGACK- signal.  BGACK- is buffered by a 74S244 tristate driver (1E) and sent to the 68010 as CBACK-.  There is at least a one-clock-period delay between CBACK- and PBG-; it is during this period the prospective bus masters arbitrate.  (A 74S240 inverter [1Y] increases the drive capability of CBACK+; signals CBACK- and CBACK+ are delivered throughout the Central Microprocessor Board to enable various other signals.)

3.2.11.2   Fast Bus Grant

When the asserted bus grant (PBG-) signal was sent to the controllers, it was ORed with signal  FBG- (Fast Bus Grant) in a 74LS08 AND gate (7T).  The output from the gate is buffered by a 74S244 tristate driver (1E) and then placed on the system I/O bus (connector J01, pin C13) , to be delivered to the peripheral device controller boards.  The fast bus grant signal is generated to give the controllers more time for bus arbitration during heavy DMA activity.

Signal FBG- is asserted only when a 68010 memory bus cycle is underway and the 68010 would give a bus grant anyway.  FBG— is asserted on the falling edge of the K8MHZ- clock when (a) there is a bus request, (b) the address strobe is ac-tive, and (c) timing signal CSTOF+ still is low.  Although the resulting window is not very long, it can help to speed up heavy DMA activity.

3-21

BFISD 8079

### 3.2.12  Address Space Decoding Logic

Some devices on the Central Microprocessor Board are meant to be read from and written to, and others are meant to be read-only or write-only.  (Table 3-5 shows the address space decoding.)  This allows a simplification in design, in that a READ or a WRITE strobe may be combined with the chip enable strobe going to the restricted device.

Table 3-5.  Address Space Decoding

ADDRESS

(HEX)        READ/WRITE                  DEVICE ENABLED

OXXXXX          Both           PROM at reset, main memory after first WRIT

2XXXXO          WRITE          Test Point TSTOL

2XXXX2          WRITE          Test Point TSTERL

2XXXX4          WRITE          Inhibit parallel port and parity

2XXXX6          WRITE          Parity data forced

2XXXX8          WRITE          Inhibit serial port drivers

2XXXXA          WRITE          Turn on LED

2XXXXC          WRITE          Inhibit parity response

2XXXX2          READ           Memory Parity Error Upper Register

2XXXX4          READ           Memory Parity Error Lower Register

2XXXXA          READ           CMB Status READ

2XXXXE          READ           CMB general status READ

4XXXXX          READ           System PROM

60XXXX          Both           SCC I/O (serial ports 0 and 1)

62XXXX          Both           PI/T I/O (parallel port)

64XXXX          WRITE          Baud Rate Selector

68XXXX          Both           NVRAM READ/WRITE

6AXXXX          READ           NVRAM store

6CXXXX          READ           NVRAM recall

70XXXX          WRITE          Floppy address counter reset

72XXXX          READ           Floppy status (read only)

76XXXX          WRITE          Floppy control latch WRITE

78XXXX          Both           Floppy controller chip select

7AXXXX          Both           Floppy buffer READ/WRITE

8XXXXX          WRITE          MMU base WRITE

AXXXXX          Both           MMU limit write/status READ

CXXXXX          Both           System I/O bus device controllers

3-22

BFISD 8079

This is done with decoder chip 7Z.  (Refer to the CMB Logic Diagram, sheet 9.) The chip decodes A20+A, A21+A, A22+A and A23+A, the four high-order address bits from the 68010 (via address drivers).  Three decoder outputs are active during READ cycles only; four outputs are active during WRITE cycles only; and one output is active during both READ and WRITE cycles (MDENB+). Except for the MDENB+ (Memory Data ENBable) line, the output lines are enabled only in the 68010 supervisor mode (when signal FDC5R6+ [Function DeCode 5 oR 6, explained in paragraph 3.2.2] is asserted).  An address space decoding diagram is shown in figure 3-3.

TBD

Figure 3-3.  Address Space Decoding Diagram

3-23

BFISD 8079

3.2.12.1  READ Cycle Decoding

When the decoder chip (7Z) is used for READ cycles, signal RD- must be active, and BOOT+ must be inactive (low),  to enable the decoder.  BOOT+ active enables the Boot PROMs,  rather than the system memory,  for all addressing at reset.

When the first WRITE cycle is processed, however, BOOT+ is negated; this allows the initial vectors to be obtained from the PROMs at reset time and then to be modified after that. Signal RD- is an inverted R/W- (Read/Write) signal from the 68010.

Another decoder, a 74S138 (4K), generates two status READ strobes, using low-order address bits A01+A, A02+A, and A03+A, from the 68010.  These strobes are used to read the CMB status register and the parity error address.

3.2.12.2 WRITE Cycle Decoding

Most of the WRITE cycle outputs from the address space decoder chip (7Z) are used to clock data into registers on the trailing edge.  To ensure that the data still is valid when clocked into a register, signal CDS- (instead of a de-rivative of the address strobe [AS-]) is used as one of the enable inputs for the decoder chip. (CDS- must be asserted to allow WRITE cycle decoding.)  CDS- (Combined Data Strobe) is the OR of the upper and lower data strobes (CLDS- and CUDS-) from the 68010.  The enable inputs of the WRITE cycle decoder also re-quire an active WR- (WRite) signal, which is the buffered R/W- control signal from the 68010.

3.2.12.3 Memory Select Decoding

Signal MDENB+ (Memory Data ENaBle,  explained in paragraph 3.2.15.3), from the address space decoder chip (7Z), goes to the memory array boards.  (Refer to the CMB Logic Diagram, sheet 9.) MDENB+, in combination with MAD17+ through MAD20+, on the memory array boards, selects one of a maximum of six boards.

MDENB+ is enabled by one of three possible conditions.

The three conditions are as follows:

o  A peripheral has control of the  system I/O bus - all communication with

the Central Microprocessor Board is through memory; signal CBACK- (Cpu Bus

grant ACKnowledge,  explained in paragraph  3.2.11) is active during this

condition and is an input to the address space decoder (7Z).

o  The 68010 is in user mode - all  accesses are to memory rather than I/O;

signal CFC2+A (Function Code 2 from the 68010,  explained in paragraph

3.2.2) is inactive during the user mode and is an input to the address

space decoder (7Z).

o  The 68010 is in supervisor mode  - except during boot, all accesses to ad-

dresses 000000  through 1FFFFF are to memory.  FDC5R6+ (Function DeCode 5

oR  6, explained in paragraph 3.2.2) is active during the supervisor mode

and is an input to the address space decoder (7Z).

3-24

BFISD 8079

When MDENB+ is inactive, column address strobes are prevented from going to the memory array boards, thereby deselecting the main memory. (A column address strobe is one of two enable signals required by a dynamic RAM chip--the other signal is the row address strobe [both are explained in paragraph 3.2.15].)

3.2.12.4  Local I/O Decoding

Some of the local I/O devices (e.g., floppy disk controller, PI/T,  etc.) must receive single, rather than separate, enable strobes  for both  READ cycles and WRITE cycles.  These are provided by the local I/O decoder chip (8Z).  (Refer to the CMB Logic Diagram, sheet 10.)  Address bits A04+A, A05+A, A08+A, and A17+A through A23+A are input to the decoder chip.  In addition, READ signal RD-, Combined Data Strobe CDS-, Processor Data Transfer ACKnowledge strobe PDTACK-, and the Function DeCode  5 oR 6 (FDC5R6+) control signal are input to the local I/O decoder chip to further qualify the chip's output signals.  The resulting strobes, with their qualifying (hex) addresses, are as follows:

CMBRE- (read CMB status)           2XXXXX/3XXXXX

Z80IO- (byte mix/floppy control)   6XXXXX/7XXXXX

SCCCE- (serial ports)              60XXXX

PITCE- (parallel port)             62XXXX

ENBRREG-  (Baud rate selector)     64XXXX

NVRCE- (NVRAM READ/WRITE)          68XXXX

NVRST- (NVRAM store)               6AXXXX

NVRRC- (NVRAM recall)              6CXXXX

### 3.2.13  Byte Interface Control Logic

An 8-bit-wide local data bus is present on the Central Microprocessor Board. All the local byte-wide chips operate off this bus.  These include the Floppy Disk Controller (FDC), the Serial Communications Controller (SCC), the Parallel Interface/Timer (PI/T), and the non-volatile RAM (NVRAM).  The byte-wide local data bus is controlled by strobes LUDS- (Local Upper Data Strobe) and LLDS- (Local Lower Data Strobe).  (Refer to the CMB Logic Diagram, sheet 25.)

The 16-bit data bus from the 68010 is multiplexed by two 74LS245 bidirectional buffers (2L and 3L), whose direction is controlled by WR-,  the READ/WRITE sig-nal.  A buffer is enabled when the 68010 is either accessing local I/O (Z80IO- active) or processing an Interrupt ACKnowledge Level 5 (IACKL5- active).

### 3.2.14  Memory Address Bus

The address bus to the memory array boards consists of eight multiplexed ad- dress lines and four memory array board select lines.  (The multiplexed address lines are required by the dynamic RAM chips [explained in paragraph 3.2.15].

High-order ["column"] addresses or low-order ["row"] addresses are placed on the multiplexed lines; signal CADSEL+, from the dynamic memory support logic, selects between the two groups.)  The address lines and board select lines are explained in the following paragraphs.

3-25

BFISD 8079

3.2.14.1  Memory Array Board Selection

MAD17+ through MAD20+ are the memory array board select strobes.  (Refer to the CMB Logic Diagram, sheet 39.)  The strobes are generated in one of two ways:

•  When the 68010 is in the supervisor mode,  or a system I/O peripheral

device controller is  the bus master, system I/O bus address  bits AB17-

through AB20-  are driven onto  the memory address bus; the driver is a

74S240 tristate inverter (1Y), enabled by signal PAENB- asserted.

•  When the 68010 is in the user mode, address bits A17+A through A20+A,

translated by the memory management unit, are driven onto the memory

address bus; the driver is a 74S244  (1Z) enabled by PAENB+ inactive.

Signal PAENB- (Physical Address ENaBle) is derived from the OR of CBACK- and CFC2-.  (The two signals are ORed in a 74LS08 AND gate [7W, CMB Logic Diagram, sheet  38].) PAENB- active indicates either the 68010 is in the supervisor mode (CFC2- active) or a peripheral controller  is the  bus master (CBACK- active).

Address bits MAD18+ through MAD20+ select a memory array board, and bit MAD17+ selects between two 128K-byte banks of 64K X 1 RAM chips on the board.  Note that signal  MDENB+ also must be low for a memory array board to be selected.

3.2.14.2  Memory Address Bus Multiplexing

When the dynamic RAM memory timing circuit first asserts the row address strobe (MRAS+), the CADSEL+ (Column ADdress SELect) strobe is low. (Refer to the CMB Logic Diagram, sheets 37 and 38.)  This enables a 74S244 tristate driver (IV) and places low-order address bits AB01- through AB08- onto the memory address bus (which carries the multiplexed address bits [MAI- through MA8-] to the mem-ory array boards). Address bits AB01- through AB08- come from one of the fol-lowing three sources.  (Refer to the CMB Logic Diagram, sheets 12, 13 and 24).

•  The 68010,  via a 74LS244 driver (4S)

•  A  system I/O bus peripheral device controller, via connector J02

•  The dynamic RAM refresh circuitry, via 74LS240 inverters (1T and 1Y)

Then, after a 60-nanosecond delay, CADSEL+ goes high and the 74S244 driver (1V) delivering the low-order address bits turns off.  Now the memory address bus receives high-order addresses from one of the following two sources.

•  System I/O bus address bits AB09- through  AB16-. These come from the

68010, when it is in the supervisor mode, or from an I/O bus peripheral

device controller, when that controller is the bus  master; the driver is  a

74S244 (1W) enabled by an OR of those conditions (CBACK+ or CFC2+A high).

•  Address bits A09+A through A16+A.  These are translated addresses from the

memory management  unit (explained in paragraph 3.2.16.5) and are selected

with the 68010 in the  user mode; the driver  is a 74S240 (IX, CMB Logic

Diagram, sheet 30) enabled by a NAND of signals PAENB- and CADSEL+ high.

3-26

BFISD 8079

### 3.2.15  Dynamic Memory Support

The memory array boards,  which plug into the Central Microprocessor Board, use dynamic RAM chips.  Interfacing with these is more complex than for static RAM chips. This is because the dynamic RAM chips require address multiplexing, for which timing is more critical.  The dynamic RAM chips are arranged internally in two-dimensional arrays of bits; each has a row address and a column address.

Both addresses share common lines; hence the requirement for the multiplexing of addresses.

The multiplexing of addresses requires one more pin for control than on static RAM chips.  The chip select of a static RAM chip has been replaced by row and column selects.  These indicate which address is on the address lines when the chip is selected.  (The low-order address bits from the bus master become the row address, and the high-order bits become the column address.)

Input signals to the row and column selects are called row and column address strobes.  The timing of the strobes and the address bits is critical.  The row address has to be held long enough to satisfy setup and hold-time constraints; then it has to be removed quickly enough to let the column address set up.but the memory timing circuitry needs to keep the row address timing short to meet the memory cycle time requirements.  The timing for the control signals is pre-sented in figure  3-4.

L = Low = asserted signal

Figure 3-4.  Timing Relationships for the Signals of a Dynamic RAM Chip

3-27

BFISD 8079

Finally, unlike static RAMs, dynamic RAM chips cannot retain data indefinitely without external support logic.  This is because data is stored as electrical charge in small "capacitors," and the charge tends to dissipate over a period of time.  Hence it is necessary to refresh memory periodically.

For these reasons, and because the memory system is designed to operate without 68010 wait states, memory timing can be rather involved.  To make the design less critical, however, the memory timing circuitry has been centralized on the Central Microprocessor Board, as opposed to including separate timing circuits on each memory array board.  A simplified block diagram of the dynamic memory support subsystem is shown in figure 3-5.  The following paragraphs describe the memory timing circuitry.

3.2.15.1  Memory Timing

High-speed logic multiplexes the eight address lines from one of three sources: the high address bits, the low address bits, or the refresh counter (discussed in subsequent paragraphs). Delays are generated from a tapped delay line and are designed to satisfy the setup times for the row and column addresses.  An asserted address strobe from either the 68010 or a peripheral device controller indicates the beginning of a memory bus cycle.

A 100-nanosecond,  10-tap delay line (DL2, CMB Logic Diagram, sheet 37) deter-mines all the subsequent memory timing.  The Address Strobe (AS-) comes from Central Microprocessor Board connector J02, pin A31.  Either a system I/O bus peripheral device controller or the 68010 can drive AS-.  AS- is inverted by a 74S240 (6X) and sent to the delay line.

3.2.15.2  Row Address Strobe

Signal MRAS+ (Memory Row Address Strobe) is driven onto the memory array bus connector (J03, pin C12) by a 74AS1000 NAND gate (6V).  The gate ORs two pos-sible conditions to create MRAS+:  One input to the gate is an AND (in a 74S00 NAND gate [8X]) of the 10-nanosecond delay line tap output and the complement of signal AS-.  The resulting delay of MRAS+ provides an additional 10 nano-seconds of row address strobe precharge for the dynamic RAMs.  (Chip specifica-tions require a minimum quiescent time for the precharge of internal circuits.)

The other input to the NAND gate is refresh signal REFADRS- (REFresh ADdRess Strobe)—since memory refresh cycles need only row addresses, REFADRS- inputs directly to the  gate to create the MRAS+ signal.  When MRAS+ is asserted, the low-order address bits are multiplexed onto the eight memory address bus lines, by two 74S244 tristate drivers (1V and 1W, CMB Logic Diagram, sheet 38).

3.2.15.3  Column Address Strobes

During non-refresh cycles, signal CADSEL+ (Column ADdress SELect), from the 50- nanosecond delay line tap, disables the row addresses and enables the column addresses. These are now multiplexed onto the memory array bus address lines.

3-28

BFISD 8079

TBD

Figure 3-5.  Simplified Block Diagram, Dynamic Memory Support Subsystem

3-29

BFISD 8079

Because 8-bit or 16-bit (byte or word) data are accessible in one memory cycle, two column address strobes are required: MCASL- (Memory Column Address  Strobe Lower) and MCASU- (Memory Column Address Strobe Upper).  Two 74S22 NAND gates (6Y and 6Z) decode both column address strobes: one pair is for memory write cycles, and one pair is for memory read cycles, determined by the  R/W- (Read/ Write) signal.  The strobes are driven onto connector J03, pins C15 and C16.

A read cycle upper/lower column address strobe is gated by four signals:

o   the 80-nanosecond tap from the delay line (high),

o   MRD+ (Memory ReaD) asserted,

o   MDENB+ (Memory Data ENaBle) asserted,  and

o   the appropriate upper or lower data strobe (MUDS+ or MLDS+) asserted.

A write cycle upper/lower column address strobe is also gated by four signals:

o   the 80-nanosecond tap from the delay line (high),

o   R/W+ (Read/Write) asserted (high),

o   MWINH- (Memory Write INHibit)  inactive, and

o   the appropriate upper or lower data strobe (MUDS+ or MLDS+) asserted.

Signal MRD+ is the complement of R/W+; R/W+ is the complement of R/W-. R/W- comes from the system I/O bus and, when asserted (low), indicates that either the 68010 or an I/O bus peripheral device controller is doing a write cycle.

Signal MDENB+ inactive deselects the memory by preventing the column address strobe from going to the memory array boards during an access beyond the memory address space (above address 1FFFFF [hex]  [paragraph 3.2.12]).  Signal MWINH- asserted prevents main memory from  being written during certain situations (by preventing a write strobe from producing a  column address strobe).

Signals LDS- (Lower Data Strobe) and UDS- (Upper Data Strobe) come from the system I/O bus and are generated by the 68010 or an I/O bus peripheral device controller.  The two signals are inverted by a 74S240 tristate inverter (10Y) to generate signals MLDS+ (Memory Lower Data Strobe) and MUDS+ (Memory Upper Data Strobe).  Note that, during a 68010 write cycle, the data strobes are ac-tive one clock cycle after the address strobe is asserted.  This means that the data strobes, rather than the 80-nanosecond delay line output, become the main gating factor into the 74S22 NAND gates (6Y and 6Z).  Figure 3-6 shows the mem- ory control timing.

3.2.15.4  Memory Refresh

Dynamic memory refresh is accomplished by reading each cell in the 64K-bit RAM memory periodically, about every 4 milliseconds.

3-30

BFISD 8079

TBD

Figure  3-6.  Memory Control Timing Diagram

To make this burden more tolerable,  dynamic memory chips are arranged in two-dimensional arrays of  bits,  so that all bits in a row are refreshed when one bit in that row is read.  Hence, refreshing requires only that each row of bits be read every 4 milliseconds.  Since a 64K-bit RAM chip is arranged in arrays of 256 X 256, refresh  must be done at the rate of 256 reads per refresh period (1 read per 15 microseconds).

3.2.15.5  Refresh Address and Request Generation

To generate a sequence of addresses for refresh cycles, a 74LS393 4-bit binary counter (2T) is used as a modulo (divide by) 256 counter. (Refer to the CMB Logic Diagram, sheet 24.)  One of the 4-bit counters in the 74LS393 is clocked at the end of the refresh cycle by signal REFADRS+ (REFresh ADdResS), and the other counter is clocked by the overflow from the first counter.  With each tick of the refresh clock, the counter advances and the controller generates a memory request at the new (row) address.  The outputs from both counters are driven onto the system I/O bus (by a 74S240 [1T]).  (The counter may be cleared and held by pulling RAMDIS- high [may be done for testing purposes].)

A 74LS161 4-bit synchronous counter (9J) is used to generate a RFREQ+ (ReFresh REQuest) signal every 15 microseconds.  (Refer to the CMB Logic Diagram, sheet 24.)  The counter is clocked by a continuous, 1-megahertz clock (K1MHZ+), and the input is hard-wired for  binary 1.  When the count reaches binary 15, the ripple carry output goes  high. Inverted by a 74LS04 (10V), this output is fed back to the LOAD input of the  counter.  Consequently, on the next low-to-high transition of the  K1MHZ+ clock, the  counter is loaded with an input value of binary 1, the ripple carry output goes low, and counting resumes from 1.

3-31

BFISD 8079

The ripple carry output is asserted (high) for 1 clock cycle, or 1 microsecond.

This is ANDed with the negative-going half cycle of the clock to produce the RFREQ+ signal, with a 500-nanosecond assertion time. (Jumper R can be inserted to eliminate refresh cycles during testing.)

3.2.15.6 Refresh Arbitration

All refresh cycles require a system I/O bus arbitration procedure.  The refresh circuitry has the highest priority on the system I/O bus; but this circuitry will not get the bus until the current bus master gives itup.  (Refer to the CMB Logic Diagram, sheet 23.)

All system I/O bus arbitration, including refresh arbitration, is synchronized with an 8-megahertz clock (K8MHZ-).  In the refresh arbitration circuitry, this clock toggles five 74S112 J-K flip-flops (5G, 5H and 5J).  The flip-flops form a simple state machine that sequences through the signals required for system I/O bus arbitration.

The memory refresh arbitration cycle begins when the refresh request  (RFREQ+) signal (explained in paragraph 3.2.15.5) goes high.  The asserted RFREQ+ signal is latched by  one the 74S112 flip-flops (5J), and the Q output is driven onto the system I/O bus by a 74S38 open-collector NAND gate (2G); there it becomes the Bus Request (BR-) signal and is sent to the 68010.

When the 68010 returns the BGNT-A (Bus GraNT) signal, and the current bus cycle is not an interrupt acknowledge cycle, signal SRFSHFO+ is created in a 74LS260 NOR gate (7J).  SRFSHFO+ is latched by another of the flip-flops (5G).  The Q output pulls down the three bus priority lines (BPRO-, BPR1- and BPR2-) through three 74S38 open-collector NAND gates  (2G).  (The bus priority lines are dis-cussed in paragraph 3.2.11.)  Note: the interrupt acknowledge signal (IACK+) is factored into  SRFSHFO+ because the bus priority lines also are used by the pe-ripheral device controllers for interrupt acknowledge arbitration.

When the current bus master cycle has completed (indicated by MAS+ and CBACK+ released), signals BGACK- (Bus Grant ACKaowledge), IBGACK- (Internal Bus Grant ACKnowledge) and REFADRS+ (REFresh ADdRess Strobe) are created by the remaining flip-flops (5G and 5H) according to the timing diagram in figure 3-7.

Signal BGACK-, driven by a 74LS38 open-collector NAND gate (8J), notifies all peripheral device controllers and the 68010 that the system I/O bus is in use; IBGACK- enables the refresh address on the I/O bus; and REFADRS- generates a row address strobe to the memory array boards.

In summary, the sequence of events that takes place for a refresh cycle is as follows:

o  Fifteen microseconds elapse, and the refresh arbitration circuits request

the system I/O bus.

o  System I/O bus arbitration takes place, and, after the current cycle is

completed, the system I/O bus is granted.

3-32

BFISD 8079

o  The refresh circuitry acknowledges the bus grant and drives the modulo 256

counter output (8 bits) onto the system I/O bus.

o  The refresh circuitry issues a row address strobe, 250 nanoseconds in

length, to the memory array boards.

o  The refresh circuitry releases the system I/O bus.

o  The modulo 256 counter is incremented.

### 3.2.16  Memory Management Unit

A Memory Management Unit, or MMU, on the Central Microprocessor Board, includes the necessary hardware for the implementation of the memory management scheme used by the operating system software.  The MMU hardware provides for the two cooperating memory management techniques known as segmentation and swapping.

3.2.16.1  Segmentation

One function of the MMU is to logically partition system memory into a set of variable-length, numbered segments. To achieve this the MMU translates logical addresses into physical addresses. (Logical addresses are the outputs of the 68010 address lines; physical addresses are real memory locations, including RAM, ROM and memory-mapped I/O addresses.)

TBD

Figure 3-7.  Refresh Timing Diagram

3-33

BFISD 8079

The starting location and length of each segment are defined by the contents of segment registers on the Central Microprocessor Board (CMB). A logical address from the 68010 specifies the segment number and the offset into that segment.

The content of the selected segment register then determines the actual memory location to be accessed by the 68010.  (A simplified block diagram of the MMU is shown in figure 3-8.)  Segmentation facilitates the exchange of programs be-tween main memory  and a disk, a process called "swapping."

3.2.16.2  Swapping

Another function of the MMU is to allow programs located on a disk to be trans-ferred to the system (main) memory for execution.  This ability is necessary when there is limited main memory (as there always is) and a multiprogramming environment is desired. Swapping works in conjunction with segmentation; it is transparent to the programmer (or user).

"Swapping" is the term used because segments in main memory can be exchanged with segments on the disk.  However, unless a segment in main memory has been written to, there is no point in wasting overhead storing it on the disk if an image of the segment already exists there.  The reporting of a segment having been written to is yet another function of the MMU hardware.

3.2.16.3   Other MMU Functions

The MMU will report (flag) user access violations of the physical address space to the operating system.  This occurs when an attempt is made to do one of the following accesses.

o   A write to a  read-only segment

o   An instruction fetch from a data segment

o   An access to a non-existent segment

o  An access to an address beyond the length of a segment

o  An access to an address beyond the end of a stack

o  An access to an address in the warning area of a stack

(The MMU also will flag separately any legal write cycle to any segment, for the reason explained in paragraph 3.2.16.7.)  Each of these six violations, when detected, causes the following three major events to occur, in the order presented.

a.  A write cycle to main memory is prevented.

b.  A bus error condition is created, forcing the 68010 to process an

exception and force the program to branch to the appropriate service

routine in the operating system software.

c.  The latched violation flags are read by the system software to

determine the cause of the MMU error.

3-34

BFISD 8079

TBD

Figure 3—8.  Simplified Block Diagram, Memory Management Unit

3-35

BFISD 8079

All of these detection functions can be set in CMB hardware.  (A logical block diagram of the MMU error detection and status reporting functions is shown in figure 3-9.)  How the CMB hardware performs these and the other functions dis-cussed in previous paragraphs is explained in the following paragraphs.

3.2.16.4  Supervisor and User Access of the MMU

It is important to remember that the MMU is in use only while the 68010 is in user mode; and the base address, limit address and segment attribute registers (described in subsequent paragraphs), which are part of the MMU,can be updated only in supervisor mode.  Also, all DMA (Direct Memory Access) transfers are physical address transfers and do not use the MMU.

Address translation (also called address mapping) by the MMU when the 68010 is in user mode and no DMA transfers are in progress is enabled by signals PAENB-(Physical Address ENaBle) high and PAENB+ low.  PAENB+ low also enables the MMU errors (described in paragraph 3.2.16.8).  (Refer to the CMB Logic Diagram, sheets 30 and 31.)

TBD

Figure 3-9. Logical Block Diagram, MMU Status Reporting/Error Detection

3-36

BFISD 8079

3.2.16.5  MMU Address Translation

The MMU translates address bits A09+ through A23+ from the 68010.  Bits A01+

through A08+ are not translated but go directly to the memory (thus setting the

inimum segment size to 512 bytes).  (Address bit A00 does not exist outside the 68010.  This bit is used internal to the 68010, in conjunction with the data size specification of each instruction, to generate the two UDS- and LDS- signals [Upper Data Strobe and Lower Data Strobe].  These determine which byte of a 16-bit [word-wide] memory location is being addressed.)

The resulting address translation provides each user with eight variable-length memory segments (which are transparent to the user), in physical memory (RAM). Each segment has associated with it a 12-bit base address, a 12-bit limit ad-dress, 4 bits of segment attributes and 4 bits of segment status.  These 32 bits of information (called a segment descriptor) are stored at one address in eight 74S189 16- X 4-bit storage registers (3W, 3X, 3Y, 3Z, 4X, 4Y, 4Z and 7X). (Refer to the CMB Logic Diagram, sheets 30 through 34.)

The eight registers are in parallel with respect to the address lines connected to them.  Only eight of the sixteen available 4-bit registers in each of the eight storage  registers are used.  Hence, all of the A3 address inputs to the 74S189s are pulled low.

Each of the eight segment registers is addressed by signals MFA1+, MFA2+, and MFA3+.  These come from a 74S157 l-of-2 data selector (3T).  (Refer to the CMB Logic Diagram, sheet 32.)  Address bits A01+A, A02+A, and A03+A are selected when the 68010 is in the supervisor mode; A21+, A22+, and A23+ are selected in the user mode.  Thus, when in the supervisor mode, the 68010 addresses the seg-ment registers to update the segment descriptors; and, when in the user mode, the 68010 addresses these registers to perform address translation.  The CFC2- (CPU Function Code 2, explained in paragraph 3.2.2) signal into the data selec-tor (3T) performs the selection.  In the multi-user mode, the operating system software loads the next user's segment descriptors into the segment registers with each context switch.

Base Address

The base addresses are stored in three 74S189 storage registers (3X, 3Y, and 3Z). (Refer to the CMB Logic Diagram, sheets 30 and 31.)  The operating system software does this (in the supervisor mode) by writing to the input/output ad-dress (8XXXXX [hex]) that enables signal MMBWE- (paragraph 3.2.12.2).  The seg-ment base descriptor word format is as follows:

15   14   13  12   11  10  09  08  07  06  05  04  03  02  01  00

R    X   TYPE    A20 A19 A18 A17 A16 A15 A14 A13 A12 All A10 A09

(Attributes R, X and TYPE are explained in paragraph 3.2.16.6.) During a 68010 memory cycle, the physical addresses represented by bits A09 through A20 are obtained by summing the base address, contained in the three storage registers, with the logical addresses represented by bits A09 through A20, from the 68010.

3-37

BFISD 8079

The addition is done in three 74S283 4-bit full adders (2X, 2Y and 2Z).  (Refer to the CMB Logic Diagram, sheets 30 and 31.)  The summed A09 through A16 are the column addresses for the memory array (MA1- through MA8-); these are driven onto the memory address bus by a 74S240 tristate inverter (IX), enabled by the NAND of PAENB- (Physical Address ENaBle) and CADSEL+ (Column ADdress SELect).

The summed A17 through A20 are the memory array bank and board selects (MAD17+ through MAD20+); these are driven onto the memory address bus by a 74S244 tri-state driver (1Z), enabled by PAENB+.

Limit Address

Once a base address is established, the segment length is defined by a logical limit address, and any access that violates this limit will generate an error signal.  This violation detection function is required for the prevention of user programs from accidentally (or otherwise) destroying any other users' pro-grams located  in other segments.

The limit addresses for the eight segments are stored in three 74S189 storage registers (4X, 4Y and 4Z).  (Refer to the CMB Logic Diagram, sheets 32 and 33.)

The system software does this (in the supervisor mode) by writing to the input/ output (I/O) address (AXXXXX [hex]) that enables MMLWE- (paragraph3.2.12.2).

The segment limit descriptor word format is as follows:

15   14  13   12  11  10  09  08  07  06  05  04  03  02  01  00

0   0   0    0  A20 A19 A18 A17 A16 A15 A14 A13 A12 All A10 A09

In a 68010 memory cycle, the logical address from the 68010 is compared with the limit address stored in the 74S189 registers by three 74S85 magnitude com-parators (5X, 5Y, and 5Z). These devices create signals ADEQLM+ (ADdress EQual to LiMit),  when the logical address is equal to the limit address, and ADLTLM+ (ADdress Less Than LiMit), when the logical address is less than the limit.

3.2.16.6  Segment Attributes

One 74S189 storage register (3W) holds the segment attributes.  (Refer to the CMB Logic Diagram, sheet 31.) When a segment is to be read only, the bit cor-responding  to the D03 output of the 74S189 is a logical 1 (high).  If a write is attempted in that segment, then the high output of D03 will be ANDed with SEGWRT+ (SEGment WRiTe) and PAENB- to produce the MMWERR+ and MMWERR- (Memory Management Write ERRor) signals.

Similarly, when a segment is to be data only, the bit corresponding to the D04 output of the 74S189 is a logical 1.  If a program fetch is attempted in that segment, then the high output of D04 will be ANDed with FDC2+ (Function DeCode, user mode) to create MMXERR+ and MMXERR- (Memory Management eXecute ERRor).

Finally, bits D01 and D02 of the 74S189 are decoded by a 74S139 l-of-4 decoder (4T)  to generate four error signals, all of which translate into the Memory Management ERRor (MMERR-, explained in paragraph 3.2.16.8) signals.

3-38

BIFSD 8079

These are the ABSEG- (ABsent SEGment) and SEGDC(X)- (SEGment DeCode)  signals:

D02    D01      SIGNAL                      EXPLANATION

0       0      ABSEG-      Generates a memory management error (MMERR-)

when an absent segment is addressed

0       1      SEGDC1-     Generates a memory management error when the

logical address is equal to or greater than the

limit address

1       0      SEGDC2-     Generates a memory management error when the

logical address is less than the limit address.

Used for stack overflow

1       1      SEGDC3-     Generates a memory management error when the

logical address is less than or equal to the

the limit address.  Used for stack overflow

(less than) and for warning of an impending

stack overflow (equal to)

3.2.16.7  Segment Status

Each MMU segment has an associated 4-bit status word that is readable by the 68010 in supervisor mode.  The status word is generated and then stored in a 74S189 storage register (7X) during the time a segment is accessed (in the user mode).  (Refer to the CMB Logic Diagram, sheet 34.)  The status word is not de-coded.  Each bit in the status word, when a logical 1, means the following:

BIT                          EXPLANATION

D01          A segment has been written to (not an error condition)

D02          A segment execute error has occurred (error)

D03          A segment write error has occurred (error)

D04          A segment limit or absent segment error has occurred (error)

The status word, driven onto the buffered data bus (DBOO- through DB03-) by a 74S240 tristate inverter (6X), is enabled by signal MMSTRE- (Memory Management STatus REad).  The status word is read by the system software after a memory management error has occurred, to determine which of the foregoing three error conditions has taken place (D02, D03 or D04).

Bit D01 of the segment status word is the one bit in the word that is not used for reporting an error condition.  In a multiprogramming system that uses pro-gram swapping (such as this one), a record must be kept of any segment having been written to, or modified.  This is so that, when swapping occurs, the con-tents of that segment will be stored on a disk (backing store) instead of being overwritten  by the incoming program.  Hence the segment status word is read by the system software during context switch to check for the segment-written bit before loading the next program.

3-39

BFISD 8079

(Refer to the (MB Logic Diagram, sheet 34.)  The W output of a 74LS151 l-of-8 data selector (7V) is the input to the segment-written bit of the 74S189 (7X).

The W output always is high while the 68010 is in the supervisor mode.  This is to allow the segment-written bit to be initialized before the 68010 switches to the user mode.

In the user mode, when a segment is written to, W is goes low and is stored in the 74S189. If the segment subsequently is read, then W will be the inverted value of the flip-flop (7S), which has been storing the segment-written bit of the 74S189.  Thus the segment-written bit is preserved, even when a segment-read cycle occurs during the same segment access period.  Timing signal CSTOF+ clocks the segment-written bit, in the status word register, into the flip-flop at the beginning of each memory access cycle.

A 74LS10 NAND gate (8S) and a 74LS08 AND gate (7W) create a write pulse for the status word register during user mode access or supervisor mode initialization.

These gates AND signal CSTOF+ with PAENB- and the complement of CST1F+ to pro-duce a 125-nanosecond pulse.  The pulse is gated through to the 74S189 status word register (7X) Write Enable input during a user mode memory access.  During a supervisor mode write to the base address register, however, MMBWE- asserted provides the Write Enable input to the status word register.

Signal SEGWRT+ (SEGment WRiTe) is asserted when a memory write cycle occurs during the user mode.  SEGWRT+ generates the Memory Management Write ERRor sig-nal (MMWERR+/MMWERR-) described in paragraph 3.2.16.8.  This can occur only when the bit corresponding to output D03 of the 74S189 segment attribute reg-ister (3W) is set (refer to paragraph 3.2.16.6).

3.2.16.8  MMU Error Generation

The IvMERR- (Memory Management ERRor) signal is generated by any one of six MMU error conditions, as listed in paragraph 3.2.16.3.  A 74S30 NAND gate (10X) ORs those conditions.  (Refer to the CMB Logic Diagram, sheet 35.)  MMERR- goes to the memory array stack via connector J03, pin C11.  If the signal is asserted at the selected memory array board,  then the PDTACK- (Processor Data Transfer ACKnowledge, required by the 68010 to complete a memory cycle) signal is block-ed from returning to the Central Microprocessor Board; the absence of PDTACK- creates a bus error exception signal, which is sent to the 68010, as described in paragraph 3.2.10.

Signal MMERR+ is latched and held by a 74LS109 flip-flop (10R) at the end of the current cycle.  The latched error becomes signal MMERF+ (Memory Management ERror Flag) and is read in a (MB status read cycle, as described in paragraph 3.2.4.  The error is reset at the end of the read, because the input of the flip-flop is low from CMBSTRE- ((MB  STatus REad) asserted.

Signal SEGOVF- (SEGment OVer Flow) is generated by two MMU error conditions:

a.  The memory access is a normal program fetch or data access (indicated

by SEGDC1+ asserted), and the address is equal to, or greater than,

the limit address (indicated by ADLTLM+ inactive).

3-40

BFISD 8079

b.  The memory  access is a stack access (indicated by SEGDC2- or SEGDC3-

asserted), and the address is less than the limit address (the stack

address is out of bounds, indicated  by ADLTLM+ asserted).

SEGOVF-, ORed with ABSEG-,  produces the SAERR- (Segment Access ERRor) signal, which is written to the segment status word register, as described in paragraph 3.2.16.7.  (ABSEG- also is one of the ORed error conditions that generates the MMERR- signal.)

Signals MMWERR+ (Memory Management Write ERRor) and MMXERR+ (Memory Management eXecute ERRor) are inverted by two 74S00 NAND gates (8X) to produce signals SWERR- (Segment Write ERRor) and SXERR- (Segment eXecute ERRor).

Signal SSWARN- (Stack Segment overflow WARNing) is the NAND (74LS08 [9S] and 74LS04 [7R]) of SEGDC3+ and ADEQLM+ (logical ADdress EQual to LiMit address).

SSWARN- indicates a stack segment is in the warning area (i.e., the last 512 bytes before overflow). (SSWARN- is one of the ORed error conditions that gen-erates the MMERR- signal.)

SSWARN- also is latched and held by a 74LS109 J-K flip-flop (7S) (to become SSWARNF- [Stack Segment overflow WARNing Flag]) until the flip-flop is read by a CMB STatus REad (CMBSTRE-) signal.  The flip-flop then is reset at the end of the status read cycle, when the K- input is low from the CMBSTRE- signal.

Signal RAMDIS- (RAM DISable) is provided to disable the MMU registers during "bed of nails" testing.  (Refer to the CMB Logic Diagram, sheet 30.)  When the input of the 74LS04 inverter (4V) is pulled low by the tester, RAMDIS- goes high and disables the outputs of the 74S189 storage registers in the MMU.

### 3.2.17  Serial Ports

The following paragraphs cover detailed information on the serial interfacing of the Model 4108 Base Unit to peripheral devices.  Controller circuitry that

will support two serial I/O ports is contained on the Central Microprocessor Board, inside the Base Unit.  Each port is an independent, 0- to IM-bit-per-second, full-duplex RS 232 channel.  The ports can have different baud rates for transmitting and for receiving, and each port can support a printer, modem or terminal.  Figure 3-10 shows a simplified block diagram of the serial port circuitry, and the following circuit descriptions begin with a brief review of some basic serial interfacing principles.

3.2.17.1  Serial/Parallel Conversion

The serial port controller contains a bus interface through which the 68010 can send commands to the ports, read port status, and access input  and output data registers in the ports.  An interrupt line notifies the 68010 of the completion of an operation.  As in any serial port, a conversion takes place between the serial and the parallel data streams.  Hence the interface with the 68010 is a parallel interface through  which eight data bits are transmitted during a sin-gle transaction.

3-41

BFISD 8079

TBD

Figure 3-10.  Simplified Block Diagram, CMB Serial Ports

3-42

BFISD 8079

The interface with a serial peripheral device, on the other hand, is a serial interface in which those same data bits are transmitted on a single output line or received on a single input line, one bit at a time.  The conversion occurs in the LSI serial communications controller chip, on the Central Microprocessor Board.  The serial communications controller chip is a Zilog 8530 (2C).  (Refer to the CMB Logic Diagram,  sheet 28.)  The chip is a byte-wide device, residing on the byte-wide I/O data bus (described in paragraph 3.2.13).  It is a multi-protocol and dual-channel  device; and each independent channel, or port, can handle 0- to 1M-bits-per-second data transfer rates and full-duplex operation.

A simplified block diagram of the 8530 chip is presented in figure 3-11.

Within the serial communications controller chip, an output register is loaded in parallel from the  byte-wide data bus.  This register, in turn, provides a parallel dump to a shift register.  Hence data is loaded into the parallel reg-ister, then passed to the shift register,  where the bits are collected until the register is full. Conversely, input data from a serial peripheral device are passed in parallel from an input shift register to an input data register and then to the 68010, via the byte-wide data bus.

TBD

Figure 3-11.  Simplified Block Diagram, 8530 SCC Chip

3-43

BFISD 8079

Serial Data Reception

The receive and transmit sections each have separate data registers because of a need to buffer data in transit through the port.  There is a variable delay between the receipt of a byte-wide datum from a peripheral and the availability of a 68010 bus cycle that will accept that datum. Hence, the receive register accepts the datum and holds it during the time the input shift register is re-ceiving the next character.  As each successive bit of the next arriving char-acter appears, the shift register shifts its present content to make room for the new datum.

This prevents the leading bits of the next character from overwriting the re-ceived datum.  When the final bit of a character is received, the completed byte passes to the input buffer register, thus freeing the shift register to accept the next byte of serial information.

Serial Data Transmission

A similar, but reverse, series of events occurs during the transmit cycle. The benefit in this case stems from the elimination of idle time between character bytes on the serial output line.  The moment the final bit of a character byte leaves the output port, a new data byte is moved into the output shift register from the output buffer register.  Now the 68010 has the entire 8-bit character interval to reload the output buffer register.  This ability to eliminate idle time between characters is of fundamental importance in synchronous communica-tions protocols.

3.2.17.2  Communications Protocol Selection

A communications protocol is a convention for data transmission that includes at least the following functions.

o  Timing

o  Formatting

o  Control

o  Representation  of data

The Model 4108 Base Unit provides flexibility in configuring the transmit and receive parameters of the serial ports  for various protocols.  The ports can support three catagories  of serial protocols.  Each port can be configured as

o  synchronous,

o  standard asynchronous, or

o  asynchronous, with programmable split baud rate (i.e., transmit and

receive can  be  at different rates, from 150 baud to 19.2K baud).

3-44

BFISD 8079

Synchronous Protocol

In the synchronous mode, each successive datum in a data stream is controlled by a master data clock.  Hence the clock controls not only the bits within a character byte, but the character-to-character spacing as well.  (One benefit of this method is higher communication speed, as an entire block of data may be exchanged, with only normal bit spacing between characters.)  The master clock is received as an additional signal, separate from the incoming data stream.

This clock appears at the Port A DB-25 connector (J09, pin 17) as signal RTXCA+ (Receive/Transmit Clock, Port A).

From there it is routed, via a 74LS153 l-of-4 data selector (2J), to the RTXCA- input of the serial communications controller chip, or SCC.  (Refer to the CMB Logic Diagram, sheets 28 and 29.)  A similar path is found from the Port B DB- 25 connector (J10, pin 17) to the SCC.

Standard Asynchronous Protocol

The standard asynchronous mode selects the 3.6864 MHz clock from a local oscil-lator (2K) and feeds that to the SCC via the same data selectors (2H and 2J).

In asynchronous serial data transmission, each character is treated as an indi-vidual message; each appears in the data stream at an arbitrary time.  Thus it is the responsibility of each character to inform the receiving serial port of the beginning and the end of that character.  It does this with start bits and stop bits.  When no data is being transmitted, the data line carries a logic 1 level (high voltage).

When a datum appears on the line, the first bit received is a logic 0 (low); this commands the SCC to begin sampling the datum. The next 8 bits are data bits, and the final 1, 1-1/2, or 2 bits are stop bits.  The stop bits are al-ways at logic 1 (high).

Split Baud Rate Asynchronous Protocol

The split baud mode allows serial transmission at one data rate and reception at another. The mode is selected by system software using data bits CD02+ and CD03+ (or CDOO+ and CD01+ for Port B).  These data bits are latched in a 74S373 transparent latch (3K).  Refer to the CMB Logic Diagram, sheet 29.)  The local baud rate clock for transmitting data is selected by data bits CD05+, CD06+ and CD07+, latched in the same 74S373.  The SCC is programmed directly to set the baud rate of the receive clock.

A 74LS163 binary counter (3G) divides by 8 the output of a 4.915 MHz oscillator (4G). A 74LS393 binary counter (3H) generates 8 clock rates, each equal to 16 times the frequency of the requested baud rate. These are the clocks that are selected by data bits CD05+ through CD07+.

Data bits CD05+ through CD07+ are decoded in a 74LS151 l-of-8 data selector (3J). The other data bits select which of the three possible clock sources is to be used for each port on the SCG.

3-45

BFISD 8079

They are selected by the 74LS153 data selectors that were mentioned earlier (2J and 2H).  The control and data bits are available to the SCC when the SCC is selected by the local I/O address decoder (discussed in paragraph 3.2.12.4) in the Central Microprocessor Board.

3.2.17.3  Electrical Configuration Selection

To further define the asynchronous serial communications protocol used in the Model 4108 Base Unit,  we separate the logical conventions from the electrical connection requirements.  The electrical connections used in asynchronous pro-tocols usually are referred to as one of the following:

o   RS-232-C

o   20 mA current loop

o   RS-422, RS-423, or RS-449

Of these,  the Base Unit uses only RS-232-C and RS-422.

RS-232-C

The RS-232-C standard originally was intended to provide a specification for using modems (modulator/demodulator) to connect remote devices to computers, via the telephone network.  The standard now is used to connect the computers directly to terminals and to serial printers, in addition to modems.

The RS-232-C standard defines 21 signals and a 25-pin electrical connector for asynchronous serial data communication. In order to accommodate terminals and serial printers in addition to modems the serial port circuitry in the Central Microprocessor Board must be electrically configured for the desired peripheral device. Hence that circuitry contains several connections for jumpers to allow the necessary reconfiguration. Table 3-6 shows the signal names, their corre-sponding cable pin number, jumper reference letters, and the circuit board pin numbers of the pins that must be connected together by the jumper wires for a particular configuration.

Note that only kind of one cable is needed to support printers, terminals or modems.  All signal switching is done on the Central Microprocessor Board via the jumpers. The RS-232 cable is a pin-for-pin connection; no signals or pins are cross-connected.

RS-422

The RS-422 standard describes the electrical characteristics of a port that is designed to allow a higher signaling rate bandwidth over longer distances than is provided by the RS-232-C.  This standard defines a double-ended electrical interface that can signal at data rates well in excess of the 20-kHz bandwidth allowed by RS-232-C (20 kHz = 20K data bits/second).

3-46

BFISD 8079

Table 3-6.  Serial Port Electrical Configuration Jumper Connections

PORT A:

MODEM                 TERMINAL              PRINTER

Name     Jumper A   Cable      Jumper A   Cable      Jumper A   Cable

CTS       7 and 8   pin 5       7 and 9   pin 4       7 and 9   pin 4

DSR       3 and 4   pin 6      *1 and 3   pin 20      1 and 3   pin 20

DTR       1 and 2   pin 20     *2 and 4   pin 6       2 and 4   pin 6

RTS       9 and 10  pin 4       8 and 10  pin 5       8 and 10  pin 5

RXD      11 and 12  pin 3      11 and 13  pin 2      11 and 13  pin 2

TXD      13 and 14  pin 2      12 and 14  pin 3      12 and 14  pin 3

RNG      In Place   pin 22

TRXC     In Place   pin 15

DCD      In Place   pin 8

PORT B:

MODEM                TERMINAL              PRINTER

Name     Jumper B   Cable      Jumper B    Cable      Jumper B    Cable

CTS       7 and 8   pin 5       7 and 9    pin 4       7 and 9    pin 4

DSR       3 and 4   pin 6       3 and 1    pin 20      3 and 1    pin 20

DTR       1 and 2   pin 20      2 and 4    pin 6       2 and 4    pin 6

RTS       9 and 10  pin 4       8 and 10   pin 5       8 and 10   pin 5

RXD      13 and 14  pin 3       13 and 15  pin 2       13 and 15  pin 2

TXD      15 and 16  pin 2       14 and 16  pin 3       14 and 16  pin 3

Jumper G              Jumper G               Jumper G

RXD      15 and 16  pin 3      15 and 16   pin 2       15 and 16  pin 2

DCD      17 and 18  pin 8      17 and 18   pin 8

TRXC     10 and 20  pin 15     19 and 20   pin 15

23 and 24             23 and 24

Jumper H              Jumper H

DCD      1 and 2               1 and 2

Jumper K              Jumper K              Jumper K

D422    *1 and 2               *1 and 2              *1 and 2

NOTE: Be sure to disconnect all unused jumper positions on port B.

*This jumper disables the RS-422 drivers.

3-47

BFISD 8079

In the Model 4108 Base Unit, only Port B can be configured for RS-422; although either port may be used as a synchronous data channel, it may be advantageous to use port B, because of the balanced link associated with the RS-422 config-uration.  In the serial port input/output circuitry, the RS-422 line drivers are 26LS31s (4D), and the receivers are 26LS32s (4C).  (Refer to the CMB Logic Diagram, sheet 28.1.)

3.2.17.4  Addressing and Control

The 8530 SCC chip (20) is enabled with a 68010 supervisor read or write to ad-dress 60XXXY (hex).  The internal registers of the SCC chip are addressed by address bits A014A and A02-fA, from the 68010. Port A is selected when A02+A is high; Port B is selected when that bit is low.  Address bit A01+A. informs the the SCC that either data or control parameters are being sent.

The read and write strobes to the SCC are synchronized by ANDing their comple-ments with the CST4F+ timing signal to meet SCC timing requirements.  This is done by a 74LS51 combination gate (9M).  (Refer to the CMB Logic Diagram, sheet 25.) A reset on RSTF2+ will cause both a read and a write to be sent to the SCC, creating the required reset condition.  Table 3-7 shows the data bus bit patterns required for selecting the various serial port logical configurations and data rates.

Once a port has been selected and configured, and data transfer is in progress, the system software needs to be informed of when a datum has been transferred between a shift register and a buffer register in the SCC chip.  This is so that a driver routine can either load a new byte into the transmit buffer or transfer the new byte in the receive buffer to the 68010.

When a byte of data has been tranferred between a buffer register and a shift register,  control logic in the SCC chip activates the interrupt pin (INT-) of the chip.  (Refer to the CMB Logic Diagram, sheet 28.)  When this pin is low, signal INT5- (INTerrupt level 5) is encoded by a 74LS148 8-line-to-3-line pri-ority encoder (3E).  (Refer to the CMB Logic Diagram, sheet 22.)  This consti-tutes an interrupt request to the 68010.

Thus an interrupt request level 5 is encoded on the 68010 interrupt request lines (IPLO- through IPL2-).  If the priority of the interrupt is greater than the current processor priority, then the interrupt processing sequence begins. The 68010 places the interrupt priority number on the lines carrying the three least significant address bits.  These are decoded by a 74LS151 1-of-8 data se-lector (10K, CMB Logic Diagram, sheet 22).

For priority number 5, the CVPA- (CPU Valid Peripheral Address) output of the data selector is low (active).  In response to CVPA-, the 68010 internally gen-erates a vector number that is determined by the interrupt level number.  (The vector number [when multiplied by four] is the address in the lowest 1K bytes of main memory that contains the beginning address of the routine that will handle the interrupt.)  The content of the vector number is fetched and loaded into the 68010 program counter, and normal instruction execution commences in the interrupt service routine.

3-48

BFISD 8079

Table 3-7.  Bit Patterns for Serial Port Configuration and Data Rate Selection

DATA BUS

CD03+   CD02+  CD01+  CDOO+          LOGICAL PORT CONFIGURATION

0       0       X      X               Port A, Synchronous

0       1       X      X               Port A, Asynchronous

1       0       X      X               Port A, Split Baud Rate

X       X       0      0               Port B, Synchronous

X       X       0      1               Port B, Asynchronous

X       X       1      0               Port B, Split Baud Rate

CD07+   CD06+  CD05+  CD04+             TRANSMIT BAUD RATE

0       0       0      X                    19,200

0       0       1      X                     9,600

0       1       0      X                     4,800

0       1       1      X                     2,400

1       0       0      X                     1,200

1       0       1      X                       600

1       1       0      X                       300

1       1       1      X                       150

Note:  1  = High;  0 = Low; X = Don't care

The program now can read the status register in the SCC to determine whether the interrupt was due to the transmission or reception of data; then the 68010 can move data to or from the SCC chip.

At the same time that the priority number on the address bus was being decoded to produce CVPA-, a 74LS138  1-of-8 decoder (10L, CMB Logic Diagram, sheet 20) also decoded those address bits.  The output is the IACKL5- signal.  This in-terrupt acknowledge signal is synchronized to the system clock in a 74LS74 D flip-flop (10J).  (Refer to the CMB Logic Diagram, sheet 25).  The output of the flip-flop is the SCC INT- input to the SCC chip, which resets the interrupt logic in the chip.

3-49

BFISD 8079

### 3.2.18  Parallel Port

In the following paragraphs we discuss the interfacing of external devices to the Model 4108 Base Unit through the parallel I/O port.  Controller circuitry to support the parallel port is contained on the Central Microprocessor Board, inside the Base Unit. Although the port is a general-purpose I/O channel that can be used for a variety of 8-bit parallel interfaces, it usually will be used to interface a printer with the CentronicsTM "standard" interface. The follow-ing detailed discussion assumes that such a printer is connected to the port.

The parallel port uses a Motorola 68230 Parallel Interface/Timer, or PI/I. The PI/T (5D) is a byte-wide device and resides on the byte-wide I/O data bus (de-scribed in paragraph 3.2.13). (Refer to the CMB Logic Diagram, sheet 26.)  The PI/T has two 8-bit ports and also has a timer with a separate interrupt output.

The PI/T is permanently configured with Port A as the output port and Port B as the input port.

3.2.18.1  Addressing and Control

The 68230 PI/T chip (5D) is enabled with a 68010 supervisor read or write to address 62XYYX (hex).  This provides the PI/T Chip Select (CS-) input with an enable strobe that is the AND of signals PITCE- and CST1F+ (from a 74LS00 NAND gate [4E].  Signal PITCE- (PI/T Chip  Enable) comes from the local I/O decoder described in paragraph  3.2.12.4.  Signal CST1F+ is a timing signal that comes from the timing generator described in paragraph 3.2.10.1.  The two signals are ANDed so that the PI/T can start the strobes on a clean clock edge (CST1F+).

The internal registers of the PI/T chip are addressed by address bits A044A through A084A,  from the 68010.  The read and write strobe to the PI/T is the CRNW- (CPU Read Not Write) strobe from the 68010.  The pin labeled DTACK pro-
vides a Processor Data Transfer ACKnowledge (PDTACK-) signal, required by the 68010 during a bus cycle to indicate the number of wait states, if any, to in-
sert in the cycle (this is discussed in paragraph 3.2.10). Pins HI and H2 are
for input and output "handshake" strobes.

Pin H4 is tied to pin B7,  which receives the high-order bit (PB07+) of the in-
put parallel port; this is a BUSY bit from the printer, which is used to gener-
ate an interrupt.  The parallel control ports are wired for interrupt level 1
(INT1-), and the timer for interrupt level 6 (INT6-).

(Although the parallel port has the lowest interrupt priority [level 1], the
timer in the PI/T chip has the highest priority, next to the power fail detect
interrupt.  This is because the interrupt generated by that timer is used to
provide the "time slices" required for multi-user operation.)

When the printer is ready toreceive a byte of data, the BUSY bit (PB07+), from
the printer, goes goes high. Since this bit also enters pin H4 of the PI/T,
the chip asserts the interrupt  signal from the pin labeled  PIRQ-. This signal
signal (INT1-) is encoded  by a 74LS148 8-line-to-3-line priority encoder (3E).
(Refer to the CMB Logic Diagram, sheet 22.)  The output of the encoder consti-
 tutes an interrupt request to the 68010.

3-50

BFISD 8079

Thus an interrupt request level 1 is encoded on the 68010 interrupt request lines (IPLO- through IPL2-).  If the priority of the interrupt is greater than the current processor priority, then the interrupt processing sequence begins.

The 68010 places the interrupt priority number on the lines carrying the three least significant address bits.  These are decoded by a 74LS151 l-of-8 data se-lector (10K, CMB Logic Diagram, sheet 22).

For priority number 1,  the CVPA- (CPU Valid Peripheral Address) output of the data selector is low (active).  In response to CVPA-, the 68010 internally gen-erates a vector number that is determined by the interrupt level number.  (The vector number [when multiplied by four] is the address in the lowest 1K bytes of main memory that contains the beginning address of the routine that will handle the interrupt.)

The content of the vector number is fetched and loaded into the 68010 program counter, and normal instruction execution commences in the interrupt service routine.  The program now can write a data byte to the data register in the PI/T, for transmission to the printer.

3.2.18.2  Data Transmission to  a Printer

The output data format from the parallel port is ASCII (American Standard Code for Information Interchange); it's the  same format used in the serial ports.

The parallel data output is asynchronous,  and the data transfer rate is deter-mined by the transfer program, which normally is interrupt driven.  The drivers and receivers in the parallel port circuitry are 74LS244s (4B and 5A).  (Refer to the CMB Logic Diagram, sheet 27.)  These are connected to J13, the parallel port connector, which has 37 pins.  Table  3-8 is a list of the J13 signals.  A printer connected to the Model 4108 Base Unit parallel port typically will use the so-called "Centronics parallel interface standard." Table 3-9 gives a de-scription of the Centronics protocol.

### 3.2.19  Floppy Disk Controller

Two floppy disk(ette) drives may be mounted inside the Model 4108 Base Unit of the MAI® 2000 SeriesDesktop Computer System.  The driven diskettes are 5.25 inches in diameter, contain 96 tracks per inch (TPI) of diskette radius and are double-sided.  Controller circuitry to support both floppy drives is provided on the Central Microprocessor Board.  The circuitry provides for soft-sectored and double-density recording techniques. Figure 3-12 shows a simplified block diagram of the controller, and the following paragraphs describe the circuitry, beginning with a very brisk review of a few basic disk recording principles.

3.2.19.1  Soft Sectoring

Soft-sectoring means there are no sector holes in the diskette to identify the head position with respect to a track. Instead, a single hole provides a phys-ical reference point, and sector information is recorded magnetically on the disk within each sector.

3-51

BFISD 8079

Each sector contains an identifier field that appears on the data stream just before the data field.  To read data, the head is first positioned at the cor-rect track, where it reads the data stream continuously.  When the read/write head detects an identifier with thecorrect sector number, the data block fol-lowing that identifier is accepted.

To write a new data block, the disk controller first reads data continuously until an identifier is located with a matching sector number.  The controller then rewrites the new data over the existing data block in that sector.  The identifiers, however, are never rewritten during normal  operation, though the controller has the capability of writing those identifiers onto a blank disk-ette when that diskette is being initialized for first use.  The soft-sectoring technique is so called because the system software can revise the sector format of a diskette by rewriting the sector  identifiers.

Table 3-8.  Parallel Port (J13) Connector Signals

PIN           PI/T SIGNAL      DRIVER/RECEIVER SIGNAL     FUNCTION

1               PAOO+                PDTOO+

2               PA01+                PDT01+

3               PA02+                PDT02+

4               PA03+                PDT03+

5               PA04+                PDT04+

6               PA05+                PDT05+

7               PA06+                PDT06+

8               PA07+                PDT07+

9               PBOO+                PDTIO+

10               PB01+                PDTI1+

11               PB02+                PDT12+

12               PB03+                PDTI3+               PAPER EMPTY

13               PB04+                PDTI4+               SAFETY SWITCH

14               PB05+                PDTI5+               SELECT

15               PB06+                PDTI6+

16               PB07+                PDTI7+               BUSY

17-27                                 GND

28                                    DTISTB1+

29                                    GND

30                                    DTOSTB1-

31-35                                 GND

36                                    +5V

37                                    N/C

3-52

BFISD 8079

Table 3-9.  Centronics Protocol

SIGNAL                      DESCRIPTION                CONNECTOR (J13) PIN

Data Strobe         Sent  by the Model 4108 Base'Unit               30

to cause the printer to accept

information on the data lines.

The data lines must stabilize at

least 50 nanoseconds before the

Data  Strobe is sent.  The Data

Strobe must be present for at

least 100 nanoseconds and must

be removed at least 50 nanoseconds

before the data is taken from the

data  lines

Busy                Sent  by the printer to indicate that           16

the printer cannot accept data

ACKNLG-             Sent  by the printer to indicate that           28

a  character or a function code has

been  accepted

Data Bit 1          Sent  by the Model 4108 Base Unit                1

Data Bit 2          Sent  by the Model 4108 Base Unit                2

Data Bit 3          Sent  by the Model 4108 Base Unit                3

Data Bit 4          Sent  by the Model 4108 Base Unit                4

Data Bit 5          Sent  by the Model 4108 Base Unit                5

Data Bit 6          Sent  by the Model 4108 Base Unit                6

Data Bit 7          Sent  by the Model 4108 Base Unit                7

Data Bit 8          Sent  by the Model 4108 Base Unit to             8

control the optional character set

SS                  Always at 0 volts                                ??13??

PE                  Sent  from the printer to indicate an            ??12??

out-of-paper condition or that the

printer cover is open.  A positive

level is logical true

SLCT                Sent  from the printer when the +5V              ??14??

supply is on, the paper is loaded,

the front cover is closed, and the

operator has activated ON LINE

3-53

BFISD 8079

TBD

Figure  3-12.  Simplified Block Diagram, CMB Floppy Disk Controller

3-54

BFISD 8079

A hard-sectored format, on the other hand, allows somewhat greater data density than does a soft-sectored.  This is because no identifier field occupies space that otherwise is usable for data.  However, the advantages of a soft-sectored format are many, and the double-density disk recording techniques, described in paragraph 3.2.19.2, more than compensate for the data density problem.

3.2.19.2  Double-Density Recording

The double-density recording scheme also is known as MFM (modified-frequency modulation) encoding.  This encoding scheme may best be understood by first reviewing the Kansas City Standard (KSC) for cassette recording.  The KSC en- coding technique is shown in figure 3-13.  A binary 0 is recorded as four full cycles of a 1200—Hz square wave.  A binary 1 is recorded as eight full cycles of a 2400-Hz square wave.  Clearly, with this encoding scheme the transmission rate for one data bit is 1/8 of 2400 Hz, or 300 data bits/second.

The transitions that are common to both the binary 0 and the binary 1 are used to synchronize a local oscillator to the incoming data rate, when the data are recovered from the recording. Therefore, when a transition occurs between the clock ticks, the data recovery circuitry may assume that a 1 is encoded; other-wise the circuitry may assume the code is a binary 0.

TBD

Figure 3-13.  Signal Encoding and Derived Clock, Kansas City Standard

3-55

BFISD 8079

The transmission rate of the Kansas City Standard can be increased by simply using fewer transitions to encode each datum.  Figure 3-14(a) shows a binary 1100 sequence encoded at a transmission rate of 1200 bits/second.  Here the bi-nary 0 requires one full cycle of 1200 Hz, and the binary 1 requires two cycles of 2400 Hz.  Figure 3-14(b) shows the standard pushed to the maximum data rate of 2400 bits/second.  In this scheme a binary 0 is recorded as half a cycle of 1200 Hz, and a 1 is recorded as a full cycle of 2400 Hz.

Regardless of the data rate, the information in Kansas City Standard recordings is in the transitions of the recorded data. At a maximum data transfer rate, the derived clock rate is identically equal to the frequency of the logic 1 cycle.  Therefore, the logic 1 cycle has a transition in the middle of a clock cycle.  On the other hand, the logic 0 cycle has no such transition.  A maximum data transfer rate is used in FM encoding.  The FM encoding technique records on the disk only the transitions of the data square waves, as shown in figure 3-15.  This means that the clock frequency can be increased to pack the data bits more closely on the disk track than can be done when the entire square wave is recorded, as with cassette recording.

This is not the final limit, however.  There is a way of recovering the clock-ing information without wasting half the bits, thereby doubling the number of information bits on a disk. The method is called both double-density and MFM encoding. With this scheme, the encoder discards the clock bits so that only the data bits are present in the output bit stream.

TBD

Figure 3-14.  Maximum Data Rate Recording, Kansas City Standard

3-56

BFISD 8079

TBD

Figure 3-15. Encoded Data for FM Recording

Clearly, both the data transfer rate and the amount of data on the diskette now can be doubled with respect to the (single-density) FM method.  To recover the data, the detector section of the disk controller circuitry generates a pulse stream equal in frequency to the data rate.  These narrow pulses create a bit window in which a logic 1 is detected as a flux transition in the middle of that window, and a logic 0 is detected as an absence of a transition.  So the controller can be sure of the location of each 0 in a long string of 0s, the encoder section records (on the diskette) the clocking information by inserting a clock transition between two adjacent 0s, as shown in figure 3-16.

Hence, the MFM detector is more complex than the FM detector, because it must respond to the inserted clock bits, which appear coincident with the bit window pulses.  The FM and MFM detectors usually are called data separators, because the detector works with a phase-locked loop to separate the composite clock and data signal into clock-only and data-only signals.

3.2.19.3  MFM Data Separation

Data separation in the case of MFM is somewhat different from that of FM.  In FM data separation, the data and the clock components of the composite signal are truly separated: only data pulses go to the controller data input.  On the other hand, in MFM data recovery, the data input to the controller comprises all the original bits from the disk, both data and clock.

The clock input to the floppy disk controller is not the clock pulses contained in the composite signal but is a synthesized version, generated by a local os-cillator in a phase-locked loop.  The clock pulses from that phase-locked loop create a window during which a data bit is expected.  The data input from the diskette to the controller is gated from that window.  Separation of the data bits from the clock bits takes place inside the floppy disk controller chip (paragraph 3.2.19.5), where the actual window gating occurs.  (In FM detection the gating usually takes place in the data separator.)

3-57

BFISD 8079

TBD

Figure  3-16.  Encoded Data for Modified FM (MFM) Recording

Phase Detection

Data separation is enabled by the VCOE+ (VCO Enable) signal input to a 74LS51 combination gate (13X).  (Refer to the CMS Logic Diagram, sheet 51.)  The VCOE+ signal comes from the floppy disk controller chip and is asserted (high) when the chip is ready to transfer data to or from the diskette.  The pin 6 output of the combination gate directs the data from the diskette (DSKDAT-A [DiSKette DATa]) to a 74LS221 one-shot (14Z).  The one-shot delays the data pulse so that a phase detector can detect any clock pulse (generated by a local oscillator) occuring prior to the delayed data pulse, for synchronization purposes.  (After the delay, the data pulse is regenerated by another 74LS221 one-shot after an-other short delay through the other section of the combination gate [pin 8]).

At the moment the one-shot is toggled by a data pulse, the Q output (pin 5) enables the phase detector logic of the phase-locked loop, by clocking a 74LS74 D flip-flip (14X, pin 3) to a cleared condition.  Before or after the one-shot clears, a clock pulse from the local oscillator will trigger another 74LS74 D flip-flop (14X, pin 11)--this is guaranteed because this clock pulse represents twice the data transfer rate.  When the one-shot clears, the Q- output clocks yet another 74LS74 D flip-flop (14V), which indicates the leading edge of the delayed data pulse.

The Q- outputs from the last two flip-flops mentioned are ANDed in a 74LS02 NOR gate (14W).  Any time these outputs are coincident (both low), the NOR gate output sets the flip-flop (14X, pin 4) that enabled the phase detector logic.

This flip-flop, in turn, clears the other two flip-flops (14V and 14X), effec-tively turning off  the phase detector.

Thus the phase detector is enabled and disabled once for every pulse on the data line from the diskette.  This allows synchronization of the clock to the data even though the data input to the phase-locked loop is not a square wave with a 50% duty cycle, but rather a stream of narrow pulses, with many pulses missing from their nominal location.

3-58

BFISD 8079

A simplified and generalized block diagram of the phase detector logic is shown in figure 3-17.  To help the reader to understand the phase detector logic, the block diagram contains only generic logic blocks, and all signals are positive logic (active high), regardless of their true active voltage level.  State changes occur only on rising edges.

Clearly, there was some delay between the time one flip-flop was triggered by the data pulse and the  time the other flip-flop was triggered by the clock. The delay is indicated  by a low output from the NOR gate (14W, pin 10), which allows the phase detector to  continue working.  The delay also is represented by positive-going pulses from one of the phase detector flip-flops and by neg-ative-going pulses from the other.

These PUMP UP (negative-going) and PUMP DOWN (positive-going) signals, when filtered, drive a voltage-controlled oscillator, or VCO.  PUMP UP tends to in-crease the average frequency of the VCO, and PUMP DOWN does the opposite.  This action indicates  the  outcome of the race between a pulse in the incoming data stream and a VCO clock pulse.

TBD

Figure 3-17.  Simplified Block Diagram, Data Separator Phase Detector Logic

3-59

BFISD 8079

For example, if the VCO clock pulse (via a 74LS161 synchronous 4-bit counter [15T]) toggles the flip-flop (14X) connected to it before the pulse from the diskette toggles the other flip-flop, then PUMP DOWN will produce a pulse. The pulse informs the VCO that it is generating too high a frequency, and the pulse will bring down the voltage reference going to the MC4024 VCO chip. The pulse will be active for the time between the leading edge of the VCO clock pulse and the leading edge of the delayed data pulse, indicated by the Q- output of the one-shot (14Z, pin 12) going low.

The opposite happens when a delayed data pulse appears before the clock ticks.

In this case, PUMP UP is a negative pulse, whose width is proportional to the error between the two pulses.  The clock used for comparison is taken from the third bit of a synchronous 4-bit counter (15T) to provide a clock frequency of two times the actual bit transfer rate.  This is so the VCO will synchronize with both the data bits and the inserted clock bits in the input data stream (the inserted clock bits occur at twice the data bit rate).

(To maintain a nominal VCO frequency when no data is being transferred to or from the diskette, the VCO is synchronized with a signal (2XWRCLK+ [2X Write CLocK]) that is twice the frequency of the clock used to send data to the disk- ette.   When the VCOE+ signal goes low, the pin 6 output of the 74LS51 combina- tion gate (13X) replaces the data with the 2XWRCLK+ signal, and synchronization occurs as before.)

Analog Error Detection

The pulse width of the PUMP UP and PUMP DOWN error signals is proportional to
the required amount of frequency correction.  Each of these pulse trains looks
like a pulse-width-modulated replica of the input data stream.  The difference
in the average voltages of the pulse trains determines the output frequency of
the VCO, which is an MC4024 (15V).  Only one of these error signals is active
at any given time; neither is active when synchronization is exact.  However,
when synchronization is exact, both flop-flops will be set when the data pulse
and the clock pulse arrive at the CLOCK inputs to the flip-flops.  This means
that both flop-flops will be set for a short period of time, until the low out-
put from a NOR gate (14W) turns off the phase detector logic and resets them.

During this time, the high pulse on the PUMP DOWN line is supplied through a
diode (CR4) and series resistance to a capacitor (C125).  The capacitor charges
to a positive level.  The charge creates an "automatic bias" for the base of
one of the transistors (Q2) used to adjust the VCO control voltage. This nomi-
nal bias level sets the reference voltage for the VCO.  The bias increases (be-

comes more  positive)  when a positive pulse comes in on the PUMP DOWN line; but,

when a negative pulse (actually a low positive pulse) arrives on the PUMP UP

line, the bias charge will "leak" out through the other diode (CR3), to ground,

and thereby decrease the bias to the error amplifier input transistor.

The error amplifier is a dc amplifier consisting of two 2N2222 transistors con-
nected in a superalpha configuration, for proper impedance matching and good
stability.  An RC (R33/C124) negative feedback loop helps filter the high fre-
quencies in the pulse transitions.

3-60

BFISD 8079

Thus the error amplifier and phase detector logic circuits provide necessary
corrections to the VCO frequency to ensure synchronous clocking of data bits
from the diskette into the floppy disk controller chip.  However, certain ac-
tivity occurs during the writing of data onto the diskette that degrades the
read data and that cannot adequately be compensated for by the data separator.

The phenomenon is known as "bit-shifting."

3.2.19.4  Bit-Shifting

A problem peculiar to magnetic disk recording, especially MFM recording, is
that the high bit densities cause the recovered data to appear shifted from
their nominal position. Figure 3-18 shows the phenomenon as it appears to the
floppy disk controller chip. The upper trace shows five data pulses recorded
on the diskette at the apparent positions indicated.  When the pulses are read
back from the diskette, they are shifted in time from their apparent recorded
position (i.e., some pulses appear later; o.thers appear earlier), as shown in
the lower trace.

Several factors, which include nonlinearities in the pickup electronics and
magnetic interactions, are responsible for bit-shifting. For example, the data
pulses correspond with magnetic domains on the diskette. As shown in the upper
trace of figure  3-18, the leftmost bit has a bit on its right but not on its
left.  Therefore, its magnetic domain is influenced by a like magnetic pole on
the right, but not on the left.  The magnetic flux of the leftmost bit thus is
distorted and tends to move away from the nearby right-hand pole.  Also, the
situation may be aggravated by a real movement of the domain to the left.

TBD

Figure 3-18.  Bit Shifting

3-61

BFISD 8079

Consequently, the read head, responding to the magnetic flux lines of the re-
corded data bit, sends the bit to the drive electronics as if it were repelled
by the bit that will arrive after it (which is the bit to its right in figure
3-18).  This means that the bit seems to arrive early.

The data separator circuits (discussed in paragraph 3.2.19.3) cannot adequately
compensate for bit-shifting; this is because the phase-locked loop in the data
separator is a feedback-control system that cannot follow sudden changes in in-
put frequency, but rather settles over a period of time to its steady-state be-
havior .

Therefore, another means of bit-shift compensation is provided.  The method
used does not actually compensate for the bit shifting of recorded data; but
rather it compensates for the anticipated bit shift, before data actually is
recorded.  The method is called "precompensation."

Precompensation

Fortunately, the data bit flux transitions appear early or late in a completely
predictable manner.  Their time of arrival (at the read electronics) depends on
the location of other bit transitions in their immediate vicinity.  Since the
floppy disk controller chip holds a byte of data before that data goes to the
diskette,  the controller is in a position to analyze the locations of the data
bits within that byte and, in turn, to determine which bits will suffer from
bit-shifting.

For example, if a data bit is a 0 and has a 1 bit on each side of it, then the
neighboring bits will be shifted toward the missing data pulse when they are
recorded on the diskette.  Hence, the first bit should be written early and the
second bit should be written late, to compensate for the shifting.  The appro-
priate commands for this are provided by the floppy disk controller chip and
delivered to the precompensation logic.

Precompensation Control

The amount of precompensation is determined by a 74LS195 4-bit parallel-access
shift register (13S).  (Refer to the CMB Logic Diagram,  sheet 49.)  Each time
a data pulse (WD4- [Write Data]) arrives from the floppy disk controller chip,
the pulse is synchronized with FDCCLK+ (Floppy Disk Controller CLocK) and clock
signal K4MHZ- (origin of both is in the clock generator section of the Central
Microprocessor Board).  This gives the broadside input logic, of the shift reg-
ister enough time to set up before it latches the timing control commands from
the floppy disk controller chip and begins shifting.

If the shift register receives an EARLY+ command from the controller chip, then
that command becomes the data bit and is shifted out of the shift register 125
nanoseconds earlier than the nominal write time.  This will compensate for the
shift that occurs when that bit is written to the diskette.  (The EARLY+ com-
mand is gated through a 74LSOO NAND gate [13R] to input C of the shift regis-
ter.)

3-62

BFISD 8079

Likewise, if the shift register gets a LATE+ command from the controller chip,
then that command becomes the data bit and is shifted out of the shift register
125 nanoseconds later than the nominal write time.  (The LATE+ command is gated
through the 74LSOO NAND gate [13R] to input A of the shift register.)

However, if both commands are inactive (low), then they are ANDed by the 74LS00
NAND gate (13R) and sent to input B of the shift register.  In this case, that
ANDed signal becomes the data bit and is shifted out at the nominal write time.

The data bit output of the shift register is taken from the QD- pin and is sent

to the drive electronics via a 7406 open-collector inverter (14J, pin 8).

Although the preceding discussions have assumed the reader is acquainted with
the WD1793 floppy disk controller chip, such an acquaintance is not absolutely
mandatory to understand the material up to this point. However, as we continue
with functional descriptions of the remaining circuits in the floppy controller
section, it becomes more important to understand the basic architecture of the
chip.  An overview of the chip is presented in the following paragraph.

3.2.19.5  Floppy Disk Drive Control

The floppy disk controller section of the Central Microprocessor Board is based
on the WD1793 floppy disk controller chip (14R).  (Refer to the CMB Logic Dia-
gram,  sheet 50.)  The chip has the capability to read and write in single or
double density.  But it is used only in the double-density mode in our system.

The chip controls head motion by issuing step pulses and head-load commands to
the drive.  Step pulses move the read/write head arms from from track to track.

The head-load command makes the head contact the diskette surface. (When the
head is not loaded, it is physically lifted from the diskette surface.) The
chip also combines the clock and the data bits to form a composite serial data
stream, to be recorded on the diskette.  And it also assembles the separated
data and clock bits into 8-bit bytes for transmission the 68010.

Note that only a few external chips are required to interface the controller to
the floppy diskette drive, since almost all aspects of diskette control are em-

bedded in the controller chip.  It operates on its own 2 MHz clock and has an
on-chip processor designed for disk drive control.  The chip occupies four mem-
ory addresses: the internal command/status, track, sector and data registers
each have unique addresses, and can be read from and written to. (The register
layout is shown in figure 3-19.)

The track register contains the track number of the arm position of the disk-
ette drive that is presently selected. When a new drive is selected, the track
register momentarily is incorrect. But when a system software command is given
to the controller chip to read the diskette, the track identifier, as it passes
under the head,  is loaded into that register.

The sector register indicates which sector is to be read from or written to.

When the controller executes a read or a write instruction, it first puts the
head in contact with the diskette (it "loads the head").  Then it reads the
sector IDs at the present arm position.

3-63

BFISD 8079

TBD

Figure 3-19.  Register Layout, WD1793 Floppy Disk Controller Chip

The controller checks each ID for a match against the contents of the track and
sector registers.  As the disk rotates, the correct sector arrives under the
head.  This is indicated by a match of the ID to the track and the sector reg-
isters.  Now the controller is ready to read or write the data immediately fol-
lowing the sector ID.  The data read from the diskette are accumulated  bit by
bit in the controller until a full byte is present.  The byte is in the data
register (in the chip) and will be passed to the 68010 over the byte-wide data
bus.

Data to be written to the diskette flow from the 68010 to the controller chip
over the same byte-wide data bus.  These data are stored in the data register
(in the chip) by parallel 8-bit write cycles. They then are output as a serial
bit stream to the diskette drives.

The remaining two registers are the command register and the status register.

These occupy a single address in the floppy controller I/O address space.  Data
read from this address are status reports to be returned to the 68010; data
written to this address are commands interpreted by the controller chip.

3-64

BFISD 8079

There are 11 commands available on the WD1793;  they are listed in table 3-10.

The Type I commands move the arm to the correct track.  STEP IN and STEP OUT
commands move the arm one track in or out.  The STEP command moves the arm one
track in the same direction as the last arm movement.  The SEEK command allows
the arm to be moved several tracks in a single step.  This command accepts a
target track number, contained in the data register, and then issues the cor-
rect number of step pulses to move the head arm from the present track to the
target track.

The Type I commands generate the appropriate signals at the controller chip
pins labeled STEP+ and DIRECTION*.  In addition to these arm control signals,

there are four output signals for writing data:

o  WD+ (Write Data)

o  WGATE+ (Write GATE)

o  TG43  (Track Greater  than 43)

o  HLD (Head LoaD)

The WGATE+ signal asserts when WD+ contains the combined clock and data serial
bit stream to be recorded.  Signal TG43 forces the drive to reduce the record-
ing current on tracks 44 and higher to reduce bit-shifting (discussed in para-
graph 3.2.19.4).  However,  this function is not used in the Model 4108 Base
Unit.

Table 3-10.   Command List, WD1793 Floppy Disk Controller Chip

TYPE              COMMAND

I               RESTORE

I               SEEK

I               STEP

I               STEP IN

I               STEP OUT

II               READ SECTOR

II               WRITE SECTOR

III               READ ADDRESS

III               READ TRACK

III               WRITE TRACK

IV               FORCE INTERRUPT

3-65

BFISD 8079

Signal HLD commands the drive to load the read/write heads.  In the Model 4108
Base Unit, however,  the heads are automatically loaded whenever motor power is
on; so the HLD signal is sent directly to the HLT input of the floppy disk con-
troller chip.

Type II commands are used to read and write data.  They function when a drive
has been selected, the arm has been moved to the correct track, and the track
and the sector registers have been loaded with track and sector numbers. The
Type III and IV commands are used for several additional functions, such as
diskette memory allocation, initialization, diagnostics and interrupts.

There also are five status signals:

o  WPRT- (Write PRoTect)

o  TROO- (TRack number 00)

o  IP- (Index Pulse)

o  READY

o  HLT (Head  Load Timeout)

Signal WPRT- is asserted to abort any attempts to write to the diskette if the
diskette is notched for such protection. Signal TROO- is asserted when the arm
is located on the outermost track of the diskette. Signal IP- is asserted each
time the index hole on the diskette passes under a photosensitive diode. The
controller uses this signal to count diskette revolutions and abort incomplete
operations if they do  not finish inside of the allotted number of revolutions.

Signal READY usually is connected the drive power or to a switch on the door of
the drive.  The signal informs the controller chip that the diskette is in the
proper position inside the drive, the door is closed, and power is applied to
the drive.  However, in the Model 4108 Base Unit, the READY signal is synthe-
sized by a 74LS32 OR gate (12J).

The READY input to the controller is the OR of two MOTORON(X)+ signals from the
gate.  Note that the presence of the READY signal does not guarantee that the
correct drive has the motor on, nor does it check to determine whether the se-
lected drive is up to speed. Signal HLT informs the controller chip that the
head has been properly loaded and to commence read or write operations.

For additional, more detailed, information on the Western Digital WD1793 floppy
disk controller chip,  the reader should refer to the manufacturer's literature.

The next few paragraphs discuss how data is transferred to and from the flopp
disk controller chip.

3.2.19.6  Buffered Data Transfer

To improve system throughput, all data involved in transfers between the floppy
controller chip and the 68010 are buffered in the floppy sector buffer.

3-66

BFISD 8079

Since the transfer of data between the system memory and the floppy disk con-
troller is under program control, this method allows the shortest data transfer
time.  The buffer memory is a 6116 2K X 8 static RAM chip (12S), which holds
data for a complete sector. (Refer to the CMB Logic Diagram,  sheet 46.)  A
jumper (D) can select an optional 8K X 8 RAM by bringing in an extra address
line and by moving the Write Enable line to accommodate the larger RAM.  Normal
operation is with the jumper going from 2 to 3, for a 2K  X 8 static RAM. Data
transfer between the sector buffer and the floppy disk controller chip is con-
trolled by DMA (direct memory access) logic.  This is so that the transfer rate
between the sector buffer and the floppy disk controller chip can keep up with
the transfer rate of the serial data moving to and from the diskette.

The sector buffer RAM receives read/write strobes from a 74LS157 1-of-2 data
selector (11R).  Signal BUFCS- to the data selector controls the source of the
read/write signals.  The read/write inputs to the data selector may originate
from the 68010, when the 68010 is filling or emptying the buffer,  or from the
DMA logic,  when the buffer is under DMA control and the data flow is between
the floppy disk controller chip and the buffer RAM.

Floppy Sector Buffer Addresses and Data

During data transfers between the floppy sector buffer and the floppy disk con-
troller chip, a local address counter generates the range of addresses needed
to access the entire sector of information.  This 12-bit counter consists of
four cascaded 74LS393 4-bit counters (UN and 12K). (Refer to the CMB Logic
Diagram, sheet 45.)

Signal INC BUFADR+ (INCrement BUFfer ADdRess), which is asserted at the end of
every completed DMA state machine cycle (described in later paragraphs), serves
to increment the address counter throughout the entire range.  The address then
is latched into two 74LS374 transparent latches (12L and 12N),  whose Q outputs
are the sector buffer RAM address lines.

In addition to the addresses from the floppy buffer address counter, the sector
buffer also receives addresses from the 68010, when data transfer is between it
and the sector buffer. The lower 12 address lines from the 68010 and the eight
data lines from the byte-wide data bus are buffered for the sector buffer RAM
and the controller chip.  The address lines are buffered by a pair of 74LS244
tristate drivers (11L and 11M), enabled by signal BUFCS+  (BUFfer Chip Select),
from the DMA state machine.  (Refer to the CMB Logic Diagram, sheet 42.)  The
byte-wide data bus is bidirectional and is buffered by a 74LS245 transceiver

(13M), controlled by the RD- (Read) signal.  The data bus is active only when
the floppy sector buffer or the floppy disk controller chip is being addressed.

Once an address is set up on the sector buffer address lines,  two decoders (a 74LS139 [12W] and a 74S138 [12X]) generate the appropriate read or write strobe with the correct timing for the static RAM.  (Refer to the CMB Logic Diagram, sheet 44.) Signal FMEMWE- (Floppy MEMory Write Enable) is the write enable for the sector buffer RAM.  The signal is asserted when LCIOWE- (LoCal I/O Write Enable) goes active for a period between the time that timing signal CST1F+ is asserted and timing signal CST2F+ is asserted (125-nanosecond write window).

3-67

BFISD 8079

Signal FMEMRE- (Floppy MEMory Read Enable) is the read enable for the sector
buffer RAM.  This signal is asserted from the 74LS139 (12W) when LCIORE- (LoCal
I/O Read Enable) is active.  Both FMEMWR- and FMEMRE- require MEM- (MEMory) to
be asserted;  MEM- is generated by the floppy controller address decoder (dis-
cussed in a later paragraph).  Signals FMEMWR- and FMEMRE- are selected for use
as the sector buffer read and write strobes by a 74LS157 l-of-2 data selector
(11R).  The corresponding output signals are MEMWE- (MEMory Write Enable) and
MEMRD- (MEMory ReaD).  (Refer to the CBM Logic Diagram, sheet 46.)  These are
enabled by BUFCS- (BUFfer Chip Select), from the state machine described next.

Floppy Sector Buffer Control

The transfer of data between the floppy sector buffer and the floppy disk con-troller chip is controlled by the floppy buffer state machine.  (Refer to the CMB Logic Diagram, sheet 43.)  The floppy buffer state machine functions as a DMA sequencer; it comprises a 74LS164 8-bit serial-to-parallel converter (11W); a 74LS175 quad D flip-flop (11T); and a 74LS157 l-of-2 data selector (US). At the beginning of the state machine operation, a single bit is loaded into the serial-to-parallel converter.

The bit then is shifted at the K2MHZ+ clock rate from one output of the con-
verter to the next;  and each output defines a single machine state. One output
directly increments the sector buffer address counter, and some other outputs
are first ORed and then latched in a D flip-flop, on the falling edge of the
K2MHZ+ clock.  Another output is both ORed and latched directly, also on the
falling edge of the K2MHZ+ clock.

Finally,  several of those flip-flop outputs are used directly for chip control
while others are decoded further by the data selector.  All the state machine's
operations are controlled by data bits BDOO+ and BD01+, from the byte-wide data
bus.  Bit DBOO+ comes out of a floppy drive interface D flip-flop (discussed in
paragraph 3.2.19.7) as BUFW/R- (BUFfer Write/Read); likewise, DB01+ is latched
in that interface as CMD+ (CoMmanD).  BUFW/R- controls the direction of the
data transfer between the sector buffer and the floppy disk controller chip;
CMD+ enables the state machine logic.

A third signal,  DRQ+A (Data ReQuest), produced by the floppy controller chip,
commands the state machine to begin operations.  DRQ+A is asserted when the
floppy  disk controller chip is ready to transfer a byte of data to or from the
buffer.

When the state machine is enabled by CMD+, each occurrence of DRQ+A transfers
a data byte between the floppy sector buffer and the floppy disk controller
chip.  Thus the 74LS164 serial-to-parallel converter (11W) starts shifting when
CMD+ and DRQ+A are both active.  CMD+ informs the state machine that a disk
read or a disk write cycle is requested,  and DRQ+A indicates that no floppy
controller chip interrupt is pending.  If one or both of these signals is low,
the state machine will remain in an idle loop.  Note that the state machine is
not resettable in the middle of a cycle,  as the BUSY- signal must be released
for the sequencing to begin.  (A list of the machine states is presented in
table 3-11.)  Each state lasts 500 nanoseconds, and the states are as follows:

3-68

BFISD 8079

State 1    Latch buffer address (LTCHBUFADR+):  latches the sector buffer

addresses in two 74LS374 8-bit latches (12L and 12N). (Refer to

the CMB Logic Diagram, sheet 45.)  The local address bus is dis-

abled from the main address bus.  The BUSY- line is asserted to

prevent the state machine from restarting while it is in the

middle of a cycle.

State 2    Assert chip select,  enable address:  signal BUFCS- asserts to

enable the 8-bit latches (12L and  12N), sending the address to

the  sector buffer RAM.  BUFCS- also outputs signal FDCCS- from a

74LS157  l-of-2 data selector (11R),  and enables the controller

chip.   (Refer to the CMB Logic Diagram, sheet 46.)

State 3    Assert read and write enables: sector buffer RAM enable signals

BUFMEMWE- and BUFMEMRE- go low at the outputs of another 74LS157

(US). (Refer to the CMB Logic Diagram,  sheet 43.)

State 4    Removes write enable: BUFMEMWE- releases.

State 5    Removes read enable: BUFMEMRE- releases.

State 6    Removes local address enables:  BUFCS- and BUFCS+ release.

State 7    Increments the local address counter: INCBUFADR+ asserts.

Table 3-11.   State Machine States

OUTPUT SIGNAL  STATE 1  STATE 2  STATE 3  STATE 4   STATE 5  STATE 6  STATE 7

R W      R W      R W      R W       R W      R W      R W

BUSY-          1 1      1 1      1 1      1 1       1 1      0 0      0 0

INCBUFADR+     0 0      0 0      0 0      0 0       0 0      0 0      1 1

BUFCS+         0 0      1 1      1 1      1 1       1 1      0 0      0 0

BUFCS-         0 0      1 1      1 1      1 1       1 1      0 0      0 0

LTCHBUFADR+    1 1      0 0      0 0      0 0       0 0      0 0      0 0

BUFMEMRE-      0 0      0 0      1 0      1 0       0 0      0 0      0 0

BUFMEMWE-      0 0      0 0      0 1      0 0       0 0      0 0      0 0

BUFFDCRE-      0 0      0 0      0 1      0 0       0 0      0 0      0 0

BUFFDCWE-      0 0      0 0      1 0      1 0       0 0      0 0      0 0

R = Read cycle      1 =  Asserted signal

W = Write cycle     0 =  Inactive signal

3-69

BFISD 8079

Thus the floppy buffer state machine controls data flow between the floppy disk controller chip and the floppy sector buffer.  When the state machine is not in control of the buffer, however, the operating system software may fill or empty it under program control, as mentioned earlier.  Also, at that time, the system software may issue commands to, or receive status information from,  the floppy disk controller section of the Central Microprocessor Board.

3.2.19.7  Floppy Disk Controller Section Control

All control of the floppy disk controller section of the Central Microprocessor Board is by the operating system software; the software controls the following:

o   The transfer of all control information from the 68010 to the floppy disk
controller section.  This includes (a) the reset for the floppy sector
buffer local address counter; (b) the enable and the selection of read or write for the floppy buffer state machine; (c) the selection of a drive
and of the side of the diskette within that drive;  (d) the power to the
selected drive motor; (e) the selection of FM or MFM at the floppy disk
controller chip; (f) the selection of double density or standard density
recording; and (g) all commands to the floppy disk controller chip command
register.

o  The transfer of all status information from the floppy disk controller section to the 68010.  These include (a) interrupt and data requests from the controller chip; (b) the index hole pulse from the drive; (c) the busy signal from the floppy buffer state machine; and (d) reset and interrupt enable status.

o  All data flow between the floppy sector buffer and the 68010.

Controller Section Programming

The floppy disk controller section options are programmed through the use of a 74LS273 octal D flip-flop (13J).  (Refer to the CMB Logic Diagram, sheet 47.)

The flip-flop is accessed at address 70XXXX (hex) and latches the control bit pattern from the byte-wide I/O data bus that determines the direction of data flow in the floppy sector buffer state machine.  Floppy drive recording density and encoding format also are chosen here.

The recording density is selected when the HD/SD- (High Density/Standard Densi-
ty) signal from the flip-flop (13J) selects the appropriate clock outputs from a 74LS157 l-of-2 data selector (11J, CMB Logic Diagram, sheet 48). The chosen clock output signals go to both the floppy disk controller chip and the data separator logic.

Floppy Drive Control

Another 74LS273 (13K) is the floppy control latch that holds control signals for the drive.  (Refer to the CMB Logic Diagram, sheet 47.)

3-70

BFISD 8079

It latches the control bit pattern from the byte-wide I/O data bus that deter-
mines which drive is to be used (SELO-/SEL1- and MOTORONO-/MOTORON1-) and which side of the diskette in the chosen drive is to be used (SIDE-).  The latch is mapped in with a write to FLOPLTCH-, at address 76XXXX (hex). The DOORLOCK(X)- signals do not apply to the drives presently used in the Model 4108 Base Unit.

Status Transfer Control

To decide when to send the control signals, the system software must receive certain status information from the floppy disk controller section.  Address 72XXXX (hex) activates the STATUS- signal.  This signal, along with the LCIORE- (LoCal I/O Read Enable) signal, enables a 74LS373 transparent latch (13L, CMB Logic Diagram, sheet 47).

Unlike the two latches used for programming and drive control,  this latch re-
ceives information from the floppy disk controller section and then drives that information on the byte-wide I/O data bus.  Thus the latch provides the system software with a "snapshot" of the floppy disk controller section status. The various status signals are listed in a preceding paragraph.

Status Interrupt Control

When the system software needs to be informed of when a byte of data is being transferred to or from the diskette or when the floppy disk controller chip has completed an entire transfer of sector data, an appropriate signal is generated at the chip and may be used to interrupt the 68010.  A 74LS51 combination gate (10W) collects the two kinds of interrupts (INTR+A [INTeRrupt] and DRQ+A [Data ReQuest]) from the floppy disk controller chip.  (Refer to the CMB Logic Dia- Diagram,  sheet 44.)

The two signals are enabled by ENB1NTR+ (ENaBle INTeRrupt) and ENBDRQ+ (ENaBle Data ReQuest).  When one, or both, of these signals is enabled, and the corres-
ponding interrupt is active, then a 74LS74 D flop-flop (14V) asserts signal INT3- (INTerrupt level 3).  The flip-flop holds the interrupt until the 68010 returns an interrupt acknowledge signal (IACKL3- [Interrupt ACKnowledge Level 3]).

When the INT3- signal is asserted, it is encoded by a 74LS148 8-line-to-3-line priority encoder (3E).  (Refer to the CMB Logic Diagram, sheet 22.) This con-
stitutes an interrupt request to the 68010.  Thus an interrupt request level 3 is encoded on the 68010 interrupt request lines (IPLO- through IPL2-). If the priority  of the interrupt is greater than the current processor priority, then the interrupt processing sequence is started:  The 68010 places the interrupt priority number on the lines carrying the three least significant address bits.

These are decoded by a 74LS151 l-of-8 data selector (10K, CMB Logic Diagram, sheet 22).

For priority number 3,  the CVPA- (CPU Valid Peripheral Address) output of the data selector is low (active).  In response to CVPA-, the 68010 internally gen- erates a vector number that is determined by the interrupt level number.

3-71

BFISD 8079

(The vector number [when multiplied by four] is the address in the lowest 1K bytes of main memory that contains the address of the routine that will handle the interrupt.)  The content of the vector number is fetched and loaded into the 68010 program counter, and normal instruction execution commences in the interrupt service routine.

At the same time that the priority number on the address bus was being decoded to produce CVPA-, a 74LS138 1-of-8 decoder (10L, CMB Logic Diagram, sheet 20) also decoded those address bits.  The output was the IACKL3- signal mentioned above. This is the interrupt acknowledge signal required to reset the flip-
flop that generated 1NT3-.

## 3.3  MEMORY ARRAY BOARD FUNCTIONAL DESCRIPTION

This information will be available at a later date.

## 3.4  BASE UNIT POWER SUPPLY FUNCTIONAL DESCRIPTION

This information will be available at a later date.

3-72

BFISD 8079

SECTION IV

# MAINTENANCE

## 4.1  INTRODUCTION

This section contains maintenance information for the Central Microprocessor Board (CMB), Base Unit Power Supply and peripheral controller boards contained in the Model 4108 Base Unit of the MAI® 2000 Series Desktop Computer System.

Included are procedures for preventive maintenance and trouble analysis, along with a diagrammed presentation of a system power-up check and a discussion of diagnostic programs.  (Refer to Sections VII, VIII and IX in this manual for preventive maintenance and trouble analysis of the disk drive systems.)

It is recommended that the service representative become thoroughly familiar with the material contained in this manual before performing the following preventive maintenance and trouble analysis procedures.

## 4.2  SPECIAL TOOLS

Maintenance procedures contained in this manual require no special tools or special test equipment.

## 4.3  PREVENTIVE MAINTENANCE (INCOMPLETE)

Preventive maintenance consists of performing recommended inspection, cleaning and adjustments at regular intervals to prevent equipment failures.  Because of the electronic structure of the equipment, preventive tasks consume little of the service representative's time and are well worth the effort in terms of the increase in equipment reliability. The preventive maintenance procedures are summarized in table 4-1.

Table  4-1.  Preventive Maintenance Summary

EQUIPMENT          INTERVAL          ACTION              REFERENCE

Base Unit Power        __ months    Check voltage         Table 4-2

Supply                              tolerance, adjust

as required

Winchester Drives      __ months    Verify/adjust         Sections VIII

power supply          and IX in this

voltages, inspect     manual

cables, clean and

adjust

Floppy Disk Drive       __ months   Verify/adjust         Section VII in

power supply          this manual

voltages, inspect

cables, clean and

adjust

4-1

BFISD 8079

Table 4-2.   Base Unit Power Supply Voltage Adjustments

MEASUREMENT      TEST POINT           VOLTAGE                ADJUSTMENT

1                TPx             +xx.x V to +xx.x V        Rxx

2                TPx             +xx.x V to +xx.x V        None

3                TPx             +xx.x V to +xx.x V        None

4                TPx             +xx.x V to +xx.x V        None

## 4.4   TROUBLE ANALYSIS

The steps that follow provide an organized, general approach toward trouble-
shooting the system. Proceed as follows:

1. Obtain an accurate description of the malfunction from the operator

or other responsible person; then verify the problem.

2. Perform the System Power-Up Check (paragraph 4.5) as secondary veri-

fication of the suspected problem or as confirmation that basic system

functions are in order.

3. If the problem is of an intermittent nature, run the appropriate

diagnostic program in an effort to induce the problem on a controlled

basis.

4. Perform a visual inspection and verify that all cabling is connected

properly (including ground wires) and all connectors and PCBAs are

seated properly.

5. Check the ac line as a possible cause of problems, i.e., sharp drops

in voltage, transients and poor grounds are common problems.  Check

dc voltage levels on power supply test points (refer to table 4-2).

6. Verify that all switches and jumpers on controller PCBAs are properly

configured, i.e., device addresses, DMA numbers, etc. (refer to

section V of this manual).

7. Disconnect the suspected peripheral from the system, and operate it

off-line to isolate the problem or to confirm proper operation.

8. When replacing a PCBA appears to solve the problem, reinstall the sus-

pected faulty PCBA to verify that the problem was not caused by bad

contacts or poor seating.

9. After the suspected problem has been solved, run the applicable diag-

nostic programs before placing the entire system back in its normal

operation.

10. Refer to the appropriate disk drive sections (VII, VIII, IX) in this

manual for trouble analysis of suspected disk drive problems.

NOTE: The remaining maintenance information will be furnished at a later date.

4-2

BFISD 8079

SECTION V

# REMOVAL/REPLACEMENT

## 5.1  INTRODUCTION

This section provides detailed procedures for replacing major subassemblies,

and includes jumper/switch installation/settings and cable part numbers.

## 5.2  REPLACING THE CENTRAL MICROPROCESSOR BOARD (CMB)

To remove the Central Microprocessor Board, proceed as follows:

1.  Shut down the system, and turn the Base Unit power OFF.

2.  Unplug all connections to the Base Unit, including all attached peri-

pherals.

3.  Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover, and push in to disengage the

the latch.  Repeat with the left-hand side, and remove the cover.

4.  Remove the Memory Array PCBAs,  located in the front right-hand corner

of the CMB, by simply lifting the "stack" of PCBAs away from the CMB,

unplugging the bottom memory array  PCBA from the CMB.

5.  Unplug the ribbon  cable(s) going from the Winchester Drive(s) to the

Winchester Drive Controller  (WDC) PCBA, located in the card cage at

the rear right-hand corner of the CMB.  (Note: two of the drive con-

nectors on the WDC  PCBA are situated side by side; the right-hand

connector [JO] receives the "0" drive cable, and the left-hand con-

nector [Jl] receives the "1" drive cable.)

6.  Remove the controller PCBA(s) by lifting the PCBA(s) away from the

CMB,  unplugging the (bottom) PCBA from the CMB.  (When more than one

PCBA is present, the entire stack may be removed as a unit.)

7.  Remove the front and rear facias by pulling up slightly on each plas-

tic card holder until the corresponding facia is disengaged from the

card holder.

8.  Remove the Winchester drive(s) as follows:

a. Using a screwdriver, or similar tool, push back the two (2) plas-

tic latches at the bottom rear of the Winchester drive chassis,

while lifting the back of the drive to clear the latches.

b. Unplug the 4-pin power plug, located at the bottom rear left-hand

corner of the drive chassis, on the Master Electronics PCBA.

5-1

BFISD 8079

c. Push the drive slightly toward the rear of the CMB so that the

flange at the  bottom front of the drive clears the slot in the

Base Unit bottom panel, and lift the Winchester drive chassis from

the CMB.

9.  Remove the floppy drive(s) as follows:

a. Unplug the 4-pin power connector at the rear of the drive chassis.

b. Using a screwdriver, or similar tool, push back the two (2) plas-

tic latches at the bottom  rear of the floppy drive chassis, while

lifting the back of the drive to clear the latches.

c. Push the drive slightly to the rear so that the flange at the bot-

tom front of the drive clears the slot in the Base Unit panel.

d. Unplug the ribbon cable from the CMB, and lift the floppy drive

chassis from the CMB. (Note: the two floppy drive connectors on

the CMB are  situated side by side. The right-hand connector re-

ceives the "0" cable; the left-hand connector receives the "1"

cable.

10.  Remove the Base Unit Power Supply by removing the two (2) Phillips

head screws at the bottom right-hand side of the Power Supply and

lifting the Supply from the CMB, unplugging the Supply from the CMB.

The Central Microprocessor Board now may be removed from the Base Unit bottom panel. To install the replacement CMB, proceed as follows (refer to figure 5-1 for jumper locations and to figure 5-2 for cable part numbers):

11.  Connect jumper N between points 1 and 2. (This jumper allows the mas-

ter oscillator to be disconnected from the dividers and buffers.  An

external oscillator can be injected at this point.  Normal operation

is with jumper N installed.)

12.  Connect jumpers C and P. These jumpers configure the board to accept

four different size EPROMs, used for system diagnostics and the debug-

ger.  The Central Microprocessor Board can handle 2732, 2764, 27128

and 27256 EPROMs.  As received, the CMB has jumpers in etch to handle

either 2732s or 2764s; no modification is necessary.  To use the other

size EPROMs, or to switch back to the 2732 or the 2764, after using a

larger EPROM, follow the chart below.

EPROM                    JUMPER C        JUMPER  P

2732 (4K x 8)             1 and 2          1 and 2

2764 (8K x 8)             1 and 2          1 and 2

27128 (16K x  8)          2 and 3          1 and 2

27256 (32K x  8)          2 and 3          2 and 3

NOTE: An earlier version of the CMB (Rev. 1) could only handle 2716s

and 2732s.  On this CMB, jumper C must be connected as follows:

5-2

BFISD 8079

Figure 5-1.  Location of Jumpers on Central Microprocessor Board

5-3

BFISD 8079

Figure 5-2.  Central Microprocessor Board Cable Part Numbers

5-4

BFISD 8079

EPROM                   JUMPER C

2716 (2K x 8)           2 and 3

2732 (4K x 8)           1 and 2

13.  Connect jumper R.  (This jumper, when disconnected, disables the mem-

ory refresh circuitry, thereby allowing easier debugging of memory and

bus arbitration circuits.  Normal operation is with jumper R connected

between points 1 and 2.)

14.  Connect jumpers A, B, G, H and K according to the following tables.

(The serial port has two programmable ports.  Each can be configured

as RS-232 and support a modem, a printer or a terminal.  Additionally,

port B supports X-21.  Note that only one cable is needed to support

printers, terminals or modems.  All signal switching is done on the

Central Microprocessor Board via the jumpers.  The RS-232 cable is a

pin-for-pin connection.  No signals or pins are cross-connected.)

PORT A:

MODEM                 TERMINAL              PRINTER

Name     Jumper A   Cable      Jumper A   Cable      Jumper A   Cable

CTS       7 and 8   pin 5       7 and 9   pin 4       7 and 9   pin 4

DSRA      3 and 4   pin 6      *1 and 3   pin 20      1 and 3   pin 20

DTR       1 and 2   pin 20     *2 and 4   pin 6       2 and 4   pin 6

RTSA      9 and 10  pin 4       8 and 10  pin 5       8 and 10  pin 5

RXDA     11 and 12  pin 3      11 and 13  pin 2      11 and 13  pin 2

TXDA     13 and 14  pin 2      12 and 14  pin 3      12 and 14  pin 3

RNGA     In Place   pin 22

TRXCA    In Place   pin 15

DCDA     In Place   pin 8

PORT B:

MODEM                TERMINAL              PRINTER

Name     Jumper B   Cable      Jumper B   Cable      Jumper B   Cable

CTSB      7 and 8   pin 5       7 and 9   pin 4       7 and 9   pin 4

DSRB      3 and 4   pin 6       3 and 1   pin 20      3 and 1   pin 20

DTRB      1 and 2   pin 20      2 and 4   pin 6       2 and 4   pin 6

RTSB      9 and 10  pin 4       8 and 10  pin 5       8 and 10  pin 5

RXDB     13 and 14  pin 3      13 and 15  pin 2      13 and 15  pin 2

TXDB     15 and 16  pin 2      14 and 16  pin 3      14 and 16  pin 3

Jumper G              Jumper G              Jumper G

RXDB     15 and 16  pin 3      15 and 16  pin 2      15 and 16  pin 2

DCDB     17 and 18  pin 8      17 and 18  pin 8

TRXCB    10 and 20  pin 15     19 and 20  pin 15

23 and 24             23 and 24

5-5

BFISD 8079

Jumper H              Jumper H

DCDB     1 and 2               1 and 2

Jumper K              Jumper K              Jumper K

D422    *1 and 2              *1 and 2              *1 and 2

NOTE:  Be sure to disconnect all unused jumper positions on port  B.

PORT B - RS-422:

Jumper   Connect    AND    Jumper   Connect

G       1 and 2            B      11 and 12

G       3 and 4            B      15 and 16

G       5 and 6            H       2 and 3

G       7 and 8

G       9 and 10

G      11 and 12

G      13 and 14

G      21 and 22

NOTE:  When RS-422 is used in port B, be sure that jumpers

G:15 and 16,

G:19 and 20,  and

K:  1 and 2

are disconnected.

*This  jumper disables the RS-422 drivers.

15.  Connect jumpers L and M.  (The serial ports  are capable of communi-

cating at a number of different speeds and can communicate both syn-

chronously and asynchronously.  Jumper L connects the master clock

to the Baud rate generator, used for asynchronous input/output. Jum-

per M connects the synchronous clock to the port.  These clocks are

disconnectable for service purposes.  Normal operation is with both

jumpers [L and M] inserted, connecting pins 1 and 2 on each jumper

block.)

16.  Connect jumper D according to the following  table.  (The floppy disk

drive support logic, on the Central Microprocessor Board, can support

both 2K x 8 and 8K x 8 static  buffers.  This RAM is used as a sector

buffer to speed up overall system performance when using the floppy

drive.  In addition, an optional 8K x 8 buffer may be used so that an

entire track of information may be input/output to the 68010 micropro-

cessor at one time without the processor having to read from the disk

sector by sector.)

5-6

BFISD 8079

RAM SIZE        JUMPER  D

2K x 8          2 and 3

8K x 8          1 and 2

17.  Connect Jumper E.  (The floppy disk controller,  located on the Central

Microprocessor Board, has three different data  separators available:

the Analog, the Standard Microsystems Corp. [SMC], and the Western

Digital [WD].  The installation of the jumper depends on which data

separator is used.)

SEPARATOR:

Analog                 SMC                  WD

Data   1 and 2      Data    3 and  4        Data    5 and  6

Clock  7 and 8      Clock   9 and  10       Clock  11 and  12

18.  Connect jumper F according to the following  table. (This jumper se-

lects between Standard Density and High Density decoding on the

Western Digital data separator.  The system described in this manual

uses Standard Density disk drives.)

MEDIA              JUMPER F

Standard Density       1 and  2

High Density           3 and  4

19.  Verify that jumper S is not connected.  (This jumper is only to be

used when calibrating the Western Digital data separator.  The jumper

grounds the VFOE input to the WD1691, simulating a read condition.

Normal operation is the jumper disconnected.)

20.  For a standard Central Microprocessor Board configuration, recheck the

jumper installation by referring to the jumper configuration table

(5-1).  The following assumptions are made:

2732 or 2764 EPROMs

2K x 8 sector buffer

Standard RS-232 DCE on serial  ports  A and B

Analog Data Separator

Standard density disk drives

21.  Reinstall the Central Microprocessor Board onto the Base Unit chassis.

22.  Plug the Base Unit Power Supply into the Central Microprocessor Board,

and replace the two (2) Phillips head screws at the bottom right-hand

side of the Power Supply.

23.  Reinstall the floppy  disk drives(s) by completing the following steps.

a.  Lower the floppy drive chassis into position on the CMB.

5-7

BFISD 8079

Table 5-1.  CMB Jumper Configuration

JUMPER      CONNECT                      FUNCTION

A         7 and 9        Serial Port A - CTS

A         8 and 10       Serial Port A - RTS

A        11 and 13       Serial Port A - RXDA

A        12 and 14       Serial Port A - TXDA

B         1 and 3        Serial Port B - DSRB

B         2 and 4        Serial Port B - DTRB

B         7 and 9        Serial Port B - CTS

B         8 and 10       Serial Port B - RTSB

B        13 and 15       Serial Port B - RXDB

B        14 and 16       Serial Port B - TXDB

C          None          EPROM Size Select - 2732, 2764

D         2 and 3        Floppy Sector Buffer Size Select - 2K x 8

E         1 and 2        Floppy Data Separator Select - Data

E         7 and 8        Floppy Data Separator Select - Clock

F         1 and 2        Floppy Density Select

G        15 and 16       Serial Port B - RXDB

G        17 and 18       Serial Port B - DCDB

G        19 and 20       Serial Port B - TRXCB

G        23 and 24       Serial Port B - TRXCB

H         1 and 2        Serial Port B - DCDB

K         1 and 2        Serial Port B - RS-422 Disconnect

L         1 and 2        Baud Rate Generator Connect

M         1 and 2        Serial Communications Synchronous Clock Connect

N         1 and 2        Master Oscillator Connect

P          None          EPROM Size Select - 2732, 2764

R          None          Refresh Enable

S          None          WD Data Separator Enable (Floppy Calibrate)

5-8

BFISD 8079

b.  Plug  the ribbon cable into the CMB. (Note: the two connectors on

the CMB are situated side by side.  The right-hand connector re-

ceives the "0" cable; the left-hand connector receives the "1"

cable.

c.  Pull the drive slightly to the front of the CMB so that the flange

at the bottom of the drive chassis enters the slot in the Base

Unit front panel.

d.  Lower the back of the drive chassis so that it pushes back the two

(2) plastic latches on the CMB at the bottom rear of the drive.

The drive chassis will "snap" in place.

e.  Connect the 4-pin power plug to the connector located at the top

right-hand corner of the floppy drive chassis.

24.   Reinstall the Winchester drive(s) by completing the following steps.

a.  Lower the Winchester drive chassis into position on the CMB, and

pull the drive slightly to the front of the CMB so that the flange

at the bottom of the drive chassis enters the slot in the Base

Unit front panel.

b.  Connect the 4-pin power plug to the connector located at the bot-

tom rear left-hand corner of the drive chassis,  on the Master

Electronics PCBA.

c.  Lower the back of the drive chassis so that it pushes back the two

(2) plastic latches on the CMB at the bottom rear of the drive.

The drive chassis will "snap" in place.

25.   Replace the front and rear facias by reversing the removal procedure

in Step 7.

26.   Reinstall the controller PCBA(s) into the card cage at the rear right-

hand corner of the CMB by plugging the PCBA into the CMB.  (When  more

than one controller PCBA is present, the entire "stack" may be rein-

stalled as a unit.)

27.   Plug the ribbon cables from the hard disk drive(s) into the Winchester

Drive Controller (WDC) PCBA, at the top of the card cage.  (Note: the

two narrower ribbon connectors on the WDC PCBA are situated  side  by

side; the right-hand connector [J0] receives the "0" drive cable, and

the left-hand connector [Jl] receives the "1" drive  cable.)

28.   Reinstall the Memory Array PCBAs into the card cage  at the front

right-hand corner of the CMB by plugging the bottom PCBA into the CMB.

(The entire stack may be reinstalled as a unit.)

29.   Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to snap in place.

5-9

BFISD 8079

30. Plug In all connections to the Base Unit, including all previously at-

tached peripherals.

5.3  REPLACING THE BASE UNIT POWER SUPPLY

To replace the Base Unit Power Supply, proceed as follows:

1.  Shut down the system, and turn the Base Unit power OFF.

2.  Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover, and push in  to disengage the

the latch.  Repeat with the left-hand side, and remove the cover.

3. Disconnect the 4-pin power plug from the connector located at the bot-

tom left-hand corner of the Winchester drive(s) chassis, on the Master

Electronics PCBA.

4. Disconnect the 4-pin power plug from the connector located at the top

right-hand corner of the floppy drive(s) chassis.

5. Unplug all connections to the Base Unit, including all attached peri-

pherals.

6. Unplug the ribbon cable(s) going from the Winchester Drive(s) to the

Winchester Drive Controller (WDC) PCBA, located in the card cage at

the rear right-hand corner of the OMB.  (Note: two of the drive con-

nectors on the WDC PCBA are situated side by side; the right-hand con-

nector [J0] receives the "0" drive cable, and the left-hand connector

[Jl] receives the "1" drive cable.)

7. Remove the controller PCBA(s) by lifting the PCBA(s) away from the

CMB, unplugging the (bottom) PCBA from the CMB.  (When more than one

PCBA is present, the entire stack may be removed as a unit.)

8. Remove the rear facia by pulling up slightly on the plastic card hold-

er until the facia is disengaged from the card holder.

9.  Remove the Base Unit Power Supply by removing the two (2) Phillips-

head screws at the bottom right-hand side of the Power Supply and

lifting the Supply from the CMB,  unplugging the Supply from the CMB.

To install the replacement Base Unit Power Supply, proceed as follows :

NOTE

The  correct Base Unit Power Supply for the

available power line voltage must be installed.

See the parts listing for the part numbers.

5-10

BFISD 8079

10.  Reinstall the Base Unit Power Supply by lowering the Supply into the

Base Unit, onto the CMB, and plugging the Supply into the CMB.

11.  Replace the two (2) Phillips-head screws at the bottom right-hand side

of the Power Supply.

12.  Replace the rear facia by reversing the removal procedure in Step 8.

13.  Reinstall the controller PCBA(s) into the card cage at the rear right-

hand corner of the (MB by plugging the PCBA into the CMB.  (When more

than one controller PCBA is present, the entire "stack" may be rein-

stalled as a unit.)

14.  Plug the ribbon cable(s) coming from the Winchester Drive(s) into the

Winchester Drive Controller (WDC) PCBA, at the top of the card cage.

(Note: the two narrower ribbon connectors on the WDC PCBA are situated

side by  side;  the right-hand connector [JO] receives the "0" drive

cable, and the left-hand connector [Jl] receives the "1" drive cable.)

15.  Connect the nearest 4-pin power plug to the connector located at the

top rear right-hand corner of the floppy drives(s) chassis.

16.  Connect the nearest 4-pin power plug to the connector located at the

bottom rear left-hand corner of the Winchester Drive(s) chassis.

17.  Turn the Base Unit power ON.

18.  Connect the positive test probe of a digital multimeter (DMM) to the

+5VDC test point on the Power Supply.  This point is accessible from

the top of the Power Supply cover , through the square hole near the

front left-hand corner.  (An edge of a printed circuit board can be

seen through this hole, and the test points for the voltages produced

by the supply are located near this edge; they are clearly marked.)

19.  Adjust the +5-volt supply output for a DMM reading of 5.05040.010

volts dc.  (This adjustment may be made by using a small, non-conduc-

tive screwdriver to turn the +5VDC adjust potentiometer. This poten-

tiometer is accessible through the [round] hole at the top of the

Power Supply cover, at the front left-hand corner.

20.  Turn the Base Unit power OFF.

21.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into place.

22.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

5.4  REPLACING THE MEMORY ARRAY MODULES

To replace the Memory Array PCBAs, proceed as follows:

5-11

BFISD 8079

CAUTION

Do not remove these boards when power is

applied to the Base Unit.

1. Shut down the system, and turn the Base Unit power OFF.

2. Insert a screwdriver,  or similar device, into the slot at the bottom

right-hand side of the Base Unit cover, and push in to disengage the

the  plastic  latch.  Repeat with the left-hand side, and remove the

cover.

3. Remove the Memory Array PCBAs, located in the front right-hand corner

of the CMS, by simply lifting the "stack" of PCBAs away from the CMB,

unplugging the bottom memory array PCBA from the CMB.

To  install the replacement Memory Array PCBA(s), proceed as follows:

4. Set the appropriate switches for the desired physical address of the

Memory Array PCBA.  See table 5-2 for a listing of switch settings,

and refer to figure 5-3 for switch locations.  Be careful not to

duplicate addresses of existing Memory Array PCBAs; compare the switch

settings of all the PCBAs.

Table 5-2. Memory Array Module Address Switch Settings

ADDRESS

(K Bytes)          S1          S2         S3         S4         S5         S6

0 to 256        ON          ON     DON'T CARE     ON         ON         ON

256 to 512        ON          ON     DON'T CARE     ON         ON         OFF

512 to 768        ON          ON     DON'T CARE     ON         OFF        ON

768 to 1024       ON          ON     DON'T CARE     ON         OFF        OFF

1024 to 1280       ON          ON     DON'T CARE     OFF        ON         ON

Note: OFF = OPEN and ON = CLOSED

5-12

BFISD 8079

Figure 5-3.  Location of Address Switches on Memory Array Module

5-13

BIFSD 8079

5.  Reinstall the Memory Array PCBAs into the card cage at the front

right-hand corner of the CMB by plugging the bottom PCBA into the CMB.

(Each board may be plugged into another, and the entire stack may be

installed as a unit.)

6.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into place.

7.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

## 5.5  REPLACING THE 4-WAY CONTROLLER BOARDS

To replace the 4-Way Controller PCBA(s), proceed as follows:

CAUTION

Do not remove these boards when power is

applied to the Base Unit.

1.  Shut down the system, and turn the Base Unit power OFF.

2.  Insert a screwdriver, or similar device, into the slot at the  bottom

right-hand side of the Base Unit cover, and push in to disengage the

the plastic latch.  Repeat with the left-hand side, and remove the

cover.

3.  Unplug the WDC Bus Adapter PCBA and the WDC PCBA (which carries the

WDC PCBA) as a single unit from the top of the  "stack."  (This step

may not be necessary; refer to step 4.)

4.  Unplug from the stack any other controller PCBAs that might be present

(after first disconnecting their cables) until the desired 4-Way Con-

troller PCBA is accessible.  Record the order of board removal.  (When

more than one device controller board is present, the entire stack may

be removed as a unit, and the 4-Way Controller PCBA[s] then may be

removed from the stack while it is outside of the Base Unit.)

The 4-Way Controller PCBA(s) now may be removed from the Central Microprocessor Board, or from the PCBA it is plugged into.  To install the replacement 4-Way Controller PCBA(s), complete the following steps.

5.  Set the appropriate switches on the 4-Way Controller PCBA for the con-

troller board address/DMA arbitration number and for the kind of peri-

pheral(s) served  by the Base Unit according to the listings shown in

table 5-3.  See figure 5-4 for the location of the switches.

5-14

BFISD 8079

Table 5-3.   4-Way Controller PCBA Switch Settings

SWITCH S1

_           DMA Arbitration                       PCBA Address    _

S1     S2      S3     S4     S5     S6     S7     S8     S9     S10

Board 1    ON     OFF     OFF    OFF    OFF    OFF    OFF    ON     OFF    ON

Board 2    ON     OFF     OFF    ON     OFF    OFF    OFF    ON     OFF    OFF

Board 3    ON     OFF     OFF    ON     ON     OFF    OFF    OFF    ON     ON

Board 4    ON     OFF     OFF    ON     ON     ON     OFF    OFF    ON     OFF

SWITCHES PGM1-4*

For PGM1 through PGM4, connect the pins according to the PCB detail used:

PCB detail 904741-001  (current production)

TERMINAL/PRINTER                 MODEM

1 to 7                      1 to 2

2 to 8                      3 to 4

3 to 4                      7 to 8

9 to 10                     9 to 10

13 to 15                    13 to 14

14 to 16                    15 to 16

PCB detail 904943-001 (future production)

TERMINAL/PRINTER                 MODEM

1 to 3                      1 to 2

2 to 4                      3 to 4

9 to 11                     9 to 10

10 to 12                    11 to 12

13 to 15                    13 to 14

14 to 16                    15 to 16

*PGM1 through 4 are actually jumpers (as opposed to switches) enclosed in plas-
tic rectangular "boxes."  Each box may be pulled from its. position and then reinstalled to connect any two adjacent pins.  There is one PGM "group" per controller port, six  boxes per PGM group, and 16  pins per PGM group.

5-15

BFISD 8079

Figure 5-4.  Location of Switches on 4-Way Controller PCBA

5-16

BFISD 8079

6.  Plug the 4-Way Controller PCBA into the CMB (or into the PCBA from

which the original was removed) at the rear right-hand corner of the

CMB.  Replace any other boards that were removed in step 4, in the or-

der recorded in that step.

7.  Plug the WDC Bus Adapter PCBA and the WDC PCBA (mounted above the com-

ponent side of the WDC Bus Adapter) into the PCBA at the top of the

stack.

8.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into  place.

9.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals that may have been removed during this procedure.

## 5.6  REPLACING THE WINCHESTER DRIVE CONTROLLER (WDC) BOARD

To replace the WDC PCBA, proceed as follows (2-PCBA configuration only):

CAUTION

Do not remove this board when power

is applied to the Base Unit.

1.  Shut down the system, and turn the Base Unit power OFF.

2.  Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover,  and push in to disengage the

the plastic latch.  Repeat with the left-hand side, and remove the

cover.

3.  Unplug  the ribbon cable(s) going from the Winchester Drive(s) to the

Winchester Drive Controller (WDC) PCBA,  located in the card cage at

the rear right-hand corner of the Central Microprocessor Board (CMB).

(Note:  two of the drive connectors on the WDC PCBA are situated side

by side; the right-hand connector  [J0] receives the "0" drive cable,

and the left-hand connector [Jl] receives the "1" drive cable.)

4.  Unplug the 4-pin power connector from J3 on the WDC PCBA.

5.  Unplug the ribbon cable (connecting the WDC PCBA to the WDC Bus Adapt-

er) from J4 on the WDC PCBA.

6.  Remove the WDC PCBA from the WDC Bus Adapter PCBA by releasing the

retainers on the (4) plastic standoffs at each corner of the WDC PCBA

and lifting the WDC PCBA upward.

5-17

BFISD 8079

To Install the replacement Winchester Drive Controller PCBA, proceed as follows:

7.  Verify that the jumpers listed below are not installed, for normal

operation.  See figure 5-5 for the location of the jumpers.

Jumper  A to B

Jumper  C to D

Jumper  E to F

Jumper  G to H

Jumper  0 to P

8.  Lower the WDC PCBA onto the WDC Bus Adapter PCBA so that the Winches-

ter Drive connectors (JO, Jl, J2, J3) are facing the front of the Base

Unit and the four standoffs enter the holes in the WDC PCBA.  Push

down on each corner of the WDC PCBA until the retainers on the stand-

offs hold it in place on the WDC Bus Adapter PCBA.

9.  Plug the ribbon cable coming from the WDC Bus Adapter into connector

J4 at the rear of the WDC PCBA.

10.  Plug the 4-pin power connector coming from the WDC Bus Adapter PCBA

into connector J3 at the front right-hand corner of the WDC PCBA.

11.  Plug the ribbon cable(s) coming from the Winchester drive(s) into the

WDC PCBA.  (Note:  the two narrower ribbon connectors on the WDC PCBA

are situated side by side; the right-hand connector [J0] receives the

"0" drive cable, and the left-hand connector [Jl] receives the "1"

drive cable.)

12.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into place.

13.  Plug in all connections to the Base Unit, including all previously

attached peripherals.

## 5.7  REPLACING THE MAGNETIC CARTRIDGE STREAMER CONTROLLER (MCSC) BOARD

To replace the Magnetic Cartridge Streamer Controller PCBA, proceed as follows:

CAUTION

Do not remove this board when power

is applied to the Base Unit.

1.  Shut down the system, and turn the Base Unit power OFF.

5-18

BFISD 8079

Figure 5-5.  Location of Jumpers on the Winchester Drive Controller PCBA

5-19

BFISD 8079

2.  Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover, and push in to disengage the

the plastic latch.  Repeat with the left-hand side,  and remove the

cover.

3.  Unplug the WDC Bus Adapter PCBA and the WDC PCBA (which carries the

WDC PCBA) as a single unit from the top of the "stack."  (This step

may not be necessary; refer to step 4.)

4.  Unplug from the stack any other controller PCBAs that might be present

(after first disconnecting their cables) until the Magnetic Cartridge

Streamer Controller (MCSC) PCBA is accessible.  Record the order of

board removal.  (When more than one device controller board is pre-

sent, the entire stack may be removed as a single unit, and the MCSC

PCBA then may be removed from the stack While  it is  outside  of the

Base Unit.)

To install the replacement MCSC PCBA,  complete the following steps.

5.  Set the appropriate switches on the MCSC PCBA for the correct bus arb-

itration number and mode according to the listing shown below.  See

figure 5-6 for the location of the switches.

SWITCH SW1

Bus Arbitration

-----------------------------------------------------

S1         S2        S3        S4        S5        S6        S7        S8

ON         ON        ON        ON        OFF       OFF       ON        ON

6.  Plug the Magnetic Cartridge Streamer Controller PCBA into the CMB (or

into the PCBA from which the original MCSC PCBA was  removed) at the

rear right-hand corner of the CMB.  Replace any other PCBAs that were

removed in steps 3 and 4 of this procedure, in the order recorded in

those steps .

7.  Plug the WDC Bus Adapter PCBA and the WDC PCBA (mounted above the com-

ponent side of the WDC Bus Adapter) into the PCBA at the top of the

stack.

8.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into place.

9.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

## 5.8  REPLACING THE WINCHESTER DRIVE CONTROLLER (WDC) BUS ADAPTER BOARD

To replace the Winchester Drive Controller Bus Adapter PCBA, proceed as

follows:

5-20

BFISD 8079

Figure  5-6. Location of Switch on Magnetic Cartridge Streamer Controller PCBA

5-21

BFISD 8079

CAUTION

Do not remove this board when power

is applied to the Base Unit.

1.   Shut down the system, and turn the Base Unit power OFF.

2.   Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover, and push in to disengage the

the plastic latch.  Repeat with the left-hand side, and remove the

cover.

3.  Unplug the WDC Bus Adapter PCBA and the WDC PCBA (which  carries the

WDC PCBA), as a single unit, from the CMB or from the top of the

"stack,"  if other device controller boards are present.

4.  Unplug the 4-pin power connector from J3 on the WDC PCBA.

5.  Unplug the ribbon cable (connecting the WDC PCBA to the WDC Bus Adap-

ter) from J4 on the WDC PCBA.

6.  Remove the WDC PCBA from the WDC Bus Adapter PCBA by releasing the re-

tainers on the (4) plastic standoffs at each corner of the WDC PCBA

and lifting the WDC PCBA upward.

To install the replacement Winchester Drive Controller  Bus Adapter PCBA, pro-

ceed as follows :

7.  Set the appropriate switches on the WDC Bus Adapter PCBA for the cor-

rect bus arbitration number according to the listing shown below. See

figure 5-5 for the location of the switches.

SWITCH SW1

Bus Arbitration

------------------------------------------------------

S1         S2         S3        S4        S5        S6         S7       S8

OFF        OFF        OFF       ON        ON        ON         DON'T CARE

8.  Lower the WDC PCBA onto the WDC Bus Adapter PCBA so that the Winches-

ter drive connectors (JO,Jl,J2,J3) are facing the front of the Base

Unit and the four standoffs enter the holes in the WDC PCBA.  Push

down on each corner of the WDC PCBA until the retainers on the stand-

offs hold it in place on the WDC Bus Adapter PCBA.

9.  Plug the ribbon cable coming the WDC Bus Adapter into connector J4 at

the rear of the WDC PCBA.

5-22

BFISD 8079

10.  Plug the 4-pin power connector coming from the WDC Bus Adapter into

J3 on the WDC PCBA.

11.  Plug the WDC Bus Adapter PCBA into the CMB (or into the PCBA from

which it was removed) at the rear right-hand corner of the CMB.

12.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into place.

13.  Plug in all connections to the Base Unit, including all  previously

attached peripherals.

## 5.9  REPLACING THE LOCAL AREA NETWORK (LAN) BOARD

To replace the Local Area Network PCBA, proceed as follows:

CAUTION

Do not remove this board when power

is applied to the Base Unit.

1.  Shut down the system, and turn the Base Unit power OFF.

2.  Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover , and push in to disengage the

the plastic latch.  Repeat with the left-hand side, and remove the

cover.

3.  Unplug the WDC Bus Adapter PCBA and the WDC PCBA (which carries the

WDC PCBA) as a single unit from the top of the "stack."  (This step

may not be necessary; refer to step 4.)

4.  Unplug from the stack any other controller PCBAs that might be present

(after first disconnecting their cables) until the Local Area  Network

Controller (LANC) PCBA is accessible.  Record the order of board re-

moval. (When more than one device controller board is present,  the

entire stack may be removed as a single unit, and the LANC PCBA then

may be removed from the stack while the stack is outside the Base

Unit.)

To install the replacement LANC PCBA,  proceed as follows:

5.  Set the LANC board station address.  The address uniquely identifies

this station to all other stations on the network.  To set it, first

locate and identify the address switch on the LANC board. It  will be

found next to the cable connector (J3), as shown in figure 5-7.

5-23

BFISD 8079

LAN CONTROLLER (LANC)

Figure 5-7. Location of Switches on Local Area Network  Controller PCBA

5-24

BFISD 8079

The address switch comprises eight smaller switches, and each switch

is set individually.  The "off" position of each switch represents

binary 1.

SWITCH SW1

Bias   Terminator                   Station Address               _

S1       S2       S3       S4       S5       S6       S7        S8

*        **       ↑        ↑        ↑        ↑        ↑         ↑

* represents the "bias."  Switch 1 is set to 1 (off) on only one IAN

controller board in a network; all other LAN controllers must have

this switch set to 0 (on).  A maximum of two LAN controller boards

per Base Unit is allowable, but one per Base Unit is the normal

configuration.

** represents the terminator setting.  Only two controllers, one at

each end of the network,  may have this switch on; all other con-

trollers must have the switch off.

↑ represents the binary coded station address bit positions.  Switch

S8 is the least significant bit, and switch S3 is the most signifi-

cant bit.  Each LAN controller board has one unique address:  the

first address is 000001, and the 63rd address is 111111 (i.e., all

switches turned off).  (Note: 000000 is illegal.)

Switch S1 is the Bias switch and normally is set to the on position;

however, for each part of a  network cable that connects two repeaters,

one  station must have this switch turned off  to bias the line.  Switch

S2 is on only at the ends of a network;  all other controllers must

have this switch off.

Switches S3 through S8 are set for the desired address; these  may be

treated as a 6-bit binary word, with switch no. 8 as the least signi-

ficant bit.  There are 64 possible combinations of settings.  With on

= 0 and off = 1, the switches may be set for any one of 63 addresses

(address 00 must not be used).

For example:

100101 = address  37

111111 (all switches off) = address 63.

Another set of switches also must be set for the bus arbitration

number and board address. These are set at the factory but should be

verified by the installer before continuing. See figure 5-7 for the

switch location.

5-25

BFISD 8079

SWITCH SW2

Bus Arbitration                _      Address  Decode

S1        S2       S3       S4       S5       S6        S7        S8

OFF       OFF      OFF      ON       ON       OFF       ON        OFF

OFF       OFF      OFF      ON       ON       ON        OFF       ON

Note:  The top line is for for a single board; a second board normally

is used only with diagnostics.

The Local Area Network Controller board is now ready to be installed.

6.  Plug the Local Area Network Controller PCBA into the CMB (or into the

PCBA from which the original LANC PCBA was removed) at the rear right-

hand corner of the CMB.  Replace any other PCBAs that were removed in

steps 3 and 4 of this procedure, in the order recorded in those steps.

7.  Plug the WDC Bus Adapter PCBA and the WDC PCBA (mounted above the com-

ponent side of the WDC Bus Adapter), if they are present, into the

board at the top of the stack.

8.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to "snap" into place.

9.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

## 5.10  REPLACING THE WINCHESTER DRIVE

To replace the Winchester Drive(s), proceed as follows:

1.  Shut down the system, and turn the Base Unit power OFF.

2.  Insert a  screwdriver, or similar device, into the slot at the bottom

right-hand  side of the Base Unit cover, and push in to disengage the

the plastic latch.  Repeat with the left-hand side, and remove the

cover.

3.  Remove the Memory Array PCBAs, located in the front right-hand corner

of the CMB, by simply lifting the "stack" of PCBAs away from the CMB,

unplugging the bottom memory array PCBA from the CMB.

4.  Remove the front facia by pulling up slightly on the plastic card

holder until the facia is disengaged from the card holder.

5.  Unplug the ribbon cable(s) going from the Winchester Drive(s) to the

Winchester Drive Controller (WDC) PCBA, located in the card cage at

the rear right-hand corner of the CMB.

5-26

BFISD 8079

(Note: two of the drive connectors on the WDC PCBA are situated side

by side; the right-hand connector [JO] receives the "0" drive cable,

and the left-hand connector [Jl] receives the "1" drive cable.)

6.  Using a screwdriver,  or similar tool, push back the two (2) plastic

latches at the bottom rear of the Winchester Drive chassis, while

lifting the back of the Drive to clear the latches.

7.  Unplug the 4-pin power plug, located at the bottom rear left-hand cor-

ner of the Drive chassis,  on the Master Electronis PCBA.

8.  Push the Drive slightly toward the rear of the CMB so that the flange

at the bottom front of the Drive clears the slot in the bottom panel

of the Base Unit.

9.  Lift the Winchester Drive chassis from the CMB.

To install the replacement Winchester Drive,  complete the following steps.

10.  Refer to Section VIII (20 MB drive) or Section IX (50 MB drive) in

this manual for jumper information and other data, if necessary.

11.  Lower the Winchester Drive chassis into position on the CMB.

12.  Pull the Drive slightly to the front of the CMB so that the flange at

the bottom of the Drive chassis enters the slot in the Base Unit front

panel.

13.  Connect the 4-pin power plug to the connector located at the bottom

left-hand corner of the Drive chassis, on the Master Electronics PCBA.

14.  Lower the back of the Drive chassis so that it pushes back the two (2)

plastic latches on the CMB at the bottom rear of the Drive.  The Drive

chassis will "snap" in place.

15.  Plug the ribbon cables from the Winchester Drive(s) into the WDC PCBA.

(Note: the two narrower ribbon connectors on the WDC PCBA are situ-

ated side by side;  the right-hand connector [J0] receives the "0"

drive cable, and the left-hand connector [Jl] receives the "1" drive

cable.)

16.  Replace the front facia by reversing the removal procedure in Step 4.

17.  Reinstall the Memory Array PCBAs into the card cage at the front

right-hand corner of the CMB by plugging the bottom PCBA into the CMB.

(The entire stack may be reinstalled as a unit.)

18.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to snap into place.

19.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

5-27

BFISD 8079

## 5.11  REPLACING THE FLOPPY DISK DRIVE

To replace the floppy disk drive(s), proceed as follows:

1.  Shut down the system, and turn the Base Unit power OFF.

2.  Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover, and push in to disengage the

the latch.  Repeat with the left-hand side, and remove the cover.

3.  Remove the Memory Array PCBAs, located in the front right-hand corner

of the CMB, by simply lifting the "stack" of PCBAs away from the CMB,

unplugging the bottom memory array PCBA from the CMB.

4.  Remove the front facia by pulling up slightly on the plastic card

holder until the facia is disengaged from the card holder.

5.  Unplug the 4-pin power connector at the rear of the drive chassis.

6.  Using  a screwdriver, or similar tool, push back the two (2) plastic

latches at the bottom rear of the floppy drive chassis, while lifting

the back of the drive to clear the latches.

7.  Push the drive slightly toward the rear of the CMB so that the flange

at the bottom front of the drive is out of the slot in the bottom pan-

el of the Base Unit.

8.  Unplug the ribbon cables from the CMB.  (Note: the two  floppy  drive

connectors on the CMB are situated side by side; the right-hand con-

nector receives the "0" drive cable, and the left-hand connector re-

ceives the "1" drive cable.)

9.  Lift the floppy disk drive chassis from the CMB.

To install the replacement floppy disk drive(s), complete the following steps.

10.  Refer to Section VII  in this manual for jumper information and other

data, if necessary.

11.  Lower the floppy disk drive chassis into position on the CMB.

12.  Plug the ribbon cable into the CMB.  (Note: the two connectors on the

CMB are situated side by side.  The right-hand connector receives the

"0" drive cable, and the left-hand connector receives the "1" cable.)

13.  Pull the drive slightly to the front of the CMB so that the flange at

the bottom of the drive chassis enters the slot in the Base Unit front

panel.

14.  Lower the back of the drive chassis so that it pushes back the two (2)

plastic latches on the CMB at the bottom rear of the drive.  The drive

chassis will "snap" in place.

5-28

BFISD 8079

15.  Connect the 4-wire power cable to the connector located at the top

right-hand corner of the floppy drive chassis.

16.  Replace the front facia by reversing the removal procedure.

17.  Reinstall the Memory Array PCBAs into the card cage at the front

right-hand corner of the CMB by plugging the bottom PCBA into the CMB.

(The entire stack may be reinstalled as a unit.)

18.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to snap into place.

19.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

5-29

BFISD 8079

SECTION VI

# ILLUSTRATED PARTS LIST

## 6.1  INTRODUCTION

This section provides parts list information for the assemblies/subassemblies

recommended for replacement at the field level.

NOTE

Refer to Engineering Change Notices and appropriate

documents for changes to the parts list and for

drawings not included.  All changes should be kept

with this manual.

## 6.2  INDEX OF ASSEMBLIES

The following is an index of the assemblies/subassemblies covered in this

section:

FIGURE/

TABLE                   TITLE                        PAGE

6-1           Central Microprocessor Board PCBA    6-2/3

6-2           Memory Array PCBA                    6-8/9

6-3           WDC Bus Adapter PCBA                 6-10/11

6-4           4-Way Controller PCBA                6-14/15

6-5           MTCS Controller PCBA                 6-18/19

6-6           LAN Controller PCBA                  6-22/23

6-7           Winchester Drive (Single-Board)

Controller PCBA                      6-26/27

6-8           Power Supply Input Module PCBA       6-28/29

6-9           Power Supply Output Module PCBA      6-32/33

6-10          Power Supply Control Module PCBA     6-35/36

6-1

BFISD 8079

Figure 6-1. CMB PCBA

6-2

BFISD 8079

Table 6-1.  CMB PCBA (MM531011) Parts List

REFERENCE

PART NUMBER                   DESCRIPTION                  DESIGNATION

903441-001   PCBA, CMB (MM531011)

903442-001   PCB, CMB

Diagram, Schematic

Capacitors

104001-002   Capac, Ceram Z5U 1000 pFD 5V 20%              C125

104001-016   Capac, Ceram Z5U 0.47 MFD 50V 20%             C52

104003-006   Capac, Ceram X7R 0.01 MFD 100V 10%            C124

104003-007   Capac, Ceram X7R 0.1 MFD 100V 10%             C115

104004-010   Capac, Ceram COG 39 pFD 5V 5%                 C120,127

104004-013   Capac, Ceram COG 82 pFD 5V 5%                 C113,121,126

104010-001   Capac, Ceram Z5U Axial 0.1 MFD 50V +80/-20%   C1-51,53-57,59-64,

66-75, 78-112, 114,

117,118,122,123

102000-012   Capac, Tant 33MFD 10V 20%                     C76,77

Connectors

300091-002   Conn, D Fml Rt Ang PC MT Metal Face 25-Pos    J9,10

300091-003   Conn, D Fml Rt Ang PC MT Metal Face 37-Pos    J13

300093-001   Conn, DIN Male 3x32 0.025Sq 64  Pos A&C        Jl,2,3

300032-002   Conn Hdr, 0.025Sq Dbl Row 100 6-Pos           JMPA.JMPB (2 REQD)

300032-003   Conn Hdr, 0.025Sq Dbl Row 100 4-Pos           JMPA (2 REQD) JMPB,

JMPF

300032-008   Conn Hdr, 0.025Sq Dbl Row 100 12-Pos          JMP E

300032-010   Conn Hdr, 0.025Sq Dbl Row 100 24-Pos          JMP G

300032-016   Conn Hdr, 0.025Sq Dbl Row 100 34-Pos          J4,5

325026-001   Conn Hdr, Sgl Row 1-Pos 100 Tail              TP1-11,JMPH

325026-002   Conn Hdr, Sgl Row 2-Pos 100 Tail              JMPH,K,L,M.N,R,S

325026-003   Conn Hdr, Sgl Row 3-Pos 100 Tail              JMPC,D,P,MOUNT ON S1

300017-006   Conn PCB, Dbl Readout 22/44                   J6

Diodes

130006-001   Diode, Switching 1N914B                       CR2,3,4,5,6

152001-001   LED, Green Diff Lens                          DS1

Inductors

135006-004   Inductor, 22.0uH                              L1

Integrated Circuits

101051       IC, Resis Ntwk 220/330 Ohm                    4A(R12)

101315       IC, 74S00 Quad 2-Input Pos NAND               6L,8X,9Y

101316       IC, 7406 Quad Buffer/Driver                   14J,14K

6-3

BFISD 8079

Table  6-1.   CMB PCBA Parts list (continued)

REFERENCE

PART  NUMBER                    DESCRIPTION                  DESIGNATION

Integrated Circuits

101612        IC, MC1489L Quad Line Receiver                1C,3C,ID,3D

101613        IC, MC1488L Quad Line Driver                  1B,3B

101615        IC, 74S08 Quad 2-Input Pos AND                7T,8Y

101624        IC, 74S20 Dual 4-Input NAND                   10N

101626        IC, SN74S37 Quad 2-Input Pos NAND Buffer      6V

101627        IC, SN74S38 Quad 2-Input Pos NAND Buffer      2G,8J,9K,7N

101629        IC, SN74S74 Dual D-Type F/F                   6K

101630        IC, 74S112 Dual J-K Edge Trig F/F             5G,5H,5J

101631        IC, 74S138 Decoder/DeMUX                      8M,8N,12X

101632        IC, SN74S151 Data Select/MUX                  8K

101633        IC, SN74S157 Quad 2-1 Linedata Select/MUX     3T

101637        IC, SN74S260 Dual 5-Input Pos NOR             11V

101642        IC, 74LS163 Binary Counter Sync               3G

101655        IC, 74S02 Pos NOR Totem-Pole                  9N

101656        IC, 74LS04 Hex Inverter                     7R,9R,4V,10V,13W

101657        IC, 74LS157 Quad 2-1 Line Data Select/MUX    11J,11R,11S,13T

101671        IC, 74S280 9-Bit Odd/Even Parity Gen          2V,3V

101672        IC, 74LS20 Pos NAND                           9W

101709        IC, 74LS00 Quad 2-Input NAND                  4E,13R,9T,4W

101710        IC, 74LS02 Quad 2-Input NOR                   10T,14W

101711        IC, 74LS08 Quad 2-Input AND                   9S,7W,13Z

101712        IC, 74LS10 Triple Input NAND                  8S

101714        IC, 74LS32 Quad 2-Input OR                    12J.9V.4M

101715        IC, 74S51 Dual 2-Wide 2-Input AND/OR Inv      6M.7Y

101718        IC, 74LS109 Dual J-K Pos-Edge Trig F/F        10R,7S,8V

101719        IC, 74LS138 3-8 Line Decoder/DeMUX     4K,10L,8R,12Y,9Z,11Z

101720        IC, 74LS151 8-1 Line Data Select/MUX          3J,10K,7V

101722        IC, 74LS175 Quad D-Type Edge Trig F/F         11T

101724        IC, 74LS195A 4-BitPar Access S/R              13S

101736        IC, NE555 Timer                               5B

101737        IC, 74S30 8-Input NAND                        10X

101740        IC, 74LS51 Dual 2-Wide 2-Input AND/OR Inv     10W,13X,9M

101741        IC, 74LS74 Dual D-Type Pos Edge Trig F/F      10J,14V,14X

101783        IC, 74LS112 Dual J-K Edge Trig F/F            8T,8Z

101786        IC, 74LS21 Dual 4-Input AND                   9X

155002-005    IC, Digital Delay Line Term - 100ns           5L(DL2)

161001        IC, 74S139 Dual 2-4 Line Decoder              4T

161003        IC, 74S161 4-Bit Binary Counter               6J,15T

161009        IC, 74S240 Octal Buffer 3-State TTL      1F,4H,1J,IN,1R,1S,

1T,1X,6X,10Y,4F,1Y

161013        IC, 74LS373 Octal D-Type Latch 3-State        13L

161015        IC, 74LS14 Hex Schmitt Trig Inv               2E

161017        IC, 26LS31 Quad Diff Line Driver              4D

161018        IC, 26LS32 Quad Diff Line Receiver            4C

161020        IC, 74LS161A 4-Bit Binary Counter             9J

161022        IC, 74S85 4-Bit Magnitude Comp                5X,5Y,5Z

161023        IC, 74LS273 Octal D-Type F/F                  13J,13K

161024        IC, 74S283 4-Bit Binary Full Adder            2X,2Y,2Z

161028        IC, 74LS393 Dual 4-Bit Binary Counter         3H,12K,11N,2T

6-4

BFISD 8079

Table 6-1.  CMB PCBA Parts List (continued)

REFERENCE

PART NUMBER                   DESCRIPTION                   DESIGNATION

Integrated Circuits

161039-001   IC, 74LS164 8-Bit Par Output Ser S/R           11W

161053-001   IC, 74LS38 Quad 2-Input Pos NAND Buffer        3F

161055-001   IC, 74LS221 Dual Monostable MVB                14Z

161061-001   IC, 74S299 8-Bit Univ. S/R                     7K

161064-001   IC, 74LS240 Octal Buffer/Line Driver,3-State   1K,1L,1M

161065-001   IC, 74LS374 Octal Register D-Type F/F          12L,3N,12N,3R,3S

161066-001   IC, 74LS245 Octal Bus Receiver                 2L,3L,13M

161068-001   IC, 74LS244 Octal Buffer/Line Driver           5A,11L,2M,3M,11M,

14M,4N,4R,4S,4B

161069-001   IC, 74LS259 Latch 8-Bit ADD                    10M

161074-001   IC, 74S244 Octal Buffer                        1E,1H,1Z,IV,1W

161077-001   IC, 74S373 Transparent Latch                   3K

161086-001   IC, 74LS139 Decoder/DeMUX                      12W

161108-001   IC, RAM Static 2Kx8 CMOS 200ns                 12S

161128-001   IC, 74LS260 Dual 5-Input NOR                   7J

161129-001   IC, 74S22 Dual 4-Input NAND OC                 6Y,6Z

161133-001   IC, 74LS148 8-3 Priority Encoder               3E

161141-001   IC, 74LS153 Dual 4-1 Select/MUX                2H,2J,9L,2W

161152-001   IC, 74LS629 VCO                                13Y

161155-001   IC, 74S40 Dual 4-Input NAND TP                 6W

162031-001   IC, Serial Communications Controller           2C

162032-001   IC, Floppy Disk Controller                     14R

162041-001   IC, 2210D 64x4 Nonvolatile Static RAM          4L

162042-001   IC, 68010 16-Bit Vrtl Mem MPU 8.0MHz           5S

162052-001   IC, 1691 Floppy Support Logic                  15R

163001-001   IC, 4024 MVB Dual Controller                   15V

165042-001   IC, 68230L8 Parallel Intfce/Timer              5D

165047-015   IC, PROM 2764-CMB Kernel Firmware 0            6S

165047-016   IC, PROM 2764-CMB Kernel Firmware 1            6N

Oscillators

150001-001   Osc, Xtal Clock 16 MHz                         Y3(5K)

150001-012   Osc, Xtal Clock 4.915 MHz                      Y2(4G)

150001-021   Osc, Xtal Clock 3.6864 MHz                     Y1(2K)

Potentiometers

118008-003   Poten, Multi-Turn 20K Ohm 0.5W 10%             R36

118008-004   Poten, Multi-Turn 50K Ohm 0.5W 10%             R37,43

Resistors

111000-019   Resis, Comp 47 Ohm 5%                          R32

111000-023   Resis, Comp 8.2K Ohm 5%                        R39,40

111000-029   Resis, Comp 330 Ohm 5%                         R19,20,45,48

6-5

BFISD 8079

Table 6-1.   CMB PCBA Parts List  (continued)

REFERENCE

PART NUMBER               DESCRIPTION                      DESIGNATION

Resistors

111000-031    Resis, Comp 1K Ohm 5%                         Rll,15,16,18,21,22,

111000-033    Resis, Comp 39K Ohm 5%                        R30

111000-052    Resis, Comp 470 Ohm 5%                        R46,47

111000-043    Resis, Comp 100 Ohm 5%                        R38

111000-044    Resis, Comp 120 Ohm 5%                        Rl,2,8,44

111000-048    Resis, Comp 220 Ohm 5%                        R50

111000-052    Resis, Comp 470 Ohm 5%                        R46,47

111000-060    Resis, Comp 4.7K Ohm 5%                       R52,53,54,57,58

111000-065    Resis, Comp 20K Ohm 5%                        R34

111000-069    Resis, Comp 47K Ohm 5%                        R29

111000-072    Resis, Comp 1M Ohm 5%                         R13,14

111000-077    Resis, Comp 12K Ohm 5%                        R35

111000-091    Resis, Comp 3.9K Ohm 5%                       R33,41

111000-109    Resis, Comp 13K Ohm 5%                        R55,56

116000-117    Resis, Metal Film 15K Ohm 0.125W 1%           R42

119000-001    Resis Ntwk, DIP 470 Ohm 16-Pin 15 Resis       R9(1G)

119000-003    Resis Ntwk, DIP IK Ohm 16-Pin 15 Resis        R10(2F),R23(10S)

119000-005    Resis Ntwk, DIP 10K Ohm 16-Pin 15 Resis       13N(R24)

119000-007    Resis Ntwk, DIP 220 Ohm 16-Pin 15 Resis       R26(14L)

119001-004    Resis Ntwk, DIP 10K Ohm 8-Pin 7 Resis         R17

119004-004    Resis Ntwk, DIP 1K Ohm 10-Pin 9 Resis         R3-7

Sockets

325005-003    Socket, IC DIP 4-Leaf Cont Gold 14-Pos (1C,3C,ID,3D,IB,3B)

325005-007    Socket, IC DIP 4-Leaf Cont Gold 28-Pos        (6N,6S,12S)

325005-010    Socket, IC DIP 4-Leaf Cont Gold 40-Pos        (2C,14R)

325005-013    Socket, IC DIP 4-Leaf Cont Gold 64-Pos        (5S)

325038-001    Socket, LSI DIP Low Profile 48-Pos            (5D)

Transistors

101306        Trans, 2N2222A NPN Silicon                    Q1,Q2

Miscellaneous

760006        Adhesive, Ethyl Cyanoacrylate

907420-002    Catch, CMB PCBA                               (J1.J2.J3)

907443-001    Cover Plate, CMB                              (J9,10,13)

325033-001    Jumper, 0.025Sq Gold P1                       JMPA,B,D,E,F,G,H,

K,L,M,N,HEADER MTD

ON S1

762022-003    Label, Tab,0.375x1.250 Yel

208000-001    Rivet, Blind 0.116DX, 188L Alum               (J9,10,13)

202000-010    Screw, Pan Hd Phillips                        (J1,J2,J3,)

100114        Screwlock, Fml 4-40 Thd D Type                (J9,10,13)

241008-008    Standoff, Alum 1/4" Hex 0.562L                (Jl,2,3)

6-6

BFISD 8079

THIS PAGE LEFT BLANK INTENTIONALLY

6-7

BFISD 8079

Figure 6-2.  Memory Array 256K PCBA

6-8

BFISD 8079

Table 6-2.  Memory Array 256K PCBA (MM531030) Parts List

REFERENCE

PART NUMBER                   DESCRIPTION                  DESIGNATION

903368-001   PCBA, Memory Array 256K (MM531030)

904693-001   PCB, Memory Array

Diagram, Schematic

Capacitors

104007-001   Capac, Ceram Z5U DIP 0.1 MFD 50V 20%          C3-C49

108016-003   Capac, Alum Elect 47 MFD 10V -20+50%          Cl,2

Connectors

300092-001   Conn, D Fml 3x32 Press-Fit,64-Pos A&C         Jl

Integrated Circuits

101315       IC, 74S00 Quad 2-Input Pos NAND               U4M

101627       IC, SN74S38 Quad 2-Input Pos NAND Buffer      U4N

101673       IC, 74S86 Quad 2-Input Exclusive NOR          U4P

161009       IC, 74S240 Octal Buffer 3-State TTL           U1L,U3L,U4L

161066-001   IC, 74LS245 Octal Bus Receiver                U1P,U3P

161074-001   IC, 74S244 Octal Buffer                       U1N,U3M

161129-001   IC, 74S22 Dual 4-Input NAND CC                L1M

162023-001   IC, 4164,64K Dynamic RAM,150ns                U1A-U1J,U2A-U2J,

U3A-U3J,U4A-U4J

Resistors

119000-003   Re sis Ntwk, DIP 1K Ohm 16-Pin 15 Resis       R5

313145-001   Resis Ntwk, DIP 33 Ohm                        Rl(l) ,R2(2K),

R3(3K),R4(4K)

Switches

331008-006   Switch, Rocker DIP 6-Pos                      S1

Miscellaneous

907420-001   Catch, I/C PCBA

907388-001   Ejector, Euro-DIN Conn Stack

214027-001   Fastener, Push-On 0.312 Dia Stud

310019-001   Housing/Guide, Conn DIN 3x32                  (Jl)

762022-002   Label, Tab 0.250x1.700 Yel

907389-001   Latch, Euro-DIN  Conn Stack

6-9

BFISD 8079

Figure 6-3.  WDC Bus Adapter PCBA

6-10

BFISD 8079

Table 6-3.  WDC Bus Adapter PCBA (MM531100) Parts List

REFERENCE

PART NUMBER                   DESCRIPTION                   DESIGNATION

903439-001   PCBA, WDC Bus Adapter (MM531100)

904854-001   PCB, WDC Bus Adapter

Diagram, Schematic

Capacitors

104007-001   Capac, Ceram Z5U DIP 0.1 MFD 50V 20%           C3-32

108016-004   Capac, Alum Elect 100 MFD 6V -20/+75%          Cl,2

Connectors

300092-001   Conn, D Fml 3X32 Press-Fit 64-Pos              Jl,2

300032-012   Conn Hdr, 0.025Sq Dbl Row 50-Pos               J3

Diodes

152001-001   LED, Green Diff Lens                           CR1

Integrated Circuits

101051       IC, Pesis Ntwk 220/330 Ohms                    5C

101315       IC, 74SOO Quad 2-Input Pos NAND                5L

101514       IC, 7438 Buffer Quad 2-Input NAND              5B

101615       IC, 74S08 Quad 2-Input Pos AND                 2L

101623       IC, 74S11 3-Input AND                          3G

101625       IC, 74S32 Quad 2-Input Pos NOR                 2K

101627       IC, SN74S38 Quad 2-Input Pos NAND Buffer       1A,2F

101628       IC, 74S64 4-2-3-2 Dual D-Type F/F              2C,2H,3D,5D

101630       IC, 74S112 Dual J-K Edge Trig F/F              3E,5F

101631       IC, 74S138 Decoder/DEMUX                       2J

101633       IC, SN74S157 Quad 2-1 Linedata Select/MUX      3B

101637       IC, SN74S260 Dual 5-Input Pos NOR              2E

101655       IC, 74S02 Pos NOR Totem-Pole                   2D,3C

101656       IC, 74LS04 Hex Inv                             5G

101709       IC, 74LSOO Quad 2-Input NAND                   5H,5J

101710       IC, 74LS02 Quad  2-Input NOR                   3K

101711       IC, 74LS08 Quad 2-Input AND                    3L,5K

101719       IC, 74LS138 3-8 Line Decoder/DeMUX             3H

101740       IC, 74LS51 Dual 2-Wide 2-Input AND/OR Inv      4C

101741       IC, 74LS74 Dual D-Type Pos Edge Trig F/F       1D

161009       IC, 74S240 Octal Buffer 3-State TTL            1F,1G

161015       IC, 74LS14 Hex Schmitt Trig Inv                4C

161023       IC, 74LS273 Octal D-Type F/F                   4J

161064-001   IC, 74LS240 Octal Buffer/Line Driver 3-State   1E,3J

161065-001   IC, 74LS374 Octal Register D-Type  F/F         3N,3P,4G,4H,4K,4M,4N

161068-001   IC, 74LS244 Octal Buffer/Line Driver           4L,4P

161074-001   IC, 74S244 Octal Buffer                        1H

161076-001   IC, 74S133 13-Input NAND                       2G

161111-001   IC, 74LS640 Octal Bus Receiver                 1K,1L,4D

161145-001   IC, 74LS697 Sync U/D Binary Counter            1J,1M,1N,1P,2P

6-11

BFISD 8079

Table 6-3.   WDC Bus  Adapter  PCBA Parts List  (continued)

REFERENCE

PART NUMBER                   DESCRIPTION                  DESIGNATION

Integrated Circuits

911006-008   IC, PAL WDC Controller/Host Sequencer         4E

911009-004   IC, PAL WDC Host/Controller Sequencer         4F

Resistors

111000-029   Resis, Comp 330 Ohm 5%                        R3

119001-002   Resis Ntwk, DIP 1K Ohm 8-Pin 7 Resis          Rl,2

Sockets

325005-011   Socket, IC DIP 4-Leaf Cont Gold 20-Pos       (4F,4E)

Switches

331005-002   Switch, SPST DIP 8-Pos                        SW1 (4B)

Miscellaneous

907634-001   Cable, Assy DC Pwr-WDC/Bus Adapter-WDC

907420-001   Catch, I/O PCBA                               (Jl,2)

907388-001   Ejector, Euro-DIN Conn Stack                  (Jl,2)

214027-001   Fastener, Push-On 0.312 Dia Stud              (Jl,2)

310019-001   Housing/Guide, Com DIN 3X32                   (Jl,2)

762022-003   Label, Tab 0.375 X 1.250 Yel

907389-001   Latch, Euro-DIN Conn Stack                    (Jl,2)

216021-001   Standoff,  Ins 0.50L Snap-In

6-12

BFISD 8079

THIS PAGE LEFT BLANK INTENTIONALLY

6-13

BFISD 8079

Figure 6-4.  4-Way Controller PCBA

6-14

BFISD 8079

Table 6-4.  4-Way Controller PCBA (JM531040 ) Parts List

REFERENCE

PART NUMBER                   DESCRIPTION                   DESIGNATION

903390-001   PCBA, 4-Way Controller (MM531040)

904741-001   PCB, 4-Way Controller

Diagram, Schematic

Capacitors

104007-001   Capac, Ceram 250 DIP 0.1 MFD 50V 20%            Cl-4

104008-004   Capac, Ceram X/R DIP 220 pFD 50V 5%             C9-54

101127       Capac, Tant Sleeved 47 MFD 20V 10%              C5,6

102000-012   Capac, Tant 33 MFD 10V 20%                      C(l-4)

Connectors

300091-001   Conn, D Fml Rt/Ang PC Mtg Metal 9-Pos           Pl-4

300092-001   Conn, DIN Fml 3X32 Press-Fit 64-Pos             J1.2

300032-002   Conn Hdr, 0.025Sq Dbl Row 6-Pos                 PGM1-4

300032-003   Conn Hdr, 0.025Sq Dbl Row 4-Pos                 PGM1-4

Diodes

152003-001   LED                                             DS1

Integrated Circuits

101315       IC, 74S00 Quad 2-Input Pos NAND                 4D

101541       IC, 74S04 Hex Inverter                          2H,4G,4K

101612       IC, MC1489L Quad Line Receiver                  2B,3B,3C,5B,6B

101613       IC, MC1488L Quad Line Driver                    4C,5C,6C

101615       IC, 74S08 Quad 2-Input Pos AND                  4F,4N,4P

101625       IC, 74S32 Quad 2-Input Pos-OR                   4L

101627       IC, SN74S38 Quad 2-Input Pos NAND Buffer        1F, 1G

101628       IC, 74S64 4-2-3-2-Input AND/OR Inv              1E

101629       IC, SN74S74 Dual D-Type F/F                     2D,2E

101630       IC, 74S112 Dual J-K Edge Trig F/F               2F,2G

101633       IC, SN74S157 Quad 2-1 LineData  Select/MUX      1C

101637       IC, SN74S260 Dual 5-Input Pos NOR               3R

101655       IC, 74S02 Pos NOR Totem-Pole                    2C,3E

101713       IC, 74LS30 8-Input NAND                         3J

101719       IC, 74LS138 3-8 Line Decoder/DeMUX              2R,3R,5N,5P

101740       IC, 74LS51 Dual 2-Wide  2-Input AND/OR Inv      3F

101741       IC, 74LS74 Dual D-Type Pos Edge Trig F/F        4H,4R,6R

101742       IC, 74LS85 4-Bit Magnitude Comparator           1C

101776       IC, 74LS11 Triple 3-Input Pos AND               4E

161009       IC, 74S240 Octal Buffer 3-State TTL             1H,1J,2J

161013       IC, 74LS373 Octal C-Type Latch 3-State          2K,3N

161023       IC, 74LS273 Octal C-Type F/F                    2M,2N,2P,3G

161049-001   IC, 74279 Quad Shift Reg Latch                  5R

161064-001   IC, 74LS240 Octal Buffer Line Driver, 3-State   1L,1M,1N,1P,1R

161065-001   IC, 74LS374 Octal Register D-Type F/F           2L,3K,3L,3M

161066-001   IC, 74LS245 Octal Bus Receiver                  5L

6-15

BFISD 8079

Table 6-4.   4-Way Controller PCBA Parts List (continued)

REFERENCE

PART NUMBER                   DESCRIPTION                  DESIGNATION

Integrated Circuits

161086-001    IC, 74LS139 Decoder/DeMUX                     5M

161108-001    IC, RAM Static 2Kx8 CMOS 200ns                5J

162002-002    IC, Z80A 8-Bit Micro-P                        6N

162031-001    IC, Serial Communications Controller          5F,6F

161111-001    IC, 74LS640 Octal Bus Receiver                1K

Resistors

111000-043    Resis, Comp 100 Ohm 5%                        R4,5

119000-003    Resis Ntwk, DIP IK Ohm 16-Pin 15 Resis        R1(4J)

119000-006    Resis Ntwk, DIP 3.9K Ohm 16-Pin 15 Resis      R2(4B),R3(1B)

Sockets

325005-003    Socket, IC DIP 4-Leaf Cont Gold 14-Pos        (2B,3B,3C,4C,5B,5C,

325005-007    Socket, IC DIP 4-Leaf Cont Gold 28-Pos        (5J,6J)

325005-010    Socket, IC DIP 4-Leaf Cont Gold 40-Pos        (5F,6F,6N)

Switches

331008-010    Switch, Rocker DIP 10-Pos                     S1(1A)

Miscellaneous

907388-001    Ejector, Euro-DIN Conn Stack

214027-001    Fastener, Push-On 0.312 Dia Stud

310019-001    Housing/Guide, Conn DIN 3X32                  (Jl,2)

000000-000    Interim Component-Pending Spec                6J

325033-001    Jumper, 0.025Sq Gold PI                       (PGM1-4)

762022-003    Label, Fab

907389-001    Latch, Euro-DIN Conn Stack

907420-001    Latch, I/O PCBA

907402-001    Plate, Conn 4-Way  Controller

208000-001    Rivet, Blind 0.116DxO.188L Alum               (Pl-4)

100114        Screwlock, Fml 4-40 Thd D-Type                (Pl-4)

6-16

BFISD 8079

THIS PAGE LEFT BLANK INTENTIONALLY

6-17

BFISD 8079

Figure 6-5.  MTCS Controller PCBA

6-18

BFISD 8079

Table 6-5.  MTCS Controller PCBA (MM531070) Parts List

REFERENCE

PART NUMBER                   DESCRIPTION                   DESIGNATION

903406-001   PCBA, MTCS Controller(MM531070)

904769-001   PCB, MTCS Controller

Diagram, Schematic

Capacitors

108016-004   Capac, Alum Elect 100 MFD 6V,-20/+75%           Cl,2

101144       Capac, Ceram 0.1 MFD 50V 20%                    C40

104004-018   Capac, Ceram COG 33 pFD 50V 5%                  C41

104007-001   Capac, Ceram Z5U DIP 0.1 MFD 50V 20%            C3-36,38,39,42-57,

C59-76

102000-007   Capac, Tant 2.2 MFD 35V 10%                     C37

Connectors

300091-004   Conn, D Fml Rt/Ang PC Mtg 50-Pos                J4

300092-001   Conn, DIN Fml 3x32 Press-Fit 64-Pos             J1,2

300032-012   Conn  Hdr, 0.025Sq Dbl Row 50-Pos               J3

Diodes

152001-001   LED, Green Diff Lens                           DS1

Integrated Circuits

101315       IC, 74S00 Quad 2-Input Pos NAND                 4B

101514       IC, 7438 Buffer Quad 2-Input NAND               1E,4J

101623       IC, 74S11 3-Input AND                           6D

101625       IC, 74S32 Quad 2-Input Pos OR                   6K

101627       IC, 74LS38 Quad 2-Input Pos NAND Buffer         1C

101628       IC, 74S64 4-2-3-2-Input AND/OR INV              2C

101629       IC, SN74S74 Dual D-Type F/F                     3B,5C

101630       IC, 74S112 Dual J-K Edge Trig F/F               4C,6C,1H

101637       IC, SN74S260 Dual 5-Input Pos NOR               3D

101655       IC, 74S02 Pos NOR Totem-Pole                    2B

101709       IC, 74LSOO Quad 2-Input NAND                    5H

101710       IC, 74LS02 Quad, 2-Input NOR                    5R

101711       IC, 74LS08 Quad 2-Input AND                     2E

101712       IC, 74LS10 Triple Input NAND                    5L

101714       IC, 74LS32 Quad 2-Input OR                      2D,5E,5K,1G,4D

101719       IC, 74LS38 3-8 Line Decoder/DeMUX               3H,4H

101740       IC, 74LS51 Dual 2-Wide W-IN-AND-OR-INV          5D

101741       IC, 74LS74 Dual D-Type Pos Edge-Trig F/F        6F,5H

101776       IC, 74LS11 Triple 3-Input Pos AND               5G

161009       IC, 74S240 Octal Buffer 3-State TTL             2H,1K,2N,1F

161010       IC, 74S241 Octal Non-Inv Buffer 3-State         2K

161023       IC, 74LS73 Octal D-Type F/F                     6J

161064-001   IC, 74LS40 Octal Buffer/Line Driver 3-State     5J

161065-001   IC, 74LS74 Octal Register D-Type F/F            1N,6P

161066-001   IC, 74LS45 Octal Bus XCVR                       5P

161068-001   IC, 74LS44 Octal Buffer/Line Driver             6H

6-19

BFISD 8079

Table 6-5.  MTCS Controller PCBA Parts List (continued)

REFERENCE

PART NUMBER                   DESCRIPTION                  DESIGNATION

Integrated Circuits

161076-001   IC, 74S133 13-Input NAND                      1D

161107-002   IC, RAM Static 2Kx8 100ns                     4E,4R

161111-001   IC, 74LS40 Octal Bus XCVR                     5N

161134-001   IC, 74LS34 Octal D-Reg Inv 3-State            1L,2L,1M,2M

161145-001   IC, 74LS97 Sync U/D Binary Counter            2J,1P,2P,1R,2R

162002-002   IC, Z80A 8-Bit Micro-P                        4K

162020-001   IC, 8253-5 Programmable Interval Timer        4M

162043-001   IC, 8x60 FIFO RAM Controller                  4G

165047-012   IC, PROM 8Kx8 2764 MTCS Control Firmware      4N

168001-001   IC, 74F157 Quad 2-Input MUX                   1B

168002-001   IC, 74F240 Octal Buffer/Line Driver 3-State   6L

168002-002   IC, 74F245 Octal Bidir XCVR 3-State           6N

168002-003   IC, 74F374 Octal D F/F 3-State                6R

911008-001   IC, PAL Tape Sequencer                        6G

911009-001   IC, PAL Controller/Host Sequencer             2F

911009-002   IC, PAL Host To Controller Sequencer          2G

911010-001   IC, PAL MTCS Controller                       1J

Resistors

111000-031   Resis, Comp IK Ohm 5%                         Rl,2,6,7,8,13

111000-034   Resis, Comp 82K Ohm 5%                        R4

111000-039   Resis, Comp 22 Ohm 5%                         R5

111000-047   Resis, Comp 200 Ohm 5%                        R9

112001-013   Resis, Comp 56 Ohm 0.5W 5%                    R3

101053       Resis Ntwk, DIP 220/330 Ohm 14-Pin            R11(6M)

119000-003   Resis Ntwk, DIP 1K Ohm 16-Pin 15 Resis        R10(3C)

119001-002   Resis Ntwk, DIP 1K Ohm 8-Pin 7 Resis          R12

Sockets

325005-001   Socket, IC DIP 4-Leaf Cont Gold 24-Pos        (4E.4M.4R)

325005-007   Socket, IC DIP 4-Leaf Cont Gold 28-Pos        (4N,4G)

325005-010   Socket, IC DIP 4-Leaf Cont Gold 40-Pos        (4K)

325005-011   Socket, IC DIP 4-Leaf Cont Gold 20-Pos        (1J,2F,2G,6G)

Switches/Transistors

331005-002   Switch, DIP SPST 8-Pos                        S1(1A)

141018-001   Transistor, 2N2907A PNP Silicon Switch        Q1

Miscellaneous

907420-001   Catch, I/O PCBA

907388-001   Ejector, Euro-DIN Conn Stack

214027-001   Fastener, Push-On 0.312 Dia Stud

310019-001   Housing/Guide, Conn DIN 3x32                  (J1,2)

762022-003   Label, Tab 0.375x1.250 Yel

907389-001   Latch, Euro-DIN Conn Stack

907498-001   Plate, Cover MTC8C

100114       Screwlock, Rnl 4-40xThd D Type

6-20

BFISD 8079

THIS PAGE LEFT BLANK INTENTIONALLY

6-21

BFISD 8079

Figure 6-6.  LAN Controller PCBA

6-22

BFISD 8079

Table 6-6.  IAN Controller PCBA  (MM531060) Parts List

REFERENCE

PART NUMBER                    DESCRIPTION                  DESIGNATION

903405-001   PCBA, LAN Controller (MM531060)

904773-001   PCB, IAN Controller

Diagram, Schematic

Capacitors

104003-008   Capac, Ceram X7R 220 pFD 100V 20%             C83

104007-001   Capac, Ceram Z5U DIP 0.1 MFD 50V 20%          C2-69,71-82,84-86

104009-002   Capac, Ceram COG DIP 47 pFD 50V 5%            C70

102000-010   Capac, Tant 100 MFD 6V 20%                    Cl

Connectors

300092-001   Conn, DIN Fml 3x32 Press-Fit 64-Pos           Jl,2

325026-001   Conn Hdr, Sgl Row 1-Pos 0.100 Tail            TP1-7

325026-002   Conn Hdr, Sgl Row 2-Pos 0.100 Tail            JMPA

325044-001   Conn Hdr, Sgl Row R/A LK 3-Pos                J3

Diodes

152001-001   LED, Green Diff Lens                          CR2

152001-002   LED, fed Diff Lens                            CR1

Integrated Circuits

101315       IC, 74S00 Quad 2-Input Pos NAND               2C

101541       IC, 74S04 Hex Inverter                        3D

101623       IC, 74S11 3-Input AND                         3C

101625       IC, 74S32 Quad 2-Input Pos OR                 5G,6G

101627       IC, SN74S38 Quad 2-Input Pos NAND Buffer      1E,1G

101628       IC, 74S64 4-2-3-2-Input AND/OR Inv            2G

101629       IC, SN74S74 Dual D-Type F/F                   1C,3G

101630       IC, 74S112 Dual J-K Edge Trig F/F             1B

101633       IC, SN74S157 Quad 2-1 Line Data Select/Mux    1F

101637       IC, SN74S260 Dual 5-Input Pos  NOR            2D

101655       IC, 74S02 Pos NOR Totem-Pole                  2B,3F

101656       IC, 74S04 Hex Inverter                        5B,5E

101672       IC, 74LS20 Pos NAND                           6C

101709       IC, 74LS00 Quad 2-Input NAND                  4D

101711       IC, 74LS08 Quad 2-Input AND                   4F,5H

101712       IC, 74LS10 Triple Input NAND                  4H

101715       IC, 74S51 Dual 2-Wide 2-Input  AND/OR Inv     2E

101719       IC, 74LS138 3-8 Line Decoder/DeMUX            5F,6F

101740       IC, 74LS51 Dual 2-Wide 2-Input AND/OR Inv     6B,6E

101741       IC, 74LS74 Dual D-Type Pos Edge Trig F/F      4C,5D,4E

101744       IC, 74LS174 Hex D-Type F/F                    2M

101783       IC, 74LS112 Dual J-K Edge Trig F/F            5C,4G,6M

161009       IC, 74S240 Octal Buffer 3-State TTL           1D,1K,1L,1M

161023       IC, 74LS273 Octal D-Type F/F                  2J

161064-001   IC, 74LS240 Octal Buffer Line OR 3-State      2K,2L,1N,3N,1P,3P,1R

6-23

BFISD 8079

Table  6-6.   LAN Controller  PCBA Parts  List  (continued)

REFERENCE

PART NUMBER                    EESCRIPTION                  EESIGNATION

Integrated Circuits

161065-001    IC, 74LS374 Octal Register D-Type F/F         2H,3H,3J,4K,3L,4L,

2P,2R

161068-001    IC, 74LS244 Octal Buffer/Line  Driver         1J,3K,6L,4M,4P

161074        IC, 74S244 Octal Buffer                       3M

161076-001    IC, 74S133 13-Input NAND                      4N

161085-001    IC, 7407 Hex Buffer/Driver                    6H

161137-001    IC, 74LS54 4-Wide AND/OR Inv                  6D

161138-001    IC, 74LS283 4-Bit Binary Full Adder           2N

161139-001    IC, 75174 Quad DIF Line Receiver              3B,IC75174

161140-001    IC, 75175 Quad DIF Line Driver                2A,IC75175

400548-001    IC  Set, Data Link Controller                 5K

400548-003    IC  Set, Microproceser                        5R

400548-002    IC  Set, Unbuffered Gate Array                5N

Oscillators

150001-002    Oscillator, Xtal Clock 20 MHz                 Yl

Resistors

111000-029    Resis, Comp 330 Ohm 5%                        R7,8

111000-031    Resis, Comp 1K Ohm 5%                         R3,4,5,6,9,13

111000-060    Resis, Comp 4.7K Ohm 5%                       Rl,2

119000-003    Resis Ntwk, DIP IK Ohm 16-Pin 15 Resis        R12(5A)

119000-004    Resis Ntwk, DIP 4.7K Ohm 16 Pin 15 Resis      R11(4B),R10(2F)

Sockets

325005-004    Socket, IC DIP 4-Leaf Cont Gold 16-Pos         (2A,3B)

325005-007    Socket, IC DIP 4-Leaf Cont Gold 28-Pos         (5K)

325005-010    Socket, IC DIP 4-Leaf Cont Gold 40-Pos         (5N,5R)

Switches

331005-002    Switch, DIP SPST 8-Pos                         SW1(4A) ,SW2(2E)

Miscellaneous

907420-001   Catch, 1/C PCBA

907388-001   Ejector, Euro-DIN Conn Stack

214027       Fastener, Push-On 0.312 Dia Stud

310019-001   Housing/Guide Conn DIN 3x32 ML                 (J1.2)

325033-001   Jumper, 0.025Sq Gold PL                        (JMPA)

762022-003   Label, Tab 0.375x1.250 Yel

907389-001   Latch, Euro-DIN Conn Stack

907531-001   Plate, Conn LAN Controller

208000-001   Rivet, Blind 0.116Dx0.188L Alum

213005-003   Washer, Shoulder Insulating #4x0.135

6-24

BFISD 8079

THIS PAGE LEFT BLANK INTENTIONALLY

6-25

BFISD 8079

Figure  6-7.   Winchester Drive (Single-Board) Controller PCBA

6-26

BFISD 8079

Table 6-7.  WDC Controller PCBA (MM531150) Parts List

ITEM  PART NUM      QTY-PER  UM  HREV PART  DESCRIPTION                          STAT  REMARKS

----  -----------  --------  --  ---- -----------------------------------------  ----  ---------------------

0001  9O4923-001      1.000  EA  A    PCB 5 1/4 DISK CONTROLLER                  REL   *

0003  762022-003      1.000  EA  C    LABEL TAB . 375X1. 250 YEL                 REL   *

O005  165007-001      1.000  EA  F    IC PROM 256 BIPOLAR                        REL   IN

0006  1650O7-OO4      1.000  EA  F    IC PROM 256 BIPOLAR                        REL   3K

0007  1650O7-O03      1.000  EA  F    IC PROM 256 BIPOLAR                        REL   8B

0009  161008-001      2.000  EA  A    IC 29O1 4-BIT PROCESSER SLICE -  STANDARD  REL   4F, 4H

0011  101514          2.000  EA  A    IC 7438 BUFFER QUAD 2 INPUT NAND           RES   IK,8N

0012  101700          1.000  EA  A    IC 74125 QUAD BUS BUF GATE M/3 STATE OUT   RES   8A

0013  161005          3.000  EA  A    IC 74273 OCTAL D-TYPE FLIP-FLOP            RES   IP, 2J, 2M

0015  161015          1.000  EA  A    IC 74LS14 HEX SCHMITT TRIGGER INVERTER     REL   2P

0016  101785          8.000  EA  A    IC 74LS193 4-BIT SYNC UP/DOWN COUNTER      RES   2B, 2C, 2D,2K, 2L, 3C,

3D, 3L

0018  101315          4.000  EA  A    IC 74S00 QUAD 2 INPUT POS NAND GATE        RES   2N, 6L, 6N, 7N

0019  101655          2.000  EA  A    IC 74S02 POS-NOR GATE TOTEM-POLE           RES   3N,7K

0020  101541          3.000  EA  A    IC 74S04 INVERTER HEX                      REL   3P, 6M,7H

0021  101615          3.000  EA  B    IC 74SO8 QUAD 2 INPUT POS AND GATE         RES   4P, 6C, 7L

0022  1O1543          2.000  EA  A    IC 74S10 GATE TRIPLE 3-INPUT NAND          RES   6K, 8J

0023  101624          1.000  EA  A    IC 74S20 DUAL 4-INPUT NAND GATE            REL   3E

0024  101625          4.000  EA  A    IC 74S32 QUAD 2 INPUT POSITIVE-OR GATE     RES   3M, 4N, 6B,7J

0025  101715          1.000  EA  A    IC 74S51 DUAL 2 WIDE 2 IN AND OR INVERT    RES   70

0026  101629          7.000  EA  C    IC SN74S74 DUAL D-TYPE FLIP/FLOP           REL   3A, 5K, 5M,5N, 6P,7P,€

0027  101673          1.000  EA  A    IC 74S86 QUAD 2-INPUT EXCLUSIVE OR GATE    REL   7B

0028  101631          3.000  EA  A    IC 74S138 DECODER/DEMULTIPLXR              RES   1A, 2A, 3B

0029  1610O1          1.000  EA  A    IC 74S139 DUAL 2 TO 4 LINE DECODER         RES   7F

0030  101633          4.000  EA  A    IC SN74S157 QUAD 2-1 LINEDATA SELECT/MUX   RES   IF,10,6A,7A

0031  101635          4.000  EA  A    IC 74S175 QUAD D-TYPE F/F                  REL   IE, 4L, 4M, 8H

0032  101777          1.000  EA  A    IC 74S182 (LOOK AHEAD CARRY GENERATOR)     RES   6H

0033  161OO9         11.000  EA  A    IC 74S240 OCTAL BUFFER THREE-STATE TTL     REL   1C, ID, 1J, 1L, 1M,2E,

8M,9C, 9D,9F, 90

0034  161010          1.000  EA  A    IC 74S241 OCTAL NON-INV BUFFER 3 STATE     RES   1H

0035  101726          3.000  EA  A    IC 74S251 DATA SELECT/MUX 3 STATE          RES   6D, 7D, 7E

0036  161007          9.000  EA  A    IC 74S253 DUAL-DATA SELECTOR 3 STATE       RES   3F, 3G,3H,3J,6E,6F,

60, 6J, 7C

0037  161O06         11.000  EA  A    IC 74S374 OCTAL D-TYPE FLIP-FLOP           RES   20, 2H, 5A,SB,5C,5D,

5E, 5J, 8C,8D,80

O041  119OOO-OO3      2.000  EA  F     RES NTWK DIP 16 PIN 15 RES 1. OK OHM      REL   Rl( 4K », R2( 8P )

O042  101051          3.000  EA  D     IC RES NTWK 220/330 OHMS                  REL   R3< 5P )• R4( 9B ), R5< 9H

0044  102000-012      7.000  EA  H     CAP SOLID TANTALUM 33UF 20% 1OV           REL   Cl-7

O045  104010-001    117.000  EA  B     CAP CERAMC Z5U AXIAL . 1UF +80 -20% 5OV   REL   C8-124

O046  104011-002      1.000  EA  A     CAP CERAMIC X7R  AXIAL 22OPF 20%  1OOV    REL   C125

0048  325003-061      1.000  EA  D     CONN HDR .025SQ PCB 50 POS RA W/LG LATCH  RES   P2

O049  325003-059      2.000  EA  D     CONN HDR .025SQ PCB 34 POS RA W/LG LATCH  RES   P3,4

OO50  325005-011      5.000  EA  F     SOCKET IC DIP FOUR-LEAF CONT GOLD 20 POS  REL   ( 4A, 4B, 4C,4D,4E )

0001  903460-001      1.000  EA  D     PCBA 5 1/4 DISK CONTROLLER

0002  165006-128      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-R 4A

0003  165006-129      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-R 4B

OOO4  165006-130      1.000  EA  AH    IC 4O96 BIT (512 X 8) BIPOLAR PROM-R 4C

0005  165006-131      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-R 4D

OO06  165006-132      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-R 4E

OO02  165006-133      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-M 4A

OO03  165006-134      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-M 4B

0004  165006-135      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-M 4C

0005  165006-136      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-M 4D

OO06  165006-137      1.000  EA  AH    IC 4096 BIT (512 X 8) BIPOLAR PROM-M 4E

6-27

BFISD 8079

Figure 6-8.  Power Supply Input Module PCBA

6-28

BFISD 8079

Table 6-8.  Power Supply Input Module (MM533000) Parts List

ITEM  PART NUM      QTY-PER  UM  HREV PART  DESCRIPTION                          REMARKS

----  -----------  --------  --  ---- -----------------------------------------  ---------------------

0001  904761-001      1.000  EA  X1   PCB INPUT MCOLLE  P/S                      *

0002  762022-003      l.000  EA  B    LABEL TAB .375X1.250 YEL                   *

0001  123004-003      2.000  EA  E    THERMISTOR INRUSH PROTECT 15 AMP .03 OHM   R1,2

0004  000000-000      1.000  RF  X1   INTERIM COMPUNENT-PENDING SPEC             VR1

BFISD P/N 199C19-001

0003  113001-018      2.000  EA  D    RES CARBUN COMP ?? 5% 39K UHM              R3,4

0008  107006-002      1.000  EA  B    CAP METAL FILM .047UF 10% 250 VAC          C14

0009  000000-000      2.000  RF  X1   INTERIM COMPONENT-PENDING SPEC             C12,13 CAPACITOR .04

7 BFIS P/N 104007-00

3

0010  107006-OOi      3.000  EA  B    CAP METAL FILM .47UF 10% 250 VAC           C4,5,6

0011  108019-002      1.000  EA  B    CAP FILM POLYFRCP 2.0UF +-10% 200VDC       C11

0012  105000-003      1.000  EA  C    CAP ALUM ELECT 390UF  +100 - 10% 40V       C1

0013  000000-000      4.000  RF  X1   INTERIM COMPONENT-PENDING SPEC             C7,8,9,10 CAP 470 MF

BFIS P/N 108023-001

0016  130006-001      4.000  EA  A    DIODE SWITCHING 1N9148                     D10,11,12,13

0017  130016-001      2.000  EA  C    DIODE RECTIFIER 1 AMP-1N4936               D8,9

0018  130000-002      2.000  EA  C    DIODE RECT 1A 100V 1N4002                  D5,6

0019  130009-004      2.000  EA  A    DIODE RECTIFIER HIGH CURRENT               D1,3

0021  1520C3-001      1.000  EA  B    LED                                        D7

0023  141021-001      2.000  EA  A    TRANSISTOR  NPN  2N66IS 1QA  43U%          Q1,2

0027  180054-001      1.000  EA  A    TRANSFORMER E*I BALbN                      T2

0028  180053-001      2.000  EA  A    TRANSFORMER BASE  CRWE                     T3,4

0029  180055-001      1.000  EA  A    TRANSFORMER PC*£R 36V                      T1

0030  135036-001      2.000  EA  A    INDUCTOR 40.2LH                            L1,2

0031  137001-001      1.000  EA  C    FUSE GLASS  TUBE FST BLUM 6A 250V          F1

0033  338009-001      1.000  EA  A    FUSEHOLDER 3AG PC MOUNT                    (F1)

0034  330006-001      1.000  EA  A    SWITCH ROCKER DPST SNAP-IN PNL PT 10 AMP   S1

0035  907485-001      1.000  EA  X3   BRACKET PCB/SWITCH MOUNTING                *

0036  315062-001      1.000  EA  A    KECPT AC PwH PALE CEE 6A 230V PC BKC MT    Jl

0037  325042-001      1.000  EA  A    CONN HOR &GL POfe  «i5&CIS .045SU  8 PG^   42

0038  325043-001      1.000  EA  A    CONN FML Sui PUM  .100CTS HOK11 PT 10 HJS  J3

0039  000000-000      1.000  RF  X1   INTERIM COMPONENT-PENOING  SPEC            J4

BF1SU P/N  J2502lh-OJl

0041  235023-001      4.000  EA  A    HEATS1NK TO-J SCLCERABLE                   IQi»2)

004b  214019-003      2.000  EA  A    NUT KEP 6-J2                               Ul t21

0047  202015-003      2.000  EA  C    SCREW ??? 4-4CX.31                         1Jll

0048  214019-001      2.000  EA  A    NUT KEP 4-40                               IJU

0049  222001-001      2.000  EA  D    AD INS SEMICCNO 10-03

0050  784007-037      0.700  FT  B    WIRE INS 300V BOG ULl061 18AWG             *

0051  186000-020      0.200  FT  B    WIRE SOLID HOCK-UP

904761-001      1.000  EA  X1   PCB INPUT MODULE P/S

0002  762022-003      1.000  EA  B    LABEL TAB .375X1.250 YEL

0003  125004-003      2.000  EA  E    THERMISTOR INRUSH PROTECT IS AMP .03 CHM   R1,2

0004  000000-000      2.000  RF  X1   INTERIM CUMPOfcEfcT-PENOlNG  SPEC          VR1t2

BFISD P/N  l*9U9-COi

113001-018      2.000  EA  D    RES CARBCN  CO^P I*  54 J9K  OHM           HJ»4

0008  107006-002      1.000  EA  B    CAP METAL FIL*  .04/UF 104  450 VIC        C14

0009  000000-000      2.000  RF  X1   INTERIM COMPONENT-PENDING SPEC             114*13 CAPACUUft  .04

7 BF1S P/N I0404I-O.C

3

0010  107006-003      3.000  EA  B    CAP METAL FILM  .47UF 10% 250  VAC         C495t6

0011  106019-002      1.000  EA  B    CAP FIL* POLVFRCP 2.0UF +-10% 200VAC       Cll

105000-003      1.000  EA  C    CAP ALU* ELECT  390UF  «100  -101 40%      Cl

0013  000000-000      4.000  RF  X1   INTERIM COMPONENT-PENDING SPEC             C7,8,9,10 CAP 470 MF

BFIS P/N 108023-001

0016  130006-001      4.000  EA  A    DIODE SWITCHING 1N9148                     010tlltl2tlJ

0017  130016-001      2.000  EA  C    OIOOE RECTIFIER 1 AMP-1N4936               Oit9

0018  130000-002      2.000  EA  C    DIODE RECT 1A 100V  1N4002                 D5»6

0019  130009-004      4.000  EA  A    DIODE RECTIFIER HIGH CURRENT               01tJt3t4

0021  152003-001      1.000  EA  B    LED                                        01

6-29

BFISD 8079

Table  6-8. Power Supply Input Module PCBA Parts List (continued)

ITEM  PART NUM      QTY-PER  UM   HREV  PART  DESCRIPTION                          REMARKS

----  -----------  --------  --   ----  -----------------------------------------  ---------------------

0023  141021-001      2.000  EA   A     TRANSISTOR NPN 2N6675 10A 450V             Uit2

0027  180054-001      1.000  EA   A     TRANSFORMER E?I BALUN                      12

0028  180053-001      2.000  EA   A     TRANSFORMER BASE DRIVE                     13,4

0029  180055-001      1.000  EA   A     TRANSFORMER PCMEK J6V                      II

0030  135036-001      2.000  EA   A     INDUCTOR 40.2UH                            1.1

0032  137001-000      1*000  EA   C     FUSE GLASS TUBE FST BLU? 3A 250V           Fl

0033  338009-001      1.000  EA   A     FUSEHOLDER 3A PC MOUNT                     IF11

0034  3300C6-001      1.000  EA   A     SWITCH ROCKER DPST SNAP-IN PNL PT 10 AMP   S1

0035  907485-001      1.000  EA   X3    BRACKET PCB/SWITCH MOUNTING                *

0036  315062-001      1.000  EA   A     RECPT AC PWR MALE CEE 6A 250V PC BRO MT    Jl

0037  325042-001      1.000  EA   A     CONN HDR SGL RUW .I56CTS .045SM B POS      J2

0038  325043-001      1.000  EA   A     CONN FML SGL ROW .100CTS HU??? PT 10 POS   J3

0039  000000-000      1.000  RF   X1    INTERIM COMPONENT-PENDING SPEC             J4

BFISD P/N 325026-0

0041  235023-001      2.000  EA   A     HEATSINK TO-3 SOLDERABLE                   (????)

0046  214019-003      2.0DO  EA   A     NUT KEP 6-32

0047  202015-003      2.000  EA   C     SCREQ HWH 4-4OX.31                         (J1)

0046  214019-001      2.000  EA   A     NUT KEP 4-40                               (J1)

0049  22200i-00i      2.000  EA   D     PAD INS SEMICCND TO-03                     *

0050  784007-037      0.700  FT   B     WIRE INS 300V 80C UL1061 18AWG WHITE       *

0051  786000-020      0.200  FT   B     WIRE SOLID HOCK-UP                         *

6-30

BFISD 8079

THIS PAGE LEFT BLANK INTENTIONALLY

6-31

BFISD 8079

Figure 6-9.  Power Supply Output Module PCBA

6-32

BFISD 8079

Table 6-9. Power Supply Output Module PCBA (MM533000) Parts List

ITEM  PART NUM      QTY-PER  UM  HREV  PART DESCRIPTION                           STAT  REMARKS

----  ----------    -------  --  ----  -----------------------------------------  ----  ----------------------

0001  904859-001      1.000  EA  A     PCB POWER SUPPLY OUTPUT MODULE             REL    *

0002  762022-003      1.000  EA  C     LABEL TAB . 375X1. 250  YEL                REL    *

0003  116000-229      3.000  EA  P     RES METAL FILM . 125W IX 11.0 OHM          REL    R11,60,61

0004  116OOO-230      1.000  EA  P     RES METAL FILM . 125W IX 22. 6 OHM         REL    R8

0005  116000-231      1.000  EA  P     RES METAL FILM . 125W IX 1. 18K OHM        REL    R7

0006  116000-201      1.000  EA  P     RES METAL FILM . 125W IX 2  8OK OHM        REL    R6

0007  116000-126      1.000  EA  P     RES METAL FILM . 125W IX 3. 74K OHM        REL    R16

0008  116000-031     12.000  EA  P     RES METAL FILM . 125W IX 4  99K OHM        REL    R15,17,18,20,22,23

26,32,35,42,29,47

0009  116000-233      1.000  EA  P     RES METAL FILM . 125W 1% 6. O4K OHM        REL    R9

0010  116000-117      1.000  EA  P     RES METAL FILM . 125W 1% 15 OK OHM         REL    R39

0011  116000-228      1.000  EA  P     RES METAL FILM . 125W 1% 16. 9K OHM        REL    R14

0012  116000-177      4.000  EA  P     RES METAL FILM . 125M 1% 20. OK OHM        REL    R27,37,38,45

0013  116000-108      1.000  EA  P     RES METAL FILM . 125W 1% 23. 2K OHM        REL    R19

0014  101918          1.000  EA  P     RES METAL FILM . 125W 1% 29. 4K OHM        REL    R40

0019  116000-215      2.000  EA  P     RES METAL FILM . 125W 1% 40 2K OHM         REL    R34,46

0016  116000-235      1.000  EA        RES METAL FILM . 125M 1% 46. 4K OHM        REL    R21

OO17  101915          1.000  EA        RES METAL FILM . 125W 1% 10OK OHM          REL    R43

OO18  116OOO-232      1.000  EA        RES METAL FILM . 125W 1% 4. 32K OHM        REL    Rl

OO19  116OOO-234      1.000  EA        RES METAL FILM . 125W 1% 15. 8K OHM        REL    R59

OO20  116000-156      1.000  EA        RES METAL FILM . 125W 1% 1  65K OHM        REL    R28

O022  1O1917          1.000  EA        RES METAL FILM . 125W 1% 10. OK OHM        REL    R30

OO24  116OOO-2O5      1.000  5   P     RES METAL FILM . 125W 1% 4. 87K OHM        INA    R44

OO28  116000-107      1.000  EA  P     RES METAL FILM . 125W 1% 22 6K OHM         REL    R33

O"^   1110OO-031      3.000  EA  L     RES CARBON FILM . 25W  SX IK OHM           REL    R52, 53. 54

C     1110OO-032      1.000  EA  L     RES CARBON FILM . 25W  5X 2. OK OHM        REL    R50

OO_.  111OOO-085      1.000  EA  L     RES CARBON FILM . 25W  5X 2. 7K OHM        REL    R24

0032  111OOO-091      2.000  EA  L     RES CARBON FILM . 25W  5X 3. 9K OHM        REL    R4, 10

0033  111000-060      5.000  EA  L     RES CARBON FILM . 25W  5X 4. 7K OHM        REL    R12,31,36,48,62

0034  111OOO-OO9      1.000  EA  L     RES CARBON FILM . 25W  5X 1. 5K OHM        REL    R41

0035  111OOO-065      2.000  EA  L     RES CARBON FILM . 25W  5X 2OK OHM          REL    R2,13

0036  111000-095      1.000  EA  L     RES CARBON FILM . 25W  5X 51 OHM           REL    R58

O038  113OOO-OO1      1.000  EA  E     RES CARBON COMP 1W SX 10 OHM               REL    R51

0040  115006-011      2.000  EA  D     RES PWR WW 3W 0.04 OHM IX                  REL    R56. 57

OO41  115OO9-OO6      1.000  EA  B     RES PWR WW 1OW 1OO OHMS 5X                 REL    R3

OO42  1130OO-109      1.000  EA  E     RES CARBON COMP 1W 5X 8.2  OHM             REL    R5

O043  115003-005      1.000  EA  B     RES PWR WW 5W 33 OHM  10X                  REL    R49

OO45  118OO5-011      1.000  EA  B     POT RD CERMET LOW SINGLE  TURN 5OO OHM     REL    R25

0051  104OO8-OO7      2.000  EA  B     CAP CERAMIC  X7R DIP 33OPF  5X 50V         REL    C26. 31

OO52  1O4OO8-OO8      1.000  EA  B     CAP CERAMIC  X7R DIP 1OOOPF 5X 50V         REL    C27

O053  104008-003      2.000  EA  B     CAP CERAMIC  X7R DIP .  022UF SX 50V       REL    C1.6

O054  104011-006      1.000  EA  A     CAP CERAMIC  X7R AXIAL 8, 20OPF 5X 50V     REL    C2

0055  104008-005      1.000  EA  B     CAP CERAMIC  X7R DIP   01UF  5X 50V        PEL    C21

OO56  104011-011      1.000  EA  A     CAP CERAMIC  X7R AXIAL . O33UF 5X 5OV      REL    C22

0057  104008-009      1.000  EA  B     CAP CERAMIC  X7R DIP 330OPF 5X 5OV         REL    C23

O059  104009-002      1.000  EA  B     CAP CERAMIC  COG DIP 47PF 5X 5OV           REL    C25

6-33

BFISD 8079

Table 6-9. Power Supply Output Module PCBA Parts List (continued)

ITEM  PART NUM      QTY-PER  UM  HREV  PART DESCRIPTION                           STAT  REMARKS

----  -----------  --------  --  ----  -----------------------------------------  ----  ------------------------

0063  104010-002     10.000  EA  B     CAP CERAMC Z5U AXIAL .01UF 20% 100V        REL   C5,14,15,16,17,18,

,42,50,51

0066  1O4010-OO1     12.000  EA  B     CAP CERAMC Z5U AXIAL .1UF +80 -20% 50V     REL   C8,9, 13, 20,28,29,3

39, 40, 44, 45, 49

0067  102OOO-006      2.000  EA  H     CAP SOLID TANTALUM  1 OUF 20% 35V          REL   C52,53

0070  107OO1-OO3      1.000  EA  A     CAP FILM POLYPROPLENE .O1UF 5% 400VDC      REL   C32

0071  103000-003      1.000  EA  0     CAP MICA DIPPED RADIAL 3OOOPF 5% 500V      REL   C3

0072  108000-OO8      1.000  EA  E     CAP FILM POLYESTER .022UF 10% 6OOV         REL   C4

0073  104OO3-OO2      2.000  EA  H     CAP CERAMIC X7R .1UF 10% 50V               REL   C24,41

0074  108022-OO5      2.000  EA  D     CAP ALUM ELECT MINI 1OOUF +-20% 35V        REL   C35, 36

0075  108024-OO1      2.000  EA  A     CAP ALUM ELECT ESR/LIFE 330UF +100% 16V    REL   C47,48

0076  1O8O20-OO2      2.000  EA  D     CAP ALUM ELECT LOW ESR PCB 56OUF 40V       REL   C33,34

0077  108020-003      3.000  EA  D     CAP ALUM ELECT LOW ESR PCB 4,700UF 7.5V    REL   C10,11,12

0080  130006-001     11.000  EA  A     DIODE SWITCHING 1N914B                     REL   CR1,2,3,4,7,8,10,1

12,24,25

0081  13O016-OO1      4.000  EA  C     DIODE RECTIFIER 1 AMP-1N4936               REL   CR9,19,20,22

0082  13OO08-001      2.000  EA  A     DIODE PWR SCHOTTKY SD51 120A 45 PIV        REL   CR5,6

0083  130O25-O02      1.000  EA  B     DIODE DUAL 16A T0220 150V                  REL   CR15

0084  130001-001      2.000  EA  D     DIODE FST RECOVERY MR852                   REL   CR16,17

0085  13OO26-OO1      1.000  EA  A     DIODE SCHOTTKY 10A T0220 45V               REL   CR21

0086  101304          1.000  EA  0     DIODE ZENER 1N5242B                        REL   CR23

0087  131OO2-033      1.000  EA  C     DIODE ZENER 1N4747A                        REL   CR18

0088  131001-007      1.000  EA  0     DIODE ZENER 500MW 1N5233B                  REL   CR13

O090  101323          1.000  EA  AX1   TRANS TIP 121                              RES   Ql

0091  142003-001      1.000  EA  A     TRANS N-CHANNEL MOSFET 27A 60V             REL   Q2

0094  101799          4.000  EA  B     IC LM339 QUAD COMPARATOR                   REL   U1,2,3,5

0095  164OO9-001      1.000  EA  A     IC LM358 DUAL LOW POWER OP AMP             REL   U4

0096  162049-001      1.000  EA  A     IC 4011 CMOS QUAD 2-INPUT NAND             REL   U6

0097  141020-001      1.000  EA  A     TRANSISTOR QUAD 3725 NPN                   REL   U9

0098  101697          1.000  EA  B     IC MC7812CT  3 TERM POS VOLT REG           REL   U10

0099  132006-002      1.000  EA  A     REG NEG VOLTAGE 1.5A -5.2V 7905            REL   U7

0100  132006-006      1.000  EA  A     REG NEG VOLTAGE 1.5A -12.5V 7912           REL   U8

0109  180056-001      1.000  EA  E     TRANSFORMER OUTPUT                         RES   T2

0110  18OO57-O01      1.000  EA  A     TRANSFORMER CURRENT SENSE                  REL   Tl

0111  180058-001      1.000  EA  B     TRANSFORMER CURRENT SENSE                  REL   T3

0112  135037-002      1.000  EA  C     INDUCTOR 19UH 50A                          RES   L1

0113  135040-001      2.000  EA  B     INDUCTOR 0.22UH                            REL   L2. 5

0114  135038-001      1.000  EA  B     INDUCTOR 90UH 10A                          PRF   L4

0115  135039-OO1      1.000  EA  C     INDUCTOR 180UH COUPLED                     REL   L3

0118  325014-OO2      1.000  EA  A     CONN HDR RT ANG .045SQ .156CTS 3  POS      REL   Jl

0119  325043-002      1.000  EA  A     CONN FML SOL ROW .100CTS HORIZ MT 20 POS   REL   J2

0120  325043-001      1 000  EA  A     CONN FML SOL ROW .100CTS HORIZ MT 10 POS   REL   J3

0121  300096-001      1.000  EA  A     CONN FML HDR 156 CTS RT/ANG PC MT 8 POS    RES   J4

0123  907594-001      1.000  EA  A     HEATSINK 1 OUTPUT MODULE PCBA              REL   *

0125  907479-001      1.000  EA  C     CABLE ASSY P/S DRIVE  1&2                  REL   PA1&PA2

0127  784OO7-037      9.000  FT  C     WIRE INS 300V 8OC UL1061 18AWG  WHITE      REL   *

6-34

BFISD 8079

Figure 6-10. Power Supply Control Module PCBA

6-35

BFISD 8079

Table  6-10. Power Supply Control Module PCBA (MM533000) Parts List

ITEM  PART NUM      QTY-PER  UM  HREV  PART DESCRIPTION                           REMARKS

----  -----------   -------  --  ----  -----------------------------------------  ----------------------

0001  904765-001      1.000  EA  B     PCB CONTROL MODULE P/S                     *

0003  762022-003      1.000  EA  C     LABEL TAB .375X1.250 YEL                   *

0004  325026-037      1.000  EA  AX3   CONN HDR SOL ROW .100 10 POS .275 LG       J2

0005  325026-038      1.000  EA  AX3   CONN HDR SOL ROW .100 20 POS .275 LG       Jl

0006  116000-156      1.000  EA  N     RES METAL FILM .125W 1% 1.65K OHM          R4

0007  116000-166      1.000  EA  N     RES METAL FILM .125W 1% 2.49K OHM          R33

0008  116000-226      1.000  EA  N     RES METAL FILM .125W 1% 5.49K OHM          R2

0009  116000-195      5.000  EA  N     RES METAL FILM .125W 1% 11.0K OHM          R9, 34,36,38*40

0010  116000-228      1.000  EA  N     RES METAL FILM .125W 1% 16.9K OHM          R8

0011  116OOO-127      1.000  EA  N     RES METAL FILM .125W 1% 24.3K OHM          R39

0012  116000-227      1.000  EA  N     RES METAL FILM .125W 1% 105K OHM           R41

0013  116000-225      1.000  EA  N     RES METAL FILM .125W 1% 121K OHM           R15

0014  116000-236      1.000  EA  N     RES METAL FILM .125W 1% 787K OHM           R14

0017  111000-001      2.000  EA  J     RES CARBON FILM .25W 5% 10 OHM             R26,32

0018  111000-040      1.000  EA  J     RES CARBON FILM .25W 5% 30 OHM             R3

0019  1110OO-055      4.000  EA  J     RES CARBON FILM .25W 5% 680 OHM            R22, 25,28,31

0020  111000-032      3.000  EA  J     RES CARBON FILM .25W 5% 2.0K OHM           R21,27,43

0021  111000-006      2.000  EA  J     RES CARBON FILM .25W 5% 15K OHM            RIO,37

0022  1110OO-065      8.000  EA  J     RES CARBON FILM .25W 5% 2OK OHM            R7, 11, 12, 17, 18, 19

20, 42

0023  111000-071      2.000  EA  J     RES CARBON FILM .25W 5% 100K OHM           R6, 13

0024  111000-123      1.000  EA  J     RES CARBON FILM .25W 5% 300K OHM           R5

0025  111000-072      1.000  EA  J     RES CARBON FILM .25W 5% 1M OHM             R16

0026  111000-O99      1.000  EA  J     RES CARBON FILM .25W 5% 10M OHM            Rl

0027  111000-047      2.000  EA  J     RES CARBON FILM .25W 5% 200 OHM            R44,45

0030  1180O8-002      1.000  EA  AX1   POT SQ MULTI TURN . 5W 5K OHM 10%          R35

0031  104008-001      3.000  EA  B     CAP CERAMIC X7R DIP 1500PF 5X 50V          C3,4,20

0032  104008-005      1.000  EA  B     CAP CERAMIC X7R DIP .01UF 5% 50V           C17

0033  104010-002      5.000  EA  A     CAP CERAMC Z5U AXIAL .01UF 20% 100V        Cl, 11, 13, 16,2

0034  104008-003      1.000  EA  B     CAP CERAMIC X7R DIP .022UF 5% 50V          CIO

0035  104010-001      9.000  EA  A     CAP CERAMC Z5U AXIAL .1UF +80 -20% 50V     C5,6,7,8,9,14,18,19

22

0036  102004-001      2.000  EA  B     CAP TANT 1UF 10% 35V                       C12, 15

0037  104008-012      1.000  EA  B     CAP CERAMIC X7R DIP 820PF 5% 50V           C21

0038  906895-001      1.000  EA  B     CUSHION RETAINER .25X.75                   *

0040  130006-001     12.000  EA  A     DIODE SWITCHING 1N914B                     Dl,3,4,6,7,8,9,10,

12,13,14, 15

0041  131002-028      2.000  EA  C     DIODE ZENER 1N4733A                        D2,5

0042  141018-001      1.000  EA  A     TRANSISTOR PNP SILICON SWITCH 2N2907A      Ql

0043  141020-001      2.000  EA  A     TRANSISTOR QUAD 3725 NPN                   U7,8

0044  101799          3.000  EA  B     IC LM339 QUAD COMPARATOR                   Ul,3,4

0045  132003-001      1.000  EA  B     IC 3524 VOLTAGE REG                        U9

0046  164010-001      1.000  EA  A     IC,VOLTAGE REFERENCE 2.5 VOLTS             U2

6-36

BFISD 8079

SECTION VII

# 5.25"  FLOPPY DISK DRIVE

## 7.1  INTRODUCTION

This section provides maintenance personnel with information necessary to in-
stall, operate and maintain the 5.25" Floppy Disk Drive.

Section VII is arranged in three subsections.  The scope of each subsection is described as follows:

7.1  INTRODUCTION - contains general information, physical and electrical

descriptions and equipment specifications.

7.2  INSTALLATION AND MAINTENANCE - contains information to enable mainte-

nance personnel to install and repair the Floppy Disk Drive.  Elec-

trical and mechanical adjustments are included.

7.3  REFERENCE INFORMATION - Contains description of input and output

lines, system timing diagram,  schematics and jumper connections.

### 7.1.1  General Description

The 5.25" Floppy Disk Drive is a removeable-media, magnetic, rotating, data storage device.  Its purpose is to allow the Model 4108 Base Unit to store and retrieve blocks of data  (records) onto and from a rotating disk, thus provid-
ing secondary storage for the MAI®  2000 Series  Computer System.  The Drive functions as an input/output device in the Base Unit.  Access to data is pro-
vided by one moving head per disk surface.  Data is recorded on the disk sur-
faces using modified frequency modulation (MFM) techniques.

The Drive incorporates an open-loop,  stepper motor positioning system.  The major mechanical components of the Drive are illustrated in figure 7-1 through figure 7-3 and are explained in the following paragraphs.

7.1.1.1  Spindle Mechanism

The Spindle Mechanism comprises the Spindle, a Center Cone, a Main Arm and a Clamp Lever (see figure  7-1).  Inserting a mini-floppy disk and pressing the button for loading the disk causes the Clamp Lever to lower the Main Arm and the Center Cone to enter the hole of the disk.  The Center Cone catches the inside diameter of the disk and sets it to the correct position.  To eject the disk, pressing the button (again) causes the Main Arm to be raised (by a spring), the Center Cone to be raised, and the disk to be released from the Spindle and ejected.  The DC Motor drives the Spindle at 300 rpm, fixed speed.

7.1.1.2  Positioning Mechanism

The Positioning Mechanism comprises the Stepper Motor, the Carriage Assembly, a Guide Bar, a Pulley, and a Steel Belt (see figure 7-2).  The rotation of the

7-1

BFISD 8079

Figure 7-1.  Spindle Mechanism

Stepper Motor is converted into rectilinear motion,  by the Pulley/Steel Belt assembly (connected directly to the Stepper Motor axle),  to drive the Carriage Assembly.  The Carriage Assembly consists of the Carriage, the Side 0 R/W Head, and the Side 1 R/W Head.  The Stepper Motor rotates 3.6 degrees per step.

7.1.1.3  Head Load/Interlock Mechanism

The Head Load/Interlock Mechanism consists of a Solenoid,  the Head Load arm, the Stabilizer Pad,  the Head Load Arm Bracket, the Interlock Arm, and a Latch and Latch Spring (see figure 7-3).  When the Solenoid is actuated by the HEAD LOAD signal, the Head Load Arm is pulled down, and the Stabilizer Pad presses the disk to prevent the disk from vibrating.  Also, the Side 1 R/W Head is pressed against the disk.  Moreover, since the Interlock Arm presses the Latch Spring, the Latch does not move, and the disk cannot be ejected. When the HEAD LOAD signal is turned off, the Stabilizer Pad and the Side 1 R/W Head move from the disk, thus lowering the Interlock Arm and moving the Latch.  In this state, the disk can be ejected.

### 7.1.2  Functional Concepts

The simplified block diagram in figure 7-4 shows the functional concepts of the Floppy Disk Drive.  The Drive uses LSls for the major circuits, thus reducing the number of circuit parts to 25 percent of the amount used in conventional products.  This increases the reliability of the Drive and miniaturizes the PCB space, thereby realizing a very thin unit.  These LSIs are of custom analog-
hybrid and digital-hybrid designs, each of which accommodates the following circuit functions.

7-2

BFISD 8079

Figure 7-3.  Head Load/Interlock Mechanism

7-3

BFISD 8079

Analog System         DC Control Circuit

Erase Amplifier Circuit

Read Amplifier Circuit

Write Circuit

Digital System        Stepper Motor Control Circuit

Index Ready Circuit

Write Protect Circuit

Head Load Solenoid Control Circuit

Brief explanations of the major circuits are presented in the following par-
agraphs.

Figure 7-4.  Functional Block Diagram

7-4

BFISD 8079

7.1.2.1  Stepper Motor Control

The Stepper Motor is a 4-phase DC motor.  The circuit in ICl controls the motor (see figure 7-5 for a block diagram of the Stepper Motor Control Circuit). The STEP signal rotates the motor 3.6 degrees (48 TPI) or 1.8 degrees (96 TPI).

The rotation of the Stepper Motor is converted to linear motion of the Read/ Write Heads by the Pulley/Steel Belt assembly.  The DIRECTION-IN signal cont-
rols the movement of the heads toward the inner tracks with a logic low level and toward the out tracks (toward track 00) with a logic high level.  Figure 
7-6 and figure 7-7 show the Stepper Motor timing.  Figure 7-8 is a Stepper Motor phase transfer chart.

Figure 7-7.  Stepper Motor Timing Diagram (96 TPI)

7-5

BFISD 8079

Figure 7-8.  Stepper Motor Phase Transfer Chart

7.1.2.2  Drive Motor Control

The Drive Motor is a brushless DC motor and is controlled by the PCBA of the Drive Motor itself.  The Drive Motor is started and stopped by the MOTOR-ON signal (Jl, pin 16).  The Drive Motor reaches the optimum speed in 800 ms after the Motor has started.  The speed is adjusted to 300 rpm (disk rotation speed) by the potentiometer located  on the Drive Motor PCBA.

7.1.2.3  Head Load Circuit

The Head Load mechanism is operated by the Solenoid.  When transister Tl is turned on by a 36 ms one shot MV in 1C1, current is supplied to the Solenoid to actuate it.  There are two methods to load the heads.  One method,  named SH (Select Head Load), is that the Head Load  Solenoid is drawn when the Drive has been selected and the Head Load signal goes to logic low.  Another method, named AH (Automatic Head Load), is that  the Head Load Solenoid is drawn when the Drive is selected,  irrespective of the Head Load signal condition.  Figure 7-9 is a simplified schematic of the Head Load Circuit,  and figure 7-10 is the Head Load timing diagram.

7.1.2.4  Motion Check LED

The motion of the Drive is indicated with green and red LEDs (light emitting diodes).  The green LED lit indicates that a disk is inserted in the Drive and the control is in the ready condition.  In this state, the disk can be ejected from the Drive.  The red LED lit indicates that a disk is inserted in the Drive and the Read/Write Heads have been loaded.  In this state the disk cannot be ejected.

7.1.2.5  Track 00 Detection

The TRACK 00 signal is provided for correcting the track position of the heads when their position is unknown. Moving the heads to Track 00 causes the TRACK 00 signal to go to logic level low.  The Track 00 detector consists of a photo switch comparator and peripheral circuit.  The Track 00 Switch is closed by the

7-6

BFISD 8079

Figure 7-10.  Head Load Timing Diagram

Head Carriage cutting off the light to the photo switch.  The TRACK 00 signal is output when the output level of the Track 00 photo switch is the same as the

output level of phase A and phase C of the Stepper Motor.  Figure 7-11 is a simplified  schematic of the Track 00 detection circuit, and figure 7-12 and figure 7-13 are Track 00 timing diagrams.

7.1.2.6  Write Protect Detector

The Write Protect Detector consists of an LED and a photo transistor.  For write protect,  the disk write protection notch is covered by an opaque cover.

Inserting a disk with the covered notch causes the photo transistor output to go to logic level low, because the light from the LED does not reach the photo transistor.  In this case, if the Select signal goes to logic level high, the WRITE PROTECT signal goes to logic level low.  Thus, the Central Microprocessor Board is notified of the write protect status.  Figure 7-14 is a simplified schematic of the Write Protect Detector circuit.

7.1.2.7  Index Detector

The Index Detector consists of an LED, a photo transistor, and a comparator, similar to the Write Protect Detector.  When the index hole is positioned bet-
ween the LED and the photo transistor, the LED light reaches the photo transis-

7-7

BFISD 8079

7-8

BFISD 8079

Figure 7-15.  Index Detection Circuit

tor, and a negative pulse of 2.5 ms to 5 ms is generated in the comparator out-
put.  This pulse enters the counter and, as a 4 ms  pulse, is conveyed to the Central Microprocessor Board as a negative pulse when the SELECT signal is ac-
tive.  Figure 7-15 is a simplified schematic of the Index Detection circuit.

7.1.2.8  Ready Detector

The Ready Detector is provided for monitoring the disk speed by the index pulse and is built into IC1.  When the index pulse time interval is over 300 ms, the IC1 READY output (pin 61) is at logic level high (inactive).  When it is below 300 ms, the READY output goes to logic level low (inactive).  Figure 7-16 shows the Ready Detector timing.

7-9

BFISD 8079

Figure 7-18. Write Start Timing Diagram

7.1.2.9  Read/Write Heads

The Read/Write Head is a tunnel erase ceramic head.  The head consists of the read/write coils and the erase coil.  The erase coil is excited in the write mode, and a noise prevention area is formed at both sides of a track recorded by the read/write coil.  The read/write coils are rolled on the core chip and center tapped.  At the write operation time, each bit of write data is alter-
nately distributed to each coil by the D flip-flop.  Writing data over the old data causes the old data to be replaced by the new data.  At the read time the output voltage is induced when the Read/Write Head gap passes over the magnet-
ized track.  Figure 7-17 is a Read/Write Head connection diagram.

7-10

BFISD 8079

7.1.2.10  Write Circuit

The Write Circuit converts the serial data passed from the Central Microproces-
sor Board into the magnetic pattern on the disk.  Figure 7-18 shows the write start timing (96 TPI).  Loading the heads and making the WRITE GATE signal log-
ic level low causes the Drive to enter the writable status.  Sending data from the Central Microprocessor Board in this state causes the write flip-flop to alternately turn on.  Hence, the write current is supplied to the two halves of the read/write coils alternately.

The alternating magnetic field corresponding to the data from the Central Mic-
roprocessor Board is stored on the disk.  When the erase enable signal is at logic level low, the erase amplifier turns on, and current is supplied to the erase coil.  The erase enable signal goes to logic level low after the WRITE GATE signal has gone to logic level low and a fixed delay time has elapsed.

Figure 7-19 is a simplified write circuit block diagram, figure  7-20 is the

Figure 7-20.  Write Timing Diagram (FM)

7-11

BFISD 8079

Figure 7-22. Erase Delay Timing Diagram

write timing diagram, figure 7-21 shows the erase delay circuit (simplified), and figure 7-22 is the erase delay timing diagram.

7.1.2.11  Read Circuit

Data stored on the floppy disk are recovered by the Read Circuit.  Loading the heads and making the WRITE GATE signal a logic level high causes the Drive to enter the readable status.  The Read Circuit consists of an IC floppy amplifier and associated circuitry.  Figure 7-23 a simplified block diagram of the Read Circuit, and figure 7-24 is the Read Timing Diagram.

7.1.2.12  Read/Write Select Circuit

The Read/Write Select Circuit consists of a diode switch.  The input side of the switch is connected to the coil of the Read/Write Head, and the output side

7-12

BFISD 8079

Note:  It is 26 msec in the 48 T.P.I. Model.

Figure 7-24.  Read Start Timing Diagram

of the switch is connected to the Read Amplifier Circuit.  When the Drive is in the write mode, the WRITE ENABLE signal is at logic level low, and the diodes are turned off.  When the Drive is in the read mode, the WRITE ENABLE signal is at logic level high, diodes D9 and Dl0 are turned on, and the Read/Write Head is connected to the Read Amplifier.  Figure 7-25 is a simplifed block diagram of the Read/Write Select Circuit.

7.1.2.13  Read Amplifier Circuit and Filter Network

The read data signal is amplified by the preamplifier and the Floppy Amplifier.

The amplified read data signal is delivered through the Filter Network (low pass) to the Active Differential Circuit.  Figure 3-26 is a simplified schem-
atic of the Read Amplifier Circuit and Filter Network.

7.1.2.14  Active Differential Circuit and Comparator

The Active Differential Circuit and Comparator are part of the Floppy Ampli-
fier.  The Active Differential Circuit is a differential amplifier whose emit-

7-13

BFISD 8079

ters are coupled through an RLC network.  The RLC network differentiates the input signal voltage so that the amplifier output is a differentiated version of the input signal.  The output of the differential amplifier is input to the Comparator.  The Comparator detects the zero-crossover point of the signal, thereby detecting the peak of the Active Differential Circuit input signal voltage.  Figure 7-27 is a simplified schematic.

7.1.2.15  Timed Main Filter and Crossover Detector

The Timed Main Filter and Crossover Detector are part of the IC Floppy Ampli-
fier. The Timed Main Filter removes any erroneous crossovers from the Comp-

7-14

BFISD 8079

arator caused by shouldering of the differentiated read data signal.  When a high resolution head is used,  shouldering sometimes occurs in the outer cir-
cumference of the Drive.  The Timed Main Filter consists of a pulse generator, a timed one-shot MV, and a timed main flip-flop.  The pulse generator outputs a short pulse to trigger the timed main one-shot at every input transfer.  The timed main one-shot pulse width is determined by the external resistance and

7-15

BFISD 8079

capacitor value.  The data passed from the Comparator is delayed by 2.2 microseconds by the timed main one-shot and loaded on the timed main flop-flop.

Even if the timed one-shot is clocked by an erroneous crossover, the timed main flip-flop output does not change, because the erroneous crossover time is shorter than 2.2 microseconds.  The Crossover Detector is triggered with every timed main flip-flop transfer.  The pulse width of the Crossover Detector is set at 450 nanoseconds.

7-16

BFISD 8079

Figure 7-28 is a block diagram of the Timed Main Filter and Crossover Detector; figure 7-29 is the read timing diagram.

7.1.2.16  DC Control Circuit

The DC Control Circuit is used to monitor the 5VDC and 12VCD Power Supplies.

When either supply voltage deviates from the limits listed below,  the write current and erase current are turned off.  Figure 7-30 is a simplified sche-
matic of the DC Control Circuit.

5  volts +4.0  volts        12  volts +8.3 volts

7.1.2.17  Power-On Reset Circuit

When the power is turned on to the Base Unit,  capacitor C (figure7-31) begins charging to 3 volts.  When the capacitor voltage is lower than the buffer threshold voltage,  the Power-On Reset signal goes to logic level low, and the initial reset pulse is generated.  Figure 7-31 is a simplified block diagram of the Power-On Reset Circuit,  and figure 7-32 is the Power-On reset timing dia-
gram.

Figure 7-32.  Power-On Reset Timing Diagram

7.1.3  Equipment Specifications

Performance characteristics  for the Floppy Disk Drive are listed in table 7-1, on the following page.

7-17

BFISD 8079

Table 7-1.   Specifications

PARAMETERS                                CHARACTERISTICS

Storage Capacity

Per Diskette                               1 MB

Per Track                                  6.25 KB

Data Transfer Rate

(bits per second)                            250 K

Average Latency Time                         100 ms

Track-to-Track

Positioning Time                             3 ms

Average Access Time                          100 ms

Head Loading Time                            25 ms

Head Settling Time                           20 ms

Motor Start Time                             800 ms

Innermost Circumference

Recording Density                            5922 BPI

Number of Tracks                             160 (both sides)

Track Density                                96 TPI

Track Radius

Outer Circumference                        57.15 mm

Inner Circumference                        34.13 mm

Modulation System                            BM or MFM

Ambient Operating

Temperature                                  5°C to 45°C

Ambient Temperature

in Transportation                            -40°C to 62°C

Non-Operating

Temperature                                  -22°C to 55°C

Relative Humidity                            20% to 80% RH

Maximum Wet Bulb                             29°C

7-18

BFISD 8079

Table 7-1.  Specifications (continued)

PARAMETERS                                CHARACTERISTICS

Error Rates

The following error rates

are valid only when the

drive is being used accord-

ing to specifications.

Media defects or equipment

failures are excluded.

Written data should be veri-

fied as being correctly

written.  All media defects

should be flagged.

Seek errors                                 1 in 1,000,000 seeks

Recoverable read errors                     1 in 1,000,000,000 bits

Nonrecoverable read errors                  1 in 1,000,000,000,000 bits

Resistance Against Vibration

in Operation

Acceleration                                1G

Vibration Sweep                             5 to 100 Hz

Vibration Direction                         X,Y,Z directions

Resistance Against Vibration

in Transportation

Acceleration                                3G

Vibration Sweep                             5 to 100 Hz

Vibration Direction                         X,Y,Z directions

Resistance Against Impulse                    Will satisfy all  specifica-

in Transportation                             tions after being dropped

from height of 100 cm  in

packed  condition

Dimensions

Width                                       150.0 mm

Height                                      33.5 mm

Depth                                       221.5 mm

Weight                                      1.2 kg

7-19

BFISD 8079

7.2  INSTALLATION AND MAINTENANCE

This subsection contains unpacking, installation and maintenance information for the Floppy Disk Drive.

7. 2.1  Unpacking

Prior to unpacking the Drive,  inspect the packaged Drive to determine Aether any damage was incurred during shipment.

1.  Using shipping documents, verify that all items have been received.

2.  Open the protective shipping carton at the top.

3.  Remove the Drive from the shipping carton.

4.  Remove the plastic cover.

5.  Inspect each package article to determine whether any damage was in-

curred during shipment.

6.  Verify that connectors, indicators and protruding parts have not been

damaged.

7.  Check the ID nameplate against the shipping papers to verify that the

drive part number and serial number are correct.

8.  When practical,  store shipping containers for reuse.

9.  Record any damage, and report damage to the applicable carrier.

7.2.2  Equipment Placement

Equipment placement consists of mounting the Drive in the Base Unit and routing the input/output cables.

7.2.3  Electrical Installation

Electrical installation of the Floppy Disk Drive system consists of routing the Drive interface (ribbon) cable to the Central Microprocessor Board (CMB), in the Base Unit, and connecting it,  and routing the 4-wire power cable to the Base Unit Power Supply and connecting it.  Detailed installation procedures are included in Section II of this manual.

7.2.4  Adjustment Procedures

Alignment and adjustment instructions for the Floppy Disk Drive are presented in the following paragraphs and are listed below.

1.  Index burst position adjustment

2.  Track position adjustment

7-20

BFISD 8079

3.  Track 00 position adjustment

4.  Rotation adjustment

5.  0-1 head gap adjustment

7.2.4.1  Index Burst Position Adjustment

a.  Load the alignment diskette, and step it to track 34.

b.  Set an an oscilloscope as follows:

Channel 1                200 mV AC

Channel 2                200 mV AC  (inverted)

Mode                     ADD

Time Base                50 microseconds

Trigger                  EXTERNAL, NORMAL, NEGATIVE

c.  Connect the Channel 1 test probe to the Drive test point labeled CHK1;

connect the Channel 2 test probe to the Drive test point labeled CHK2;

connect the Trigger input to pin 49 of IC1,  on the Main PCBA.

d.  Check that the start of the index burst is observed 200 microseconds

from the beginning of the sweep, as shown below.  Adjust side 0 first,

then side 1.  If necessary, adjust the phototransistor holder assem-

bly.  For both sides, time T should  be 200+80 microseconds.

7.2.4.2  Track Position Adjustment

a.  Loosen the Stepper Motor mounting nuts (A, B in illustration below).

b.  Insert the alignment diskette, and step it to track 16.

c.  Set an an oscilloscope as follows:

Channel 1                200 mV AC

Channel 2                200 mV AC (inverted)

7-21

BFISD 8079

Mode                     ADD

Time Base                20 milliseconds

Trigger                  EXTERNAL, NORMAL, NEGATIVE

d. Connect the Channel 1 test probe to the Drive test point labeled CHK1;

connect the Channel 2 test probe to the Drive test point labeled CHK2;

connect the Trigger input to pin 49 of IC1, on the Main PCBA.

e.  Select sides 0 and 1 alternately and monitor the waveforms on both

sides while moving the Stepper Motor to put the amplitude ratios

(small waveform divided by large waveform) within the range prescribed

by the label on the alignment diskette.

f.  Step the heads from track 15 to 16 and from track 17 to 16  to check

that the amplitudes remain within the range prescribed by the label on

the alignment diskette.

7.2.4.3  Track 00 Position Adjustment

a.  Load a normal diskette into the Drive.

b.  Set an an oscilloscope as follows:

7-22

BFISD 8079

Channel 1                5V DC

Channel 2                2V DC (inverted)

Mode                     ADD

Time Base                5 milliseconds

Trigger                  INTERNAL (CH. 2), NORMAL, NEGATIVE

c.  Connect the Channel 1 test probe to pin 54 of IC1, on the Main PCBA;

connect the Channel 2 test probe to the Drive test point labeled CHK3.

d.  Step the head between track 00 and 06 alternately.

e.  Check the switching as follows (see the waveform below):

Track 01 in the direction from track 00 to track 06

Track 00 in the direction from track 06 to track 00

If necessary, loosen the screw mounting the track 00 switch PCBA

and adjust.

7.2.4.4  Rotation Adjustment

a.  After running the heads for 10 minutes, load a normal diskette.

b.  Connect a frequency counter to the INDEX terminal of the exerciser.

c.  Adjust VRl of the Drive Motor PCBA so that the period of the index is

200+1 ms in tracks 00 and 39.

7.2.4.5  0-1 Head Gap Adjustment

a.  Adjust the position of the Head Load Arm so that the gap between side

0 and side 1 becomes 0.6+0.2 mm when the Arm is clamped without the

diskette in the Drive.

b.  Mount the Head Load Arm so that it is parallel to the Arm portion of

the Main Arm.

7-23

BFISD 8079

## 7.3  REFERENCE INFORMATION

This subsection provides schematics and other reference data for the Floppy Disk Drive.

### 7.3.1  Interface

The Floppy Disk Drive interface consists of two sections:

1.   Signal

2.   Power Supply

Each line is detailed below.

7.3.1.1   Signal Interface

The daisy chain or radial chain is used for the signal interface of the Select line, allowing connection to a maximum of four Drives.  In the case of the daisy chain, only the last Drive is terminated.  A resistance array close to connector J2 is provided for this termination.  (The resistance array is remov-able.)

The alignment of the interface connector and of the power connector is shown below.

SIGNAL CONNECTOR

Ground   Signal   Signal Name      Ground   Signal   Signal Name

Return   Pin                       Return   Pin

1       2        ----             19      20      Step

3       4      Head Load          21      22      Write Data

5       6      Select 4           23      24      Write Gate

7       8      Index              25      26      Track 00

9       10     Select 1           27      28      Write Protect

11      12     Select 2           29      30      Read  Data

13      14     Select 3           31      32      Side  Select

15      16     Motor-On           33      34      Ready

17      18     Direction-In

7-24

BFISD 8079

POWER  SUPPLY CONNECTOR

Pin No.      Power Name

1          +12VDC

2          +12V GND

3          +5V GND

4          +5VDC

The signal interface lines are illustrated in figure 7-33,  on the next page.

7.3.1.2  Input Lines

SELECT 1-4 - A maximum of four Drives can be connected in the daisy chain mode.  A jumper is used to switch each Drive.  (All Drives are set to select 1 at the factory.)  Select lines 1-4 are used to select the ranked Drive.  Only the selected Drive can send and receive signals.

MOTOR-ON - This signal is a Spindle Motor ON/OFF signal;  the motor is turned ON at logic level 0.

DIRECTION-IN - The function of this signal is to determine the direction of the read/write heads and must be set at least 1 microsecond earlier than the STEP pulse leading edge.  The direction of the head carriage by the DIRECTION-IN signal is handled as follows:

Logic level 1           Away from the center of the disk

Logic level 0           Toward the center of the disk

STEP - Sending the logic level 0 pulse to this line causes the read/write heads to move in the direction determined by the DIRECTION-IN signal.  In usual cases, this step speed is 3 ms/track.  When the WRITE GATE signal is at logic level 0, the STEP signal is inhibited.  See the timing chart in figure 7-xx.

WRITE GATE - This is a signal to control the write data and read data. The write data are valid at logic level 0, and the read data are valid at logic level 1.  In the case of a write-protected disk, the write function is inhibited within the Drive.  Another function of the WRITE GATE is to internally operate the tunnel erase, which keeps operating for 972 micro-seconds after the WRITE GATE has been closed.

WRITE DATA - This line is used to write data onto the disk. Power is sup-plied to the read/write heads when logic level 1 changes to logic level 0, which causes a magnetic flux. This line is valid when the WRITE GATE is at logic level 0. A WRITE DATA timing chart is shown in figure 7-34.

HEAD LOAD - When this line becomes logic level 0,the heads are loaded and are released at logic level 1. Depending on the jumper selection, both the HEAD LOAD and SELECT are available, or the heads can be loaded by SELECT only. In every case, the heads are loaded only when the READY sig-

7-25

BFISD 8079

Figure 7-33.  Signal Interface Lines

7-26

BFISD 8079

Figure 7-34. WRITE DATA Timing (FM)

nal is at logic level 0.  The function of this signal is to control the operation confirmation LED.

SIDE SELECT - The function of this signal is to select the two read/write heads.  Logic level 0 selects the 1 side and logic level 1 selects the 0 side.  When the heads are switched, a 200-microsecond  wait period is re-quired at read time, and a 1200-microsecond wait period is required at write time.

7.3.1.3  Output Lines

READY - This signal is issued when the disk is inserted into the Drive and is at logic level 0 during the normal select time.  Otherwise it is at logic level 1.

TRACK 00 - This signal goes to logic level 0 when the read/write heads are positioned at track 00 and is used to detect the Head Carriage position after POWER-ON.

INDEX - The Drive carries the index detection mechanism and issues the detection signal when the index hole is detected.    Normally this line is at logic level 1 and becomes logic level 0 when the index hole is de-tected (4 ms).  On the soft sector disk,  a signal at one hole indicates the start of the track.  When the disk is not inserted, the index signal remains at logic level 0.  Figure 7-35 shows the index timing.

Figure 7-35.  Index Timing

7-27

BFISD 8079

READ DATA - The function of this signal is to output the raw data that was read by the read circuit of the Drive.  Usually this line is at logic level 1 and becomes logic level 0 when the magnetic inversion exists on the track.

Figure 7-36.  READ DATA (FM)

WRITE PROTECT - The function of the signal is to notify the Central Microprocessor Board that a write-protected disk has been inserted. When the protected disk is inserted, the line becomes logic level 0, and the write onto the disk is inhibited in the Drive. For write protect, the disk write  prevention notch can be covered by an opaque label.

### 7.3.2  Jumper Pin

Selecting a jumper pin located on the Main PCBA permits a desired function to be used.  Head load, the operation confirmation LED and the door lock solenoid can be controlled by jumper pins.  A jumper pin selection tabel is presented below.  The factory jumper arrangement is shown on the following page.

Function        Content                           JJ1

S1   S2   S3   S4      SH   AH

Jumper mode at

factory before           0    X    X    X       0    X

shipment

Drive Select 1           0    X    X    X

Drive            "       2           X    0    X    X

Select           "       3           X    X    0    X

"       4           X    X    X    0

Head loading takes

place under head                                0    X

Head        loading signal

Load

Selection   Head loading takes

place by ready mode                             X    0

automatically

7-28

BFISD 8079

Figure 7-37. Factory Arrangement of Jumper

7-29

BFISD 8079

Note 1:  In 48 T.P.I Model, the period is 6 ms.

Note 2:  In 48 T.P.I Model, the period is 26 ms.

Figure 7-38.  Drive Timing Diagram

7-30

BFISD 8079

7-31

BFISD 8079

7-32

BFISD 8079

7-33/34

BFISD 8079

SECTION VIII

# 20 MEGABYTE WINCHESTER DRIVE SYSTEM

## 8.1  INTRODUCTION

This section provides maintenance personnel with information necessary to in-stall, operate and maintain the 20 MB Winchester Drive system.  Section VIII is arranged in six subsections.  The scope of each subsection is as follows:

8.1  INTRODUCTION - contains general information, physical and electrical

descriptions and equipment specifications.

8.2  INSTALLATION AND OPERATION - contains information to enable mainte-

nance personnel to inspect and install the 20 MB Winchester Drive and

includes information on  the  Winchester Drive Controller (WDC).

8.3  FUNCTIONAL DESCRIPTION - explains Drive and Controller operation and

gives a detailed description of each function.  Simplified logic and

block diagrams, timing diagrams and waveforms are included.

8.4  MAINTENANCE - contains corrective  maintenance procedures.

8.5  REMOVAL AND REPLACEMENT PROCEDURES - presents step-by-step procedures

for removing and replacing major subassemblies.

8.6  PARTS LIST

### 8.1.1  General Description

The 20 MB, 5 1/4-inch, Winchester  Drive  is a fixed-media, magnetic, rotating,

data storage device.  Its purpose is to allow the Model 4108 Base Unit to store

and retrieve blocks of data  (records)  onto and from rotating disks, thus pro-

viding storage for the MAI®  2000 Series  Computer System.  The Drive functions

as an input/output device in the Base Unit.  The Drive contains four magnetic

disks and has a total data storage capability of 20.97 megabytes, formatted.

Access to data is provided by one moving head per disk surface.  The heads are an integral part of the Head Disk Assembly (HDA) and never require alignment in the field.  Data is recorded on the disk surfaces using modified frequency mod-ulation (MFM) techniques.  The Drive incorporates an open-loop, stepper motor positioning system.  The major components of the Drive are illustrated in fig-ure 8-1 and are explained in the following paragraphs.

Head Disk Assembly - The Head Disk Assembly,  shown in figure 8-2, is a

completely sealed module that houses the read/write heads, disks, posi-

tioner assembly, stepper motor and filters.  The spindle-mounted disks

are rotated by the dc motor as the read/write heads "fly" over the sur-

face of the disk.  The stepper motor positions the heads over the disk,

using positioning information from a single-chip microcomputer.  Within

the sealed module, air movement generated by disk rotation causes air to

flow from the disk chamber  (upper chamber), through an aperture, into

the drive chamber (lower chamber) and return via a recirculating filter.

3-1

BFISD 8079

Figure 8-1.  Major Component Location

8-2

BFISD 8079

Figure 8-2. Head Disk Assembly

8-3

BFISD 8079

DC Motor and Brake - The dc motor is a brushless, two-phase external

rotor motor with integral hub.  Commutation is effected by a Hall sen-

sor.  The rotational speed of the motor is 3600 revolutions per minute

(rpm). The disk hub is grounded to the Master Electronics PCBA via the

motor shaft and a button contact.  The brake is a plunger-solenoid de-

signed to stop the motor in five seconds and to provide a restraining

torque during handling.

Disk Electronics - The disk electronics consists of three standard

printed circuit board assemblies (PCBAs): the Master Electronics PCBA;

the Preamplifier PCBA; and the Motor Control PCBA.

Power Supply - The dc supply voltages (+12 and +5 volts) to the Winches-

ter Drive are supplied by the  Base Unit Power Supply and are input to

the Drive on connector J3.

8.1.2  Functional Concepts

The simplified block diagram in figure 8-3 shows the functional concepts of the Winchester Drive.  Additional detailed explanations of the logic areas are dis-cussed in paragraph 8.3.

Figure 8-3.  Simplified Block Diagram

8-4

BFISD 8079

Interface logic - The interface logic translates the input/output sig-

nals of the Winchester Drive to ensure drive-to-controller  signal com-

patibility.  Winchester Drive logic signal levels are transistor-to-

transistor logic (TTL) compatible.  The transmission line signals are

differential signals.

Read/Write Logic - To execute read or write commands, the Drive must be

free of faults, and the selected head must be at the correct location on

the disk (i.e., on cylinder).  During a read command, the read/write

logic recovers data from the disk, processes the data, and transfers the

data to the Winchester Drive Controller (WDC) board, in the Base Unit.

During a write command, the read/write logic receives data from the WDC,

processes the data and writes it onto a disk.

Head Select Logic - The head select logic receives and decodes the ad-

dresses of a specific head.

Stepper Motor Logic - A four-phase stepper motor is used to control the

read/write heads in the proper sequence at  a rate and direction deter-

mined by a single-chip microcomputer.

Index Logic - The square wave output of the Hall sensor in the dc motor

is processed to produce a pulse every disk revolution.  This pulse is

used as an interface signal to mark a fixed reference point relative to

the disk.

Winchester Drive Controller - The Winchester Drive Controller PCBA uses

the Shugart Associates System Interface (SASI).  It communicates with

the Central Microprocessor Board (CMB) global bus via the WDC Bus Adapt-

er PCBA.  Together, these two boards interface the Winchester Drive to

the CMB.  The Winchester Drive Controller PCBA is mounted above the com-

ponent side of the WDC Bus Adapter PCBA.

8.1.3  Equipment Specifications

Performance characteristics for the 20 MB Winchester Drive are listed in table 8-1.

Table  8-1.  Specifications

PARAMETERS                                 CHARACTERISTICS

Storage Capacity

Unformatted

Disks per drive                         4

Cylinders                               320

Tracks per cylinder                     8

Data bytes per track                    10,417

Tracks per drive                        2,560

Capacity (megabytes)                    26.67

8-5

BFISD 8079

Table 8-1.  Specifications (continued)

PARAMETERS                                CHARACTERISTICS

Storage Capacity

Formatted

Data bytes per sector                  256

Data sectors per track                 32

Data bytes per track                   8,192

Capacity (megabytes)                   20.97

Recording Parameters

Bit density                              8,900 bpi (inner track, nominal)

Coding                                   Modified-frequency-modulation  (MFM)

Track density                            360 tracks per inch (average)

Rotational Parameters

Disk rotational speed                    3,600 (+1%) rpm

Data transfer rate                       5 megabits per second

Cylinder Access Time

Ramp mode

Single cylinder                        18 milliseconds (average)

320 cylinders                          215 milliseconds (maximum)

Cylinder access                        90 milliseconds (average)

3 ms step mode

Single cylinder                        18 milliseconds (average)

320 cylinders                          1,035 milliseconds (maximum)

Cylinder access                        360 milliseconds (average)

Slow pulse mode

Single cylinder                        23 milliseconds (average)

320 cylinders                          Step rate=pulse rate

Cylinder access                        Step rate=pulse rate  (average)

Data Access Time

Average latency                          8.3 milliseconds

Average data access

time/ramp mode                         98.3 milliseconds

time/3 ms step mode                    368.3 milliseconds

Head switching time                      8 microseconds (maximum)

Error Rates

The following error rates are valid

only when the drive is being used

according to specifications.  Media

defects or equipment failures are ex-

cluded.  Written data should be veri-

fied as being correctly written.

Seek errors                            1 in 1,000,000 seeks

Recoverable read errors                1 in 10,000,000,000 bits

Nonrecoverable read errors             1 in 1,000,000,000,000 bits

8-6

BFISD 8079

Table 8-1.  Specifications  (continued)

PARAMETERS                              CHARACTERISTICS

STORAGE                    TRANSIT                     OPERATING

Temperature:

-40°F to 158°F             -40°F to 158°F                50°F to 122°F

-40°C to 70°C              -40°C to 70°C                 10°C to 50°C

Temperature Gradient:

27°F per hour              20°F per hour                 18°F per hour

15°C per hour              15°C per hour                 10°C per hour

Humidity:

5-90% RH                   5-90% RH                      10-85% RH

no condensation            no condensation               no condensation

Humidity Gradient:

20% per hour               20% per hour                  20% per  hour

Altitude:

-1,000 to 40,000 feet      0 to 40,000 feet              -1,000 to 10,000  feet

Vibration:

0.2 inches  peak-peak      0.2 inches peak-              0.006 inches peak-

displacement               peak displacement             peak displacement

(5 Hz to 20 Hz)            (5 Hz to 20 Hz)               (5 Hz to 60 Hz)

Shock:

Will withstand a drop      Will withstand a              3.0 g, peak; 10 milli-

of 36 inches               drop of 36 inches             seconds duration; 2

shocks/second, maximum

RF Interference:                                         1 volt/meter rms

(1.5 HZ to 10GHz)

Magnetic field:                                          0.0003 tesla, max.

Emitted Acoustic Noise:                                  54 db, max. (cont.)

8-7

BFISD 8079

## 8.2  INSTALLATION AND OPERATION

This subsection contains unpacking, installation and checkout information for the 20 MB Winchester Drive System.

### 8.2.1  Unpacking

Prior to unpacking the Drive, inspect the packaged Drive to determine whether

any damage was incurred during shipment.

1.  Using the shipping documents,  verify that all items have been

received.

2.  Open the protective shipping carton at the top.

3.  Remove  the Drive from the  shipping carton.

4.  Remove  the plastic cover.

5.  Inspect each package article to determine whether any damage was in-

curred during shipment.

6.  Verify that connectors, indicators and protruding parts are undamaged.

7.  Check the ID nameplate against the shipping papers to verify that the

drive part number and serial number are correct.

8.  When practical, store shipping containers for reuse.

9.  Record any damage, and report damage to the applicable carrier.

### 8.2.2  Equipment Placement

Equipment placement consists of mounting the Drive in the Base Unit, installing the Winchester Drive Controller, and routing the input/output and power cables.

### 8.2.3  Shipping Lock (Read/Write Heads)

The stepper motor lock is fixed in place automatically through a relay.  The lock prevents movement of the read/write heads across the disk surface during shipment or other movement.

### 8.2.4  Step Rate Selection

The Winchester Drive has a step rate operational range of 10 microseconds to 8 milliseconds.  This operational range has three bands; two ranges are automat-ically selected by the single-chip microcomputer, and one is selected by remov-ing Link A on the Master Electronics PCBA.

Link A in:    step rate is 10 microseconds to 200 microseconds

Link B in:    step rate is 700 microseconds to 3.1 milliseconds

Link A out:   step rate is 3.1 milliseconds to 8.0 milliseconds

8-8

BFISD B079

### 8.2.5  System Installation

Installation of the Winchester Drive system consists of plugging the WDC PCBA/ WDC Bus Adapter PCBA combination into the Central Microprocessor Board, in the Base Unit, and then routing the Winchester Drive cables to the WDC and the pow-er supply and connecting them.  All components required to interface the 20 MB Winchester Drive to the Central Microprocessor Board are included. Detailed installation procedures are provided in Section II of this manual.

### 8.2.6  Operation

Operating instructions consist  of indicator functions, power-on/off procedures and voltage checks.

Indicators - When lit, the two red LEDs fixed to the Master Electronics

PCBA are visible through the facia.  The Power On LED is located closest

to the center of the facia and is used to indicate fault conditions (refer

to table 8-3).

The Power On LED will not come on, indicating an error, if the +5 volt

supply does not come up and stabilize within one second.

The Select On LED comes on (provided the Power On LED is on) when the

Drive is ready and selected by the Base Unit.

Power-On Procedures - The Drive requires +12 volts and +5 volts dc source

power, and these voltages are measured at Drive connector J3.  At power-

on, the Drive motor takes 4 amperes at +12 volts, dropping to 2.4 amperes

(maximum) after 10 seconds.  For power-up or power-down sequences, the +12

and +5 volt supplies may be applied or removed in any order.  However, if

the +5 volt power is applied first, the +12 volts should follow within 5

seconds, or the fault detection circuitry will issue an error indication.

On power-up the Drive performs an automatic recalibration sequence, which

includes a disk speed check, accurate to +1% of nominal; a seek to track

00; and an index pulse selection.  The Central Microprocessor Board uses

status READY to sense the completion of this sequence.  The time until

READY turns true is 18 seconds, maximum.

Power Supply Checks - The following loads are used to check the power

supplies.  For the 12 volt supply, the power-up current is measured using

a standard load of 3 ohms in parallel with 1 millihenry, and the operating

current is measured using 5 ohms in parallel with 1 millihenry.  With a

7 ohm resistive load on the 5 volt supply, and the aforementioned loads on

the 12 volt supply, noise and ripple should be no more than 100 millivolts

peak-to-peak, up to 500 Hz; and 50 millivolts peak-to-peak, from 500 Hz

to 5MHz.  The power requirements of the Drive are listed in table 8-2.

Table 8-2.   Power  Requirements

VOLTAGE (VDC)     TOLERANCE         NOMINAL CURRENT      MAXIMUM CURRENT

+5             +5%                 0.65A                0.75A

+12            +10%                2.0A                 2.4A

8-9

BFISD 8079

Table 8-3.   Diagnostic and Failure Code Indicators

ABNORMAL RESULT

ACTION        (DOT-DASH CODE)                       RESULT

Power-Up                              LED flashes at 0.5 second intervals

Drive

After 25 seconds maximum, the LED stops

flashing and remains on.  Heads are at

track 000

Code 1       LED displays* . . . -    No index track data burst at track 2

or track 3

Code 2       LED displays . . - .     No flag 0 from track 000 detector

Code 3       LED displays . . - -     Motor speed exceeds +_!% tolerance

during normal operation

Code 4       LED displays . - . .     Motor speed exceeds +10%, -5% toler-

ance during normal operation

Code 5       LED displays . - . -     Flag 0 always true

Code 6       LED displays . - - .     Step pulse while Write Gate true

Code 7       LED displays . - - -     Static write fault condition**

Code 8       LED displays  N/A

Code 9       LED displays - . . -     Microcomputer self-test failed

Code 10      LED displays - . - .     No index

Code 11      LED displays - . - -     Motor not up to speed

LED remains off          Firmware/microcomputer fault

LED remains on           Firmware/microcomputer fault

LED flashes (erratic)    Firmware/microcomputer fault

Code 12      LED displays - - . .     Found index track data burst, but

cannot set index

*For the fault codes, a four-bit binary code is used.  Long flash (-) = logic

1; a short flash (.) = logic 0, with the most significant bit (MSB) occuring

first.

**Write Fault conditions:

1.   Write current and no Write Gate

2.   No write current and Write Gate

3.   More than one read/write head selected

4.   12 volt supply drops below 10.3 volts

5.   5 volt supply drops below 4.5 volts

8-10

BFISD 8079

## 8.3  FUNCTIONAL DESCRIPTION

The following paragraphs describe the theory of the various electronic subsys-tems that comprise the 20 megabyte 5.25" Winchester Drive.  This information provides maintenance personnel with a comprehensive understanding of the func-tions of the Drive.  A brief  discussion of disk recording principles is fol-lowed by a functional description of the Winchester Drive unit, explaining how the Drive interfaces with the Winchester Drive Controller.

The interconnection of the logics is shown in the detailed diagram, figure 8-4.

### 8.3.1  Basic Disk Principles

The recording medium for the Drive is a stack of four 5 1/4-inch disks with eight recording surfaces (see figure 8-5).

Each disk is coated with a layer of magnetic oxide.  The coating is burnished to a flatness that allows the read/write heads to "fly" in proximity to the surface without actual physical contact.

Data is recorded in serial fashion on concentric rings on each disk surface by holding the head in a fixed position over the rotating disk.  (These rings are referred to as "tracks."  The disk drive unit positions the heads precisely over the tracks. Corresponding track positions, both upper and lower on each disk, are referred to as one "cylinder" of data.)

A center-tapped coil is mounted on the core of the read/write head to perform the read/write function.  The recording flux direction is controlled  by ener-gizing the center tap connection, causing current to flow through the bifiler winding from the center tap to either one end or the other.  When reading, the ends of the coil are switched to the input of the read amplifier.  Data is erased by writing new data on the track.  The read/write coil is mounted onto the core of the ferrite slider.

As the disk rotates, it creates an "air bearing" around its surface.  This air bearing moves under the slider and exerts an upward force on the shoe.  A down-ward pressure is placed on the slider by the spring flexure of the head.  Sup-ported by carefully balanced aerodynamic forces, the head shoe then flies at a point where the downward force of the load spring is equal in force to the air pressure under the head.  The slider's flying height is influenced, in part, by the air-bleed channel in the middle of the slider.  This channel allows some air to bleed from under the slider, decreasing the air pressure.

This, in turn, allows the head to fly closer to the disk surface.  The average flying height of the head is 19 microinches.  (The head is closer on an inner track because the inner track portion of the disk is moving at a slower speed than the outer track portion of the disk, resulting in less air pressure on the inner track than on the outer track.)

The slider is mounted to the head arm assembly via a spring gimbal-mount.  This allows the flying attitude of the slider to vary slightly so that it can follow minor surface variations without contacting the disk surface. As the disk starts, or stops, the head takes off from, or lands in, a silicone-lubricated landing area.  When the disk is not spinning, the head rests on, and actually contacts, the landing zone on the disk.

8-11

BFISD 8079

8-12

BFISD 8079

All heads are mounted on a carriage such that the heads and carriage move as one unit.  The carriage moves the heads radially over the disks' surfaces.  All the heads are positioned at the  same cylinder at any given time.

### 8.3.2  Control Lines

The control data is exchanged between the Winchester Drive and the Winchester Drive Controller board (WDC), in the Base Unit, via a control cable.  The fol-lowing paragraphs define the control interface signals.

Reduced Write Current - The Reduced Write Current signal from the WDC

enables a  current  sink during a write ,  diverting current from the head

and effectively reducing  the  write current.

Write Gate - When true, the Write Gate signal from the WDC enables the

current source and Write drive signals.  When false, this signal enables

Read Data to be transferred from the drive to the WDC.

Seek Complete - The Seek Complete status signal is generated by the sin-

gle-chip microcomputer in the Master Electronics PCBA when the value of an

internal 8-bit counter equals the desired stepper motor phase changes (de-

termined by the Step and Direction In input signals).

Track 00 - The Track 00 status line is set true when the read/write heads

are positioned over track 00.

Write Fault - The Write Fault signal is true under the following fault

conditions:

a.  Write current in a head when Write  Gate is false.

b.  No write current in any head when both Write Gate and Drive Sel-

ected are true.

c.  More than one head is selected.

d.  The 12 volt supply is below 10.3 volts.

e.  The 5 volt supply is below 4.5 volts.

f.  Motor speed exceeds +1% tolerance after the power-up sequence is

completed.

g.  Motor speed exceeds +10% tolerance.

h.  No index signal.

i.  Motor not up to speed.

j.  Step signal received  while Write Gate is true.

Head Select - Up to eight read/write heads may be selected using a 3-bit

code on the Head Select 0, Head Select 1 and Head Select 2 lines.  Table

8-4 is a head select matrix showing the logic level required on each Head

Select line to select the desired read/write head.

8-13

BFISD 8079

Table 8-4.   Head Select Decode Matix

LINE        HDO     HD1      HD2     HD3     HD4     HD5     HD6     HD7

Head Select 0    False   True     False   True    False   True    False   True

Head Select 1    False   False    True    True    False   False   True    True

Head Select 2    False   False    False   False   True    True    True    True

Index - The  Index signal is a 200-microsecond output pulse used to mark a

fixed reference point relative to the disk.

Ready - The Ready signal is true when the Drive is ready to read or write

(with or without an implied seek) and the other lines are valid.  Ready

remains true until power-off or until there is a Write Fault.  The Ready

signal is false under the following conditions:

a.  The  Drive is undergoing power-up.

b.  Motor speed is out of tolerance (+10%, -5% of nominal).

c.  Write Fault is true.

Drive Select - The Drive Select signal from the WDC corresponds with  the

Drive Select switch setting of the Drive.  If the Drive Select signal does

not correspond, and the Ready signal is true, a Drive Select true signal

is returned  to the  WDC, via the data lines.

Step - The  Step signal pulse from the WDC is used in conjunction with the

Direction In  signal to move the stepper motor.  This pulse input to the

microcomputer is used to  clock an internal 8-bit counter, which is reset

prior to  each seek.

Once the  first step pulse is received, the microcomputer issues stepper

motor phase  changes until the number of changes equals the value in the

counter .

Direction In - The  Direction In signal from the WDC determines the direc-

tion of motion of the stepper motor.  The microcomputer receives the first

step pulse of each seek, samples the input and internally stores the re-

sult.

8.3.3  Winchester Drive Controller

The Winchester Drive Controller (WDC) operates in conjunction with an. adapter

board that permits the WDC SASI interface to communicate with the Central Mic-

roprocessor Board global bus.  The two boards are "piggybacked," with the WDC

PCBA mounted above the component side of the WDC Bus Adapter PCBA.

They are electrically interconnected by a 50-pin flat ribbon connector at J4

and by a 4-pin AMP connector at J3 (power).

8-14

BFISD 8079

The simplified block diagram in figure 8-6 shows the functional organization of

the WDC.  Only the major areas are shown, and they are defined as follows:

•  Host Interface - The host interface connects the internal data bus to the

WDC Bus Adapter PCBA. The state machine controls the movement of data and

commands through the host interface.

•  Processor - The eight-bit microprocessor is the intelligence of the WDC.

It monitors and controls the operation of the WDC.

•  State Machine - The state machine controls and synchronizes the operation

of the host interface, serializer/deserializer (SERDES) and sector buffer.

•  SERDES - The serializer/deserializer (SERDES) converts parallel data from

the internal data bus to serial data for transfer to a selected Drive.  It

converts serial data from the selected Drive to parallel data, which it

places on the internal data bus.

Figure 8-6. Controller, Functional Organization

8-15

BFISD 8079

•  Data  Separator - The data separator converts serial TTL data to MFM for

transfer to the selected Drive.  It converts MFM data coming from the

selected Drive to serial TTL data for the SERDES.

•  Sector Buffer  - The sector buffer stages data transfers between the disk

and the host to prevent data overuns.  The sector buffer (FIFO) comprises

1K bytes of dual port RAM, for rapid data transfers.  No sector interleav-

ing is required.

8.3.3.1   Signal Definitions

Tables 8-5 through 8-9 list and define the signals that appear on the SASI bus lines between the WDC Bus Adapter and the Winchester Drive Controller.

The dash(-), or the lack of one, indicates the active state of a signal (the active state of a signal is that state that is required for a given operation):

When a dash is appended to the end of a signal name,

the signal is active when it is low, and

when no dash appears at the end of a signal name,

the signal is active when it is high.

Some signal lines have two so-called active (or significant) states:

When the level on the line is high, a particular operation takes

place, and

when the level on the line is low, a different operation  occurs.

The following examples show the use of these conventions.

•  BUSY-     The signal BUSY- is active when it is at low level because it

has the dash appended.

•  BUSY      The signal BUSY is active at a high level because it does not

have the dash appended.

•  C-/D      The line C-/D (command-/data) has a dual purpose: the slash (/)

indicates quality; that is, the dash after the C indicates that

when this line has a low level, the command mode is indicated,

and when the line has a high level, data mode is indicated.

Other designations used to define signal lines are listed below.

•  Drv       Driver

•  Rcvr      Receiver

•  OC        Open collector

•  Tri-State Line has three states: high, low and high impedance

•  220/330   Line termination: 220 ohms to source voltage and 330 ohms to

ground

8-16

BFISD 8079

Table 8-5.   SASI Bus Status Signals

NAME     DRV/RCVR                         DEFINITION

I-/0     Drv OC     Input-/Output:  The controller drives this line.  A low

level on this line indicates that the controller is driving

the data in on the SASI bus.  A high level on this line

indicates that the WDC Bus Adapter is driving the data out

on the SASI bus.  The WDC Bus Adapter monitors this line

and uses it to enable and disable its data bus drivers.

This signal is qualified by signal REQ-.

C-/D     Drv OC     Control-/Data:  This signal line indicates whether the in-

formation on the data bus consists of control or data

bytes.  A low means command bytes; a high means data bytes.

This signal is qualified by signal REQ-.

BUSY-    Drv OC     Busy:  The controller generates this active low signal in

response to the SEL- signal and the address bit (DBO- to

DB7-) from the WDC Bus Adapter.  The busy signal informs

the WDC Bus Adapter that the controller is ready to conduct

transactions on the SASI bus.

Table  8-6.   Summary of SASI Bus Status Signals

I-/0   C-/D   MSG-                        DEFINITION

High   Low    High   The controller receives commands from the WDC Bus Adapter.

High   High   High   The controller receives data from the WDC Bus Adapter.

Low    High   High   The controller sends data to the WDC Bus Adapter.

Low    Low    High   The controller sends an error status byte to the WDC Bus

Adapter.

Low    Low    Low    The controller informs the WDC Adapter that it has com-

pleted the current command.

Table 8-7.  Controller - Host Handshaking

NAME     DRV/RCVR                         DEFINITION

REQ-     Drv OC     Request: The controller sends this active low signal to the

WDC Bus Adapter for each byte transferred across the inter-

face.  This signal qualifies signals I-/0, C-/D and MSG-.

ACK-     Rcvr,      Acknowledge: The WDC Bus Adapter generates this active low

220/330    signal in response to the REQ- signal from the controller

when the host is ready to receive or transmit a byte of

data.  To complete the handshake, the WDC Bus Adapter must

send an acknowledge in response to each request (REQ-).

8-17

BFISD 8079

Table 8-8.  Host Bus Control Signals

NAME    DRV/RCVR                         DEFINITION

RST-     Rcvr,     Reset: The WDC Bus Adapter sends this active low signal to

220/330    the WDC to force the controller WDC to the idle state.

After RST- has become active, any controller status is

cleared. RST- also causes the deactivation of all signals

to the drives. The time requirement for the RST- signal is

as follows :

Minimum                Maximum

100 nsec                None

SEL-     Rcvr,     Select: The WDC Bus Adapter sends this active low signal to

220/330    the WDC to begin a command  transaction.  Along with SEL-,

the WDC Bus Adapter also sends an address bit to select the

controller (DBO- for controller).  The controller must not

be busy.  The WDC Bus Adapter must deactivate SEL- before

the end of the current command.

Table 8-9.  Host Bus Data Signals

NAME    DRV/RCVR                         DEFINITION

DBO-    Tri-State   These are the eight data bits (lines) of the host SASI bus

to       220/330     (DBO = LSB).

DB7-

The eight lines also are used as address bits to select a

controller, in systems using multiple controllers.  There

is a one-to-one correspondence between the data lines and

the controller select lines.  The normal connection (hard-

wired on the board) is to DBO-, which is the address of

controller 0.  Any other connection requires cutting the

existing trace on the PCBA and adding a jumper.

The following list shows the bit assignments.

DB0-   Controller 0

DBl-   Controller 1

DB2-   Controller 2

DB3-   Controller 3

DB4-   Controller 4

DB5-   Controller 5

DB6-   Controller 6

DB7-   Controller 7

8-18

BFISD 8079

8.3.3.2  Detailed Description (Handshaking and Timing)

The following paragraphs describe the interaction between the Winchester Drive

Controller (WDC) and the WDC Bus Adapter.

Controller Selection - Before the WDC Bus Adapter can begin a transaction,

it must select the controller.  The WDC Bus Adapter selects the controller

by activating the SEL- control signal and the address bit of the control-

ler.  Any bit, DBO- through DB7-, can be the address bit in a system with

multiple  controllers (all controllers leave the factory with DBO- connec-

ted to the controllers' address logic).  For this discussion, the control-

ler's address is 0.

The timing diagram in figure 8-7 shows the basic timing requirements.

Upon receiving both the SEL- signal and DBO-, the WDC activates the BUSY-

signal.  As shown in the timing diagram, both SEL- and DBO- mut be act-

ive (low) before the controller can activate the BUSY- signal.  During

the selection process, the host (the Central Microprocessor Board) has

control of the data bus as signified by the deactivation of the I-/0 line.

Selection is complete when BUSY- becomes active.  The SEL- signal must be

deactivated by the WDC Bus Adapter before the current controller operation

has completed.  It is recommended that the SEL- line be deactivated at or

before the time the first control byte is sent to the controller (WDC).

The controller then enters the command mode.

Figure 8-7.  Winchester Drive Controller Select Timing

8-19

BFISD 8079

Command Mode - The  Winchester Drive Controller  (WDC) receives commands

from the WDC Bus Adapter  using a handshaking  sequence.  The controller

places a low level  on the C-/D (Control-/Data) line to indicate that it

wants a command from the WDC Bus Adapter and places a high level on the

I-/0 line to indicate that the movement of information is from the Adapter

to the controller.  The MSG- line is high.

The controller activates the REQ- line within 10 microseconds after sig-

nals I-/0, C-/D and MSG-  have been placed at high, low and high levels.

The WDC Bus Adapter responds by activating the ACK- signal when a control

byte is ready for  the controller. The control byte placed on the data bus

by the WDC Bus Adapter must be stable within 250  nanoseconds after the

ACK- is activated.  The control byte must be held stable until REQ- is

deactivated.  The WDC Bus Adapter deactivates ACK- after REQ- goes high.

This completes the handshake for the first control byte.  Each succeeding

control byte from the WDC Bus Adapter requires the same complete handshake

sequence.  See figure 8-9 for data bus, REQ- and ACK- timing.  See table

8-5 for I-/0, C-/D and MSG- definitions.

Data Transfer - The timing diagrams in figures 8-8 and 8-9 illustrate the

required timing for data transfer.  See table 8-5 for I-/0, C-/D and MSG-

definitions.

Figure 8-8.  Data Transfer to Host, Timing

8-20

BFISD 8079

Figure 8-9.  Data Transfer from Host, Timing

Status Bytes - Two bytes of status are passed to the host at the end of

all commands.  The first byte informs the host (Central Microprocessor

Board via the WDC Bus Adapter PCBA) whether any errors occurred during

the execution of the command.  The second is a zero byte.  It signals to

the host that the command is complete.  Figure 8-8 shows the data bus,

REQ-, and ACK- timing. See table 8-5 for I-/0, C-/D and MSG- definitions.

Figure 8-11 shows the format of these two bytes.

8.3.3.3  Programming Information

The following subsection discusses communication between the Winchester Drive

Controller (WDC) and the host (Central  Microprocessor Board) from the point of

view of the codes that are passed.  The host sends commands to the controller

through the WDC Bus Adapter.  The controller then implements the commands and

reports back to the host.

8-21

BFISD 8079

8.3.3.4  Commands

The host sends a six-byte block to the controller to specify the operation.

This block is the Device Control Block (DCB).  Figure 8-10 shows the compos-ition of the DCB.  The list that follows figure 8-10 defines the bytes that make up the DCB.

At the end of a command, the controller returns two completion status bytes to the host.  The format of these bytes is shown in figure 8-11.

Control Byte - The control field, byte 5, of the DCB allows the user to

select options for several different types and makes of disk drives.  The

following list defines the bits of the control byte.

Bit 0    Half-step option: Seagate Technology and Texas Instruments.

Bit 1    Half-step option: Tandon

Bit 2    Buffer-step option: Computer Memories, Inc. and Rotating Mem-

ories, Inc. (200 microsecond pulse per step)

Bit 3-5  Spare.  Set to zero for future use.

Bit 6    If one during a read sector command, the failing sector is not

re-read on the next revolution before attempting correction.

This bit should be set to zero for normal operation.

Bit 7    Disable the retries by the controller on all disk-access com-

mands.  Set this bit only during the evaluation of the perfor-

mance of a disk drive.  Otherwise, the bit should be set to zero.

NOTE

The step option bits (0-2) are mutually exclusive,

and only one option should be selected in any given

configuration.

BIT         7    6    5     4    3  2     1     0

Byte 0       Class Code             Opcode

Byte 1          LUN         Logical Block Address

Byte 2              Logical Block Address

Byte 3           Logical Block Address (LSB)

Byte 4                Number of Blocks

Byte 5             Control Byte (reserved)

Figure  8-10.  Device Control Block (DCB) Format

8-22

BFISD 8079

Byte 0     Bits 7, 6 and 5  identify the class of the command.

Bits 4 through 0 contain the opcode of the command.

Byte 1     Bits 7, 6 and 5 identify the logical unit number (LUN).

Bits 4 through 0 contain logical block address 2.

Byte 2     Bits 7 through 0 contain logical block address 1.

Byte 3     Bits 7 through 0 contain logical block address 0 (LSB).

Byte 4     Bits 7 through 0 specify the block count.

Byte 5     Bits 7 through 0 contain the control byte.

Next to Last  Status  Byte

BIT        7      6      5       4        3        2        1        0

0      0      0       d      BUSY     EQUAL   CHECK       0

Bits 0,    Set to zero.

5, 6, 7

Bit 1      Check condition.   Sense is available.

Bit 2      Equal.  Set when any SEARCH is satisfied.

Bit 3      Busy.  Device is busy or reserved.

Last Status Byte

BIT        7      6      5      4     3       2        1         0

0      0      0      0     0       0        0         0

Bits       Set to zero.

0-7

Figure 8-11.  Completion Status Bytes

Logical Address (High, Middle, Low) - The logical address of the drive is

computed by using the following equation.

Logical Address = (CYADR * HDCYL + HDADR) * BKTRK + BKADR

Where: CYADR = Cylinder Address

HDADR = Head Address

BKADR = Block (Sector) Address

HDCYL = Number of Heads per Cylinder

BKTRK = Number of Blocks (Sectors) per Track

8-23

BFISD 8079

The commands fall into eight classes, 0 through 7; only classes 0 and 1

are used.  Class 0 commands are data, non-data transfer, and status com-

mands.  Classes 1 through 6 are reserved.  Class 7 are diagnostic com-

mands.

Each command is described below.  The description includes its class, op-

code and format.

Test Drive Ready (Class 0, Opcode 00) - This command selects a particular

drive and verifies that the drive is ready.  The following diagram shows

the format of the device control block for this command.

d =  drive, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    0    0    0    0

Byte 1      O    O    d    O    O    O    O    O

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    0    0    0    0

Byte 4      0    0    0    0    0    0    0    0

Byte 5      0    0    0    0    0    0    0    0

Rezero Unit (Class 0, Opcode 01) - This command positions the read/write

(R/W) arm to track 00.

d =  drive, 0 or 1

BIT        7    6    5    4    3    2    1    0

Byte 0     0    0    0    0    0    0    0    1

Byte 1     0    0    d    0    0    0    0    0

Byte 2     0    0    0    0    0    0    0    0

Byte 3     0    0    0    0    0    0    0    0

Byte 4     0    0    0    0    0    0    0    0

Byte 5     0    0    0    0    0    0    0    0

Reserved (Class 0, Opcode 02)  - This opcode is not used.

Request Sense Status (Class 0, Opcode 03) - The host must send this com-

mand immediately after it detects an error.  The command causes the con-

troller to return four bytes of drive and controller status.  The formats

of these four bytes are shown after the DCB.  When an error occurs on a

multiple sector data transfer (read or write), the Request Sense Status

8-24

BFISD 8079

command returns the logical address of the failing sector in bytes 1, 2

and 3.  If the Request Sense Status command is issued after any of the

format commands or the Check Track Format command, then the logical ad-

dress returned by the controller points to one sector beyond the last

track formatted, or checked, if there was no error.

If there was an error, then the logical address returned points to the

track in error.  Tables 8-10 through 8-13, which follow the formats, list

the error codes.

d = drive, 0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    0    0    0    1    1

Byte 1       0    0    d    0    0    0    0    0

Byte 2       0    0    0    0    0    0    0    0

Byte 3       0    0    0    0    0    0    0    0

Byte 4       0    0    0    0    0    0    0    0

Byte 5       0    0    0    0    0    0    0    0

SENSE BYTES

BIT          7    6    5    4    3    2    1    0

Byte 0                    SEE BELOW

Bits 0-3      Error  Code

Bits 4-6      Error  Type

Bit 7         Address valid, when set

The address valid bit in the error code byte (bit 7) is relevant  only  when

the previous  command  required a logical block address, in which case it  is

always returned as  a  one; otherwise, it is set to zero.  For  instance, if

a Recalibrate command is followed immediately by a Request Sense  Status

command,  the  address  valid  bit would be returned as zero, since this com-

mand does not require a logical block address to be passed in  its DCB.

BIT         7    6    5    4    3    2    1    0

Byte 1      000    Logical Block Address

Byte 2              Logical Block Address

Byte 3           Logical Block Address (LSB)

8-25

BFISD 8079

Table 8-10.  Type 0 Error Codes, Disk Drive

HEX

CODE                               DEFINITION

00    The controller detected no error during execution of the previous oper-

ation.

01    The controller did not detect an index signal from the drive.

02    The controller did not get a seek complete signal from the drive after

seek operation.

03    The controller detected a write fault from drive during last operation.

04    After the controller selected the drive, the drive did not respond with

ready signal.

06    After stepping the maximum number of cylinders, the controller did not

receive the track 00 signal from the drive.

Table 8-11.  Type 1 Error Codes, Controller

HEX

CODE                               DEFINITION

10    ID Read Error: the controller detected a CRC error in the target ID

field on the disk.

11    Data Error: the controller detected an uncorrectable data error in the

target sector during a read operation.

12    Address Mark: the controller did not detect the ID address mark.

13    Address Mark: the controller did not detect the data address mark.

14    Record Not Found: the controller found the correct  cylinder and head,

but not the target record.

15    Seek Error: the controller detected an incorrect cylinder or track, or

both.

18    Data Check in No Retry Mode

19    ECC Error During Verify

1A    Interleave Error

1C    Unformatted or Bad Format on Drive

1D    Self Test Failed

1E    Defective Track:  the controller detected the bad track flag.

8-26

BFISD 8079

Table 8-12.  Type 2 Error Codes, Command and Miscellaneous

HEX

CODE                               DEFINITION

20      Invalid Command: the controller has received an invalid command from

the disk.

21      Illegal Block Address: the controller detected an address that is be-

yond the maximum range.

23      Volume Overflow

24      Bad Argument

25      Invalid Logical Unit Number

The following is a summary of the error codes returned as the result of

the Request Sense Status command.

NOTE: The address valid bit (bit 7) may or may not be set and is not

included here,  for clarity.

Table  8-13.  Request Sense  Status Error Codes

ERROR CODE  (HEX)                   DEFINITION

00              No error detected (command completed okay)

01              No index detected from drive

02              No seek complete from drive

03              Write fault from  drive

04              Drive not ready after it was selected

06              Track 00 not found

10              ID field read error

11              Uncorrectable data error

12              ID address mark not found

13              Data address mark not found

14              Record not found

15              Seek error

18              Data Check in No Retry mode

19              ECC error during verify

1A              Interleave error

1C              Unformatted or bad format on drive

1D              Self test failed

1E              Defective track

20              Invalid command

21              Illegal block address

23              Volume overflow

24              Bad Argument

25              Invalid logical unit number

NOTE:  05, 07-OF, 16/17, 1B, 1F, 22 and 26-2F are not assigned.

8-27

BFISD 8079

Format Unit (Class 0, Opcode 04) - This command formats all sectors with

ID and data fields, according to the selected interleave factor.  The con-

troller will write from index to index all ID and data fields with a block

size as specified by an Immediately previous Mode Select command.  If no

Mode Select command has been executed, the previous data block size wil be

used.  On unformatted disks, or on those whose format is determined bad

(sense byte error code 1C [hex] returned following a Read command), a Mode

Select command is required prior to the Format Unit command. Data fields

are completely written with 6C (hex) unless otherwise specified in the

Format Unit command.

The ID fields will be interleaved as specified in bytes 3 and 4 of the

Command Description Block (CDB).  Under normal conditions, the Winchester

Drive Controller does not require interleaving, because of its high speed

buffer control.

An interleave number of 1 results in sequential ID fields being written on

the disk.  Any interleave number greater than 1, but less than the total

number of sectors per track, results in interleaved formatting.  A 00 in

this field will cause the default interleave factor of 2 to be used.  The

interleave number is equivalent to the number of disk revolutions required

to sequentially read one track.

When the data bit is set (bit 4, byte 1), the controller expects a list of

known bad areas in the data portion of the command (defect skipping).

Bit 3 (byte 1) is the complete list bit.  It specifies that all the known

defects on the drive are contained in the list.

Bit 2 (byte 1), if set, indicates that the next two bits (1 and 0) will be

used to define the format.  A zero indicates default.  Bit 1, if set, in-

dicates that the data pattern in byte 2 is to be used to format the disk.

A zero indicates default.  A zero in bit 0 indicates that a "Cylinder/

Head/Byte Count" format is used in the data list.

d = drive, 0 or 1

b = data bit

c = complete list bit

f = list format bit

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    0    1    0    0

Byte 1      0    0    d    b    c    f    f    f

Byte 2                 Data Pattern

Byte 3      0    0    0    0    0    0    0    0

Byte 4              Interleave Number

Byte 5      0    0    0    0    0    0    0    0

8-28

BFISD 8079

Reserved (Class 0, Opcode 05) - This opcode is not used.

Reserved (Class 0, Opcode 06) - This opcode is not used.

Reserved (Class 0, Opcode 07) - This opcode is not used.

Read (Class  0, Opcode 08) - This command transfers to the host the spec-

ified number of blocks starting at the specified logical starting block

address.  The controller will verify a valid seek address and proceed to

seek to the  specified starting logical block address.  When the seek is

complete, the controller then reads the starting address data field into

the buffer, checks the ECC and begins DMA data transfer.

Subsequent blocks of data are transferred into the buffer in a similar

manner until the block count is decremented to zero.  Cylinder switching

is transparent to the user.

On a data ECC error, the block is re-read up to five times to establish a

"solid error syndrome."  Only then is correction attempted.  Correction is

done  directly into the data buffer, transparent to the user.

d = drive, 0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    0    1    0    0    0

Byte 1       0    0    d    Logical Block Address

Byte 2               Logical Block Address

Byte 3            Logical Block Address (LSB)

Byte 4                  Block Count

Byte 5       0    0    0    0    0    0    0    0

Reserved (Class 0, Opcode 09) - This opcode is not used.

Write (Class 0, Opcode OA) - This command transfers to the target device

the specified number of blocks, starting  at the specified logical starting

block address.  The controller seeks to the specified logical starting

block.  When the seek is complete, the controller transfers the first

block into its buffer and writes its buffered data and its associated ECC

into the first logical sector.

Subsequent blocks of data are transferred as they become available from

the FIFO buffer, until the block count is decremented to zero.  Cylinder

switching  and defect skipping are transparent to the user.

8-29

BFISD 8079

d = drive, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    1    0    1    0

Byte 1      0    0    d    Logical Block  Address

Byte 2             Logical Block Address

Byte 3          Logical Block Address  (LSB)

Byte 4                 Block Count

Byte 5      0    0    0    0    0    0    0    0

Seek (Class 0, Opcode OB) - This command causes the selected drive to seek

to the specified starting address. The controller returns completion sta-

tus immediately after the seek pulses are issued and head  motion starts.

This allows the controller to free the bus and accept further commands

prior to actual seek completion.

NOTE

Any command received for a unit with a seek in progress will

immediately complete with the busy command completion status

(bit 3 set).  This is done to allow the host to use the SASI

bus to do other processing while waiting for seek to complete.

The drive is stepped to the addressed track position, but no ID field ver-

ification is attempted.  When the seek is complete, the controller recon-

nects to the host and responds with the completion status.

The Winchester Drive Controller uses an implied seek on READ, WRITE and

SEARCH commands, obviating the need for issuance of SEEK commands with

each operation.

d = drive, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    1    0    1    1

Byte 1      0    0    d    Logical Block  Address

Byte 2              Logical Block Address

Byte 3           Logical Block Address (LSB)

Byte 4      0    0    0    0    0    0    0    0

Byte 5      0    0    0    0    0    0    0    0

3-30

BFISD 8079

Reserved (Class 0, Opcode 0C) - This opcode is not used.

Reserved (Class 0, Opcode OD) - This opcode is not used.

Reserved (Class 0, Opcode OE) - This opcode is not used.

Translate (Class 0, Opcode OF) - This command performs a logical address

to physical address translation and returns  the physical location of the

requested block address in a cylinder/head/bytes-from-index format.  This

data can be used to build a defect list for the FORMAT command.

Eight bytes are returned in the format of defect descriptors, required by FORMAT.

A data error in the ID field will cause an error status to be returned.

It is then necessary to TRANSLATE the blocks before and after the targeted block to determine the location of the target block.  The use of interleaved sectors and formatted (skipped) defects may complicate the determination of the error location.

d = drive, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    1    1    1    1

Byte 1      0    0    d    Logical Block Address

Byte 2             Logical Block Address

Byte 3           Logical  Block Address (LSB)

Byte 4      0    0    0    0    0    0    0    0

Byte 5      0    0    0    0    0    0    0    0

Reserved (Class 0, Opcode 10)  - This  opcode is not used.

Reserved (Class 0, Opcode 11)  - This  opcode is not used.

Reserved (Class 0, Opcode 12)  - This  opcode is not used.

Write Data Buffer (Class 0, Opcode 13) - This command serves buffer RAM

diagnostic purposes.  The controller will fill the buffer with IK bytes

of data from the host.  There is no guarantee that this data will not be

overwritten by other operations initiated by other initiators.

8-31

BFISD 8079

d = drive, 0 or 1

BIT         76543210

Byte  0       00010011

Byte  1       OOdOOOOO

Byte  2       00000000

Byte  3       00000000

Byte  4       00000000

Byte  5       00000000

Read Buffer RAM (Class 0. Opcode 14) - Read Buffer RAM will pass the host

IK bytes of data from the  buffer.  It is intended for RAM diagnostic pur-

poses.  There is no guarantee that this data will not be overwritten by

other operations initiated by other initiators.  In addition, although

data remains in the buffer after normal data operations, the ordering of

the data found there is undefined.

d = drive, 0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    1    0    1    0    0

Byte 1       0    0    d    0    0    0    0    0

Byte 2       0    0    0    0    0    0    0    0

Byte 3       0    0    0    0    0    0    0    0

Byte 4       0    0    0    0    0    0    0    0

Byte 5       0    0    0    0    0    0    0    0

Mode Select (Class 0, Opcode 15) - This command is used to specify FORMAT

parameters  and should  always precede the FORMAT command.

A blown format error (code 1C) is detected when the controller is unable

to read  the drive information from a drive already formatted.  The user

should use  this  command to inform the controller about the drive informa-

tion.  Then the drive should be backed up and reformatted.

Byte 4 of the command specifies the number of information bytes to be pas-

sed with  the command.  A minimum of twelve bytes (OC [hex]) must be speci-

fied.  If drive parameters are being specified, the count should be 22

bytes (16 [hex]).  The Parameter List is four bytes long, with the first

three bytes reserved (zero filled).  The fourth byte contains the length,

in bytes, of the Extent Descriptor List; this is always eight. (Only a

single extent is supported.)

8-32

BFISD 8079

MODE SELECT PARAMETER LIST

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    0    0    0    0

Byte 1      0    0    0    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    1    0    0    0

EXTENT DESCRIPTOR LIST

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    0    0    0    0

Byte 1      0    0    0    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    0    0    0    0

Byte 4      0    0    0    0    0    0    0    0

Byte 5                Block Size (MSB)

Byte 6                   Block Size

Byte 7                Block Size (LSB)

Byte 0 of the Extent Descriptor List specifies  the data density of the

drive.  The Winchester Drive Controller supports only MFM, and a value of

00 is required in this byte.  Bytes 1, 2 and 3 are reserved and must be

zero, specifying that the  entire drive is to be formatted.  Bytes 5

through  7 are used to specify the data block size.  The block size must

not be less than 256 or exceed the RAM buffer capacity, which is IK bytes,

or 1,024 characters.

In this controller the block size must be set up with a value 256, 512 or

1024 bytes.  Violation of this constraint results in Check Status with an

Error Code of 24 [hex], indicating an invalid argument in parameter data.

The Extent Descriptor List and the Drive Parameter List (described next)

are a single large block of data that follows the command.

The Drive Parameter List includes all the data necessary to specify a

drive.  It is optional, but if present, it must be complete, and the items

must be within the limits stated.  If these parameters are not supplied,

the format operation will use previously supplied values, if available, or

the default values given on the following page.

The List Format Code must be 01.

8-33

BFISD 8079

DRIVE PARAMETER LIST

BIT         7    6    5    4    3    2    1    0

Byte 0             List Format Code == 01

Byte 1              Cylinder Count (MSB)

Byte 2              Cylinder Count (LSB)

Byte 3                Data Head Count

Byte 4       Reduced Write Current Cylinder (MSB)

Byte 5       Reduced Write Current Cylinder (LSB)

Byte 6       Write Precompensation Cylinder (MSB)

Byte 7       Write Precompensation Cylinder  (LSB)

Byte 8             Landing Zone Position

Byte 9          Step Pulse Output Rate Code

The Cylinder Count is the number of data cylinders on the drive.  Because of the inline defect skipping formatting, cylinders normally set aside as spares may be included in this total.  The minimum is one.  The maximum supported is 2,048.  The default value is 306.

The Data Head Count is the number of usable data surfaces. The heads will be  selected from 0 to head count minus 1.  The minimum is 1; the maximum is 16. A drive with nine or more heads will use the Reduced Write Current line as the high order head select.  The default value is two.

The Reduced Write Current Cylinder is the cylinder number beyond which the controller will assert the Reduced Write Current line. The minimum value is 0; the  maximum is 2,047.  The default value is cylinder 150.

The Write Precompensation Cylinder is the cylinder beyond which the con-troller will compensate for inner track bit shift. The specifications for this function agree with those of most disk manufacturers.  Minimum value is 0; maximum is 2,047.

The Landing Zone Position is used with the Start/Stop command to indicate the direction and number of cylinders from the last data cylinder to the shipping position.  The most significant bit indicates the direction, with a zero meaning that the landing zone is beyond the highest track, and a one indicates the landing zone is outside track 00. Thelow seven bits gives the number of cylinders. The default value is zero (land on innermost track).

The Step Pulse Output Rate Code specifies the timing of seek steps. Three options are available:

00  = non-buffered, 3 ms; 01 = buffered, 0.028 ms; 02 = buffered,  0.012  ms.

8-34

BFISD 8079

Reserved (Class 0, Opcode 16) - This opcode is not used.

Reserved (Class 0, Opcode 17) - This opcode is not used.

Reserved (Class 0, Opcode 18) - This opcode is not used.

Reserved (Class 0, Opcode 19) - This opcode is not used.

Mode Sense (Class 0, Opcode 1A) - This command is used to interrogate the

Winchester Drive Controller parameter table to determine the specific

characteristics of any disk drive currently attached.

The attached drive must have been formatted by this controller for this to

be a legal command.

Byte 4 of the command specifies the number of data bytes to be returned

from the command.  A minimum of 12 bytes (OC [hex]) must be specified.

If the drive parameter list is required, the count should be 22 bytes

(16 [hex]).

The returned information will be the four-byte parameter list, the Extent

Descriptor List and the Drive Parameter List (if requested).  These lists

take the exact format of those in the MODE SELECT command.  Please refer-

ence that command for details.

d = drive, 0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    1    1    0    1    0

Byte 1       0    0    d    0    0    0    0    0

Byte 2       0    0    0    0    0    0    0    0

Byte 3       0    0    0    0    0    0    0    0

Byte 4            Number of Bytes Returned

Byte 5       0    0    0    0    0    0    0    0

Start/Stop Unit (Class 0, Opcode 1B) - Byte  4, bit 0 of this command

should be set if this  is a START  command; otherwise, it is a STOP command.

This command is designed for use on drives with a designated shipping or

landing zone.

A STOP command will move the head to the landing zone position.

8-35

BFISD 8079

d = drive, 0 or 1

s = Start/Stop, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    1    1    0    1    1

Byte 1      0    0    d    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    0    0    0    0

Byte 4      0    0    0    0    0    0    0    s

Byte 5      0    0    0    0    0    0    0    0

Receive Diagnostic Result (Class 0, Opcode 1C) - This command sends analy-
sis data to the host (Central Microprocessor Board) after completion of a

SEND DIAGNOSTIC command.  Bytes 3 and 4 designate the size of the avail-

able buffer (in bytes).

READ DIAGNOSTIC is used to transfer data to the host and must immediately

follow a SEND DIAGNOSTIC command, which initiates the dump action.  Other-

wise, the command will be  rejected.

The data length specified should be 104 (hex) or more; however, if  a smal-

ler buffer is provided,  only that much data will be transferred, and the

command will  terminate normally.

d = drive, 0  or  1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    1    1    1    0    0

Byte 1      0    0    d    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3               Data Length  (MSB)

Byte 4               Data Length  (LSB)

Byte 5      0    0    0    0    0    0    0    0

The data received as a result of a dump will be formatted as follows (next

page):

8-36

BFISD 8079

BIT          7    6    5    4    3    2    1    0

Byte 0             Data Block Length (MSB)

Byte 1             Data Block Length (LSB)

Byte 2          Starting Address of Dump (MSB)

Byte 3          Starting Address of Dump (LSB)

Byte 4                Dumped Data (xxOO)

•

•

•

Byte 103              Dumped Data (xxFF)

Send Diagnostic (Class 0, Opcode 1D) - This command sends data to the con-

troller to specify diagnostic tests for controller and peripheral vmits.

Bytes 3 and 4 specify the length of the data to be sent.

The data length specified in the command must be at least 4 bytes long and

should be equal to the length of the data block to be passed over to the

controller.  If the length specified is longer than needed, the excess is

ignored and not read.

The first byte of the data block specifies the particular function being

requested.  The options available,  along with their associated codes are:

HEX

CODE                                DEFINITION

60                         Reinitialize Drive

61                         Dump Hardware Area (4000-40FF)

62                         Dump RAM (8000-80FF)

63                         Patch Hardware Area

64                         Patch RAM

65                         Set Read Error Handling Options

Of these options, only the patch options require a data block longer than

four bytes.

The second byte specifies a subtest or qualifiers specific to the test se-

lected by the first byte.  (Because of the potential  danger in patching

controller programs, this byte provides a safety mechanism to prevent ob-

solete patches.)  The second byte is not checked if the 65 (hex) option

code is specified.

The third byte specifies the starting address (in RAM or the memory-mapped

registers) to be patched.  The high byte of the address is implicit in the

8-37

BFISD 8079

diagnostic specified.  Therefore, a Patch RAM operation with a third byte

of Al (hex) will overwrite an area of RAM starting with 80A1 (hex).

The fourth byte gives the number of bytes to be overwritten.  This can

range from 1 to 256, with a zero yielding 256. the data block for the

Send Diagnostic Command is as follows.

BIT         7    6    5    4    3    2    1    0

Byte 0              Diagnostic Specifier

Byte 1      Diagnostic Option/Coded Release Level

Byte 2      Patch Starting Address LSB/Qualifier

Byte 3          Patch Data Length or Reserved

Byte 4               Optional Patch Data

•

•

•

Byte N+3             Optional Patch Data

Byte 2 of the data block specifies the actions to take place upon encoun-

tering an ECC check, if option 65 (hex) is selected.  The default state is

established by a controller reset.

These options, once set, stay in effect until the next reset.  They apply

only to the Logical Unit Number addressed by the command.

The Set Read Error Handling Options are:

HEX

CODE                               DEFINITION

00           Selects default operation where a correctable error

will be corrected without comment and all data trans-

ferred without check status.

If the error is not correctable, the controller will

transfer the uncorrected data and set check status with

an error code 91 (hex).  The valid address will be that

of the bad block.

01           Report all corrections and  stop.  A correctable error

will be corrected and the data transferred, but the op-

eration will stop with a check status and an error code

(hex).

An uncorrectable error will be handled as in 00 (hex),

above.

02           Do not correct.  All ECC errors will be treated as un-

correctable , except that the error code is set to 98

(hex).

8-38

BFISD 8079

Reserved (Class 0, Opcode 1E) - This opcode is not used.

Reserved (Class O, Opcode 1F) - This opcode is not used.

Reserved (Class 1, Opcode 20) - This opcode is not used.

Reserved (Class 1, Opcode 21) - This opcode is not used.

Reserved (Class 1, Opcode 22) - This opcode is not used.

Reserved (Class 1, Opcode 23) - This opcode is not used.

Reserved (Class 1, Opcode 24) - This opcode is not used.

Read Capacity (Class  1, Opcode 25) - If byte 8 of the Device Control Block

(DCB) is 00, this command  will return the address of the last block on the

unit.  It is not necessary to specify a starting block address in this

command mode.

If byte 8 is 01 (hex), this command will return the address of the block

(after the specified  starting address) at which a  substantial delay in

data transfer will be encountered (e.g., a cylinder boundary).  Any value

other than 00 or 01 (hex) in byte 8 will cause Check Status with an Error

code of 24 (hex), for an invalid argument.

In both cases, the format block size is defined by the last four bytes of

the eight-byte data field returned as a result:

4 bytes, Block Address         4  bytes,  Block  Size

d = drive, 0 or 1

r = relative address, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    1    0    0    1    0    1

Byte 1      0    0    d    0    0    0    0    r

Byte 2           Logical Block Address (MSB)

Byte 3              Logical Block Address

Byte 4              Logical Block Address

Byte 5           Logical Block Address (LSB)

Byte 6      0    0    0    0    0    0    0    0

Byte 7      0    0    0    0    0    0    0    0

Byte 8         Full or Partial Media Indicator

Byte 9      0    0    0    0    0    0    0    0

8-39

BFISD 8079

Reserved (Class 1, Opcode 26) - This opcode is not used.

Reserved (Class 1, Opcode 27) - This opcode is not used.

Reserved (Class 1, Opcode 28) - This opcode is not used.

Reserved (Class 1, Opcode 29) - This opcode is not used.

Reserved (Class 1, Opcode 2A) - This opcode is not used.

Reserved (Class 1, Opcode 2B) - This opcode is not used.

Reserved (Class 1, Opcode 2C) - This opcode is not used.

Reserved (Class 1, Opcode 2D) - This opcode is not used.

Write and Verify (Class 1, Opcode 2E) - This command is similar to the

traditional "read after write" function.  It is an extended address com-

mand that operates like a WRITE command over the specified number of

blocks and then verifies the data written on a block by block basis.  The

verify function transfers no data to the host.

Since no data is transferred to the host during verify, correctable data

checks will be treated in the same manner as uncorrectable data checks.

d = drive, 0 or  1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    1    0    1    1    1    0

Byte 1       0    0    d    0    0    0    0    0

Byte 2,           Logical Block Address (MSB)

Byte 3              Logical  Block Address

Byte 4              Logical  Block Address

Byte 5            Logical Block Address (LSB)

Byte 6       0    0    0    0    0    0    0    0

Byte 7                  Number of Blocks

Byte 8                  Number of Blocks

Byte 9       0    0    0    0    0    0    0    0

Verify (Class 1, Opcode 2F) - This command is similar to the previous

WRITE AND VERIFY except that it verifies the ECC of an already existing

set of data blocks.

It is the responsibility of the host to provide data for rewriting and

correcting when an error is detected.

8-40

BFISD 8079

d = drive, 0 or  1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    1    0    1    1    1    1

Byte 1       0    0    d    0    0    0    0    0

Byte 2            Logical  Block Address  (MSB)

Byte 3               Logical  Block Address

Byte 4               Logical  Block Address

Byte 5            Logical  Block Address  (LSB)

Byte 6       0    0    0    0    0    0    0    0

Byte 7                  Number of Blocks

Byte 8                  Number of Blocks

Byte 9       0    0    0    0    0    0    0    0

Reserved (Class 1, Opcode 30) - This opcode is not used.

Search Data Equal (Class  1, Opcode 31) - This powerful extended address

command provides for a  "search-and-compare-on-equal"  of any data on the

disk.  The starting block address and number of blocks to search are spec-

ified, and a search argument,  which includes a byte displacement and the

data to compare, is passed from the host.

The Invert bit (byte 1, bit 4) inverts the sense of the search comparison

operation.  With invert on, a SEARCH DATA EQUAL command would succeed on

data not equal; SEARCH DATA LOW would succeed on data greater or equal.

The invert bit allows SEARCH EQUAL inverted, which succeeds on the first

block not equal to the pattern.

When a search is satisfied, it will terminate with a  Condition Met Status.

A Request Sense Command can then be issued to determine the block address

of the matching record.  A Request Sense following a successful Search

Data command will:

1.  Report a Sense Key of Equal, if the search was satisfied by an ex-

act match.  If the search was satisfied by an inequality, a Sense

Key of No Sense is reported.

2.  Set the Valid bit to one.

3.  Report the address of the block containing the first matching

record in the Information Bytes.

The Request Sense command following an unsuccessful Search Data Command

will: 1) Report a Sense Key of No Sense, provided no errors occurred; and

2) Set the Valid bit to zero.

8-41

BFISD 8079

d = drive, 0 or  1

i = invert, 0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    1    1    0    0    0    1

Byte 1       0    0    d    i    0    0    0    0

Byte 2           Logical  Block  Address  (MSB)

Byte 3              Logical  Block  Address

Byte 4              Logical  Block  Address

Byte 5           Logical  Block  Address  (LSB)

Byte 6       0    0    0    0    0    0    0    0

Byte 7                 Number of Blocks

Byte 8                 Number of Blocks

Byte 9       0    0    0    0    0    0    0    0

The argument following a SEARCH command is presented on the following

page.

8-42

BFISD 8079

SEARCH COMMAND ARGUMENT

BIT          7    6    5    4    3    2    1    0

Byte 0               Record Size  (MSB)

Byte 1                  Record Size

Byte 2                  Record Size

Byte 3               Record Size  (LSB)

Byte 4           First Record Offset  (MSB)

Byte 5              First Record  Offset

Byte 6              First Record  Offset

Byte 7           First Record Offset  (LSB)

Byte 8            Number of Records (MSB)

Byte 9               Number of Records

Byte 10              Number of Records

Byte 11           Number of Records (LSB)

Byte 12         Search Argument Length  (MSB)

Byte 13            Search Argument Length

Byte 14         Search Field Displacement  (MSB)

Byte 15           Search Field Displacement

Byte 16           Search Field Displacement

Byte 17         Search Field Displacement  (LSB)

Byte 18             Pattern Length (MSB)

Byte 19                Pattern Length

Byte 20                 Data Pattern

•

•

•

Byte M+19               Data Pattern

A definition of the required data in the SEARCH argument is presented on

the following page.

8-43

BFISD 8079

SEARCH COMMAND ARGUMENT REQUIRED  DATA

BYTES                  PARAMETER

0 to 3         Record Size (bytes) - This must equal the blocksize

or zero.  Zero will be taken to mean the format

blocksize.

4 to 7         First Record Offset (bytes) - This must be zero.

8 to 11        Number of Records - This must be less than or equal

to the number of blocks specified in the command and

greater than zero.  The search will terminate upon a

match or when the smaller of these values is encoun-

tered.

12 to 13       Search Argument Length (bytes) - The number of bytes

in the following search argument.  Must equal the

pattern length plus six.

14 to 17       Search Field Displacement - The displacement from

the beginning of the record to the first byte to be

compared.  Must be zero.

18 to 19       Pattern Length (M bytes)  - The number of bytes in

the following data pattern to be compared with a

like size field in each record. Pattern length must

equal blocksize.

20 to M+19     Data Pattern - A variable length field of M bytes up

to blocksize minus displacement  bytes.  The pattern

must be one block long.

## 8.4  MAINTENANCE

The following paragraphs provide information necessary for maintenance of the 5.25" Winchester Drive.  Included are removal and replacement procedures for major subassemblies and a description of the built-in  diagnostics.  The Win-chester Drive requires no preventive maintenance and has no adjustments.

### 8.4.1  Diagnostics

All diagnostics are divided into three sections: (1) Power-Up  Diagnostics;  (2) Operational Error; (3) Fault Diagnostics.

8.4.1.1  Power-Up Diagnostics

During the power-up sequence in the Drive, a number of automatic diagnostic

routine sequences are performed before the Drive becomes ready for system

usage.  When a fault occurs, an appropriate error code is displayed in the

fault indicators. Table 8-14 lists the description of these tests and the ap-

plicable error code.

8-44

BFISD 8079

The Power On LED is used to flash error messages when fault conditions occur in the Drive.  A 4-bit binary code is used (long flash = logic 1; short flash = logic 0) with the most significant bit occuring first (e.g., short, short, long, long = 0011 =  3).

Table  8-14.   Power-Up Sequence Error Codes

ERROR CODE                    ERROR DESCRIPTION

1  (0001)        No  index  track data burst at track 2 or track 3

2  (0010)        No  flag 0  from track 00 detector

3  (0011)        Motor speed exceeds +1% tolerance

5  (0101)        Flag 0 always true

9  (1001)        Single-chip microcomputer self-test failed

10  (1010)        No Index

11  (1011)        Motor not up to speed

The power-up sequence error codes are detailed in the following paragraphs.

Codes 9, 10 and 11 - The first check is a self-test of the single-chip

microcomputer.  A checksum is performed on all the code bytes, and failure

results in the display of fault code 9.  Following the self-test, the mi-

crocomputer checks for an Index pulse (Hall sensor output) from the dc mo-

tor.  If this does not occur during a period of 8 seconds, then fault code

10 is displayed.  Since this condition is likely to be the result of the

dc motor not starting,  the  microcomputer attempts to reduce head/disk

static friction (during a period of 8 seconds) by moving the positioner

four times (one track in alternate directions).

The dc motor speed then is checked to determine whether it is within + 1%

of 3,600 rpm.  Each check takes one motor revolution, and during this time

the Power On LED is flashed at intervals of approximately 0.5 seconds.  If

the microcomputer does not see four consecutive speed samples correct to

+1%, within 25 seconds, it will display fault code 11.

Codes 5 and 2 - When the speed check is successfully completed, Write

Fault interrupts are enabled.  The microcomputer then begins the recali-

bration of the actuator to track  00.  Two possible halt codes may occur.

If  Flag 00 does not go false within 25 steps toward the center of the

disk, fault code 5 will be displayed.  After going false, if Flag 0 can-

not then be set true within 512 steps in the out direction, fault code 2

is displayed.

Codes 1 and 3 - After calibrating the actuator to track 00, the microcom-

puter initiates a routine to select the correct index pulse.  The actuator

is moved to track 2 to find the index data burst on head 0 and to select

the corresponding Hall sensor phase, thus establishing Index.  This task

8-45

BFISD 8079

involves checking for the data burst on track 3, if it cannot be located

in track 2.  If  link B is present, failure to complete this operation re-

sults in fault code 1 (but not when link B is cut).  The actuator then is

positioned on track 00, and a final check is made on the motor speed.  If

it is not within +1% tolerance, fault code 3 is displayed.

At the successful completion of the power-up routine, both Ready and Track

00 are set true, and the head selects are enabled.

8.4.1.2  Operational Error Check

During normal system usage and diagnostic self-testing, a number of built-in

self-tests are performed.  If any error conditions are detected by the micro-

computer, an error code (as described in paragraph 8.4.1.1, above) is displayed

by the Power On LED indicator.  Table 8-15 lists the error codes and the tests.

Table 8-15.   Operational Error Codes

ERROR  CODE                   ERROR DESCRIPTION

4(0100)        Motor speed exceeds +10%, -5% tolerance

6(0110)        Step pulse while Write Gate is true

7(0111)        Static Write Fault condition:

1.  Write current and no Write Gate, or

2.  No write current, no Write Gate, or

3.  More than one read/write head selected, or

4.  12 volt supply below 10.3 volts, or

5.  5 volt supply below 4.5 volts

The operational error codes are detailed in the following paragraphs.

Codes 4 and 6 -  While  waiting for a step pulse from the interface, the

microcomputer is continually monitoring the dc motor speed.  Should the

speed vary from nominal  by more than +10% or -5%, fault code 4 will be

displayed.  The microcomputer will not allow a step pulse to be received

while Write Gate is true.  This a considered a catastrophic controller

fault.  The Drive returns to Write Gate status, displaying fault code 6.

Code 7 - On receipt of a Write Fault interrupt from the Drive's hardware

detection circuitry, the microcomputer latches the interrupt and delays

for 2 seconds.  It then samples the hardware input to check whether the

Write Fault condition still exists.  If it does, fault code 7 is display-

ed; if  it does not, the  microcomputer enters the power-up routine, thus

setting the actuator to  track 00.

8.4.1.3  Fault Diagnostics

Table 8-16 shows the likely causes and corrective action for power-up sequence

and operational faults.  The simplest action is to remove and replace either

the Master Electronics PCBA or the Motor Speed Control PCBA and then recheck

the fault code display.

8-46

BFISD 8079

Table 8-16.  Fault Diagnostics

FAULT           PROBABLE CAUSE                     CORRECTIVE  ACTION

CODE

1         Fault in data burst detection      Replace Master Electronics PCBA

circuitry

Fault in head 0 or preamp          Replace the preamp PCBA

PCBA                               (not recommended)

2,5       Transit lock label not removed     Remove

Connector fault between Motor      Check connector or replace PCBA

Speed Control PCBA and step-

per motor/flag 0 assembly

Short circuit between Motor        Reinstall PCBA

Speed Control PCBA and

casting

Fault in stepper motor control     Replace the  Master  Electronics

circuitry                          PCBA  or the  Motor Speed Control

PCBA

3,4       Brake failure                      Replace

10,11     No 12 volt supply                  Check supply and connector

Faulty Motor Speed Control         Replace

PCBA

6         Controller (WDC) interface         Check WDC and connectors

fault

Faulty Master Electronics          Replace

PCBA

7         Faulty Master Electronics          Replace

PCBA

Faulty preamp PCBA                 Replace (not recommended)

5 volt or 12 volt supply           Check supply

too low

9         Faulty single-chip micro-          Replace Master Electronics  PCBA

computer

8-47

BFISD 8079

In practice, however, the most likely sources of trouble are (a) power supplies out of tolerance and (b) step rates out of the Drive constraints.  In any case, the following should be verified:

1.  The  connectors are clean and properly attached.

2.  Link A is removed for the 3.1-millisecond to 8.0-millisecond range.

3.  The  Drive chassis is free of any system metalwork.

4.  The  dc power lines are short twisted pairs.

5.  Data and control cables are properly shielded and do not run close to

high current switching circuits.

## 8.5  REMOVAL AND REPLACEMENT PROCEDURES

The following paragraphs detail the removal and replacement procedures for the major subassemblies.  Be sure to read each procedure before attempting removal or replacement.

There is no preventive maintenance on the Drive, and there are no adjustments.

Field repair is restricted to replacement of the Master Electronics PCBA, the Motor Speed Control PCBA, the Brake Assembly and the Head Disk Assembly.

NOTE

Repair of the Head Disk Assembly can be effected

only by the use of Ampex special tooling and under

Class 100 cleanroom conditions.

The tools required for field repair consist of the following:

a.   Pozidrive screwdriver, No. 2

b.   Phillips head screwdriver, medium

c.   Hex driver, Allen, 5/64 inch

d.   Slot screwdriver, medium

### 8.5.1 Master Electronics PCBA Removal and Replacement

1.  Remove the three (3) cable connections at the bottom rear of the Win-

chester Drive (PI [Drive Control], P2 [Drive Data], P3 [Power].  See

figure 8-12.

2.  Remove the four (4) shock mount plate screws, located on the bottom of

the Drive.  See figure 8-13.

8-48

BFISD 8079

Figure 8-12. Winchester Drive Assembly

8-49

BFISD 8079

Figure 8-13.  Head Disk Disassembly

8-50

BFISD 8079

3.  Remove the front facia by removing two (2) top and two (2) bottom

mounting screws (Phillips head).  See figure 8-13.

4.  Using the Allen hex drive, remove the six (6) screws securing the

Master Electronics PCBA to the Drive.  Carefully loosen connector J4

from the Preamplifier PCBA, and remove the Master Electronics PCBA.

5.  Disconnect flat cable connector J5 from the Motor Speed Control PCBA.

6.  To replace the Master Electronics PCBA, connect flat cable connector

J5 to the Motor Speed Control PCBA, ensuring that the connector is

properly polarized.

7.  Ensure that connector J4 mates properly with the Preamplifier PCBA.

8.  Secure the Master Electronics PCBA to the Drive with six (6) screws.

### 8.5.2  Brake Removal and Replacement

1.  Remove the Master Electronics PCBA as described in paragraph 8.5.1.

2.  Disconnect brake connector J6 from the Motor Speed Control PCBA.

3.  Using the box spanner, remove the two nuts securing the brake to the

casting, and remove the brake.

4.  To replace the brake, position the replacement brake, and refit the

nuts loosely.

5.  Place the feeler gauge between the motor rotor and the brake pad, and

push the brake body so that the plunger is fully depressed against its

spring.

6.  Ensure that the center line of the brake lines up with the motor cen-

ter, and lock the nuts.

7.  Reconnect the Power connector, ensuring correct polarization.

WARNING

Before powering up the Drive, make sure the

motor is free of obstructions. Do not touch

the spinning motor.

8.  Power up  the Drive with the Master Electronics PCBA lying alongside,

and verify that the brake does not contact the motor rotor. Ensure

that the Master Electronics PCBA is isolated from metallic parts.

9.  Turn the power off, and verify that stopping time is within 5 to 8

seconds.

10.  Refit the Master Electronics PCBA, as described in paragraph 8.5.1.

8-51

BFISD 8079

### 8.5.3  Motor Control  PCBA Removal and  Replacement

1.  Remove the Master Electronics PCBA, as described in paragraph 8.5.1.

2.  Disconnect brake connector J6, dc motor connector J9 and stepper motor

connector J8 from the Motor Speed Control PCBA.

3.  Unscrew both the rear standoff with ground tab and left standoff; re-

move the Motor Speed Control PCBA.

4.  If the spare Hall element is to be connected, remove the link on the

Motor Speed Control PCBA, and reconnect it as shown on the Motor Speed

Control PWBA Assembly Drawing.

5.  To replace the Motor Speed Control PCBA, install the replacement Motor

Speed Control PCBA, insert the ground tab, and tighten the rear stand-

off.  Insert and tighten the left standoff.

6.  Reconnect stepper motor connector J8, dc motor connector J9 and brake

connector J6, ensuring correct polarization  of the connectors.

7.  Refit the Master Electronics PCBA, as described in paragraph 8.5.1.

### 8.5.4  Preamplifier PCBA Removal and Replacement

(Not recommended as field replaceable)

## 8.6  PARTS LIST

Table 8-17 is a listing of field replaceable parts for replacing failed subas-

semblies.

Table  8-17.   Parts List

VENDOR PART

ICN             NUMBER                  DESCRIPTION

TT524100         400413-002       5-1/4"  WINCHESTER DISK DR.,  20MB

TT520100         ASY5023          PCBA,  MASTER ELECTRONICS

TT520110         ASY5024          PCBA,  MOTOR SPEED CONTROL

PCBA,  WINCHESTER DRIVE CONTROLLER

PCBA,  WDC BUS ADAPTOR

TT528160         TAB1004           GROUND TAB

8-52

BFISD 8079

Motor Speed Control PCBA Schematic

3-53

BFISD 8079

Master Electronics PCBA Schematic (1 of 4)

3-54

BFISD 8079

Master Electronics PCBA Schematic (2 of 4)

8-55

BFISD 8079

Master Electronics PCBA Schematic (3 of 4)

8-56

BFISD 8079

Master Electronics PCBA Schematic (4 of 4)

8-57

BFISD 8079

Motor Speed Control PCBA Layout

8-58

BFISD 8079

Master Electronics PCBA Layout

8-59/60

BFISD 8079

SECTION IX

# 50 MEGABYTE WINCHESTER DRIVE SYSTEM

## 9.1  INTRODUCTION

This section provides maintenance personnel with information necessary to in-stall, operate and maintain the 50 MB,  5 1/4-inch, Winchester Drive system.

Section IX is arranged in three subsections. The scope of each subsection is escribed as follows:

9.1  INTRODUCTION - contains general information, physical and electrical

descriptions and equipment specifications.

9.2  INSTALLATION AND OPERATION - contains information to enable mainte-

nance personnel to inspect and install the Winchester Drive system,

and includes information on the Winchester Drive Controller (WDC)

and WDC Bus Adapter PCBAs.  Instructions for the installation of

jumpers and the setting of switches are also included.

9.3  FUNCTIONAL DESCRIPTION - explains drive and Controller operation and

gives a detailed description of each function.

### 9.1.1  General Description

The 50 MB Winchester Drive is a fixed-media, magnetic, rotating, data storage evice.  Its purpose is to allow the Model 4108 Base Unit to store and retrieve locks of data (records) onto and from rotating disks, thus providing storage for the MAI® 2000 Series Computer System.  The drive functions as an input/out-put device in the Base Unit.

The 50 MB Winchester Drive contains four magnetic disks and has a total data storage capability of 42.07 megabytes, formatted.  Access to data is provided by one moving head per disk surface.  The heads are an integral part of the Head  Disk Assembly (HDA) and never require alignment in the field.  Data is recorded on the disk surfaces using modified frequency modulation (MFM) tech-niques.

The Winchester Drive incorporates a balanced, rotary, voice coil/swing arm mo-tor positioning system.  The major components of the drive are explained in the following paragraphs.

Head Disk Assembly - The Head Disk Assembly is a completely sealed

module that houses the read/write heads, disks, positioner assembly,

voice coil/swing arm motor and filters.  The spindle-mounted disks are

rotated by the dc motor as the read/write heads "fly" over the surface

of the disk.  The voice coil/swing arm motor positions the heads over

the disk, using positioning information from a microprocessor.  Within

the sealed module, air movement generated by disk rotation causes air to

flow from the disk chamber (upper chamber), through an aperture, into

the drive chamber (lower  chamber) and return via a 0.3-micron recircu-

lating filter.

9-1

BFISD 8079

DC Motor and Brake - The dc motor is a brushless, direct-coupled , two-

phase external rotor motor with integral hub.  Commutation is effected

by three Hall-effect sensors mounted within the drive motor assembly.

The rotational speed of the motor is 3600 revolutions per minute (rpm).

The disk hub is grounded to the Device Electronics PCBA via the motor

shaft and a button contact.  The brake is a plunger-solenoid designed to

stop the motor in 20 seconds and to provide a restraining torque during

handling.

Disk Electronics - The disk electronics consists of three  standard

printed circuit board assemblies (PCBAs): the Device Electronics PCBA;

the Preamplifier PCBA; and the Motor Control PCBA.

Power Supply - The dc supply voltages (+12 and +5 volts) to the Winches-

ter Drive are supplied by the Base Unit Power  Supply and  are  input to

the Drive on connector J3.

### 9.1.2  Functional Concepts

The simplified block diagram in figure 9-1 shows the functional concepts of the

Winchester Drive, which are described in the following paragraphs. Additional

detailed explanations of these logic areas are presented in paragraph 9.3.

Figure 9-1.  Simplified Block Diagram

9-2

BFISD 8079

Interface logic - The drive interface logic translates the input/output

signals of the Winchester Drive to ensure drive-to-controller signal

compatibility. Drive I/O logic signal levels are transistor-transistor

logic (TTL) compatible.  The transmission line signals are differential

signals.

Read/Write Logic - To execute read or write commands, the drive must be

free of faults, and the selected head must be at the correct location on

the disk (i.e., "on cylinder").  During a read command, the read/write

logic recovers data from the disk, processes the data, and transfers the

data to the Winchester Drive Controller (WDC) board, in the Base Unit.

During a write command, the read/write logic receives data from the WDC,

processes the data and writes the data onto a disk.

Head Select Logic - The head select logic receives and decodes the ad-

dresses of a specific head.

Voice Coil/Swing Arm Motor Logic - A voice coil/swing arm motor is used

to controltheread/write heads in the proper sequence at a rate and

direction determined by a single-chip microcomputer.  Position reference

is made to tracks recorded on a dedicated servo surface on the disk

nearest the drive motor.

Index Logic - The square wave output of the Hall sensor in the dc motor

is processed to produce a pulse every disk revolution.  This pulse is

used as an interface signal to mark a fixed reference point relative to

the disk.

Winchester Drive Controller - The Winchester Drive Controller PCBA uses

the Shugart Associates System Interface (SASI).  It communicates with

the Central Microprocessor Board (CMB) global bus via the WDC Bus Adap-

ter PCBA.  Together, these two boards interface the Winchester Drive to

the CMB.  The Winchester Drive Controller PCBA is mounted above the com-

ponent side of the WDC Bus Adapter PCBA.

9.1.3  Equipment Specifications

Performance characteristics for the 50 Megabyte Winchester Drive are listed in table 9-1.

Table 9-1.  Specifications

PARAMETERS                                 CHARACTERISTICS

Storage Capacity

Unformatted

Disks per drive                         4

Data surfaces/heads                     6

Data bytes per track                    10,416

Tracks per drive                        4,980

Capacity (megabytes)                    51.9

Number of cylinders                     830

9-3

BFISD 8079

Table 9-1.  Specifications (continued)

PARAMETERS                                CHARACTERISTICS

Storage Capacity

Formatted (33 sectors)

Data bytes per sector                  256

Data bytes per track                   8,448

Capacity (megabytes)                   42.07

MBytes per surface                     7.01

Recording Parameters

Bit density                              9,077 bpi (inner track, nominal)

Coding                                   Modified-frequency-modulation  (MFM)

Track density                            960 tracks per inch (average)

Rotational Parameters

Disk rotational speed                    3,600 (+0.5%) rpm

Data transfer rate                       5 megabits per second

Seek Time

Track-to-track                           6 milliseconds

Average                                  30 milliseconds

One-third stroke                         33 milliseconds

Maximum                                  60 milliseconds

Rotation Latency

Average                                  8.33 milliseconds

Maximum                                  16.67 milliseconds (nominal)

Start Time                                 25 seconds maximum to Drive Ready

Stop Time                                  20 seconds maximum

Error Rates

The following error rates

are valid only when the

drive is being used ac-

cording to specifications.

Media defects or equipment

failures are excluded.

Written data should be veri-

fied as being correctly

written.

Seek errors                              1 in 1,000,000 seeks

Recoverable read errors                  1 in 10,000,000,000 bits

Nonrecoverable read errors               1 in 1,000,000,000,000 bits

9-4

BFISD 8079

Table 9-1.  Specifications (continued)

PACKAGED                      UNPACKAGED                      OPERATING

Temperature:

-40°F to 149°F             -40°F to 149°F                 50°F to 115°F

-40°C to 65°C              -40°C to 65°C                  10°C to 46°C

Temperature Gradient:

43.2°F per hour            43.2°F per hour                3.6°F per 5 minutes

24°C per hour              24°C per hour                  2°C per 5 minutes

Humidity:

10-80% RH                  10-80% RH                      10-80% RH

no condensation            no condensation                no condensation

Altitude:

-1,000 to 50,000 feet      -1,000 to 50,000 feet          -200  to  7,000  feet

Vibration:

0.2 inches peak-peak       0.02 inches peak-              0.006  inches  peak-

displacement               peak displacement              peak  displacement

(5 Hz to 10 Hz).           (5 Hz to 31 Hz).               (5 Hz  to 60 Hz).

1 G peak                   1 G peak                       0.5 G  peak

(10 Hz to 44 Hz).          (31 Hz to 69 Hz).              (40 Hz to  300  Hz).

0.01 inches peak-peak      0.004 inches peak-

displacement               peak displacement

(44 Hz to 98 Hz).          (69 Hz to 98 Hz).

5 G peak                   2 G peak

(98 Hz to 300 Hz).         (98 Hz to 300 Hz).

Shock:

Will withstand a drop      Will withstand a               3.0 g, peak, 5 milli-

of 36 inches.              drop of 0.75 inches.           seconds  duration, 1/2

50 G maximum, 20 milli-    1/2 sinusoidal:                sinusoidal.

seconds duration, 1/2      40 G maximum, 5 milli-         1 G peak,  20 milli-

sinusoidal                 seconds duration;              seconds  duration, 1/2

20 G maximum, 100 milli-       sinusoidal

seconds duration

9-5

BFISD 8079

## 9.2  INSTALLATION AND OPERATION

This subsection contains unpacking, installation and checkout information for the 50 Megabyte Winchester Disk Drive.

### 9.2.1  Unpacking

Prior to unpacking the drive,  inspect the packaged drive to determine whether any damage was incurred during shipment.

1.  Using the shipping documents, verify that all items have been

received.

2.  Open the protective shipping carton at the top.

3.  Remove the drive from the shipping carton.

4.  Remove the plastic cover.

5.  Inspect each package article to determine whether any damage was in-

curred during shipment.

6.  Verify that connectors, indicators and protruding parts are undamaged.

7.  Check the ID nameplate against the shipping papers to verify that the

drive part number and serial number are correct.

8.  When practical, store shipping containers for reuse.

9.  Record any damage, and report damage to the applicable carrier.

### 9.2.2  Equipment Placement

Equipment placement consists of mounting the drive in the Base Unit, installing the Winchester Drive Controller (mounted atop the WDC Bus Adapter PCBA), and routing the input/output and power cables.

### 9.2.3  Shipping Lock (Read/Write Heads)

The voice coil/swing arm motor positioner latch is fixed in place automatically through a relay.  The latch prevents movement of the read/write heads across the disk surface during shipment or other movement.

### 9.2.4  System Installation

Installation of the 50 Megabyte Winchester Drive system consists of plugging the WDC PCBA/WDC Bus Adapter PCBA combination into the Central Microprocessor Board, in the Base Unit, and then routing the Winchester Drive cables to the WDC and the power supply and connecting them. All components required  to in-terface the 50 Megabyte Winchester Drive to the Central Microprocessor Board are included. Detailed installation procedures are provided in the following paragraphs.

9-6

BFISD 8079

### 9.2.5  Power and Interface Cables and Connectors

Electrical interface between the 50 Megabyte Winchester Drive and the WDC PCBA is accomplished via four connectors: Jl, J2, J3 and J4.  The connectors and their mating connectors are shown in figure 9-2.

The signal interface connection is made through connectors Jl and J2 on the Device Electronics PCBA.  Pin assignments for Jl, J2 and J3 are listed in table 9-2, 9-3 and  9-4.

Control signal Connector Jl is a 34-pin board-edge connector.  The signals on Jl control the Winchester Drive and transfer status to the Winchester Drive Controller (WDC) PCBA.

Data transfer connector J2 is a 20-pin board-edge connector.  The signals on J2 contain read or write data.

DC power connector J3 is a 4-pin keyed AMP connector, which delivers +5 volts and +12 volts to  the  drive.

Ground connector J4 connects the drive inner chassis ground to the system ground.  J4 is located on the Head Disk Assembly, near the left-hand shock mount (as viewed from the rear of the drive).

### 9.2.6  Drive Addressing and Interface Termination

Figure 9-3 shows the locations of Drive Address jumpers W3, W4,  W5 and W6 (for drive addresses 1, 2, 3 and 4) and Interface Terminator Pack RN1.  Drive Ad- dress jumper Wl is used for write-fault latching, and W2 is reserved.  Only one Drive Address jumper is installed on the drive, and it is addressed as drive 1 by the factory.  Each Drive Select interface line connects the corresponding addressed drive to the Winchester Drive Controller PCBA.

In multiple drive systems, each drive must have its own unique address. Ter- minator Pack RN1 provides proper termination for the interface lines.  When daisy-chaining multiple drives, the terminator is installed only in the last drive on the daisy chain.

Figure 9-2.  Power and Interface Connections

9-7

BFISD 8079

Table 9-2.  Control Signal Connector Jl Pin Assignments

Jl CONNECTOR PIN

Signal  Ground            SIGNAL NAME                   SOURCE

2        1              Reserved

4        3              Head Select 2*                WDC

6        5              Write Gate*                   WDC

8        7              Seek Complete*                Drive

10        9              Track 00*                     Drive

12       11              Write Fault*                  Drive

14       13              Head Select 0*                WDC

16       15              Reserved                      —

18       17              Head Select 1*                WDC

20       19              Index*                        Drive

22       21              Ready*                        Drive

24       23              Step*                         WDC

26       25              Drive Select 1*               WDC

28       27              Drive Select 2*               WDC

30       29              Drive Select 3*               WDC

32       31              Drive Select 4*               WDC

34       33              Direction In*                 WDC

* Signal level is low true.

9-8

BFISD 8079

Table 9-3.  Data Transfer  Connector  J2  Pin Assignments

J2 CONNECTOR PIN

Signal  Ground             SIGNAL  NAME                    SOURCE

1        2               Drive Selected*                Drive

3        4               Reserved                       —

5        6               Reserved                       —

7        8               Reserved                       —

9       10               Reserved

—        11               Ground                         —

12               Ground

13        —               MFM Write Data+                WDC

14        —               MFM Write Data-                WDC

—        15               Ground                         —

—        16               Ground                         —

17        —               MFM Read Data+                 Drive

18        —               MFM Read Data-                 Drive

19               Ground

20               Ground

* Signal level is low true.

Table 9-4.  DC Power Connector J3 Pin  Assignments

J3 PIN                      VOLTAGE

1                       +12VDC

2                       +12V RETURN

3                       +5V RETURN

4                       +5VDC

9-9

BFISD 8079

Figure 9-3.  Drive Address Jumpers and Interface Terminator

### 9.2.7  Installation of the Winchester Drive and the WDC PCBA

To install the 50 Megabyte Winchester Drive system, proceed as follows:

1.  Turn the Base Unit power OFF.

2.  Insert a screwdriver, or similar device, into the slot at the bottom

right-hand side of the Base Unit cover, and push in to disengage the

the plastic latch.  Repeat with the left-hand side, and remove the

cover.

3.  Remove the Memory Array PCBAs, located in the front right-hand corner

of the CMB, by simply lifting the "stack" of PCBAs away from the CMB,

unplugging the bottom memory array PCBA from the CMB.

4.  Remove the front facia by pulling up slightly on the plastic card

holder until the facia is disengaged from the card holder.

5.  If the WDC PCBA is already installed in the Base Unit, continue with

step 13.

9-10

BFISD 8079

6.  Examine the new WDC PCBA and verify that the jumpers listed below are

not installed, for normal operation.  See figure 9-4 for the location

of the jumpers.

Jumper A to B       Jumper  E  to  F        Jumper 0 to P

Jumper C to D       Jumper  G  to  H

7.  If the WDC PCBA is already attached to the WDC Bus Adapter PCBA, con-

tinue with step 12.

8.  Set the appropriate switches on the WDC Bus Adapter PCBA for the cor-

rect bus arbitration number according to the listing shown below.  See

figure 9-4 for the location of the switches.

SWITCH SW1

Bus Arbitration                  _

S1        S2        S3        S4        S5        S6        S7        S8

OFF       OFF       OFF       ON        ON        ON         DON'T CARE

9.  Lower the WDC PCBA onto the WDC Bus  Adapter PCBA so that the Winches-

ter Drive connectors (JO, Jl, J2, J3)  are facing power connector J4

(on the Bus Adapter  PCBA) and the  four standoffs enter the holes in

the WDC PCBA.  Push down on each corner of the WDC PCBA until the re-

tainers on the standoffs hold it securely in place.

10.  Plug the ribbon cable coming the WDC Bus Adapter into connector J4 on

the WDC PCBA.

11.  Plug the 4-pin power connector coming from the WDC Bus Adapter into

J3 on the WDC PCBA.

12.  Plug the WDC Bus Adapter PCBA into the Central Microprocessor Board

(CMB), or into the PCBA on the top of the "stack," at the rear right-

hand corner of the CMB.

13.  Lower the Winchester Drive chassis into position on the CMB.

14.  Pull the drive slightly to the front of the CMB so that the flange at

the bottom of the drive chassis enters the slot in the Base Unit front

panel.

15.  Connect the 4-pin power plug to the connector located at the bottom

left-hand corner of the drive chassis (as viewed from the rear of the

drive), on the Head  Disk Assembly.

16.  Lower the back of the drive chassis so that it pushes back the two (2^

plastic latches on the CMB at the bottom rear of the drive.  The drive

chassis will "snap" in place.

17.  Plug the ribbon cables from the Winchester Drive into the WDC PCBA.

(Note: the two narrower ribbon connectors on the WDC PCBA are situ-

ated side by side; the right-hand connector [J0] receives the "0"

cable, and the left-hand  connector [Jl] receives the "1" cable.)

9-11

BFISD 8079

Figure 9-4.  Location of Jumpers on the Winchester Drive Controller PCBA

9-12

BFISD 8079

18.  Replace the front facia by reversing the removal procedure.

19.  Reinstall the Memory Array PCBAs into the card cage at the front

right-hand corner of the CMB by plugging the bottom PCBA into the CMB.

(The entire stack may be reinstalled as a unit.)

20.  Replace the Base Unit cover by lowering the cover onto the Base Unit

and allowing it to snap into place.

21.  Plug in all connections to the Base Unit, including all previously at-

tached peripherals.

9.2.8  Operation

Operating instructions consist of indicator functions, power-on/off procedures

and voltage checks.

Indicators - When lit, the LED, located on the bezel, indicates the drive

has been selected by the Central Microprocessor Board and that the drive

is ready.

Power-On Procedures - The Winchester Drive requires +12 volts and +5 volts

dc source power, and these voltages are measured at drive connector J3.

During seek, the drive takes 2.8 amperes at +12 volts, dropping to 1.8

amperes while idling.  For power-up or power-down sequences, the +12 volt

and +5 volt supplies may be applied or removed in any order.  However, the

rise time of the +5 volts must be less than 50 milliseconds for proper op-

eration of the power-on reset circuits.

On power-up the drive performs an automatic recalibration sequence, which

includes a disk speed check, accurate to +0.5% of nominal; a seek to track

00; and an index pulse selection.  The Central Microprocessor Board uses

status READY to sense the completion of this sequence.  The time until

READY turns true is typically 20 seconds after application of power.

Power Supply Checks - The following loads are used to check the power sup-

plies.  For the  12 volt supply, the power-up current is measured using  a

standard load  of 3 ohms in parallel with 1 millihenry, and the operating

current is measured using 5 ohms in parallel with 1 millihenry.  With a 7

ohm resistive load on the 5 volt supply, and the aforementioned loads on

the 12 volt supply, noise and ripple should be no more than 100 millivolts

peak-to-peak, up to 500 Hz; and 50 millivolts peak-to-peak, from 500 Hz to

5MHz.  The power requirements of the 50 MB drive are listed in table 9-5.

Table  9-5.   Power  Requirements

VOLTAGE (VDC)     TOLERANCE        NOMINAL CURRENT        MAXIMUM CURRENT

+5                 +5%                 0.9A                  0.9A

+12                +5%,                1.8A                  3.7A

9-13

BFISD 8079

## 9.3  FUNCTIONAL INSCRIPTION

The following paragraphs describe the theory of the various electronic subsys-tems that comprise the 50 Megabyte 5.25" Winchester Drive.  This information provides maintenance personnel with a comprehensive understanding of the func-tions of the drive.

A brief discussion of disk recording principles is followed by a functional description of the Winchester Drive unit, explaining how the drive interfaces with the Winchester Drive Controller.

The interconnection of the major logic blocks is shown in figure 9-5.

### 9.3.1  Basic Disk Principles

The recording medium for the 50 megabyte drive is a stack of four 5 1/4-inch disks with six recording surfaces (see figure 9-6).  Each disk is coated with a layer of magnetic oxide.  The coating is burnished to a flatness that allows the read/write heads to "fly" in proximity to the surface without actual phys-ical contact.

Data is recorded in serial fashion on concentric rings on each disk surface by holding the head in a fixed position over the rotating disk.  (These rings are referred to as "tracks."  The disk drive unit positions the heads precisely over the tracks.  Corresponding track positions, both upper and lower on  each disk, are referred to as one "cylinder" of data.)

A center-tapped  coil is mounted on the core of the read/write head to perform the  read/write function.  The recording flux direction is controlled by ener-gizing the center tap connection, causing current to flow through the bifiler winding from the center tap to  either one end or the other.  When reading, the ends of the coil are switched to the input of the read amplifier.  Data is erased by writing new data on the track.  The read/write coil is mounted onto the core of the ferrite slider.

As the disk rotates, it creates an "air bearing" around its surface.  This air bearing moves under the slider and exerts an upward force on the shoe.  A down-ward pressure is placed on the slider by the spring flexure of the head.  Sup-ported by carefully balanced aerodynamic forces, the head shoe then flies at a point where the downward force of the load spring is equal in force to the air pressure under the head.  The slider's flying height is influenced, in part, by the air-bleed channel in the middle of the slider.  This channel allows some air to bleed from under the slider, decreasing the air pressure.  This, in turn, allows the head to fly closer to the disk surface.

The slideris mounted to the head arm assembly via a spring gimbal-mount.  This allows the flying attitude of the slider to vary slightly so that it can follow minor surface variations without contacting the disk surface.  As the disk starts, or stops, the head takes off from, or lands in, a silicone-lubricated landing area.  When the disk is not spinning, the head rests on, and actually contacts, the landing zone on the disk.

All heads are mounted on a carriage such that the heads and carriage move as one unit.  The carriage moves the heads radially over the disks' surfaces.  All the heads are positioned at the same cylinder at any given time.

9-14

BFISD 8079

9-15

BFISD 8079

### 9.3.2  Control Lines

The control data is exchanged between the Winchester Drive and the Winchester Drive Controller board (WDC), on the Central Microprocessor Board, via a con- trol cable.  The following paragraphs define each control line interface sig- nal.

Write Gate - When true, the Write Gate signal from the WDC enables the

current source and Write drive signals.  When false, this signal enables

Read Data to be transferred from the drive to the WDC.

Seek Complete - The Seek Complete status signal is generated by the micro-

processor in the Device Electronics PCBA.  Seek Complete occurs when the

value of an internal 8-bit counter equals the desired number of track

changes (determined by the Step and Direction In input signals).

Track 00 - The Track 00 status line is set true when the read/write heads

are positioned over track 00.

Write Fault - The Write Fault signal is true under the following fault

conditions:

a.  Shorted head or open head

b.  No Write Data transitions

c.  No Write current

d.  The 5 volt supply is below 4.5 volts.

e.  Motor speed exceeds +1% tolerance after the power-up sequence is

completed.

f.  Write Gate is true while Seek Complete is false, or the heads are

not positioned at nominal track center.

g.  Power dc voltages are out of tolerance.

h.  Correct spindle speed cannot be reached or  maintained.

i.  Servo fault prevents the completion of a seek operation.

Fault conditions g, h and i signal a serious malfunction.  The positioner

retracts, the spindle motor shuts down, and the Ready signal goes false.

When jumper Wl is installed, faults are latched until they can be cleared

by a select-to-deselect transition lasting no less than 50 microseconds in

each state.  When Wl is out, fault conditions are not latched.  A Write

fault caused by an out-of-tolerance dc voltage is reset automatically when

the voltage is restored to nominal.

Head Select - Up to six read/write heads may be selected using a 3-bit

code on the Head Select 0, Head Select 1 and Head Select 2 lines.  Table

9-6 is a head select matrix showing the logic level required on each Head

Select line to select the desired read/write head.  The head selection

timing diagram is shown in figure 9-7.

9-16

BFISD 8079

Figure  9-8.  Index Timing

Table  9-6.  Head  Select Decode Matix

LINE            HDD        HD1        HD2        HD3        HD4        HD5

Head Select 0      False       True       False      True       False      True

Head Select 1      False       False       True       True       False      False

Head Select 2      False       False       False      False      True       True

Index - The Index signal  is a 200-microsecond output pulse used to mark a

fixed reference point relative to the disk.  Figure 9-8  shows the Index

timing.

Ready - The Ready signal  is true when the Drive is ready to read or write

(with or without an implied seek) and the other lines are valid.  Ready

remains true until power-off or until there is a Write Fault.

Drive Select - The Drive Select signal from the WDC corresponds with the

Drive Select switch setting of the drive. If the Drive Select signal does

not correspond, and the Ready signal is true, a Drive Select true signal

is returned to the WDC, via the data lines.

Step - The Step signal pulse from the WDC is used in conjunction with the

Direction In signal to move the read/write heads.  This pulse input to the

microprocessor is used to clock an internal 8-bit counter, which is reset

9-17

BFISD 8079

prior to each seek.  Once the first step pulse is received,  the drive im-

mediately begins seeking.  Additional pulses received before completion of

the seek are buffered into the counter, and the heads move at a rate pro-

portional to the Step pulse count.

Direction In - The Direction In signal from the WDC determines the direc-

tion of motion of the read/write heads.  The microprocessor receives the

first step pulse of a seek, samples the input and stores the result.

### 9.3.3  Winchester Drive Controller

The Winchester Drive Controller (WDC) operates in conjunction with an adapter board that permits the WDC to communicate with the Central Microprocessor Board global bus, via the SASI interface.  The two boards are "piggybacked," with the WDC PCBA mounted above the component side of the WDC Bus  Adapter PCBA.  They are electrically interconnected by a 50-pin flat ribbon connector at J4 and by a 4-pin AMP connector at J3 (power).  The simplified block diagram in figure 9-9 shows the functional organization of the WDC.  Only the major areas are shown, and they are defined as follows:

•  Host Interface - The host interface connects the internal data bus to the

WDC Bus Adapter PCBA.  The state machine controls the movement of data and

commands through the host interface.

•  Processor - The eight-bit microprocessor is the intelligence of the WDC.

It monitors and controls the operation of the WDC.

•  State Machine - The state machine controls and synchronizes the operation

of the host interface, serializer/deserializer (SERDES) and sector buffer.

Figure  9-9.   Controller ,  Functional  Organization

9-18

BFISD 8079

•  SERDES - The serializer/deserializer (SERDES) converts parallel data from

the internal data bus to serial data for transfer to a selected Drive.  It

converts serial data from the selected Drive to parallel data, which it

places on the internal data bus.

•  Data Separator - The data separator converts serial TTL data to MFM for

transfer to the selected Drive.  It converts MFM data coming from the

selected Drive to serial TTL data for the SERDES.

•  Sector Buffer - The sector buffer stages data transfers between the disk

and the host to prevent data overuns.  The sector buffer (FIFO) comprises

1K bytes of dual port RAM, for rapid data transfers.  No sector interleav-

ing is required.

9.3.3.1  Signal Definitions

Tables 9-7 through 9-11 list and define the signals that appear on the SASI bus ines between the WDC Bus Adapter and the Winchester Drive Controller.

The dash(-), or the lack of one, indicates the active state of a signal.  The ctive state of a signal is that state which is required for a given operation. hen a dash is appended to the end of a signal name, the signal is active when t is low.

When no dash appears at the end of a signal name, the signal is active when it s high.

Some signal lines have two so-called active (or significant) states.  When the evel on the line is high, a particular operation takes place.  When the level on the line is low, a different operation occurs.

The following examples show the use of these conventions.

•   BUSY-     The signal BUSY- is active when it is at low level because it

has the dash appended.

•   BUSY      The signal BUSY is active at a high level because it does not

have the dash appended.

•   C-/D      The line C-/D (command-/data) has a dual purpose: the slash (/)

indicates quality; that is, the dash after the C indicates that

when this line is at a low level, command mode is indicated and

when it is at a high level, data mode is indicated.

Other designations used to define signal lines are listed below.

•  Drv        Driver

•  Rcvr       Receiver

•  OC         Open collector

•  Tri-State  Line has three states: high, low, high impedance

•  220/330    Line termination: 220 ohms to source voltage/330 ohms to ground

9-19

BFISD 8079

Table  9-7.  SASI Bus Status Signals

NAME    DRV/RCVR                          DEFINITION

I-/0     Drv OC     Input-/0utput:  The controller drives this line.  A low

level on this line indicates that the controller is driving

the data in on the SASI bus.  A high level on this line

indicates that the WDC Bus Adapter is driving the data out

on the SASI bus.  The WDC Bus Adapter monitors this line

and  uses it to enable and disable its data bus drivers.

This signal is qualified by signal REQ-.

C-/D     Drv OC     Control-/Data: This signal line indicates whether the in-

formation on the data bus consists of control or data

bytes.  A low means command bytes; a high means data bytes.

This signal is qualified by signal REQ-.

BUSY-    Drv OC     Busy:  The  controller generates this active low signal in

response to the SEL- signal and the address bit (DBO- to

DB7-) from the  WDC Bus Adapter.  The busy signal informs

the WDC Bus Adapter that the controller is ready to conduct

transactions on the SASI bus.

Table  9-8.   Summary of SASI Bus Status Signals

I-/0   C-/D   MSG-                        DEFINITION

High   Low    High   The controller receives commands from the WDC Bus Adapter.

High   High   High   The controller receives data from the WDC Bus Adapter.

Low    High   High   The controller sends data to the WDC Bus Adapter.

Low    Low    High   The controller sends an error  status byte to the WDC Bus

Adapter.

Low    Low    Low    The controller informs the WDC Adapter that it has  com-

pleted  the current command.

Table 9-9.  Controller - Host  Handshaking

NAME    DRV/RCVR                          DEFINITION

REQ-     Drv OC     Request: The controller sends this active low signal  to the

WDC Bus Adapter for each byte transferred across the inter-

face.  This signal qualifies signals I-/0, C-/D and MSG-.

ACK-     Rcvr,      Acknowledge: The WDC Bus Adapter generates this active low

220/330     signal in response  to the REQ- signal from the controller

when the host is ready to receive or transmit a byte  of

data.  To complete the handshake, the WDC Bus Adapter must

send an acknowledge in response to each request (REQ-).

9-20

BFISD 8079

Table  9-10.  Host Bus Control Signals

NAME    DRV/RCVR                         DEFINITION

RST-     Rcvr,       Reset: The WDC Bus Adapter sends this active low signal to

220/330      the WDC to force the controller WDC to the idle state.

After RST- has become active, any controller status is

cleared.  RST- also causes the deactivation of all signals

to the drives. The time requirement for the RST- signal is

as  follows:

Minimum                Maximum

100 nsec                None

SEL-     Rcvr,      Select: The WDC Bus Adapter sends this active low signal to

220/330     the WDC to begin a command transaction.  Along with SEL-,

the WDC Bus Adapter also sends an address bit to select the

controller (DBO- for controller).  The controller must not

be busy.  The WDC Bus Adapter must deactivate SEL- before

the end of the current command.

Table  9-11.  Host Bus Data Signals

NAME    DRV/RCVR                         DEFINITION

DBO-    Tri-State    These are the eight data bits (lines) of the host SASI bus

to      220/330      (DBO =  LSB).

DB7-

The eight lines also are used as address bits to select a

controller, in systems using multiple controllers.  There

is  a one-to-one correspondence between the data lines and

the controller select lines.  The normal connection (hard-

wired on  the board) is to DBO-, which is the address of

controller 0.  Any other connection requires cutting the

existing  trace on the PCBA and adding a jumper.

The following list shows the bit assignments.

DBO-    Controller 0

DB1-    Controller 1

DB2-    Controller 2

DB3-    Controller 3

DB4-    Controller 4

DB5-    Controller 5

DB6-    Controller 6

DB7-    Controller 7

9-21

BFISD 8079

9.3.3.2  Detailed Description (Handshaking and Timing)

The following paragraphs describe the interaction between the Winchester Drive Controller (WDC) and the WDC Bus Adapter.

Controller Selection - Before the WDC Bus Adapter can begin a transaction,

it must select the controller.  The WDC Bus Adapter selects the controller

by activating the SEL- control signal and the address bit of the control-

ler.  Any bit, DBO- through DB7-, can be the address bit in a system with

multiple controllers (all controllers leave the factory with DBO- connec-

ted to the controllers' address logic). For this discussion, the control-

ler's address is 0.

The timing diagram in figure 9-10 shows the basic timing requirements.

Upon receiving  both the SEL- signal and DBO-, the WDC activates the BUSY-

signal.  As shown in the timing diagram, both SEL- and DBO- must be active

(low) before the controller can activate the BUSY- signal.  During the se-

lection process, the host (the Central Microprocessor Board) has control

of the data bus as signified by the deactivation of the I-/0 line.  Selec-

tion is complete when BUSY- becomes active.  The SEL- signal must be deac-

tivated by the WDC Bus Adapter before the current controller operation  has

completed.  It is recommended that the SEL- line be deactivated at or be-

fore the time the first control byte is sent to the controller (WDC).  The

controller then enters the command mode.

Figure 9-10.  Winchester Drive Controller Select Timing

9-22

BFISD 8079

Command Mode - The Winchester Drive Controller (WDC) receives commands

from the WDC Bus Adapter using a handshaking sequence.  The controller

places a low level on the C-/D (Control-/Data) line to indicate that it

wants a command from the WDC Bus Adapter and places a high level on the

I-/0 line to indicate that the movement of information is from the Adapter

to the controller.  The MSG- line is high.

The controller activates the REQ- line within 10 microseconds after sig-

nals I-/0,  C-/D and MSG- have  been placed at high, low and high levels.

The WDC Bus Adapter responds by activating the ACK- signal when a control

byte  is ready for the controller.  The control byte placed on the data bus

by the WDC  Bus Adapter must be stable within 250 nanoseconds after the

ACK- is activated.   The control byte must be held stable until REQ- is

deactivated.  The WDC Bus Adapter deactivates ACK- after REQ- goes high.

This completes the handshake for the first control byte.  Each succeeding

control byte from the WDC Bus Adapter requires the same complete handshake

sequence.  See figure 9-11 for data bus, REQ- and ACK- timing.  See table

9-8 for I-/0, C-/D  and MSG- definitions.

Data Transfer - The timing diagrams in figures 9-11 and 9-12 illustrate

the required timing for data transfer.  See table 9-8 for I-/0, C-/D and

MSG- definitions.

Figure 9-11.  Data Transfer to Host, Timing

9-23

BFISD 8079

Figure 9-12.  Data Transfer from Host, Timing

Status Bytes - Two bytes of status are passed to the host at the end of

all commands.  The first byte informs the host (Central Microprocessor

Board via the WDC Bus Adapter PCBA) whether any errors occurred during

the execution of the command.  The second is a zero byte.  It signals to

the host that the command is complete.  Figure 9-11 shows the data bus,

REQ-, and ACK- timing.  See table 9-8 for I-/0, C-/D and MSG- definitions.

Figure 9-13 shows the format of these two bytes.

9.3.3.3  Programming Information

The following subsection discusses communication between the Winchester Drive

Controller (WDC) and the host (Central Microprocessor Board) from the point of

view of the codes that are passed.  The host sends commands to the controller

through the WDC Bus Adapter.  The controller then implements the commands and

reports back to the host.

9-24

BFISD 8079

9.3.3.4  Commands

The host sends a six-byte block to the controller to specify the operation.

This block is the Device Control Block (DCB). Figure 9-13 shows the composi-tion of the DCB.  The list that follows figure 9-13 defines the bytes that make up the DCB.  At the end of a command, the  controller returns two completion status bytes to the WDC.  The format of these bytes is shown in figure 9-14.

Control Byte - The control field, byte 5, of the DCB allows the user to

select options for several different types and makes of disk drives.  The

following list defines the bits of the control byte.

Bit 0    Half-step option: Seagate Technology and Texas Instruments.

Bit 1    Half-step option: Tandon

Bit 2    Buffer-step option: Computer Memories, Inc. and Rotating Mem-

ories, Inc. (200 microsecond pulse per step)

Bit 3-5  Spare.  Set to zero for future use.

Bit 6    If one during a read sector command, the failing sector is not

re-read on the next revolution before attempting correction.

This bit should be set to zero for normal operation.

Bit 7    Disable the retries by the controller on all disk-access com-

mands.  Set this bit only during the evaluation of the perfor-

mance of a disk drive.  Otherwise, the bit should be set to zero.

NOTE

The step option  bits (0-2) are mutually exclusive,

and only one option should be selected in any given

configuration.

BIT         7    6    5    4    3    2    1    0

Byte 0      Class  Code             Opcode

Byte 1         LUN         Logical Block Address

Byte 2             Logical Block Address

Byte 3          Logical Block  Address (LSB)

Byte 4               Number of Blocks

Byte 5            Control  Byte (reserved)

Figure 9-13.  Device Control Block (DCB) Format

9-25

BFISD 8079

Byte 0     Bits 7, 6 and 5 identify the class of the command.

Bits 4 through 0 contain the opcode of the command.

Byte 1     Bits 7, 6 and 5 identify the logical unit number (LUN).

Bits 4 through 0 contain logical block address 2.

Byte 2     Bits 7 through 0 contain logical block address 1.

Byte 3     Bits 7 through 0 contain logical block address 0 (LSB).

Byte 4     Bits 7 through 0 specify the block count.

Byte 5     Bits 7 through 0 contain the control byte.

Logical Address (High, Middle, Low) - The logical address of the drive is

computed by using the following equation.

Logical  Address = (CYADR * HDCYL + HDADR) * BKTRK + BKADR

Where:  CYADR =  Cylinder Address

HDADR = Head Address

BKADR = Block (Sector) Address

HDCYL = Number of Heads  per Cylinder

BKTRK = Number of Blocks (Sectors) per Track

Next to Last Status Byte

BIT        7      6      5      4      3      2      1      0

0      0      0      d      BUSY   EQUAL  CHECK  0

Bits  0,     Set  to zero.

5, 6, 7

Bit  1       Check condition.  Sense is available.

Bit  2       Equal.  Set  when any SEARCH is satisfied.

Bit  3       Busy.   Device is busy or reserved.

Last  Status Byte

BIT         7      6      5      4      3      2      1      0

0      0      0      0      0      0      0      0

Bits        Set  to zero.

0-7

Figure  9-14.  Completion Status Bytes

9-26

BFISD 8079

The commands fall into eight classes, 0 through 7; only classes 0 and 1 are

used.  Class 0 commands are data, non-data transfer, and status  commands.

Classes 1 through 6 are reserved.  Class 7 are diagnostic commands.

Each command is described below.  The description includes its class, opcode

and format.

Test Drive Ready (Class 0, Opcode 00) - This command selects a particular

drive and verifies that the drive is ready.  The following diagram shows

the format of the device control block for this command.

d = drive, 0 or 1

BIT         7      6      5      4      3      2      1      0

Byte 0      0      0      0      0      0      0      0      0

Byte 1      0      0      d      0      0      0      0      0

Byte 2      0      0      0      0      0      0      00

Byte 3      0      0      0      0      0      0      00

Byte 4      0      0      0      0      0      0      00

Byte 5      0      0      0      0      0      0      00

Rezero Unit (Class 0, Opcode 01) - This command positions the read/write

(R/W) arm to track 00.

d = drive, 0 or 1

BIT         7      6      5      4      3      2      1      0

Byte 0      0      0      0      0      0      0      0      1

Byte 1      0      0      d      0      0      0      0      0

Byte 2      0      0      0      0      0      0      0      0

Byte 3      0      0      0      0      0      0      0      0

Byte 4      0      0      0      0      0      0      0      0

Byte 5      0      0      0      0      0      0      0      0

Reserved (Class 0,  Opcode 02) - This opcode is not used.

Request Sense Status (Class 0, Opcode 03) - The host must send this com-

mand  immediately after it detects an error.  The command causes the con-

troller to return four bytes of drive and controller status.  The formats

of these four bytes are shown after the DCB.  When an error occurs on  a

multiple sector data transfer (read or write), the Request Sense Status

command returns the logical address of the failing sector in bytes 1-3.

9-27

BFISD 8079

If the Request Sense Status command is issued after any of the format commands or the Check Track Format command, then the logical address returned by the controller points to one sector beyond the last track formatted, or checked, if there was no error.

If there was an error, then the address returned points to the track in error.

Tables 9-12 through 9-15 list the error codes.  Table 9-15 is a summary of the error codes returned as the result of the Request Sense Status command.

d = drive, 0 or 1

BIT         7      6      5      4      3      2      1      0

Byte 0      0      0      0      0      0      0      1      1

Byte 1      0      0      d      0      0      0      0      0

Byte 2      0      0      0      0      0      0      0      0

Byte 3      0      0      0      0      0      0      0      0

Byte 4      0      0      0      0      0      0      0      0

Byte 5      0      0      0      0      0      0      0      0

SENSE BYTES

BIT         7      6      5      4      3      2      1      0

Byte 0                   SEE BELOW

Bits 0-3     Error  Code

Bits 4-6     Error  Type

Bit 7        Address valid, when set

The address valid bit in the error code byte (bit 7) is relevant only when the previous command required a logical block address.  In this case it is always returned as a one; otherwise, it is set to zero.  For instance, if a Recalibrate command is followed immediately by a Request Sense Status command, the address valid bit would be returned as zero. This is because this command does not require a logical block address to be passed in its DCB.

BIT         7      6      5      4      3      2      1      0

Byte 1      0      0      0    Logical Block Address

Byte 2             Logical Block Address

Byte 3          Logical Block Address (LSB)

9-28

BFISD 8079

Table 9-12.   Type 0 Error Codes, Disk Drive

HEX

CODE                                DEFINITION

00      The  controller detected no error during execution of the previous  oper-

ation.

01      The  controller did not detect an index signal from the drive.

02      The controller did not get a seek complete signal from the drive after

seek operation.

03      The controller detected a write fault from drive during last operation.

04      After the controller selected the drive, the drive did not respond with

ready signal.

06      After stepping the maximum number of cylinders, the controller did not

receive the track 00 signal from the drive.

Table 9-13.  Type 1 Error Codes, Controller

HEX

CODE                                DEFINITION

10      ID Read Error:  the controller detected a  CRC error in the target ID

field on the disk.

11      Data Error: the controller detected an uncorrectable data error in the

target sector during a read operation.

12      Address Mark: the controller did not detect the ID address mark.

13      Address Mark: the controller did not detect the data address mark.

14      Record Not Found: the controller found the correct cylinder and head,

but not the target record.

15      Seek Error: the controller detected an incorrect cylinder or track, or

both.

18      Data Check in No Retry Mode

19      ECC  Error During Verify

1A      Interleave Error

1C      Unformatted  or Bad Format on Drive

1D      Self Test Failed

1E      Defective Track: the controller detected the bad track flag.

9-29

BFISD 8079

Table 9-14.  Type 2 Error Codes, Command and Miscellaneous

HEX

CODE                                DEFINITION

20       Invalid Command: the controller has received an invalid command from

the disk.

21       Illegal Block Address: the controller detected an address that is be-

yond the maximum range.

23       Volume Overflow

24       Bad Argument

25       Invalid Logical Unit Number

Table 9-15.  Request Sense Status Error Codes

ERROR CODE  (HEX)                    DEFINITION

00              No error detected (command completed okay)

01              No index detected from drive

02              No seek complete from drive

03              Write fault from drive

04              Drive not ready after it was selected

06              Track 00 not found

10              ID field read error

11              Uncorrectable data error

12              ID address mark not found

13              Data address mark not found

14              Record not found

15              Seek error

18              Data Check in No Retry mode

19              ECC error during verify

1A              Interleave error

1C              Unformatted or bad format on drive

1D              Self test failed

1E              Defective track

20              Invalid command

21              Illegal block address

23              Volume overflow

24              Bad Argument

25              Invalid logical unit number

NOTE:  05, 07-OF, 16/17, 1B, 1F, 22 and 26-2F are not assigned.

The address valid bit (bit 7) may or may not be set and

is notincluded here, for clarity.

9-30

BFISD 8079

Format Unit (Class 0, Opcode 04)  -  This  command formats all sectors with

ID and data fields, according to the selected interleave factor.  The con-

troller will write from index to index all ID and data fields with a block

size as specified by an  immediately previous Mode  Select command.  If no

Mode Select command has been executed, the previous data block size will

be used.  On unformatted disks, or on those whose format is determined bad

(sense byte error code 1C [hex] returned following a Read command), a Mode

Select command is required  prior tothe Format Unit command.  Data fields

are completely written with 6C (hex) unless otherwise specified in the

Format Unit command.

The ID fields will be interleaved as specified in bytes 3 and 4 of the

Command Description  Block (CDB).  Under normal conditions, the Winchester

Drive Controller does not require interleaving, because of its high speed

buffer control.

An interleave number of 1 results in sequential ID fields being written on

the disk.  Any interleave number greater than 1, but less than the total

number of sectors per track, results  in  interleaved  formatting.  A 00 in

this field will cause the default interleave factor of 2 to be used.  The

interleave number is equivalent to the number of disk revolutions required

to sequentially read one track.

When the data bit is set (bit 4,  byte 1), the controller expects a list of

known bad areas in the data portion of the command (defect skipping).

Bit 3 (byte 1) is the complete list bit. It specifies that all the known

defects on the drive are contained in the list.

Bit 2 (byte 1), if set, indicates that the next two bits (1 and 0) will be

used to define the format.  A zero indicates default.  Bit 1, if set, in-

dicates that the data  pattern in  byte 2  is  to  be used to format the disk.

A zero indicates default.  A zero in bit 0 indicates that a "Cylinder/

Head/Byte Count" format is used in the data list.

d = drive, 0 or 1

b = data bit

c = complete list bit

f = list format bit

BIT          7      6      5      4      3      2      1      0

Byte 0       0      0      0      0      0      1      0      0

Byte 1       0      0      d      b      c      f      f      f

Byte 2                  Data Pattern

Byte 3       0      0      0      0      0      0      0      0

Byte 4              Interleave Number

Byte 5       0      0      0      0      0      0      0      0

9-31

BFISD 8079

Reserved (Class 0, Opcode 05) - This opcode is not used.

Reserved (Class 0, Opcode 06) - This opcode is not used.

Reserved (Class 0, Opcode 07) - This opcode is not used.

Read (Class 0,  Opcode 08) - This command transfers to the host the spec-

ified number of blocks starting at the specified logical starting block

address.  The controller will verify a valid seek address and proceed to

seek to the specified starting logical block address.  When the seek is

complete, the controller then reads the starting address data field into

the buffer, checks the ECC and begins DMA data transfer.

Subsequent blocks of data are transferred into the buffer in a similar

manner until the block count is decremented to zero.  Cylinder switching

is transparent to the user.

On a data ECC error, the block is re-read up to five times to establish a

"solid error syndrome."  Only then is correction attempted.  Correction is

done directly into the data buffer, transparent to the user.

d = drive, 0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    0    1    0    0    0

Byte 1       0    0    d    Logical Block Address

Byte 2               Logical Block Address

Byte 3            Logical Block Address (LSB)

Byte 4                  Block Count

Byte 5       0    0    0    0    0    0    0    0

Reserved (Class 0, Opcode 09) - This opcode is not used.

Write (Class 0,  Opcode OA) - This command transfers to the target device

the specified number of blocks, starting  at the specified logical starting

block address.  The controller seeks to the specified logical starting

block.  When the seek is complete, the controller transfers  the first

block into its buffer and writes its buffered data and its associated ECC

into the first logical sector.

Subsequent blocks of data are transferred as they become available from

the FIFO buffer, until the block count is decremented to zero.  Cylinder

switching and defect skipping are transparent to the user.

9-32

BFISD 8079

d = drive,  0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    0    1    0    1    0

Byte 1       0    0    d    Logical Block Address

Byte 2              Logical  Block Address

Byte 3           Logical Block Address (LSB)

Byte 4                  Block Count

Byte 5       0    0    0    0    0    0    0    0

Seek (Class 0, Opcode OB) - This command causes the selected drive to seek

to the  specified  starting address.  The controller returns completion sta-

tus immediately after the seek pulses are issued and head motion starts.

This allows the controller to  free  the bus and accept further commands

prior to actual seek completion.

NOTE

Any command received for a unit with a seek in progress will

immediately complete with the busy command completion status

(bit 3 set).  This is done to allow the host to use the SASI

bus to do other processing while waiting for seek to complete.

The drive is stepped to the addressed track position, but no ID field ver-

ification is attempted.  When the seek is complete, the controller recon-

nects to the host and responds with the completion status.

The Winchester Drive Controller uses an implied seek on READ, WRITE and

SEARCH commands, obviating the need for issuance of SEEK commands with

each operation.

d = drive,  0  or  1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    0    1    0    1    1

Byte 1       0   0    d    Logical Block Address

Byte 2               Logical Block Address

Byte 3           Logical Block Address (LSB)

Byte 4       0    0    0    0    0    0    0    0

Byte 5       0    0    0    0    0    0    0    0

9-33

BFISD 8079

Reserved (Class 0, Opcode 0C) - This opcode is not used.

Reserved (Class 0, Opcode OD) - This opcode is not used.

Reserved (Class 0, Opcode 0E) - This opcode is not used.

Translate (Class0, Opcode 0F) - This command performs a logical address

to physical address translation and returns the physical location of the

requested block address in a cylinder/head/bytes-from-index format.  This

data can be used to build a defect list for the FORMAT command.

Eight bytes are returned in the format of defect descriptors, required  by

FORMAT.

A data error in the ID field will cause an error status to be returned.

It is then necessary to TRANSLATE the blocks before and after the targeted

block to determine the location of the target block.  The use of inter-

leaved sectors and formatted (skipped) defects may complicate the deter-

mination of the error location.

d = drive, 0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    0    1    1    1    1

Byte 1       0    0    d    Logical Block Address

Byte 2              Logical Block Address

Byte 3            Logical Block Address (LSB)

Byte 4       0    0    0    0    0    0    0    0

Byte 5       0    0    0    0    0    0    0    0

Reserved (Class 0, Opcode 10) - This opcode is not used.

Reserved (Class 0, Opcode 11) - This opcode is not used.

Reserved (Class 0, Opcode 12) - This opcode is not used.

Write Data Buffer (Class 0, Opcode 13) - This command serves buffer RAM

diagnostic purposes.  The controller will fill the buffer with IK bytes

of data from the host.  There is no guarantee that this data will not be

overwritten by other operations initiated by other initiators.

9-34

BFISD  8079

d =  drives 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    1    0    0    1    1

Byte 1      0    0    d    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    0    0    0    0

Byte 4      0    0    0    0    0    0    0    0

Byte 5      0    0    0    0    0    0    0    0

Read Buffer RAM (Class 0, Opcode 14) - Read Buffer RAM will pass the host

1K bytes of data from the  buffer.  It is intended for RAM diagnostic pur-

poses.  There is no guarantee that this data will not be overwritten by

other operations initiated by other initiators.  In addition, although

data remains in the buffer after normal data operations, the ordering of

the data found there is undefined.

d = drive, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    1    0    1    0    0

Byte 1      0    0    d    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    0    0    0    0

Byte 4      0    0    0    0    0    0    0    0

Byte 5      0    0    0    0    0    0    0    0

Mode Select (Class 0, Opcode 15) - This command is used to specify FORMAT

parameters and should always precede the FORMAT command.

A blown format error (code 1C) is detected when the controller is unable

to read the drive information from a drive already formatted.  The user

should use this command to inform the controller about the drive inform-

ation.  Then the drive should be backed up and reformatted.

Byte 4 of the command specifies the number of information bytes to be pas-

sed with the command.  A minimum of twelve bytes (OC [hex]) must be speci-

fied.  If drive parameters are being specified, the count should be 22

bytes (16 [hex]).  The Parameter List (shown in table 9-16) is four bytes

long, with the first three bytes reserved (zero filled).  The fourth byte

contains the length, in bytes, of the Extent Descriptor List; this is

always eight.  (Only a single extent is supported.)

9-35

BFISD 8079

Table 9-16.   Mode  Select Parameter List

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    0    0    0    0    0

Byte 1      0    0    0    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    1    0    0    0

Byte 0 of the Extent Descriptor List (shown in table 9-17) specifies the

data density of the drive.  The Winchester Drive Controller supports only

MFM, and a value of 00 is  required  in this byte.  Bytes 1, 2 and 3 are

reserved and must be zero, specifying that the entire drive is to be for-

matted.  Bytes 5 through 7 are used  to  specify the data block size.  The

block size must not be less than 256 or exceed the RAM buffer capacity,

which is IK bytes, or 1,024 characters.  In this controller the block size

must be set up with a value 256, 512 or 1024 bytes.  Violation of this

constraint results in Check Status with an  Error Code of 24 [hex], indi-

cating an invalid argument in parameter data.

The Extent Descriptor List  and the Drive Parameter List (described next)

are a single large block of  data that follows the command.  The Drive

Parameter List (shown in table 9-18) includes all the data necessary to

specify a drive.  It is optional, but if present, it must be complete, and

the items must be within the limits stated.  If these parameters are not

supplied, the format operation will use previously supplied values, if

available, or the default values given  on the following page.

The List Format Code must be 01.

The Cylinder Count is the number of data cylinders on the drive.  Because

of the inline defect skipping formatting, cylinders normally set aside as

spares may be included in this total.  The  minimum is one.  The maximum

supported is 2,048. The default value is 306.

The Data Head Count is the number of usable data surfaces.  The heads will

be selected from 0 to head count minus  1.  The minimum is 1; the maximum

is 16.  A drive with nine or more heads will use the Reduced Write Current

line as the high order head select.  The default value is two.

The Reduced Write Current Cylinder is the cylinder number beyond which the

controller will assert the Reduced Write Current line.  The minimum value

is 0; the maximum is 2,047.  The default value is cylinder 150.

The Write Precompensation Cylinder is the cylinder beyond which the con-

troller will compensate for inner track bit shift.  The specifications for

this function agree with those of most disk manufacturers.  Minimum value

is 0; maximum is 2,047.

9-36

BFISD 8079

Table  9-17.   Extent Descriptor List

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    0    0    0    0    0

Byte 1       0    0    0    0    0    0    0    0

Byte 2       0    0    0    0    0    0    0    0

Byte 3       0    0    0    0    0    0    0    0

Byte 4       0    0    0    0    0    0    0    0

Byte 5                 Block Size (MSB)

Byte 6                    Block Size

Byte 7                 Block Size (LSB)

Table 9-18.   Drive Parameter List

BIT          7    6    5    4    3    2    1    0

Byte  0              List  Format Code == 01

Byte  1               Cylinder Count (MSB)

Byte  2               Cylinder Count (LSB)

Byte  3                 Data Head Count

Byte  4        Reduced  Write Current Cylinder (MSB)

Byte  5        Reduced  Write Current Cylinder (LSB)

Byte  6        Write  Precompensation Cylinder (MSB)

Byte  7        Write  Precompensation Cylinder (LSB)

Byte  8              Landing Zone Position

Byte  9           Step  Pulse Output Rate Code

The Landing Zone Position is used with the Start/Stop command to indicate

the direction and number of cylinders from the last data cylinder to the

shipping position.  The most significant bit indicates the direction, with

a zero meaning that the landing zone is beyond the highest track, and  a

one indicates the landing zone is outside track 00.  The low seven bits

gives the number of cylinders.  The default value is zero (land on inner-

most track).

9-37

BFISD 8079

The Step Pulse Output Rate Code specifies the timing of seek steps.  Three

options are available:

00  = non-buffered, 3 ms; 01 = buffered, 0.028 ms; 02 = buffered, 0.012 ms.

Reserved (Class 0, Opcode 16) - This opcode is not used.

Reserved (Class 0, Opcode 17) - This opcode is not used.

Reserved (Class 0, Opcode 18) - This opcode is not used.

Reserved (Class 0, Opcode 19) - This opcode is not used.

Mode Sense (Class 0, Opcode 1A) - This command is used to interrogate  the

Winchester Drive Controller parameter table to determine the specific

characteristics of  any disk drive currently attached.

The attached drive must have been formatted by this controller for this to

be a legal command.

Byte 4 of the command specifies the number of data bytes to be returned

from the command.  A minimum of 12 bytes (OC [hex]) must be specified.

If the drive parameter list is required, the count should be 22 bytes

(16 [hex]).

The  returned information will be the four-byte parameter list, the Extent

Descriptor List and the Drive Parameter List (if requested).  These lists

take the  exact format of those in the MODE SELECT command.  Please refer-

ence that command for details.

d =  drive,  0  or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    0    1    1    0    1    0

Byte 1       0    0    d    0    0    0    0    0

Byte 2       0    0    0    0    0    0    0    0

Byte 3       0    0    0    0    0    0    0    0

Byte 4             Number of Bytes Returned

Byte 5       0    0    0    0    0    0    0    0

Start/Stop Unit (Class 0, Opcode 1B) - Byte 4, bit 0 of this command

should be set if this  is a START command; otherwise, it is a STOP command.

This command is designed for use on drives with a designated shipping or

landing zone.

A STOP command will move the head to the landing zone position.

9-38

BFISD 8079

d = drive, 0 or  1

s = Start/Stop,  0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    1    1    0    1    1

Byte 1      0    0    d    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3      0    0    0    0    0    0    0    0

Byte 4      0    0    0    0    0    0    0    s

Byte 5      0    0    0    0    0    0    0    0

Receive Diagnostic Result (Class 0, Opcode  1C) - This command sends analy-

sis data to the host (Central Microprocessor Board) after completion of a

SEND DIAGNOSTIC command.  Bytes 3 and 4 designate the size of the avail-

able buffer (in bytes).

READ DIAGNOSTIC is used to transfer data to the host and must immediately

follow a SEND DIAGNOSTIC command, which initiates the dump action.  Other-

wise, the command will be rejected.

The data length specified should be 104 (hex) or more; however, if a smal-

ler buffer is provided, only that much data will be transferred, and the

command will terminate normally.

d = drive, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    0    1    1    1    0    0

Byte 1      0    0    d    0    0    0    0    0

Byte 2      0    0    0    0    0    0    0    0

Byte 3               Data Length (MSB)

Byte 4               Data Length (LSB)

Byte 5      0    0    0    0    0    0    0    0

The data received as a result of a dump will be formatted as follows (next

page):

9-39

BFISD 8079

BIT          7    6    5    4    3    2    1    0

Byte 0            Data  Block Length (MSB)

Byte 1            Data  Block Length (LSB)

Byte 2         Starting Address  of  Dump (MSB)

Byte 3         Starting Address  of  Dump (LSB)

Byte 4               Dumped  Data (xxOO)

•

*

•

Byte 103             Dumped  Data (xxFF)

Send Diagnostic (Class 0, Opcode 1D) - This command sends data to the con-

troller to specify diagnostic tests for controller and peripheral units.

Bytes 3 and 4 specify the length of the data to be sent.

The data length specified in the command must be at least 4 bytes long and

should be equal to the length of the data block to be passed over to the

controller.  If the length specified is longer than needed, the excess is

ignored and not read.

The first byte of the data block specifies the particular function being

requested.  The options available, along with their associated codes are:

HEX

CODE                                DEFINITION

60                        Reinitialize Drive

61                        Dump Hardware Area  (4000-40FF)

62                        Dump RAM (8000-80FF)

63                        Patch Hardware Area

64                        Patch RAM

65                        Set Read Error Handling Options

Of these options, only the patch options require a data block longer than

four bytes.

The second byte specifies a subtest or qualifiers specific to the test se-

lected by the first byte. (Because of the potential danger in patching

controller programs, this byte provides a safety  mechanism  to prevent ob-

solete patches.)  The second byte is not checked if the 65 (hex) option

code is specified.

The third byte specifies the starting address (in RAM or the memory-mapped

registers) to be patched.  The high byte of the address is implicit in the

9-40

diagnostic specified.  Therefore, a Patch RAM operation with a third byte

of A1 (hex) will overwrite an area of RAM starting with 80A1 (hex).

The fourth byte gives the number of bytes to be overwritten.  This can

range from 1 to 256, with a zero yielding 256. the data block for the

Send Diagnostic Command is as follows.

BIT          7    6    5    4    3    2    1    0

Byte 0               Diagnostic Specifier

Byte 1       Diagnostic Option/Coded Release Level

Byte 2       Patch Starting Address LSB/Qualifier

Byte 3           Patch Data Length or Reserved

Byte 4               Optional Patch Data

•

*

•

Byte N+3             Optional Patch Data

Byte 2 of the data block specifies the actions to take place upon encoun-

tering an ECC check, if option 65 (hex) is selected.  The default state is

established by a controller reset.

These options, once set, stay in effect until the next reset.  They apply

only to the Logical Unit Number addressed by the command.

The Set Read Error Handling Options are:

HEX

CODE                                DEFINITION

00           Selects default operation where a correctable error

will be corrected without comment and all data trans-

ferred without check status.

If the error is not  correctable, the controller will

transfer the uncorrected data and set check status with

an error code 91 (hex).  The valid address will be that

of the bad block.

01           Report all corrections and stop. A correctable error

will be corrected and the data transferred, but the op-

eration will stop with a check status and an error code

(hex).

An uncorrectable error will be handled as in 00 (hex),

above.

02           Do not correct.  All ECC errors will be treated as un-

correctable, except that the error code is set to 98

(hex).

9-41

BFISD 8079

Reserved (Class 0, Opcode 1E) - This opcode is not used.

Reserved (Class 0, Opcode 1F) - This opcode is not used.

Reserved (Class 1, Opcode 20) - This opcode is not used.

Reserved (Class 1, Opcode 21) - This opcode is not used.

Reserved (Class 1, Opcode 22) - This opcode is not used.

Reserved (Class 1, Opcode 23) - This opcode is not used.

Reserved (Class 1, Opcode 24) - This opcode is not used.

Read Capacity (Class  1, Opcode 25) - If byte 8 of the Device Control Block

(DCB) is 00, this command will return the address of the last block on the

unit.  It is not necessary to specify a starting block address in this

command mode.

If byte 8 is 01 (hex), this command will return the address of the block

(after the  specified  starting address) at  which a  substantial delay in

data transfer will be encountered (e.g., a cylinder boundary). Any value

other than 00 or 01 (hex) in byte 8 will cause Check Status with an Error

code of 24 (hex), for an invalid argument.

In both cases, the format block size is defined by the last four bytes of

the eight-byte data field returned as a result:

4 bytes, Block Address         4 bytes,  Block Size

d = drive,  0 or 1

r = relative address, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    1    0    0    1    0    1

Byte 1      0    0    d    0    0    0    0    r

Byte 2           Logical Block Address (MSB)

Byte 3               Logical Block Address

Byte 4               Logical Block Address

Byte 5           Logical Block Address (LSB)

Byte 6      0    0    0    0    0    0    0    0

Byte 7      0    0    0    0    0    0    0    0

Byte 8          Full or Partial Media Indicator

Byte 9      0    0    0    0    0    0    0    0

9-42

BFISD 8079

Reserved (Class 1, Opcode 26) - This opcode is not used.

Reserved (Class 1, Opcode 27) - This opcode is not used.

Reserved (Class 1, Opcode 28) - This opcode is not used.

Reserved (Class 1, Opcode 29) - This opcode is not used.

Reserved (Class 1, Opcode 2A) - This opcode is not used.

Reserved (Class 1, Opcode 2B) - This opcode is not used.

Reserved (Class 1, Opcode 2C) - This opcode is not used.

Reserved (Class 1, Opcode 2D) - This opcode is not used.

Write and Verify (Class 1,  Opcode 2E) - This command is similar to the

traditional "read after  write" function.  It is an extended address com-

mand that operates like a  WRITE command over the specified number of

blocks and then verifies the data written on a block by block basis.  The

verify function transfers no data to the host.

Since no data is transferred to the host during verify, correctable data

checks will  be treated in the same manner as uncorrectable data checks.

d = drive,  0 or 1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    1    0    1    1    1    0

Byte 1       0    0    d    0    0    0    0    0

Byte 2           Logical Block Address (MSB)

Byte 3              Logical  Block Address

Byte 4              Logical  Block Address

Byte 5           Logical Block Address (LSB)

Byte 6       0    0    0    0    0    0    0    0

Byte 7                  Number of Blocks

Byte 8                  Number of Blocks

Byte 9       0    0    0    0    0    0    0    0

Verify (Class 1, Opcode 2F) -  This command is similar to the previous

WRITE AND VERIFY except that it verifies the ECC of an already existing

set of data blocks.

It is the responsibility of the host to provide data for rewriting and

correcting when an error is detected.

9-43

BFISD 8079

d = drive,  0  or  1

BIT          7    6    5    4    3    2    1    0

Byte 0       0    0    1    0    1    1    1    1

Byte 1       0    0    d    0    0    0    0    0

Byte 2            Logical  Block Address (MSB)

Byte 3               Logical Block Address

Byte 4               Logical Block Address

Byte 5            Logical  Block Address (LSB)

Byte 6       0    0    0    0    0    0    0    0

Byte 7                  Number of Blocks

Byte 8                  Number of Blocks

Byte 9       0    0    0    0    0    0    0    0

Reserved (Class 1, Opcode 30) - This opcode is not used.

Search Data Equal (Class 1, Opcode 31) - This powerful extended address

command provides for a "search-and-compare-on-equal" of any data on the

disk.  The starting block address and number of blocks to search are spec-

ified, and a search argument, which includes a byte displacement and the

data to compare, is passed from the host.

The Invert bit (byte 1, bit 4) inverts the sense of the search comparison

operation.  With invert on, a SEARCH DATA EQUAL command would succeed on

data not equal;  SEARCH DATA LOW would succeed on data greater or equal.

The invert bit allows SEARCH EQUAL inverted, which succeeds on the first

block not equal to the pattern.

When a search is satisfied, it will terminate with a Condition Met Status.

A Request Sense Command can then be issued to determine the block address

of the matching record.  A Request Sense following a successful Search

Data command will:

1.   Report a Sense Key of Equal, if the search was satisfied by an

exact match.  If the search was satisfied by an inequality, a

Sense Key of No Sense is reported.

2.   Set the Valid bit to one.

3.  Report the address of the block  containing the first matching

record in the Information Bytes.

The Request Sense command following an unsuccessful Search Data Command

will: 1) Report a Sense Key of No Sense, provided no errors occurred; and

2) Set the Valid bit to zero.

9-44

BFISD 8079

d  =  drive,  0 or 1

i  =  invert, 0 or 1

BIT         7    6    5    4    3    2    1    0

Byte 0      0    0    1    1    0    0    0    1

Byte 1      0    0    d    i    0    0    0    0

Byte 2           Logical Block Address (MSB)

Byte 3              Logical Block Address

Byte 4              Logical Block Address

Byte 5           Logical Block Address (LSB)

Byte 6      0    0    0    0    0    0    0    0

Byte 7                 Number of Blocks

Byte 8                 Number of Blocks

Byte 9      0    0    0    0    0    0    0    0

The argument following a SEARCH command is presented in table 9-19; a def-

inition of the required data in the argument is presented in table 9-20.

9-45

BFISD 8079

Table 9-19.  Search Command Argument

BIT         7    6    5    4    3    2    1    0

Byte 0               Record Size  (MSB)

Byte 1                  Record Size

Byte 2                  Record Size

Byte 3               Record Size  (LSB)

Byte 4           First Record Offset  (MSB)

Byte 5              First Record  Offset

Byte 6              First Record  Offset

Byte 7           First Record Offset  (LSB)

Byte 8            Number of Records (MSB)

Byte 9               Number of Records

Byte 10              Number of Records

Byte 11           Number of Records (LSB)

Byte 12         Search Argument Length  (MSB)

Byte 13            Search Argument Length

Byte 14        Search Field Displacement (MSB)

Byte 15           Search Field Displacement

Byte 16           Search Field Displacement

Byte 17        Search Field Displacement (LSB)

Byte 18             Pattern Length (MSB)

Byte 19                Pattern Length

Byte 20                 Data Pattern

*

•

•

Byte M+19               Data Pattern

9-46

BFISD 8079

Table 9-20.  Search Command Argument  Required Data

BYTES                                  PARAMETER

0 to 3             Record Size  (bytes)  - This  must  equal  the blocksize

or zero.  Zero will  be taken to  mean the format

blocksize.

4 to 7             First Record Offset  (bytes) - This must be zero.

8 to 11            Number of Records -  This  must be less than or equal

to the number of blocks specified in the command and

greater than zero.  The search will terminate upon a

match or when the smaller value is encountered.

12 to 13           Search Argument Length (bytes) - The number of bytes

in the following search  argument.  Must equal the

pattern length plus  six.

14 to 17           Search Field Displacement - The  displacement  from

the beginning of the record to the first byte to be

compared.  Must be  zero.

18 to 19           Pattern Length (M bytes)  -  The number  of bytes in

the following data  pattern to be compared with a

like size field in each record.  Pattern length must

equal blocksize.

20 to M+19         Data Pattern - A variable length field of M bytes up

to blocksize minus displacement bytes.  The pattern

must be one block long.

9-47/48

BFISD 8079

SECTION X

# REFERENCE DATA

FIGURE                          TITLE                                 PAGE

10-1    PCBA, Central Microprocessor Board                           10-2

10-2    Logic Diagram, Central Microprocessor Board (59 drawings)    10-3

10-1

BFISD 8079

## PCBA, Central Microprocessor Board

Figure  10-1.  PCBA, Central Microprocessor Board

10-2

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 1 of 58)

10-3

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 2 of 58)

10-4

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 3 of 58)

10-5

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 4 of 58)

10-6

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 5 of 58)

10-7

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 6 of 58)

10-8

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 7 of 58)

10-9

BFISD 8079

Figure 10-2. Logic Diagram, Central Microprocessor Board (Sheet 8 of 58)

10-10

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 9 of 58)

10-11

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 10 of 58)

10-12

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 11 of 58)

10-13

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 12 of 58)

10-14

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 13 of 58)

10-15

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 14 of 58)

10-16

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 15 of 58)

10-17

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 16 of 58)

10-18

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 17 of 58)

10-19

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 18 of 58)

10-20

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 19 of 58)

10-21

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 20 of 58)

10-22

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet  21 of 58)

10-23

BFISD 8079

Figure  10-2.  Logic Diagram, Central Microprocessor Board (Sheet 22 of 58)

10-24

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 23 of 58)

10-25

BFISD 8079

Figure  10-2.  Logic Diagram, Central Microprocessor Board (Sheet 24 of 58)

10-26

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 25 of 58)

10-27

BFISD 8079

Figure  10-2. Logic Diagram, Central Microprocessor Board (Sheet 26 of 58)

10-28

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet  27 of 58)

10-29

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 28 of 5)

10-30

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 28.1 of 58)

10-31

BFISD 8079

Figure 10-2. Logic Diagram, Central Microprocessor Board (Sheet 29 of 58)

10-32

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 30 of 58)

10-33

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 31 of 58)

10-34

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 32 of 58)

10-35

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 33 of 58)

10-36

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 34 of 58)

10-37

BFISD 8079

Figure 10-2. Logic Diagram, Central Microprocessor Board (Sheet 35 of 58)

10-38

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 36 of 58)

10-39

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 37 of 58)

10-40

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 38 of 58)

10-41

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 39 of 58)

10-42

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board  (Sheet 40 of 58)

10-43

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 41 of 58)

10-44

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 42 of 58)

10-45

BFISD 8079

Figure  10-2. Logic Diagram, Central Microprocessor Board (Sheet 43 of 58)

10-46

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 44 of 58)

10-47

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 45 of 58)

10-48

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 46 of 58)

10-49

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 47 of 58)

10-50

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 48 of 58)

10-51

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 49 of 58)

10-52

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board  (Sheet 50 of 58)

10-53

BFISD 8079

Figure  10-2.  Logic Diagram, Central Microprocessor Board (Sheet 51 of 58)

10-54

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 52 of 58)

10-55

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 53 of 58)

10-56

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 54 of 58)

10-57

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 55 of 58)

10-58

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 56 of 58)

10-59

BFISD 8079

Figure  10-2.  Logic Diagram, Central Microprocessor Board (Sheet 57 of 58)

10-60

BFISD 8079

Figure 10-2.  Logic Diagram, Central Microprocessor Board (Sheet 58 of 58)

10-61/62

BFISD 8079

## Memory Array PCBA

Figure 10-3.  Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 1 of 9)

10-63

BFISD 8079

Figure 10-3. Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 2 of 9)

10-64

BFISD 8079

Figure 10-3.  Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 3 of 9)

10-65

BFISD 8079

Figure 10-3.  Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 4 of 9)

10-66

BFISD 8079

Figure 10-3. Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 5 of 9)

10-67

BFISD 8079

Figure 10-3. Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 6 of 9)

10-68

BFISD 8079

Figure 10-3. Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 7 of 9)

10-69

BFISD 8079

Figure 10-3. Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 8 of 9)

10-70

BFISD 8079

Figure 10-3.  Logic Diagram, Memory Array PCBA, 903369 Rev. A (Sht. 9 of 9)

10-71/72

BFISD 8079

## Winchester Disk Controller

Figure 10-4. Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 1 of 15)

10-73

BFISD 8079

Figure 10-4.   Logic Diagram,  Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 2 of 15)

10-74

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 3 of 15)

10-75

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev.  C (Sht. 4 of 15)

10-76

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 5 of 15)

10-77

BFISD 8079

Figure  10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 6 of 15)

10-78

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 7 of 15)

10-79

BFISD 8079

Figure 10-4. Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 8 of 15)

10-80

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 9 of 15)

10-81

BFISD 8079

Figure  10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 10 of 15)

10-82

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 11 of 15)

10-83

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 12 of 15)

10-84

PAGE MISSING

This Page was misprinted in my original documentation, is was page 10-85 and 10-87 printed on one page

10-85

PAGE MISSING

This Page was misprinted in my original documentation, is was page 10-85 and 10-63 printed on one page

10-86

BFISD 8079

Figure 10-4.  Logic Diagram, Winchester Disk Controller PCBA, 903461

Rev. C (Sht. 15 of 15)

10-87/88

BFISD 8079

## 4-Way Controller

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 1 of 10)

10-89

BFISD 8079

Figure  10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 2 of 10)

10-90

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 3 of 10)

10-91

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 4 of 10)

10-92

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 5 of 10)

10-93

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 6 of 10)

10-94

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 7 of 10)

10-95

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 8 of 10)

10-96

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 9 of 10)

10-97

BFISD 8079

Figure 10-5.  Logic Diagram, 4-Way Controller PCBA, 903391 Rev. E

(Sht. 10 of 10)

10-98

BFISD 8079

## Local Area Network Controller

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 2 of 20)

10-99

BFISD 8079

Figure 10-6.  Logic Diagram,  Local Area Network Controller PCBA

903410 Rev. C (Sht. 3 of 20)

10-100

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 4 of 20)

10-101

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 5 of 20)

10-102

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 6 of 20)

10-103

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 7 of 20)

10-104

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 8 of 20)

10-105

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area  Network Controller PCBA

903410 Rev. C (Sht. 9 of 20)

10-106

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 10 of 20)

10-107

BFISD 8079

Figure 10-6. Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 11 of 20)

10-108

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 12 of 20)

10-109

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 13 of 20)

10-110

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 14 of 20)

10-111

BFISD 8079

Figure  10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 15 of 20)

10-112

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 16 of 20)

10-113

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 17 of 20)

10-114

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 18 of 20)

10-115

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 19 of 20)

10-116

BFISD 8079

Figure 10-6.  Logic Diagram, Local Area Network Controller PCBA

903410 Rev. C (Sht. 20 of 20)

10-117/118

BFISD 8079

## Magnetic Cartridge Streamer Controller

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (2 of 24)

10-119

BFISD 8079

Figure  10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (3 of 24)

10-120

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (4 of 24)

10-121

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (5 of 24)

10-122

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (6 of 24)

10-123

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (7 of 24)

10-124

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (8 of 24)

10-125

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (9 of 24)

10-126

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (10 of 24)

10-127

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (11 of 24)

10-128

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (12 of 24)

10-129

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (13 of 24)

10-130

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (14 of 24)

10-131

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (15 of 24)

10-132

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (16 of 24)

10-133

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (17 of 24)

10-134

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (18 of 24)

10-135

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (19 of 24)

10-136

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (20 of 24)

10-137

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (21 of 24)

10-138

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (22 of 24)

10-139

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (23 of 24)

10-140

BFISD 8079

Figure 10-7.  Logic Diagram, Magnetic Cartridge Streamer Controller PCBA

903427 Rev. A (24 of 24)

10-141/142

BFISD 8079

## Power Supply Input Module

Figure 10-8.  Logic Diagram, Power Supply Input Module PCBA,

903443 Rev. E (Sht. 1 of 1)

10-143/144

BFISD 8079

## Power Supply Output Module

Figure 10-9.  Logic Diagram, Power Supply Output Module PCBA,

903446, Rev. B (Sht. 2 of 6)

10-145

BFISD 8079

Figure 10-9.  Logic Diagram, Power Supply Output Module PCBA,

903446, Rev. B (Sht. 3 of 6)

10-146

BFISD 8079

Figure 10-9.  Logic Diagram, Power Supply Output Module PCBA,

903446, Rev. B (Sht. 4 of 6)

10-147

BFISD 8079

Figure  10-9.  Logic Diagram, Power Supply Output Module PCBA,

903446, Rev. B (Sht. 5 of 6)

10-148

BFISD 8079

Figure 10-9.  Logic Diagram, Power Supply Output Module PCBA,

903446, Rev. B (Sht. 6 of 6)

10-149/150

BFISD 8079

## Power Supply Control Module

Figure 10-10.  Logic Diagram, Power Supply Control Module PCBA,

903404, Rev. A (Sht. 2 of 3)

10-151

BFISD 8079

Figure 10-10.  Logic Diagram, Power Supply Control Module PCBA,

903404, Rev. A (Sht. 3 of 3)

10-152